## Slide 1: Motion Planning for SpaceCraft
Andrew Best UNC Chapel Hill

## Slide 2: Introduction
Discuss problems and concepts specific to motion planning in space
  Motion planning background
  Specific challenges to space
  Path planners
    Planetary Orbital Environment and Deep Space

## Slide 3: Motivation
Space travel is the future of human civilization
Satellite networks power critical technologies
Long missions will require effective and trustworthy autopilot
Motion planning in space is difficult
Space travel is expensive
  Cost to Low Earth Orbit ~$9000 / kg
  RP-1 .81 kg/l
  $7290 per liter waste ($630)
Notes: Our planet is increasing crowded and decreasingly capable of sustaining life, we need to travel the starts
.
Space travel is REALLY expensive. Cost to LEO is $9000 per kg (averaged from Wikipedia)
RP-1 has a density of .81 kg/l meaning each wasted liter due to bad planning costs roughly $720
or… for liquid hydrogen $630
either way, it is very costly to mess this up, because these costs assume we can get more fuel to the ships

## Slide 4: Motion Planning
Wiki: process of breaking down a desired movement task into discrete motions that satisfy movement constraints and possibly optimize some aspect of the movement.
common constraints:
  Collision-free
  kinematics
  Dynamics (external system forces)

## Slide 5: Motion Planning problems
Manipulators
N-rotors (4,8, etc)
Roomba
Surgical Robots

## Slide 6: Motion Planning problems
Bipeds
Autonomous Cars
  https://www.youtube.com/watch?v=8h_W-KtQics
  18:00 – 23:00
  https://www.youtube.com/watch?v=bnv5JP8gL_k
  07:00 – 13:00

## Slide 7: General Abstraction
s = () configuration of robot in the world
set of all states, timestep i, state at
Kinematics: state evolution given control inputs
Path is set of all intermediate states between and
Notes: Given some s which represents a vector of the configuration parameters (sufficient parameters to get a complete picture of the system state)
Some discrete timestep t_i and state s_i
the “path” is the set of all intermediate states the agent / robot/ actor will pass through from t0 to T

## Slide 8: Methods to Compute a Path
PRM – Probabilstic Roadmap
Gradient Decent
RRT – Randomly-Exploring Rapid Tree
Notes: Here I will give a SHORT overview of these three techniques

## Slide 9: Planning in Space: 2 cases
Planning in space divided into two environments
  Deep-Space
    No state- dependent forces in open loop
    Reduces to double integrator control problem
      ODE like our ballistics
  Planetary Orbital Environment POE
    Strong dynamic forces
    Search For Passive Relative Orbits, Active Relative Orbits, or reconfigurations
Notes: Passive relative orbit – maintain position constraints without open-loop control
ARO - maintain constraints WITH open-loop control
Reconfiguration – search for optimal paths from ARO to PRO or ARO to ARO

## Slide 10: Planning in Space: 2 cases
Additional POE Complications
  Linear thrust produces curved trajectories
  Thrust changes eccentricity of orbit as well as moving spacecraft along path
Additional Terminology:
  Controllability: For any two configurations , there exists a time interval T and set of inputs to the control equations so that is the initial configuration and is the final.
Notes: [Caltech motion planning paper] - controllability
Passive relative orbit – maintain position constraints without open-loop control
ARO - maintain constraints WITH open-loop control
Reconfiguration – search for optimal paths from ARO to PRO or ARO to ARO

## Slide 11: Distinction: planning in space
Motion planning tends to assume no drift
  State evolution is only dependent on control inputs and kinematic
  Momentum is neglected from state to state
  Motion planning is symmetric
    Undirected graphs can be used to represent configuration spaces
Notes: Now, it gets complicated, spacecraft have drift
[stanford drift paper]

## Slide 12: Distinction: planning in space
Spacecraft have drift!
  Three key features:
    Asymmetric state evolution functions
    Inevitable collision state sets
    For some states, no evolution exists s.t.
  Mathematically:
      configuration space
      control space
    Called LQDMP (Linear Quadratic DMP)
Notes: Now, it gets complicated, spacecraft have drift
schmerling linear affine drift dynamics
For some states, it is not possible to stop v = 0
A is state Dynamics
B is kinematics
U is control inputs
Linear-Quadratic Dynamic Motion Planning

## Slide 13: Distinction: planning in space
Generally not optimizing time/path length
  Balancing a complex cost function of time + energy cost
  Additional constraints:
    Sun exposure
    Solar Pressure forces
    Plume and glint avoidance
Not all directions are equivalent
  Cost functions for given motions vary by dynamics

## Slide 14: Formation Flying
Used to control multiple spacecraft performing a single mission
  Additional constraints on fuel consumption and balance
  6N DOF problem
  Generally reduced by leader-follower algorithms
    One craft is master, plans in POE frame
    Others are followers, plan in master-relative frame

## Slide 15: Planning in Space: 2 cases
Formation Flying Passive Relative Orbit
https://www.youtube.com/watch?v=b3y_NaMIymI
Notes: Passive relative orbit – maintain position constraints without open-loop control
ARO - maintain constraints WITH open-loop control
Reconfiguration – search for optimal paths from ARO to PRO or ARO to ARO

## Slide 16: Motion Planner examples
FMT*
  Fast-Marching Trees
  Single-Query algorithm
  Greedy RRT based on arbitrary cost function
  Step 1:
    Optimal next node (ignore collisions)
  Step 2:
    Connect collision free neighbors
Notes: [Fmt Stanford paper]
Few things to note. Tree expands outward, nodes can be connected by a distance over a neighbor radius.
Look for optimatal (ignore collisions), then check best, store it if no collide

## Slide 17: Motion Planner examples
DFMT*
  Dynamic Fast Marching Trees
  Principal difference: neighborhood locality is now defined by differential constraints, not simply Euclidian distance
  More expensive, not realtime, but functional
Notes: [Fmt Stanford paper]
Few things to note. Tree expands outward, nodes can be connected by a distance over a neighbor radius.
Look for optimatal (ignore collisions), then check best, store it if no collide

## Slide 18: Motion Planner Examples
RRT
Notes: 2d cross section of a search space

## Slide 19: Motion Planner Examples
RRT
Notes: 2d cross section of a search space

## Slide 20: Motion Planner Examples
RRT
Notes: 2d cross section of a search space

## Slide 21: Motion Planner Examples
RRT
Notes: 2d cross section of a search space

## Slide 22: Motion Planner Examples
RRT
Notes: 2d cross section of a search space

## Slide 23: Motion Planner Examples
RRT
Notes: 2d cross section of a search space

## Slide 24: Motion Planner Examples
RRT
Notes: 2d cross section of a search space

## Slide 25: Motion Planner Examples
RRT
Notes: 2d cross section of a search space

## Slide 26: Motion Planner Examples
RRT
Notes: 2d cross section of a search space

## Slide 27: Motion Planner Examples
RRT
Notes: 2d cross section of a search space

## Slide 28: Motion Planner Examples
RRT
Notes: 2d cross section of a search space

## Slide 29: Motion Planner Examples
DFMT*
Notes: 2d cross section of a search space

## Slide 30: Motion Planner Examples
DFMT*
Notes: 2d cross section of a search space

## Slide 31: Motion Planner Examples
DFMT*
Notes: 2d cross section of a search space

## Slide 32: Motion Planner Examples
DFMT*
Notes: 2d cross section of a search space

## Slide 33: Motion Planner Examples
DFMT*
Notes: 2d cross section of a search space

## Slide 34: Motion Planner Examples
DFMT*
Notes: 2d cross section of a search space

## Slide 35: Motion Planner Examples
DFMT*
Notes: 2d cross section of a search space

## Slide 36: Motion Planner Examples
DFMT*
Notes: 2d cross section of a search space

## Slide 37: Motion Planner Examples
DFMT*
Notes: 2d cross section of a search space

## Slide 38: Motion Planner Examples
DFMT*
Notes: 2d cross section of a search space

## Slide 39: Motion Planner Examples
DFMT*
Notes: 2d cross section of a search space

## Slide 40: Motion Planner examples
Potential Field Method
  Like gradient decent, but using the superposition of dynamic forces as potential fields
  Theoretically applied in continuous and discrete control scenarios
  Relies on a vector of free parameters to be arbitrarily defined reflecting the impact of the dynamic constraints
Notes: http://eprints.gla.ac.uk/6/1/McInnes,_C._53__2004.pdf?origin=publication_detail
Continuous and discrete do not mean what they do in simulation. Discrete means boost and coast functions.

## Slide 41: Motion Planner examples
Potential Field Method
Paths computed by potential field
method

## Slide 42: Motion Planner examples
Geometric Reduction Planning
  Plans on a reduced constraint set
  Adapts computed path to dynamically feasible path
  Can be run in real-time
    Caveat: Paths computed in reduced set are not always dynamically feasible
  Provably sub-optimal
Notes: “2-shot planner”
Not unlike crowd simulation, run un a reduced complexity system, then adapt to the dynamic system once a path is computed.
We take a complex satellite with reaction wheels for example, and reduce it to a spheroid, so as to simplify our computation. We can then detect and respond to errors caused by the rotational dynamics.

## Slide 43: DS motion Planning DEMO
https://www.youtube.com/watch?v=4a3eY5siRRk
11:00 -
Notes: Exampe of deep space manoever

## Slide 44: Rendezvous Demo
https://www.youtube.com/watch?v=2C_GHIHbUyQ
Notes: Pro transfer orbit

## Slide 45: Conclusions
Motion planning for spacecraft uses algorithms and techniques common to many dynamical systems
  Straightforward to compute plans, if you can accurately describe the dynamics (which we have a very limited capacity to do)
  Few real-time methods exist, but work is continuing in this area by preprocessing
  Deep space motion planning is much easier that Planetary Orbital Environment, but only theoretical presently

## Slide 46: Future Work
Motion planning for extended constraints
  Solar Pressure
  Sun exposure optimization
  Formation Flying Guidance optimization
Real-time methods
Better dynamics approximation / understanding
Hardware tests of formation control

## Slide 47: KSP Demo
Rendezvous and docking in KSP http://youtu.be/aHlSmepxx-o
Notes: Kerbal Space Program is a popular space sim with linnear affine dynamics and simplified well defined dynamics

## Slide 48: KSP Demo
Rondezvous and docking in KSP
http://youtu.be/YXMYzTEH4cQ
Notes: Kerbal Space Program is a popular space sim with linnear affine dynamics and simplified well defined dynamics

## Slide 49: Thank you
Questions?