## Slide 1
Wireless and Mobile Systems
for the IoT
Nirupam Roy
M-W 2:00-3:15pm
Online
CMSC 818W : Fall 2020
Lecture 4.3: GPS - I
This zoom session is being recorded.

## Slide 2
Notes: The nominal GPS configuration consists of a network of 24 satellites in high orbits around the Earth, but up to 30 or so satellites may be on station at any given time. Each satellite in the GPS constellation orbits at an altitude of about 20,000 km from the ground, and has an orbital speed of about 14,000 km/hour (the orbital period is roughly 12 hours - contrary to popular belief, GPS satellites are not in geosynchronous or geostationary orbits). The satellite orbits are distributed so that at least 4 satellites are always visible from any point on the Earth at any given instant (with up to 12 visible at one time).
Geostationary orbits are near the equator and hence does not provide enough coverage.

## Slide 5
Global Navigation Satellite Systems:

## Slide 6
Global Navigation Satellite Systems:
https://www.gps.gov

## Slide 7
Global Navigation Satellite Systems:
Source: https://www.gps.gov

## Slide 8
Location estimation

## Slide 9
Ref: Understanding GPS Principles and Applications , 2nd Edition
Ranging and localization

## Slide 10
Ref: Understanding GPS Principles and Applications , 2nd Edition
Ranging and localization

## Slide 11
Ref: Understanding GPS Principles and Applications , 2nd Edition
Ranging and localization
What if the clock is not synchronized?

## Slide 12
Ref: Understanding GPS Principles and Applications , 2nd Edition
Independent measurement error

## Slide 13
Ref: Understanding GPS Principles and Applications , 2nd Edition
Ranging and localization: Common clock offset

## Slide 14
Triangulation vs Trilateration

## Slide 15
Triangulation
base1
observer
base2
𝚹1
𝚹1
𝚹2
𝚹2

## Slide 16
Trilateration
d
base1
observer
base2
d’

## Slide 17
Trilateration
d

## Slide 18
GPS Satellite Constellation
-- 24 satellites
Baseline configuration
-- 6 orbital planes, 4 satellites in each plane
-- 60° separation between planes
-- Orbital radius approx. 26,600 km
Geo-stationary ?
Notes: https://www.gpsworld.com/origins-gps-part-1/
https://pdfs.semanticscholar.org/d6f5/812c9f91d68862cf3e2a8af6a3f9db14ba2b.pdf

## Slide 19
Satellite orbits

## Slide 20
Satellite orbits

## Slide 21
GPS Satellite Constellation
-- 24 satellites
Baseline configuration
-- 6 orbital planes, 4 satellites in each plane
-- 60° separation between planes
-- Orbital radius approx. 26,600 km
-- Orbital period 11h 58m (half day)
at a speed of around 14000km/s

## Slide 22
GPS Satellite Constellation
Planar projection of the constellation
( 0000h, July 1, 1993 UTC)
Notes: The nominal GPS configuration consists of a network of 24 satellites in high orbits around the Earth, but up to 30 or so satellites may be on station at any given time. Each satellite in the GPS constellation orbits at an altitude of about 20,000 km from the ground, and has an orbital speed of about 14,000 km/hour (the orbital period is roughly 12 hours - contrary to popular belief, GPS satellites are not in geosynchronous or geostationary orbits). The satellite orbits are distributed so that at least 4 satellites are always visible from any point on the Earth at any given instant (with up to 12 visible at one time).
Geostationary orbits are near the equator and hence does not provide enough coverage.

## Slide 23
GPS Satellite Constellation
Planar projection of the constellation
( 0000h, July 1, 1993 UTC)
At least 4 satellites are always visible from any point on the Earth at any given instant
Notes: The nominal GPS configuration consists of a network of 24 satellites in high orbits around the Earth, but up to 30 or so satellites may be on station at any given time. Each satellite in the GPS constellation orbits at an altitude of about 20,000 km from the ground, and has an orbital speed of about 14,000 km/hour (the orbital period is roughly 12 hours - contrary to popular belief, GPS satellites are not in geosynchronous or geostationary orbits). The satellite orbits are distributed so that at least 4 satellites are always visible from any point on the Earth at any given instant (with up to 12 visible at one time).
Geostationary orbits are near the equator and hence does not provide enough coverage.

## Slide 24
Pseudo-Random Noise (PRN) code
PRN code (Coarse/Acquisition or C/A code)
Each satellite is assigned a unique CDMA code.
Notes: In 1928, Warren Marrison of Bell Telephone Laboratories developed the first quartz-crystal clock. With accuracies of up to 1 second in 30 years
Atomic clock:
Use of GPS clock: Wireless communication, TV broadcast, timestamping business transaction, frequency hopping

## Slide 25
Signal detection
Amplitude
Time/Sample
Amplitude
Time/Sample
Transmitter signal
Receiver signal

## Slide 26
Signal detection
Signal matching
Correlation
Received signal
Transmit signal template

## Slide 27
Signal detection
Correlation

## Slide 28
Pseudo-Random Noise (PRN) code
Notes: In 1928, Warren Marrison of Bell Telephone Laboratories developed the first quartz-crystal clock. With accuracies of up to 1 second in 30 years
https://pdfs.semanticscholar.org/d6f5/812c9f91d68862cf3e2a8af6a3f9db14ba2b.pdf
Atomic clock:
Use of GPS clock: Wireless communication, TV broadcast, timestamping business transaction, frequency hopping

## Slide 29
Propagation Delay
or
Time of Flight (ToF)

## Slide 30
Time of Flight (ToF)
Known starting time of the code

## Slide 31
Time of Flight (ToF)

## Slide 32
Time of Flight (ToF)

## Slide 33
Time of Flight (ToF)
Δt

## Slide 34
Range = propagation delay X speed of light
= Δt x C (C = speed of light, ~ 3x108 m/s)

## Slide 35
Time of Flight (ToF)
Starting time, t
Δt

## Slide 36
Time of Flight (ToF)

## Slide 37
Time of Flight (ToF)
Can we rely on the clocks?

## Slide 38
Mechanical clock: Oscillation of pendulum
Crystal clock: Electrical circuit that uses a piezoelectric crystal vibrating at a precise frequency.
(accuracy of 1 second in 30 years)
Clock
Atomic clock: Duration of 9,192,631,770 periods of the radiation from a Cesium 133 atom.
(accuracy of 1 second in more than 100 million years)
Notes: In 1928, Warren Marrison of Bell Telephone Laboratories developed the first quartz-crystal clock. With accuracies of up to 1 second in 30 years
Atomic clock:
Use of GPS clock: Wireless communication, TV broadcast, timestamping business transaction, frequency hopping

## Slide 39
Estimated propagation delay X speed of light
= Pseudo-Range
Satellite clock and receiver clocks are not synchronized

## Slide 40
Calculating range
Pseudo-range from ith satellite = 𝝆i
User’s true location = (xu, yu, zu)
Satellite’s location = (xi, yi, zi)

## Slide 41
Calculating range
Pseudo-range from ith satellite = 𝝆i
User’s true location = (xu, yu, zu)
Satellite’s location = (xi, yi, zi)

## Slide 42
Calculating range
Pseudo-range from ith satellite = 𝝆i
User’s true location = (xu, yu, zu)
Satellite’s location = (xi, yi, zi)

## Slide 43
Calculating range
Pseudo-range from ith satellite = 𝝆i
User’s true location = (xu, yu, zu)
Satellite’s location = (xi, yi, zi)
User’s time offset from satellite = tu

## Slide 44
Calculating range
Pseudo-range from ith satellite = 𝝆i
User’s true location = (xu, yu, zu)
Satellite’s location = (xi, yi, zi)
User’s time offset from satellite = tu