## Slide 1
Wireless and Mobile Systems
for the IoT
Nirupam Roy
M-W 2:00-3:15pm
Online
CMSC 818W : Fall 2020
Lecture 4.4: GPS - II
This zoom session is being recorded.

## Slide 2
Midterm
Class Projects
The course after the midterm

## Slide 3
Calculating range
Pseudo-range from ith satellite = 𝝆i
User’s true location = (xu, yu, zu)
Satellite’s location = (xi, yi, zi)
User’s time offset from satellite = tu

## Slide 4
How to find the satellite’s location
Ephemeris and Almanac
Information about the satellite’s precise location and trajectory are embedded in the transmitted data.
Almanac:
Long term orbit course of the satellite.
Used determine which satellites are visible.
Every satellite broadcasts this data for every satellites.
Valid for months.

## Slide 5
How to find the satellite’s location
Ephemeris and Almanac
Information about the satellite’s precise location and trajectory are embedded in the transmitted data.
Ephemeris:
Short term location of a satellite at a time of the day.
Used determine the location of a satellite.
Every satellite broadcasts its own data.
Valid for 2-4 hours.

## Slide 6
GPS signal modulation

## Slide 7
An illustration of GPS signal modulation scheme
Notes: L1 =1.575 GHz towards the Earth. The bit-rate of data packets is a mere 50 bps, but the bits are modulated with a higher frequency (1MHz) signal for detecting propagation delays.

## Slide 8
GPS signal modulation
C/A code:
1023 bits long
Repeats every millisecond
P code:
6.1871 X 1012 bits long
Repeats every week
Encoded for anti-spoofing

## Slide 9
The frame content of a GPS packet of length 1500 bits
Notes: Thus, the C/A code repeats every millisecond, resulting in 20 repetitions of the C/A code for each data bit sent. The purpose of the C/A code is to allow a receiver to identify the sending satellite and to estimate how long it took the signal to propagate from that satellite to the receiver. Typically, the GPS signals take from 64 to 89 milliseconds to travel from a satellite to the Earth’s surface. Since light travels at 300 km/ms, in order to obtain an accurate distance measurement, the receiver must estimate the signal propaga- tion delay to the microsecond level. The millisecond (NMS) and sub-millisecond (subMS) parts of the propagation time are derived very differently: the NMS is decoded from the packet frames, while the subMS propagation time is detected at the C/A code level using correlations.

## Slide 10
Time-to-First-Fix
Time-To- First-Fix (TTFF) is the elapsed time between turning on a receiver and obtaining the first location fix.

## Slide 11
Time-to-First-Fix
Time-To- First-Fix (TTFF) is the elapsed time between turning on a receiver and obtaining the first location fix.
1. Satellite Acquisition
Search with all satellites PRN codes (Coarse/Acquisition or C/A code) to find which satellites are visible at that time. Once found need to decode ephemeris and timing information. Need to adjust for unknown Doppler shifts.

## Slide 12
Time-to-First-Fix
Time-To- First-Fix (TTFF) is the elapsed time between turning on a receiver and obtaining the first location fix.
1. Satellite Acquisition
Search with all satellites PRN codes (Coarse/Acquisition or C/A code) to find which satellites are visible at that time. Once found need to decode ephemeris and timing information. Need to adjust for unknown Doppler shifts.
2. Location estimation
Finding propagation delay and solve the set of equations for location.

## Slide 13
Time-to-First-Fix
Time-To- First-Fix (TTFF) is the elapsed time between turning on a receiver and obtaining the first location fix.
1. Satellite Acquisition
Satellite Acquisition is a computationally intensive process due to the large code phase and Doppler search space. It may take more than 5 minutes.
Doppler freq.
Code delay

## Slide 14
Assisted GPS (A-GPS or aGPS)

## Slide 15
Notes: MSC = Mobile Switching Center

## Slide 16
Assisted GPS (A-GPS or aGPS)
Mobile Station Based (MSB):
Server at the station provides information (network time, almanac etc.) to the device for faster TTFF.
2) Mobile Station Assisted (MSA):
Server at the station calculates the location for the device.

## Slide 17
Differential GPS

## Slide 18
GPS ranging error

## Slide 19
GPS ranging error
Error due to unpredictable signal delay

## Slide 20
Differential GPS

## Slide 21
Differential GPS
e.g., long term average of GPS location
(1) Estimate the correct location of the reference
24 hour estimated location scatter plot

## Slide 22
Differential GPS
e.g., long term average of GPS location
(1) Estimate the correct location of the reference

## Slide 23
Differential GPS
(2) Estimate the error in received GPS signal using the location of the base station and location of the satellite.
Error
Repeat for all visible satellites

## Slide 24
Differential GPS
(3) Apply adjustment to the received GPS signal to reduce error
Send the adjustment info.

## Slide 25
Differential GPS
24 hour estimated location scatter plot
meter
meter
Regular GPS estimate (red)
Differential GPS
with geo-stationary satellite (green)
Differential GPS
with static base station (purple)

## Slide 26
Inertial Sensor (IMU) Integrated GPS

## Slide 27
GPS blockage and multipath in cities

## Slide 28
GPS blockage and multipath in cities
Regions of unreliable GPS location

## Slide 29
Dead reckoning
Track movements with inertial sensors
Location estimate drifts
-- Use reliable GPS estimates to correct inertial drift
-- Use inertial dead-reckoning in GPS regions

## Slide 30
Summary of localization techniques

## Slide 31
[Ref] http://downloads.hindawi.com/journals/jcnc/2013/185138.pdf
Localization techniques

## Slide 32
Inertial tracking
Localization techniques

## Slide 33
Localization techniques: Proximity

## Slide 34
Localization techniques: Scene analysis

## Slide 35
Localization techniques: Scene analysis

## Slide 36
Localization techniques: Scene analysis

## Slide 37
Localization techniques: Scene analysis

## Slide 38
Inertial tracking
Localization techniques

## Slide 39: COIN-GPS: Indoor Localization from Direct GPS Receiving
Shahriar Nirjon
University of Virginia
Jie Liu, Gerald DeJean, Bodhi Priyantha,
Yuzhe Jin, and Ted Hart
Microsoft Research, Redmond
Case Study

## Slide 40: ‘GPS does not work indoors’ - Everyone
Why?

## Slide 41: GPS Signal-Strength
500 W
1.4 x 10-16 W

## Slide 42: GPS Signal-Strength Indoors
1 to 10 attowatts
100 attowatts
We cannot decode packets (e.g. time stamps, navigational data)
Notes: Atto = 10^-18

## Slide 43: Heterogeneous Building Materials
Concrete
Wood
Glass
Steel
…

## Slide 44: GPS Signals Thorough Building Materials
2D electric field plots of a GPS signal propagating
through different materials
Bad
Good
E+
E-

## Slide 45: Strategy and Leverages
GPS
Use no data from the GPS packets.
Opportunistically sample signals from multiple directions.

## Slide 46: Strategy and Leverages
Leverage the slow movement of indoor receivers
Leverage the power of cloud computing

## Slide 47: COIN-GPS: Cloud Offloaded Indoor GPS
We mechanically steer the antenna with a PC and collect GPS samples for offline processing

## Slide 48: 1. The Front End
We use a high-gain, directional antenna to get GPS signals from a certain direction.
Properties:
10 x 10 Sq. Inch
1575.42 MHz
12.3 dBi gain
Half power beam width: 35°

## Slide 49: 2. The Back-End Processing
Satellite
Acquisition
From
Weak Signals
Location
Estimation
From
Inadequate
Satellites

## Slide 50: Detecting Satellites Indoor

## Slide 51: Detecting Satellites
The standard acquisition process:
The Sender

## Slide 52: Detecting Satellites (Instant GPS)
The Receiver
1 ms
demodulated GPS signals
Local C/A codes
…
*
Sat 01
*
Sat 32
Code Phase
The standard acquisition process: (Instant GPS)

## Slide 53: Satellite Acquisition from Weak Signals
The correlation plot in reality:
K = 1

## Slide 54: Satellite Acquisition from Weak Signals
The correlation plot (integrated over multiple ms)
K = 1
K = 2
K = 4
K = 8

## Slide 55: 2. The Back-End Processing
Satellite
Acquisition
From
Weak Signals
Location
Estimation
From
Inadequate
Satellites

## Slide 56: Required Satellites
How many satellites do we need?

## Slide 57: Required Satellites (in Various Techniques)
How many satellites do we need?
Type | How Fast? | Unknowns
GPS | 30 sec | 
COIN-GPS | 1 ms | 

## Slide 58: Required Satellites (in Various Techniques)

## Slide 59: Required Satellites (in Various Techniques)

## Slide 60: Required Satellites (in Various Techniques)
How many satellites do we need?
Type | How Fast? | Unknowns
GPS | 30 sec | X, Y, Z, B, C
COIN-GPS | 1 ms | 
Fig. Common bias error

## Slide 61: Required Satellites (in Various Techniques)
How many satellites do we need?
Type | How Fast? | Unknowns
GPS | 30 sec | X, Y, Z, B, C
COIN-GPS | 1 ms | 
dt
C
Actual
Wrong
Fig. Coarse time error
800 m/s

## Slide 62: Required Satellites (in Various Techniques)
How many satellites do we need?
Type | How Fast? | Unknowns
GPS | 30 sec | X, Y, Z, B, C
COIN-GPS | 1 ms | X, Y, Z, B, C
dt
C
Actual
Wrong
Fig. Coarse time error
800 m/s

## Slide 63: Required Satellites (in Various Techniques)
How many satellites do we need?
Type | How Fast? | Unknowns
GPS | 30 sec | X, Y, Z, B, C
COIN-GPS | 1 ms | X, Y, Z, B, C
dt
C
Actual
Wrong
Fig. Coarse time error
800 m/s
So… for instant GPS, we need 5 visible satellites

## Slide 64: Acquired Satellites (Indoors)
How many satellites do we see indoors?

## Slide 65: Acquired Satellites (Indoors)
How many satellites do we see indoors?
Garmin Antenna
Our Antenna

## Slide 66: Acquired Satellites (Indoors)
How many satellites do we see indoors?
Garmin Antenna
Our Antenna
N or more visible satellites
%
But … 3 < 5

## Slide 67: Handling Inadequate Satellites Problem
Our Approach: Receive, Wait and Receive again

## Slide 68: Handling Inadequate Satellites Problem
Our Approach: Receive, Wait and Receive again
10:30.000 AM

## Slide 69: Handling Inadequate Satellites Problem
Our Approach: Receive, Wait and Receive again
10:30.000 AM

## Slide 70: Handling Inadequate Satellites Problem
Our Approach: Receive, Wait and Receive again
10:30.000 AM
10:30.500 AM

## Slide 71: Handling Inadequate Satellites Problem
Our Approach: Receive, Wait and Receive again
10:30.000 AM
10:30.500 AM

## Slide 72: Handling Inadequate Satellites Problem
Our Approach: Receive, Wait and Receive again
10:30.000 AM
10:30.500 AM

## Slide 73: Handling Inadequate Satellites Problem
Our Approach: Receive, Wait and Receive again
10:30.000 AM
10:30.500 AM

## Slide 74: Handling Inadequate Satellites Problem
The COIN-GPS formula:
For a stationary receiver, the required total number of visible GPS satellites for COIN-GPS is 2n + 3, where n is the number of independent readings and the same satellite acquired in different readings is considered different.
n | 2n+3
1 | 5
2 | 7
3 | 9
4 | 11

## Slide 75: Experimental Setup
5 places
35 indoor locations
8 – 10 directions

## Slide 76: Experimental Setup
5 places
35 indoor locations
8 – 10 directions
Ground truth:
  Floor map
  Bing maps
  Laser pointer

## Slide 77: Experimental Setup
5 places
35 indoor locations
8 – 10 directions
Ground truth:
  Floor map
  Bing maps
  Laser pointer
Baseline:
  Garmin antenna with CO-GPS.
Garmin

## Slide 78: Results: Home Depot
Chart: Location Estimation Error
A | 7.7
B | 6
C | 32.5
D | 3.7
Avg. | 12.475
A
B
C
D
System | Total Locations | Got Estimates
Garmin | 4 | None
Proposed | 4 | 4

## Slide 79: Results: Starbucks
A
B
Chart: Location Estimation Error
A | 1.7
B | 7.1
Avg. | 4.4
System | Total Locations | Got Estimates
Garmin | 2 | None
Proposed | 2 | 2

## Slide 80: Concluding Remarks
If not for consumers, how about indoor profiling?

## Slide 81: Concluding Remarks
Size does matter, if not phones – how about tabs?
Surface Pro Next ?

## Slide 82: Thank You