## Slide 1
Differentiable Autonomous Driving
Xijun Wang
11/04/2021

## Slide 2
Contents
End-to-End Autonomous Driving Background
Interpretable End-to-End Autonomous Driving with Differentiable Semantic Occupancy Representation

## Slide 3
Contents
End-to-End Autonomous Driving Background
Interpretable End-to-End Autonomous Driving with Differentiable Semantic Occupancy Representation

## Slide 4
Background | Traditional Stack
[1] CVPR 2021 Tutorial: All About Self-Driving
Maps
Sensors
Perception
Det
Track
Prediction
Long Term Predictions
Planning
Motion Trajectory
Control
Steering/Acceleration

## Slide 5
Background | End-to-end Stack
Maps
Sensors
Trainable, End to End
Plan Trajectory Control variables
Advantages: single system, low reaction time, trained end-to-end;
Disadvantages: lack of interpretability, difficult to incorporate prior knowledge (e.g., Rules of traffic);
[1] CVPR 2021 Tutorial: All About Self-Driving

## Slide 6
Background | End-to-end Stack | Input
RGB Image
Semantic Image
Strengths:
  Cheap sensor
  Suitable for 2D CNN
Weaknesses
  Affected by light conditions
  Lacking accurate 3D measurements
[1] CVPR 2021 Tutorial: All About Self-Driving
Image
Lidar
HD Map
Intention
…

## Slide 7
Background | End-to-end Stack | Input
LiDAR Birds-Eye-View
LiDAR Visibility
Strengths:
  Robust measurements
  Accurate 3D information
Weaknesses
  Lack some semantic information
  More Expensive
[1] CVPR 2021 Tutorial: All About Self-Driving
Image
LiDAR
HD Map
Intention
…

## Slide 8
Background | End-to-end Stack | Input
Rasterization
Strengths:
  Suit for 2D CNN
  Simple Pipeline
Weaknesses
  Hard to encode prior knowledge
Affordance
Strengths:
  Encode prior knowledge
Weaknesses
  Hand-craft features
[1] CVPR 2021 Tutorial: All About Self-Driving
Image
LiDAR
HD Map
Intention
…
Road mask
Speed limit
Notes: Road Mask Speed limit

## Slide 9
Background | End-to-end Stack | Input
High-Level Command
[1] CVPR 2021 Tutorial: All About Self-Driving
Image
LiDAR
HD Map
Intention
…

## Slide 10
Background | End-to-end Stack | Model
[1] CVPR 2021 Tutorial: All About Self-Driving
CNN
RNN
MLP
Transformer
…
Convolutional Neural Network
Strengths:
  Effective and Efficient
  Well studied and have a lots of options
Weaknesses
  Unfriendly for temporal information

## Slide 11
Background | End-to-end Stack | Model
[1] CVPR 2021 Tutorial: All About Self-Driving
CNN
RNN
MLP
Transformer
…
Recurrent Neural Network
Strengths:
  Friendly for temporal information
Weaknesses
  Unfriendly for efficient parallel computing；

## Slide 12
Background | End-to-end Stack | Model
[1] CVPR 2021 Tutorial: All About Self-Driving
CNN
RNN
MLP
Transformer
…
Multilayer Perceptron
Strengths:
  High capacity
  Global reception
Weaknesses
  Large mount of Params and Flops
  Over fitting

## Slide 13
Background | End-to-end Stack | Model
[1] CVPR 2021 Tutorial: All About Self-Driving
CNN
RNN
MLP
Transformer
…
Transformer
Strengths:
  High capacity
  Global reception
  Suitable for large model
  Friendly for multi data modality
Weaknesses
  Hard to optimize
  Need big data to train

## Slide 14
Background | End-to-end Stack | Output
[1] CVPR 2021 Tutorial: All About Self-Driving
Actuation
Cost
Affordance
Auxiliary
…
Control Command
Waypoints
Strengths:
  Simple
  Well studied in imitation literature
Weaknesses
  Hard to encode prior knowledge
  Lack interpretability

## Slide 15
Background | End-to-end Stack | Output
[1] CVPR 2021 Tutorial: All About Self-Driving
Actuation
Cost
Affordance
Auxiliary
…
Cost / Cost Map
Strengths:
  Easy to encoder prior knowledge
  Well aligned with traditional methods
Weaknesses
  No direct supervision, hard to train.

## Slide 16
Background | End-to-end Stack | Output
[1] CVPR 2021 Tutorial: All About Self-Driving
Actuation
Cost
Affordance
Auxiliary
…
Predefined continuous / discrete values

## Slide 17
Background | End-to-end Stack | Output
[1] CVPR 2021 Tutorial: All About Self-Driving
Actuation
Cost
Affordance
Auxiliary
…
Auxiliary Outputs:
  Object Detection;
  Segmentation;
  Depth Completion;
  Optical Flow;

## Slide 18
Contents
End-to-End Autonomous Driving Background
Interpretable End-to-End Autonomous Driving with Differentiable Semantic Occupancy Representation

## Slide 19
Differentiable Semantic Occupancy Representation
[1] Sadat, A., Casas, S., Ren, M., Wu, X., Dhawan, P., Urtasun, R.: Perceive, predict, and plan: Safe motion planning through interpretable semantic representations. ECCV (2020)

## Slide 20
Differentiable Semantic Occupancy Representation
[1] Sadat, A., Casas, S., Ren, M., Wu, X., Dhawan, P., Urtasun, R.: Perceive, predict, and plan: Safe motion planning through interpretable semantic representations. ECCV (2020)
Generates scene-level occupancy representations
Uses structured cost functions
  Non-parametric sematic occupancy maps
  Interpretable subcosts encoding prior

## Slide 21
Differentiable Semantic Occupancy Representation
[1] Sadat, A., Casas, S., Ren, M., Wu, X., Dhawan, P., Urtasun, R.: Perceive, predict, and plan: Safe motion planning through interpretable semantic representations. ECCV (2020)
What is Semantic Occupancy?
  Predicting the future motion area (free space) of traffic participants;
  capturing locations of objects of different classes (i.e., vehicles, bicyclists, and pedestrians) as well as potentially occluded ones.

## Slide 22
Differentiable Semantic Occupancy Representation
[1] Sadat, A., Casas, S., Ren, M., Wu, X., Dhawan, P., Urtasun, R.: Perceive, predict, and plan: Safe motion planning through interpretable semantic representations. ECCV (2020)
How to get the Semantic Occupancies?
Traditional methods:
  Detection and tracking
  Gaussian, mixture of Gaussians;
  This incorporates strong assumptions, lacks expressivity, not stable;
The proposed Differentiable programming method:
  Remove detection and tracking  efficient and effective;
  End-to-end learnable, easy to optimize and more stable;

## Slide 23
Differentiable Semantic Occupancy Representation
[1] Sadat, A., Casas, S., Ren, M., Wu, X., Dhawan, P., Urtasun, R.: Perceive, predict, and plan: Safe motion planning through interpretable semantic representations. ECCV (2020)
Semantic Occupancy Design
  Subclasses: mutually-exclusive
Notes: mutually-exclusive

## Slide 24
Differentiable Semantic Occupancy Representation
[1] Sadat, A., Casas, S., Ren, M., Wu, X., Dhawan, P., Urtasun, R.: Perceive, predict, and plan: Safe motion planning through interpretable semantic representations. ECCV (2020)
Detail: l: the predicted logits, t: time, c: class, : neural network, : concatenated feature, ||: feature-wise concatenation, : 2x bilinear interpolation.
represent the occupancy of each class,

## Slide 25
Differentiable Semantic Occupancy Representation
[1] Sadat, A., Casas, S., Ren, M., Wu, X., Dhawan, P., Urtasun, R.: Perceive, predict, and plan: Safe motion planning through interpretable semantic representations. ECCV (2020)
Cost function
Loss function
: trajectories, f: objective function, X: input, O: occupancy, w: parameter, t: time, c: class, v: velocity;
: make sure the trajectory is safe with regards to the semantic occupancy forecasts;
: related to comfort, traffic rules and progress in the route;

## Slide 26
Differentiable Semantic Occupancy Representation
[1] Sadat, A., Casas, S., Ren, M., Wu, X., Dhawan, P., Urtasun, R.: Perceive, predict, and plan: Safe motion planning through interpretable semantic representations. ECCV (2020)
Loss function
: loss function, : Semantic Occupancy Loss (cross entropy), : Planning Loss (max-margin),
: trajectories, f: objective function, X: input, O: occupancy, w: parameter, t: time, c: class, S: spatial;
: make sure the trajectory is safe with regards to the semantic occupancy forecasts;
: related to comfort, traffic rules and progress in the route;
: imitation task-loss of trajectory, : collisions and their severity at each trajectory step
Notes: H: human

## Slide 27
Differentiable Semantic Occupancy Representation
[1] Sadat, A., Casas, S., Ren, M., Wu, X., Dhawan, P., Urtasun, R.: Perceive, predict, and plan: Safe motion planning through interpretable semantic representations. ECCV (2020)
Pick the minimum-cost trajectory
Cost functions
  Safety (occupancy predictions)
  Comfort and traffic-rules
  Route following

## Slide 28
Differentiable Semantic Occupancy Representation
[1] Sadat, A., Casas, S., Ren, M., Wu, X., Dhawan, P., Urtasun, R.: Perceive, predict, and plan: Safe motion planning through interpretable semantic representations. ECCV (2020)
Qualitative results, ego vehicle (solid black rectangle)

## Slide 29: Q&A
THANK YOU