## Slide 1
A Lightweight And Inexpensive In-ear Sensing System For Automatic Whole-night Sleep Stage Monitoring
Anh Nguyen, Raghda Alqurashi, Zohreh Raghebi
Presenters：Justin Shen & Ruomin Ba

## Slide 2
CONTENTS
Background
（Section 1, 2）
01
（Section 1, 2）
Challenges
02
（Section 3, 7）
Hardware
03
（Section 3,4,5,6,7）
Architecture
04
Evaluation
（Section 8）
05
（Section 10）
Conclusion
06

## Slide 3
01
BACKGROUND

## Slide 4
Background
Sleep is important for healthy body function and has impact on
Learning
Psychological health
Hormone regulation
Appetite
And much more
Thus, it is clinically important to reliably monitor a person’s sleep health
Figure: https://www.israel21c.org/sleep-vital-to-repair-dna-damage-israeli-study-finds/

## Slide 5
Background
Sleep Monitoring: Polysomnography (PSG)
Typically sleep studies involve Polysomnography (PSG) in a sleep laboratory
Monitors three main signals (among others):
(1) Brain activity (EEG)
(2) Eye movements (EOG)
(3) Muscle activity (EMG)
Figure: http://www.alphasleeplab.com/blog /2017/5/22/sleep-studies-part-1

## Slide 6
Background
Drawbacks of PSG:
obtrusive attachment of large number of wired sensors
need to travel to sleep laboratory
risk of losing sensor contact whenever patient move
need of well-trained expert to review sleep staging result
Propose the use of Low-cost in-ear biosignal sensing system (LIBS) to monitor sleep without these drawbacks

## Slide 7
02
CHALLENGES

## Slide 8
Challenges
The desired signal is low amplitude, thus LIBS must be able to measure the signal well without sacrificing comfort
Separation of EEG, EOG, and EMG signals from the single channel in-ear mixture
Separation algorithm must be robust to account for difference of physiological condition and other variation among individuals

## Slide 9
03
HARDWARE

## Slide 10
Hardware
Signal Acquisition: Hardware Design (1/3)
Sensor compose of a earplug base with electrode
Block foam earplug as base
  Allows the sensor to follow the shape of the ear canal
  Provides comfort while avoiding high cost associated with personalization
  Also reduces the motion noise caused by jaw motion

## Slide 11
Hardware
Signal Acquisition: Hardware Design (2/3)
Sensor compose of a earplug base with electrode
Coat surface with layers of thin silver leaves
  Conductive silver cloth acts as electrode
  Works with base for a low and consistent surface resistance -> reliable signals

## Slide 12
Hardware
Signal Acquisition: Hardware Design (3/3)
Oval shaped electrode based on anatomy of ear canal
Experimented with different materials (silver leaves, fabric, copper)
Increase of the distance between the main electrodes -> signal fidelity
Signals amplified and passed to microcontroller

## Slide 13
04
ARCHITECTURE

## Slide 14
Architecture
Three separate modules

## Slide 15
Architecture
Data Acquisition and Preprocessing
LIBS uses a brain-computer interface (BCI) board named OpenBCI to sample and digitize the in-ear signal
  6V battery source for power and safety
  Sampling rate of 2kHz and a gain of 24dB
Captured signals are preprocessed to eliminate possible signal interference (from body movement, electrical noise, etc.)
Signals are stored in an SD card and then processed offline
  Signal separation
  Signal classification

## Slide 16
Architecture
Signal Separation
The biosignal sensed by LIBS is a single channel mixture of four components: EEG, EOG, EMG and noise.
Why separate EEG, EOG, EMG and noise is difficult?
Overlapping characteristics of three signals in both time and frequency domains.
Random activation of the sources generating them.
Signal variation from person to person and in different recordings.

## Slide 17
Architecture
Signal Separation
What tools we could use to solve the problem?
A. Principle Component Analysis (PCA)
B. Independent Component Analysis (ICA)
C. Empirical Mode Decomposition (EMD)
D. Non-negative Matrix Factorization (NMF)
Why authors choose NMF?
The number of collected channels is equal to or larger than the number of source signals (except NMF)
The factorized components describing the source signal are selected manually.
The channel number that LIBS has (1 channel) is lower than the number of signals of interest (3 signals).

## Slide 18
Architecture
Signal Separation
What is Non-negative Matrix Factorization (NMF)?
NMF is one kind of non-linear dimension reduction algorithm
Optimization Target:
The non-negativity makes the resulting matrices easier to inspect

## Slide 19
Architecture
Signal Separation
What are the problems with applying NMF into LIBS?
The non-convex solution space of NMF causes the non-unique estimation of the original source signals.
The variance of the biosignals on different sleeps.
How to solve these two problems?
Combine NMF with Spectral Template Learning Algorithm
Use Itakura Saito (IS) divergence as the cost function. Since it holds a scale-invarianct property that could help minimize the variance on different sleeps.

## Slide 20
Architecture
Signal Separation
W is the spectral template matrix representing basis patterns (components).
H is the activation matrix expressing time points (positions) when the signal patterns in W is activatied.

## Slide 21
Architecture
Sleep Stage Classification
Find the pattern between sleep stage and EEG, EOG & EMG
Feature Extraction
Among All features, find what features are important
Feature Selection
Decision Tree and Random Forest
Classification

## Slide 22
Architecture
Sleep Stage Classification

## Slide 23
Architecture
Sleep Stage Classification
What is the reason to do feature selection?
The performance of a classification algorithm can degrade when all extracted features are used to determine the sleep stages.
Comment: The figure above is only the result of decision tree and random forest algorithms. Actually a lot of sophisticated classification algorithms could automatically choose the important features related to the output. For example, neural network could reduce the influence of unimportant features with sufficient training. In this case, feature selection may not be necessary.

## Slide 24
Architecture
Sleep Stage Classification
How to do feature selection?
Forward Selection (FSP) identifies the most effective combination of features extracted from in-ear signal.
Features are selected sequentially until the addition of a new feature results in no performance improvement in prediction.
A feature is added to the set of selected features if it not only improves the misclassification error but also is less redundant given the features already selected.

## Slide 25
Architecture
Sleep Stage Classification
What classification algorithms authors considered?
Neural Network
Reject Reason: Long training time and complexity
SVM
Reject Reason: Long training time and difficulty to understand the learned function
Decision Tree & Random Forest
Easy to implement and interpret
Highest performance
Flexible and work well with catrgorical data

## Slide 26
05
EVALUATION

## Slide 27
Evaluation
System Performance

## Slide 28
Evaluation
Signal Acquisition

## Slide 29
Evaluation
Signal Acquisition

## Slide 30
Evaluation
Signal Separation

## Slide 31
Evaluation
Sleep Stage Classification

## Slide 32
06
CONCLUSION

## Slide 33
Conclusion
In this paper, the authors presented the desgin, implementation and evaluation of LIBS.
LIBS could achieve similar performance like PSG in terms of sleep stages classification accuracy.
It has the advantages of low cost, easy operation and comfortable wearing during sleep.
It has the potential to become a fundamental sleep monitoring device in the future.