## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 1115
CMSC 417 : Spring 2022
Topic: Internetworking: Subnets, CIDR
(Textbook chapter 3)

## Slide 2
Does this network require IP address (network layer address) for message exchange?

## Slide 3
Does this network require IP address (network layer address) for message exchange?

## Slide 4
Destination
Source
Does this network require IP address (network layer address) for message exchange?

## Slide 5
Destination
Source
Router

## Slide 6
Destination
Source
Router
Routers will use routing algorithms to create and maintain forwarding tables.

## Slide 7
Destination
Source
Router
<addr1, n.hop1>
<addr2, n.hop2>
<addr3, n.hop3>
forwarding table
Routers will use routing algorithms to create and maintain forwarding tables.

## Slide 8
Router
IP-Addr1
IP-Addr2
IP-Addr3
IP-Addr4
IP-Addr5
IP-Addr6
Router requires the address of the network
<addr1, n.hop1>
<addr2, n.hop2>
<addr3, n.hop3>
forwarding table

## Slide 9
Router
IP-Addr1
IP-Addr2
IP-Addr3
IP-Addr4
IP-Addr5
IP-Addr6
Rather the address of the interface.
<addr1, n.hop1>
<addr2, n.hop2>
<addr3, n.hop3>
forwarding table

## Slide 10
Router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
223.1.1.6
223.1.1.X
223.1.1.7
11011111.00000001.00000001.XXXXXXX

## Slide 11
Router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
223.1.1.6
223.1.1.X
223.1.1.7
11011111.00000001.00000001.XXXXXXX
24 leading bits = Network number

## Slide 12
Router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
223.1.1.6
223.1.1.X
223.1.1.7
<223.1.1.0, Interface_number>
forwarding table

## Slide 13
Router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
223.1.1.6
223.1.1.X
223.1.1.7
<223.1.1.0, Interface_number>
forwarding table
Dest addr: 223.1.1.3

## Slide 14
Router
223.1.1.7
<223.1.1.0, Interface_number>
forwarding table
Dest addr: 223.1.1.3
11011111.00000001.00000001.00000011
Dest addr: 223.1.1.3
Mask: 255.255.255.0
11111111. 11111111. 11111111.00000000
Bitwise &
= 11011111.00000001.00000001.00000000
223.1.1.0

## Slide 15
Router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
223.1.1.6
ISP
The ISP provided the network address space: 223.1.1.X

## Slide 16
Router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
223.1.1.6
ISP
The ISP provided the network address space: 223.1.1.X
223.1.2.X
223.1.3.X

## Slide 17
Router
The ISP provided the network address space: 223.1.1.X
Two separate networks are needed. How can we assign addresses to these “sub” networks?

## Slide 18
Router
The ISP provided the network address space: 223.1.1.X
223.1.1.X
223.1.2.X

## Slide 19
Router
The ISP provided the network address space: 223.1.1.X
223.1.1.X
223.1.2.X
Use subnetting

## Slide 20
Router
The ISP provided the network address space: 223.1.1.X
223.1.1.X
11011111.00000001.00000001.XXXXXXX
Use part of the host bits to identify separate subnets.

## Slide 21
Router
The ISP provided the network address space: 223.1.1.X
11011111.00000001.00000001.XXXXXXX
Use part of the host bits to identify separate subnets.
11011111.00000001.00000001.0XXXXXX
11011111.00000001.00000001.1XXXXXX
Subnet mask = 11111111. 11111111. 11111111.10000000

## Slide 22: Obtaining a Block of Addresses
Internet Corporation for Assigned Names and Numbers (ICANN)
  Allocates large blocks to Regional Internet Registries
Regional Internet Registries (RIRs)
  E.g., ARIN (American Registry for Internet Numbers)
  Allocates to ISPs and large institutions
Internet Service Providers (ISPs)
  Allocate address blocks to their customers
  Who may, in turn, allocate to their customers…

## Slide 23: A reverse problem (Supernettting/CIDR)

## Slide 24
200.20.1.X
200.20.2.X
200.20.3.X

## Slide 25
200.20.1.0/24
200.20.2.0/24
200.20.3.0/24

## Slide 26
200.20.1.0/24
200.20.2.0/24
200.20.3.0/24

## Slide 27
200.20.1.0/24
200.20.2.0/24
200.20.3.0/24
Route aggregation

## Slide 28: Classless Addressing
Route aggregation with CIDR

## Slide 29: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
200.23.16.0–200.23.17.255

## Slide 30
IP addressing: CIDR
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
forwarding table
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address

## Slide 31: Classless Inter-Domain Routing (CIDR)
IP Address : 12.4.0.0 IP Mask: 255.254.0.0
00001100
00000100
00000000
00000000
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network.
Network number = IP address + Mask
Written as 12.4.0.0/15

## Slide 32: Hierarchical Address Allocation
Hierarchy is key to scalability
  Address allocated in contiguous chunks (prefixes)
  Today, the Internet has about 400,000 prefixes
12.0.0.0/8
12.0.0.0/16
12.254.0.0/16
12.1.0.0/16
12.2.0.0/16
12.3.0.0/16
:
:
:
12.3.0.0/24
12.3.1.0/24
:
:
12.3.254.0/24
12.253.0.0/19
12.253.32.0/19
12.253.160.0/19
:
:
:
:
:

## Slide 33: Separate Forwarding Entry Per Prefix
Prefix-based forwarding
  Map the destination address to matching prefix
  Forward to the outgoing interface
host
host
host
LAN 1
...
host
host
host
LAN
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 34: CIDR Makes Packet Forwarding Harder
Forwarding table may have many matches
  E.g., entries for 201.10.0.0/21 and 201.10.6.0/23
  The IP address 201.10.6.17 would match both!
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2

## Slide 35: Longest Prefix Match Forwarding
Destination-based forwarding
  Packet has a destination address
  Router identifies longest-matching prefix
  Cute algorithmic problem: very fast lookups
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
201.10.6.17
destination
forwarding table
Serial0/0.1
outgoing link

## Slide 36
Subnets “toy” example

## Slide 37
Address space assigned to you:

## Slide 41: Getting an IP address: DHCP

## Slide 42: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/…
DHCP: Dynamic Host Configuration Protocol: dynamically get address from a server
  “plug-and-play”

## Slide 43: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network

## Slide 44: DHCP: Dynamic Host Configuration Protocol
DHCP overview:
  host broadcasts “DHCP discover” msg
  DHCP server responds with “DHCP offer” msg
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 45: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 46
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 47: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 48: Dynamic Host Configuration Protocol (DHCP)
DHCP server is responsible for providing configuration information to hosts
DHCP server maintains a pool of available addresses
There is at least one DHCP server for an administrative domain (a server or a relay agent per subnet)

## Slide 49: DHCP
Newly booted or attached host sends DHCPDISCOVER message to a special IP address (255.255.255.255)
DHCP relay agent unicasts the message to DHCP server and waits for the response

## Slide 50
Check our IP addresses
(ifconfig/ipconfig)

## Slide 51: Private Address Space

## Slide 53: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers

## Slide 54: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 55: NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 56: NAT: network address translation
implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 57: NAT: network address translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT challenges:
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  NAT traversal: what if client wants to connect to server behind NAT?