## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2024
Topic:
Link layer: Introduction, Ethernet (Textbook chapter 2)
April 9th, 2024

## Slide 2: What is a Link?
Communication Medium
Network Adapter

## Slide 3
Ripple: Communicating through Physical Vibrations
NSDI 2015
Vibration as medium

## Slide 5
Motion sensor
(accelerometer)
Vibration motor
Notes: Now, what could be the “RECEIVER” for such vibrations?
Observe that almost all mobile devices today have a motion sensor called … ACCELEROMETERS

## Slide 6
Motion sensor
(accelerometer)
Vibration motor
Notes: Thus, if the vibrating transmitter comes in CONTACT with the accelerometer … by literally TOUCHING the accelerometer … then the accelerometer can SENSE the vibrations and DECODE the data bits from it.
We have built such vibratory transmitters inside smartwatches and finger rings.
When the human finger touches the accelerometer … the vibration flows the the finger bone … and the data is transferred.
Of course, the human does not feel anything at all …

## Slide 7
Light as medium: LiFi

## Slide 8: Adaptors Communicating
Sending side
  Encapsulates packet in a frame
  Adds error checking bits, flow control, etc.
Receiving side
  Looks for errors, flow control, etc.
  Extracts datagram and passes to receiving node
sending
node
frame
receiving
node
packet
frame
adapter
adapter
link layer protocol
packet

## Slide 11: Link Layer Addresses (Recap) (Discussed earlier in the context of ARP)

## Slide 12: MAC addresses and ARP
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  e.g.: 1A-2F-BB-76-09-AD
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)

## Slide 13: ARP protocol
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 14: As an Aside: Promiscuous Mode
Normal adapter: receives frames sent to
  The local MAC address
  Broadcast address FF-FF-FF-FF-FF-FF
Promiscuous mode
  Receive everything, independent of destination MAC
Useful for packet sniffing
  Network monitoring
  E.g., wireshark, tcpdump

## Slide 15: Why Not Just Use IP Addresses?
Links can support any network protocol
  Not just for IP (e.g., IPX, Appletalk, X.25, …)
  Different addresses on different kinds of links
An adapter may move to a new location
  So, cannot simply assign a static IP address
  Instead, must reconfigure the adapter’s IP address
Must identify the adapter during bootstrap
  Need to talk to the adapter to assign it an IP address

## Slide 17: Collisions
Single shared broadcast channel
  Avoid having multiple nodes speaking at once
  Otherwise, collisions lead to garbled data
71-65-F7-2B-08-53
1A-2F-BB-76-09-AD
0C-C4-11-6F-E3-98

## Slide 18: Multi-Access Protocol
Divide the channel into pieces
  In time
  In frequency

## Slide 19: Multi-Access Protocol
Time Division Multiple Access
Frequency Division Multiple Access
Code Division Multiple Access

## Slide 20: Multi-Access Protocol
Divide the channel into pieces
  In time
  In frequency

## Slide 21: Multi-Access Protocol
Divide the channel into pieces
  In time
  In frequency
Take turns
  Pass a token for the right to transmit

## Slide 22: Multi-Access Protocol
Divide the channel into pieces
  In time
  In frequency
Take turns
  Pass a token for the right to transmit
Defer action
  Let collisions happen
  … and detect and recover from them
Carrier Sense Multiple Access

## Slide 23: Like Human Conversation…
Carrier sense
  Listen before speaking
  …and don’t interrupt!
Collision detection
  Detect simultaneous talking
  … and shut up!
Random access
  Wait for a random period of time
  … before trying to talk again!

## Slide 24: Carrier Sense Multiple Access (CSMA)

## Slide 25: Carrier Sense Multiple Access (CSMA)
Listen for other senders
  Then transmit your data
Collisions can still occur
  Propagation delay
  Wasted transmission

## Slide 26
CSMA: The time-space graph of collision

## Slide 27
CSMA: The time-space graph of collision

## Slide 28: CSMA: The time-space graph of collision

## Slide 29: CSMA: The time-space graph of collision
The time-space region of collision

## Slide 30: Comparing the Three Approaches
Divide the channel into pieces
  In time
  In frequency
Take turns
  Pass a token for the right to transmit
Defer action
  Let collisions happen
  … and detect and recover from them
Carrier Sense Multiple Access

## Slide 31: Comparing the Three Approaches
Channel partitioning
  Efficient and fair at high load
  Inefficient at low load
“Taking turns”
  Eliminates empty slots without collisions
  Vulnerable to failures (e.g. lost token)
Random access
  Efficient at low load
  Collision overhead at high load

## Slide 32
Automatic Repeat request
Flow control
Not implemented in wired LAN (e.g. Ethernet)

## Slide 33: Ethernet

## Slide 34: Ethernet
Dominant wired LAN technology
First widely used LAN technology
Kept up with speed race: 10 Mbps – 40 Gbps
Metcalfe’s
Ethernet
sketch

## Slide 36: Ethernet Uses CSMA/CD
Carrier Sense: wait for link to be idle
  Channel idle: start transmitting
  Channel busy: wait until idle
  A strategy is p-persistent if, after waiting for the line to clear, the sender sends with probability p≤1.
Collision Detection: listen while transmitting
  No collision: transmission is complete
  Collision: abort transmission, and send jam signal
Random Access: exponential back-off
  After collision, wait random time before trying again
  After mth collision, choose K randomly from {0, …, 2m-1}
  … and wait for K*512 bit times before trying again

## Slide 37: CSMA/CD Collision Detection
Detect collision
  Abort transmission
  Jam the link
Wait random time
  Transmit again
Hard in wireless
  Must receive data while transmitting

## Slide 38: CSMA/CD Collision Detection
Without collision detection
With collision detection and abort

## Slide 40
Collision does not happen like this. :-D

## Slide 41
Collision happens when both packet overlaps at the receiver.

## Slide 42
Preparing for the worst-case scenario of collision
Collision happens when both packet overlaps at the receiver.

## Slide 43
Thank you

## Slide 44
Preparing for the worst-case scenario of collision

## Slide 45
Preparing for the worst-case scenario of collision

## Slide 46
Preparing for the worst-case scenario of collision

## Slide 47
Preparing for the worst-case scenario of collision
The packet should be at least for 2d seconds long so that the sender can get the notification of the collision (through the jamming signal)

## Slide 48
Preparing for the worst-case scenario of collision
The packet should be at least for 2d seconds long so that the sender can get the notification of the collision (through the jamming signal)
Transmission time >= 2*propagation time

## Slide 49
Preparing for the worst-case scenario of collision
Formula for minimum packet size (P) or maximum length (L)

## Slide 50
Two questions
1. Why does the receiver send jamming signal after
detecting collision?
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.

## Slide 51
Two questions
Host A
Host B
Host C
1. Why does the receiver send jamming signal after
detecting collision?

## Slide 52
Two questions
Collision
Host C detects
collision
Host A
Host B
Host C
1. Why does the receiver send jamming signal after
detecting collision?

## Slide 53
Two questions
Collision
Attenuation makes
the signal weak. This may lead to missed detection.
Host A
Host B
Host C
1. Why does the receiver send jamming signal after
detecting collision?

## Slide 54
Two questions
Collision
Host A
Host B
Host C
Host B sends jamming signal to ensure collision
detection.
1. Why does the receiver send jamming signal after
detecting collision?

## Slide 55
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.

## Slide 56
Preparing for the worst-case scenario of collision

## Slide 57
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.
Host A
Host C
Host B
Pkt: A
Pkt: B

## Slide 58
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.
Host A
Host C
Host B
Pkt: A
Pkt: B
Collision

## Slide 59
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.
Host A
Host C
Host B
Pkt: A
Pkt: B
Collision

## Slide 60
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.
Host A
Host C
Host B
Pkt: A
Pkt: B
Collision
This situation is
not possible under our
assumptions.

## Slide 61
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.
Host A
Host C
Host B
Pkt: A
Pkt: B
Pkt: A
Valid scenario.

## Slide 62
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.
Host A
Host C
Host B
Pkt: A
Pkt: B
Pkt: A
Valid scenario.

## Slide 63
Two questions
2. In the worst-case collision scenario, why did we
consider collision with the first bit of the packet?
Is it possible to have collision in the middle or at
the end in this scenario.
Host A
Host C
Host B
Pkt: A
Pkt: B
Pkt: A
Not a valid scenario:
Host B won’t start transmission
as the channel is busy.

## Slide 64
Preparing for the worst-case scenario of collision

## Slide 66
Preparing for the worst-case scenario of collision
Repeater
(3 us delay)
Repeater
(3 us delay)

## Slide 67: Ethernet Frame Structure
Sending adapter encapsulates packet in frame
Preamble: synchronization
  Seven bytes with pattern 10101010, followed by one byte with pattern 10101011
  Used to synchronize receiver, sender clock rates

## Slide 68: Ethernet Frame Structure
Addresses: source and destination MAC addresses
  Adaptor passes frame to network-level protocol
    If destination is local MAC address or broadcast address
  Otherwise, adapter discards frame
Type: indicates the higher layer protocol
  Usually IP
  But also Novell IPX, AppleTalk, …
CRC: cyclic redundancy check
  Checked at receiver
  If error is detected, the frame is simply dropped

## Slide 69: Unreliable, Connectionless Service
Connectionless
  No handshaking between send and receive adapter
Unreliable
  Receiving adapter doesn’t send ACKs or NACKs
  Packets passed to network layer can have gaps
  Gaps can be filled by transport protocol (e.g., TCP)
  Otherwise, the application will see the gaps

## Slide 70: Star topology and collision-free Ethernet
Star topology
Bus topology

## Slide 71: Star topology and collision-free Ethernet
Star topology with hub and switch

## Slide 72: Repeaters, Hubs, Bridges and Switches

## Slide 75: Physical Layer: Repeaters
Distance limitation in local-area networks
  Electrical signal becomes weaker as it travels
  Imposes a limit on the length of a LAN
Repeaters join LANs together
  Analog electronic device
  Continuously monitors electrical signals
  Transmits an amplified copy

## Slide 76: Physical Layer: Hubs
Joins multiple input lines electrically
  Designed to hold multiple line cards
  Do not necessarily amplify the signal
Very similar to repeaters
  Also operates at the physical layer
hub
hub
hub
hub

## Slide 77
Physical Layer: Hubs

## Slide 78: Limitations of Repeaters and Hubs
One large shared link
  Each bit is sent everywhere
  So, aggregate throughput is limited
Cannot support multiple LAN technologies
  Does not buffer or interpret frames
  Can’t interconnect between different rates/formats
Limitations on maximum nodes and distances
  Shared medium imposes length limits
  E.g., cannot go beyond 2500 meters on Ethernet

## Slide 79: Link Layer: Bridges
Connects two or more LANs at the link layer
  Extracts destination address from the frame
  Looks up the destination in a table
  Forwards the frame to the appropriate segment
Each segment can carry its own traffic
host
host
host
host
host
host
host
host
host
host
host
host
Bridge

## Slide 80: Link Layer: Switches
Typically connects individual computers
  A switch is essentially the same as a bridge
  … though typically used to connect hosts
Supports concurrent communication
  Host A can talk to C, while B talks to D
switch
A
B
C
D

## Slide 81: Bridges/Switches: Traffic Isolation
Switch filters packets
  Frame only forwarded to the necessary segments
  Segments can support separate transmissions
hub
hub
hub
switch/bridge
segment
segment
segment

## Slide 82: Advantages Over Hubs/Repeaters
Only forwards frames as needed
  Avoid unnecessary load on segments
Wider geographic span
  Separate segments allow longer distances
Improves privacy
  Hosts can “snoop” traffic traversing their segment
  … but not all the rest of the traffic
Can join segments using different technologies

## Slide 83
Switch table
Traffic Isolation: Example

## Slide 84: Self Learning: Building the Table
When a frame arrives
  Inspect the source MAC address
  Associate the address with the incoming interface
  Store the mapping in the switch table
  Use a timer to eventually forget the mapping
A
B
C
D
Switch learns how to reach A.

## Slide 85: Self Learning: Handling Misses
When frame arrives with unfamiliar destination
  Forward the frame out all of the interfaces
  … except for the one where the frame arrived
  Hopefully, this case won’t happen very often!
A
B
C
D
When in doubt, shout!

## Slide 86
Exercise problems related to
learning-bridges/switches

## Slide 87
Switch vs Router

## Slide 88: Summary: Multiple Layers
Different devices switch different things
  Network layer: packets (routers)
  Link layer: frames (bridges and switches)
  Physical layer: electrical signals (repeaters and hubs)
Application
Transport
Router
Bridge, switch
Repeater, hub
Frame header
Packet header
TCP header
User
data