## Slide 1
Randal E. Bryant
Carnegie Mellon University
CS:APP
CS:APP Chapter 4
Computer Architecture
Sequential
Implementation
http://csapp.cs.cmu.edu

## Slide 2: Y86 Instruction Set
Byte
0
1
2
3
4
5
pushl rA
A
0
rA
8
jXX Dest
7
fn
Dest
popl rA
B
0
rA
8
call Dest
8
0
Dest
rrmovl rA, rB
2
0
rA
rB
irmovl V, rB
3
0
8
rB
V
rmmovl rA, D(rB)
4
0
rA
rB
D
mrmovl D(rB), rA
5
0
rA
rB
D
OPl rA, rB
6
fn
rA
rB
ret
9
0
nop
0
0
halt
1
0
addl
6
0
subl
6
1
andl
6
2
xorl
6
3
jmp
7
0
jle
7
1
jl
7
2
je
7
3
jne
7
4
jge
7
5
jg
7
6

## Slide 3: Building Blocks
Combinational Logic
  Compute Boolean functions of inputs
  Continuously respond to input changes
  Operate on data and implement control
Storage Elements
  Store bits
  Addressable memories
  Non-addressable registers
  Loaded only as clock rises
Register
file
A
B
W
dstW
srcA
valA
srcB
valB
valW
Clock
A
L
U
fun
A
B
MUX
0
1
=
Clock

## Slide 4: Hardware Control Language
  Very simple hardware description language
  Can only express limited aspects of hardware operation
    Parts we want to explore and modify
Data Types
  bool: Boolean
    a, b, c, …
  int: words
    A, B, C, …
    Does not specify word size---bytes, 32-bit words, …
Statements
  bool a = bool-expr ;
  int A = int-expr ;

## Slide 5: HCL Operations
  Classify by type of value returned
Boolean Expressions
  Logic Operations
    a && b, a || b, !a
  Word Comparisons
    A == B, A != B, A < B, A <= B, A >= B, A > B
  Set Membership
    A in { B, C, D }
      Same as A == B || A == C || A == D
Word Expressions
  Case expressions
    [ a : A; b : B; c : C ]
    Evaluate test expressions a, b, c, … in sequence
    Return word expression A, B, C, … for first successful test

## Slide 6: SEQ Hardware Structure
State
  Program counter register (PC)
  Condition code register (CC)
  Register File
  Memories
    Access same memory space
    Data: for reading/writing program data
    Instruction: for reading instructions
Instruction Flow
  Read instruction at address specified by PC
  Process through stages
  Update program counter
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Bch
valE
Addr
, Data
valM
PC
valE
,
valM
newPC

## Slide 7: SEQ Stages
Fetch
  Read instruction from instruction memory
Decode
  Read program registers
Execute
  Compute value or address
Memory
  Read or write data
Write Back
  Write program registers
PC
  Update program counter
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Bch
valE
Addr
, Data
valM
PC
valE
,
valM
newPC

## Slide 8: Instruction Decoding
Instruction Format
  Instruction byte icode:ifun
  Optional register byte rA:rB
  Optional constant word valC
5
0
rA
rB
D
icode
ifun
rA
rB
valC
Optional
Optional

## Slide 9: Executing Arith./Logical Operation
Fetch
  Read 2 bytes
Decode
  Read operand registers
Execute
  Perform operation
  Set condition codes
Memory
  Do nothing
Write back
  Update register
PC Update
  Increment PC by 2
OPl rA, rB
6
fn
rA
rB

## Slide 10: Stage Computation: Arith/Log. Ops
  Formulate instruction execution as sequence of simple steps
  Use same general form for all instructions
OPl rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB OP valA
Set CC
Execute
Perform ALU operation
Set condition code register
Memory
R[rB]  valE
Write
back
Write back result
PC  valP
PC update
Update PC

## Slide 11: Executing rmmovl
Fetch
  Read 6 bytes
Decode
  Read operand registers
Execute
  Compute effective address
Memory
  Write to memory
Write back
  Do nothing
PC Update
  Increment PC by 6
rmmovl rA, D(rB)
4
0
rA
rB
D

## Slide 12: Stage Computation: rmmovl
  Use ALU for address computation
rmmovl rA, D(rB)
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M4[PC+2]
valP  PC+6
Fetch
Read instruction byte
Read register byte
Read displacement D
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB + valC
Execute
Compute effective address
M4[valE]  valA
Memory
Write value to memory
Write
back
PC  valP
PC update
Update PC

## Slide 13: Executing popl
Fetch
  Read 2 bytes
Decode
  Read stack pointer
Execute
  Increment stack pointer by 4
Memory
  Read from old stack pointer
Write back
  Update stack pointer
  Write result to register
PC Update
  Increment PC by 2
popl rA
b
0
rA
8

## Slide 14: Stage Computation: popl
  Use ALU to increment stack pointer
  Must update two registers
    Popped value
    New stack pointer
popl rA
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[%esp]
valB  R [%esp]
Decode
Read stack pointer
Read stack pointer
valE  valB + 4
Execute
Increment stack pointer
valM  M4[valA]
Memory
Read from stack
R[%esp]  valE
R[rA]  valM
Write
back
Update stack pointer
Write back result
PC  valP
PC update
Update PC

## Slide 15: Executing Jumps
Fetch
  Read 5 bytes
  Increment PC by 5
Decode
  Do nothing
Execute
  Determine whether to take branch based on jump condition and condition codes
Memory
  Do nothing
Write back
  Do nothing
PC Update
  Set PC to Dest if branch taken or to incremented PC if not branch
jXX Dest
7
fn
Dest
XX
XX
fall thru:
XX
XX
target:
Not taken
Taken

## Slide 16: Stage Computation: Jumps
  Compute both addresses
  Choose based on setting of condition codes and branch condition
jXX Dest
icode:ifun  M1[PC]
valC  M4[PC+1]
valP  PC+5
Fetch
Read instruction byte
Read destination address
Fall through address
Decode
Bch  Cond(CC,ifun)
Execute
Take branch?
Memory
Write
back
PC  Bch ? valC : valP
PC update
Update PC

## Slide 17: Executing call
Fetch
  Read 5 bytes
  Increment PC by 5
Decode
  Read stack pointer
Execute
  Decrement stack pointer by 4
Memory
  Write incremented PC to new value of stack pointer
Write back
  Update stack pointer
PC Update
  Set PC to Dest
call Dest
8
0
Dest
XX
XX
return:
XX
XX
target:

## Slide 18: Stage Computation: call
  Use ALU to decrement stack pointer
  Store incremented PC
call Dest
icode:ifun  M1[PC]
valC  M4[PC+1]
valP  PC+5
Fetch
Read instruction byte
Read destination address
Compute return point
valB  R[%esp]
Decode
Read stack pointer
valE  valB + –4
Execute
Decrement stack pointer
M4[valE]  valP
Memory
Write return value on stack
R[%esp]  valE
Write
back
Update stack pointer
PC  valC
PC update
Set PC to destination

## Slide 19: Executing ret
Fetch
  Read 1 byte
Decode
  Read stack pointer
Execute
  Increment stack pointer by 4
Memory
  Read return address from old stack pointer
Write back
  Update stack pointer
PC Update
  Set PC to return address
ret
9
0
XX
XX
return:

## Slide 20: Stage Computation: ret
  Use ALU to increment stack pointer
  Read return address from memory
ret
icode:ifun  M1[PC]
Fetch
Read instruction byte
valA  R[%esp]
valB  R[%esp]
Decode
Read operand stack pointer
Read operand stack pointer
valE  valB + 4
Execute
Increment stack pointer
valM  M4[valA]
Memory
Read return address
R[%esp]  valE
Write
back
Update stack pointer
PC  valM
PC update
Set PC to return address

## Slide 21: Computation Steps
  All instructions follow same general pattern
  Differ in what gets computed on each step
OPl rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
[Read constant word]
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB OP valA
Set CC
Execute
Perform ALU operation
Set condition code register
Memory
[Memory read/write]
R[rB]  valE
Write
back
Write back ALU result
[Write back memory result]
PC  valP
PC update
Update PC
icode,ifun
rA,rB
valC
valP
valA, srcA
valB, srcB
valE
Cond code
valM
dstE
dstM
PC

## Slide 22: Computation Steps
  All instructions follow same general pattern
  Differ in what gets computed on each step
call Dest
Fetch
Decode
Execute
Memory
Write
back
PC update
icode,ifun
rA,rB
valC
valP
valA, srcA
valB, srcB
valE
Cond code
valM
dstE
dstM
PC
icode:ifun  M1[PC]
valC  M4[PC+1]
valP  PC+5
valB  R[%esp]
valE  valB + –4
M4[valE]  valP
R[%esp]  valE
PC  valC
Read instruction byte
[Read register byte]
Read constant word
Compute next PC
[Read operand A]
Read operand B
Perform ALU operation
[Set condition code reg.]
[Memory read/write]
[Write back ALU result]
Write back memory result
Update PC

## Slide 23: Computed Values
Fetch
  icode Instruction code
  ifun Instruction function
  rA Instr. Register A
  rB Instr. Register B
  valC Instruction constant
  valP Incremented PC
Decode
  srcA Register ID A
  srcB Register ID B
  dstE Destination Register E
  dstM Destination Register M
  valA Register value A
  valB Register value B
Execute
  valE ALU result
  Bch Branch flag
Memory
  valM Value from memory

## Slide 24: SEQ Hardware
Key
  Blue boxes: predesigned hardware blocks
    E.g., memories, ALU
  Gray boxes: control logic
    Describe in HCL
  White ovals: labels for signals
  Thick lines: 32-bit word values
  Thin lines: 4-8 bit values
  Dotted lines: 1-bit values

## Slide 25: Fetch Logic
Predefined Blocks
  PC: Register containing PC
  Instruction memory: Read 6 bytes (PC to PC+5)
  Split: Divide instruction byte into icode and ifun
  Align: Get fields for rA, rB, and valC

## Slide 26: Fetch Logic
Control Logic
  Instr. Valid: Is this instruction valid?
  Need regids: Does this instruction have a register bytes?
  Need valC: Does this instruction have a constant word?

## Slide 27: Fetch Control Logic
bool need_regids =
icode in { IRRMOVL, IOPL, IPUSHL, IPOPL,
IIRMOVL, IRMMOVL, IMRMOVL };
bool instr_valid = icode in
{ INOP, IHALT, IRRMOVL, IIRMOVL, IRMMOVL, IMRMOVL,
IOPL, IJXX, ICALL, IRET, IPUSHL, IPOPL };

## Slide 28: Decode Logic
Register File
  Read ports A, B
  Write ports E, M
  Addresses are register IDs or 8 (no access)
Control Logic
  srcA, srcB: read port addresses
  dstA, dstB: write port addresses

## Slide 29: A Source
OPl rA, rB
valA  R[rA]
Decode
Read operand A
rmmovl rA, D(rB)
valA  R[rA]
Decode
Read operand A
popl rA
valA  R[%esp]
Decode
Read stack pointer
jXX Dest
Decode
No operand
call Dest
valA  R[%esp]
Decode
Read stack pointer
ret
Decode
No operand
int srcA = [
icode in { IRRMOVL, IRMMOVL, IOPL, IPUSHL } : rA;
icode in { IPOPL, IRET } : RESP;
1 : RNONE; # Don't need register
];

## Slide 30: E Destination
None
R[%esp]  valE
Update stack pointer
None
R[rB]  valE
OPl rA, rB
Write-back
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
Write-back
Write-back
Write-back
Write-back
Write-back
Write back result
R[%esp]  valE
Update stack pointer
R[%esp]  valE
Update stack pointer
int dstE = [
icode in { IRRMOVL, IIRMOVL, IOPL} : rB;
icode in { IPUSHL, IPOPL, ICALL, IRET } : RESP;
1 : RNONE; # Don't need register
];

## Slide 31: Execute Logic
Units
  ALU
    Implements 4 required functions
    Generates condition code values
  CC
    Register with 3 condition code bits
  bcond
    Computes branch flag
Control Logic
  Set CC: Should condition code register be loaded?
  ALU A: Input A to ALU
  ALU B: Input B to ALU
  ALU fun: What function should ALU compute?

## Slide 32: ALU A Input
valE  valB + –4
Decrement stack pointer
No operation
valE  valB + 4
Increment stack pointer
valE  valB + valC
Compute effective address
valE  valB OP valA
Perform ALU operation
OPl rA, rB
Execute
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
Execute
Execute
Execute
Execute
Execute
valE  valB + 4
Increment stack pointer
int aluA = [
icode in { IRRMOVL, IOPL } : valA;
icode in { IIRMOVL, IRMMOVL, IMRMOVL } : valC;
icode in { ICALL, IPUSHL } : -4;
icode in { IRET, IPOPL } : 4;
# Other instructions don't need ALU
];

## Slide 33: ALU Operation
valE  valB + –4
Decrement stack pointer
No operation
valE  valB + 4
Increment stack pointer
valE  valB + valC
Compute effective address
valE  valB OP valA
Perform ALU operation
OPl rA, rB
Execute
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
Execute
Execute
Execute
Execute
Execute
valE  valB + 4
Increment stack pointer
int alufun = [
icode == IOPL : ifun;
1 : ALUADD;
];

## Slide 34: Memory Logic
Memory
  Reads or writes memory word
Control Logic
  Mem. read: should word be read?
  Mem. write: should word be written?
  Mem. addr.: Select address
  Mem. data.: Select data

## Slide 35: Memory Address
OPl rA, rB
Memory
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
No operation
M4[valE]  valA
Memory
Write value to memory
valM  M4[valA]
Memory
Read from stack
M4[valE]  valP
Memory
Write return value on stack
valM  M4[valA]
Memory
Read return address
Memory
No operation
int mem_addr = [
icode in { IRMMOVL, IPUSHL, ICALL, IMRMOVL } : valE;
icode in { IPOPL, IRET } : valA;
# Other instructions don't need address
];

## Slide 36: Memory Read
OPl rA, rB
Memory
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
No operation
M4[valE]  valA
Memory
Write value to memory
valM  M4[valA]
Memory
Read from stack
M4[valE]  valP
Memory
Write return value on stack
valM  M4[valA]
Memory
Read return address
Memory
No operation
bool mem_read = icode in { IMRMOVL, IPOPL, IRET };

## Slide 37: PC Update Logic
New PC
  Select next value of PC

## Slide 38: PC Update
OPl rA, rB
rmmovl rA, D(rB)
popl rA
jXX Dest
call Dest
ret
PC  valP
PC update
Update PC
PC  valP
PC update
Update PC
PC  valP
PC update
Update PC
PC  Bch ? valC : valP
PC update
Update PC
PC  valC
PC update
Set PC to destination
PC  valM
PC update
Set PC to return address
int new_pc = [
icode == ICALL : valC;
icode == IJXX && Bch : valC;
icode == IRET : valM;
1 : valP;
];

## Slide 39: SEQ Operation
State
  PC register
  Cond. Code register
  Data memory
  Register file
  All updated as clock rises
Combinational Logic
  ALU
  Control logic
  Memory reads
    Instruction memory
    Register file
    Data memory

## Slide 40: SEQ Operation #2
  state set according to second irmovl instruction
  combinational logic starting to react to state changes

## Slide 41: SEQ Operation #3
  state set according to second irmovl instruction
  combinational logic generates results for addl instruction

## Slide 42: SEQ Operation #4
  state set according to addl instruction
  combinational logic starting to react to state changes

## Slide 43: SEQ Operation #5
  state set according to addl instruction
  combinational logic generates results for je instruction

## Slide 44: SEQ Summary
Implementation
  Express every instruction as series of simple steps
  Follow same general flow for each instruction type
  Assemble registers, memories, predesigned combinational blocks
  Connect with control logic
Limitations
  Too slow to be practical
  In one cycle, must propagate through instruction memory, register file, ALU, and data memory
  Would need to run clock very slowly
  Hardware units only active for fraction of clock cycle