## Slide 1
Randal E. Bryant
Carnegie Mellon University
CS:APP
CS:APP Chapter 4
Computer Architecture
Pipelined
Implementation
Part II
http://csapp.cs.cmu.edu

## Slide 2: Overview
  Make the pipelined processor work!
Data Hazards
  Instruction having register R as source follows shortly after instruction having register R as destination
  Common condition, don’t want to slow down pipeline
Control Hazards
  Mispredict conditional branch
    Our design predicts all branches as being taken
    Naïve pipeline executes two extra instructions
  Getting return address for ret instruction
    Naïve pipeline executes three extra instructions
Making Sure It Really Works
  What if multiple special cases happen simultaneously?

## Slide 3: Pipeline Stages
Fetch
  Select current PC
  Read instruction
  Compute incremented PC
Decode
  Read program registers
Execute
  Operate ALU
Memory
  Read or write data memory
Write Back
  Update register file

## Slide 4: PIPE- Hardware
  Pipeline registers hold intermediate values from instruction execution
Forward (Upward) Paths
  Values passed from one stage to next
  Cannot jump past stages
    e.g., valC passes through decode

## Slide 5: Data Dependencies: 2 Nop’s
0x000:
irmovl
$10,%
edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x006:
irmovl
$3,%
eax
F
D
E
M
W
F
D
E
M
W
0x00c:
nop
F
D
E
M
W
F
D
E
M
W
0x00d:
nop
F
D
E
M
W
F
D
E
M
W
0x00e:
addl
%
edx
,%
eax
F
D
E
M
W
F
D
E
M
W
0x010: halt
F
D
E
M
W
F
D
E
M
W
10
# demo-h2.ys
W
R[
%
eax
]

3
D
valA

R[
%
edx
]
=
10
valB

R[
%
eax
]
=
0
•
•
•
W
R[
%
eax
]

3
W
R[
%
eax
]

3
D
valA

R[
%
edx
]
=
10
valB

R[
%
eax
]
=
0
D
valA

R[
%
edx
]
=
10
valB

R[
%
eax
]
=
0
•
•
•
Cycle 6
Error

## Slide 6: Data Dependencies: No Nop
0x000:
irmovl
$10,%
edx
1
2
3
4
5
6
7
8
F
D
E
M
W
0x006:
irmovl
$3,%
eax
F
D
E
M
W
F
D
E
M
W
0x00c:
addl
%
edx
,%
eax
F
D
E
M
W
0x00e: halt
# demo-h0.ys
E
D
valA

R[
%
edx
]
=
0
valB

R[
%
eax
]
=
0
D
valA

R[
%
edx
]
=
0
valB

R[
%
eax
]
=
0
Cycle 4
Error
M
M_
valE
= 10
M_
dstE
=
%
edx
e_
valE

0 + 3 = 3
E_
dstE
=
%
eax

## Slide 7: Stalling for Data Dependencies
  If instruction follows too closely after one that writes register, slow it down
  Hold instruction in decode
  Dynamically inject nop into execute stage
0x000: irmovl $10,%edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x006: irmovl $3,%eax
F
D
E
M
W
0x00c: nop
F
D
E
M
W
bubble
F
E
M
W
0x00e: addl %edx,%eax
D
D
E
M
W
0x010: halt
F
D
E
M
W
10
# demo-h2.ys
F
F
D
E
M
W
0x00d: nop
11

## Slide 8: Stall Condition
Source Registers
  srcA and srcB of current instruction in decode stage
Destination Registers
  dstE and dstM fields
  Instructions in execute, memory, and write-back stages
Special Case
  Don’t stall for register ID 8
    Indicates absence of register operand
E
M
W
F
D
Instruction
memory
Instruction
memory
PC
increment
PC
increment
Register
file
Register
file
ALU
ALU
Data
memory
Data
memory
Select
PC
rB
dstE
dstM
Select
A
ALU
A
ALU
B
Mem
.
control
Addr
srcA
srcB
read
write
ALU
fun.
Fetch
Decode
Execute
Memory
Write back
icode
data out
data in
A
B
M
E
M_
valA
W_
valM
W_
valE
M_
valA
W_
valM
d_
rvalA
f_PC
Predict
PC
valE
valM
dstE
dstM
Bch
icode
valE
valA
dstE
dstM
icode
ifun
valC
valA
valB
dstE
dstM
srcA
srcB
valC
valP
icode
ifun
rA
predPC
CC
CC
d_
srcB
d_
srcA
e_Bch
M_Bch

## Slide 9: Detecting Stall Condition
0x000: irmovl $10,%edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x006: irmovl $3,%eax
F
D
E
M
W
0x00c: nop
F
D
E
M
W
bubble
F
E
M
W
0x00e: addl %edx,%eax
D
D
E
M
W
0x010: halt
F
D
E
M
W
10
# demo-h2.ys
F
F
D
E
M
W
0x00d: nop
11
Cycle 6
W
D
•
•
•
W_dstE = %eax
W_valE = 3
srcA = %edx
srcB = %eax

## Slide 10: Stalling X3
0x000: irmovl $10,%edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x006: irmovl $3,%eax
F
D
E
M
W
bubble
F
E
M
W
bubble
D
E
M
W
0x00c: addl %edx,%eax
D
D
E
M
W
0x00e: halt
F
D
E
M
W
10
# demo-h0.ys
F
F
D
F
E
M
W
bubble
11
Cycle 4
•
•
•
W
W_dstE = %eax
D
srcA = %edx
srcB = %eax
•
•
•
M
M_dstE = %eax
D
srcA = %edx
srcB = %eax
E
E_dstE = %eax
D
srcA = %edx
srcB = %eax
Cycle 5
Cycle 6

## Slide 11: What Happens When Stalling?
  Stalling instruction held back in decode stage
  Following instruction stays in fetch stage
  Bubbles injected into execute stage
    Like dynamically generated nop’s
    Move through later stages
0x000: irmovl $10,%edx
0x006: irmovl $3,%eax
0x00c: addl %edx,%eax
Cycle 4
0x00e: halt
0x000: irmovl $10,%edx
0x006: irmovl $3,%eax
0x00c: addl %edx,%eax
# demo-h0.ys
0x00e: halt
0x000: irmovl $10,%edx
0x006: irmovl $3,%eax
bubble
0x00c: addl %edx,%eax
Cycle 5
0x00e: halt
0x006: irmovl $3,%eax
bubble
0x00c: addl %edx,%eax
bubble
Cycle 6
0x00e: halt
bubble
bubble
0x00c: addl %edx,%eax
bubble
Cycle 7
0x00e: halt
bubble
bubble
Cycle 8
0x00c: addl %edx,%eax
0x00e: halt
Write Back
Memory
Execute
Decode
Fetch

## Slide 12: Implementing Stalling
Pipeline Control
  Combinational logic detects stall condition
  Sets mode signals for how pipeline registers should update

## Slide 13: Pipeline Register Modes
Rising
clock
Rising
clock


Output = y
y
y
Rising
clock
Rising
clock


Output = x
x
x
x
x
n
o
p
Rising
clock
Rising
clock


Output =
nop
Output = x
Input = y
stall
= 0
bubble
= 0
x
x
Normal
Output = x
Input = y
stall
= 1
bubble
= 0
x
x
Stall
Output = x
Input = y
stall
= 0
bubble
= 1
Bubble

## Slide 14: Data Forwarding
Naïve Pipeline
  Register isn’t written until completion of write-back stage
  Source operands read from register file in decode stage
    Needs to be in register file at start of stage
Observation
  Value generated in execute or memory stage
Trick
  Pass value directly from generating instruction to decode stage
  Needs to be available at end of decode stage

## Slide 15: Data Forwarding Example
  irmovl in write-back stage
  Destination value in W pipeline register
  Forward as valB for decode stage
0x000:
irmovl
$10,%
edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x006:
irmovl
$3,%
eax
F
D
E
M
W
F
D
E
M
W
0x00c:
nop
F
D
E
M
W
F
D
E
M
W
0x00d:
nop
F
D
E
M
W
F
D
E
M
W
0x00e:
addl
%
edx
,%
eax
F
D
E
M
W
F
D
E
M
W
0x010: halt
F
D
E
M
W
F
D
E
M
W
10
# demo-h2.ys
Cycle 6
W
R[
%
eax
]

3
D
valA

R[
%
edx
]
=
10
valB

W_
valE
=
3
•
•
•
W_
dstE
=
%
eax
W_
valE
= 3
srcA
=
%
edx
srcB
=
%
eax

## Slide 16: Bypass Paths
Decode Stage
  Forwarding logic selects valA and valB
  Normally from register file
  Forwarding: get valA or valB from later pipeline stage
Forwarding Sources
  Execute: valE
  Memory: valE, valM
  Write back: valE, valM

## Slide 17: Data Forwarding Example #2
Register %edx
  Generated by ALU during previous cycle
  Forward from memory as valA
Register %eax
  Value just generated by ALU
  Forward from execute as valB

## Slide 18: Implementing Forwarding
  Add additional feedback paths from E, M, and W pipeline registers into decode stage
  Create logic blocks to select from multiple sources for valA and valB in decode stage

## Slide 19: Implementing Forwarding
## What should be the A value?
int new_E_valA = [
# Use incremented PC
D_icode in { ICALL, IJXX } : D_valP;
# Forward valE from execute
d_srcA == E_dstE : e_valE;
# Forward valM from memory
d_srcA == M_dstM : m_valM;
# Forward valE from memory
d_srcA == M_dstE : M_valE;
# Forward valM from write back d_srcA == W_dstM : W_valM;
# Forward valE from write back
d_srcA == W_dstE : W_valE;
# Use value read from register file
1 : d_rvalA;
];

## Slide 20: Limitation of Forwarding
Load-use dependency
  Value needed by end of decode stage in cycle 7
  Value read from memory in memory stage of cycle 8

## Slide 21: Avoiding Load/Use Hazard
  Stall using instruction for one cycle
  Can then pick up loaded value by forwarding from memory stage

## Slide 22: Detecting Load/Use Hazard
Condition | Trigger
Load/Use Hazard | E_icode in { IMRMOVL, IPOPL } && E_dstM in { d_srcA, d_srcB }

## Slide 23: Control for Load/Use Hazard
  Stall instructions in fetch and decode stages
  Inject bubble into execute stage
0x000:
irmovl
$128,%
edx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x006:
irmovl
$3,%
ecx
F
D
E
M
W
F
D
E
M
W
0x00c:
rmmovl
%
ecx
, 0(%
edx
)
F
D
E
M
W
F
D
E
M
W
0x012:
irmovl
$10,%
ebx
F
D
E
M
W
F
D
E
M
W
0x018:
mrmovl
0(%
edx
),
%
eax
# Load %
eax
F
D
E
M
W
F
D
E
M
W
# demo
-
luh
.
ys
0x01e:
addl
%
ebx
,
%
eax
# Use %
eax
0x020: halt
F
D
E
M
W
E
M
W
10
D
D
E
M
W
11
bubble
F
D
E
M
W
F
F
12
Condition | F | D | E | M | W
Load/Use Hazard | stall | stall | bubble | normal | normal

## Slide 24: Branch Misprediction Example
  Should only execute first 8 instructions
0x000: xorl %eax,%eax
0x002: jne t # Not taken
0x007: irmovl $1, %eax # Fall through
0x00d: nop
0x00e: nop
0x00f: nop
0x010: halt
0x011: t: irmovl $3, %edx # Target (Should not execute)
0x017: irmovl $4, %ecx # Should not execute
0x01d: irmovl $5, %edx # Should not execute
demo-j.ys

## Slide 25: Handling Misprediction
Predict branch as taken
  Fetch 2 instructions at target
Cancel when mispredicted
  Detect branch not-taken in execute stage
  On following cycle, replace instructions in execute and decode by bubbles
  No side effects have occurred yet

## Slide 26: Detecting Mispredicted Branch
Condition | Trigger
Mispredicted Branch | E_icode = IJXX & !e_Bch

## Slide 27: Control for Misprediction
Condition | F | D | E | M | W
Mispredicted Branch | normal | bubble | bubble | normal | normal

## Slide 28: Return Example
0x000: irmovl Stack,%esp # Initialize stack pointer
0x006: call p # Procedure call
0x00b: irmovl $5,%esi # Return point
0x011: halt
0x020: .pos 0x20
0x020: p: irmovl $-1,%edi # procedure
0x026: ret
0x027: irmovl $1,%eax # Should not be executed
0x02d: irmovl $2,%ecx # Should not be executed
0x033: irmovl $3,%edx # Should not be executed
0x039: irmovl $4,%ebx # Should not be executed
0x100: .pos 0x100
0x100: Stack: # Stack: Stack pointer
  Previously executed three additional instructions
demo-retb.ys

## Slide 29: Correct Return Example
0x026: ret
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
0x00b:
irmovl
$5,%
esi
# Return
F
D
E
M
W
# demo
-
retb
F
D
E
M
W
F
valC

5
rB

%
esi
F
valC

5
rB

%
esi
W
valM
=
0x0b
W
valM
=
0x0b
•
•
•
  As ret passes through pipeline, stall at fetch stage
    While in decode, execute, and memory stage
  Inject bubble into decode stage
  Release stall when reach write-back stage

## Slide 30: Detecting Return
Condition | Trigger
Processing ret | IRET in { D_icode, E_icode, M_icode }

## Slide 31: Control for Return
0x026: ret
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
0x00b:
irmovl
$5,%
esi
# Return
F
D
E
M
W
# demo
-
retb
F
D
E
M
W
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal

## Slide 32: Special Control Cases
Detection
Action (on next cycle)
Condition | Trigger
Processing ret | IRET in { D_icode, E_icode, M_icode }
Load/Use Hazard | E_icode in { IMRMOVL, IPOPL } && E_dstM in { d_srcA, d_srcB }
Mispredicted Branch | E_icode = IJXX & !e_Bch
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Mispredicted Branch | normal | bubble | bubble | normal | normal

## Slide 33: Implementing Pipeline Control
  Combinational logic generates pipeline control signals
  Action occurs at start of following cycle

## Slide 34: Initial Version of Pipeline Control
bool F_stall =
# Conditions for a load/use hazard
E_icode in { IMRMOVL, IPOPL } && E_dstM in { d_srcA, d_srcB } ||
# Stalling at fetch while ret passes through pipeline
IRET in { D_icode, E_icode, M_icode };
bool D_stall =
# Conditions for a load/use hazard
E_icode in { IMRMOVL, IPOPL } && E_dstM in { d_srcA, d_srcB };
bool D_bubble =
# Mispredicted branch
(E_icode == IJXX && !e_Bch) ||
# Stalling at fetch while ret passes through pipeline
IRET in { D_icode, E_icode, M_icode };
bool E_bubble =
# Mispredicted branch
(E_icode == IJXX && !e_Bch) ||
# Load/use hazard
E_icode in { IMRMOVL, IPOPL } && E_dstM in { d_srcA, d_srcB};

## Slide 35: Control Combinations
  Special cases that can arise on same clock cycle
Combination A
  Not-taken branch
  ret instruction at branch target
Combination B
  Instruction that reads from memory to %esp
  Followed by ret instruction

## Slide 36: Control Combination A
  Should handle as mispredicted branch
  Stalls F pipeline register
  But PC selection logic will be using M_valM anyhow
JXX
E
D
M
Mispredict
JXX
E
D
M
Mispredict
E
ret
D
M
ret
1
E
ret
D
M
ret
1
E
ret
D
M
ret
1
Combination A
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Mispredicted Branch | normal | bubble | bubble | normal | normal
Combination | stall | bubble | bubble | normal | normal

## Slide 37: Control Combination B
  Would attempt to bubble and stall pipeline register D
  Signaled by processor as pipeline error
Load
E
Use
D
M
Load/use
E
ret
D
M
ret
1
E
ret
D
M
ret
1
E
ret
D
M
ret
1
Combination B
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Combination | stall | bubble + stall | bubble | normal | normal

## Slide 38: Handling Control Combination B
  Load/use hazard should get priority
  ret instruction should be held in decode stage for additional cycle
Load
E
Use
D
M
Load/use
E
ret
D
M
ret
1
E
ret
D
M
ret
1
E
ret
D
M
ret
1
Combination B
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Combination | stall | stall | bubble | normal | normal

## Slide 39: Corrected Pipeline Control Logic
  Load/use hazard should get priority
  ret instruction should be held in decode stage for additional cycle
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Combination | stall | stall | bubble | normal | normal
bool D_bubble =
# Mispredicted branch
(E_icode == IJXX && !e_Bch) ||
# Stalling at fetch while ret passes through pipeline
IRET in { D_icode, E_icode, M_icode }
# but not condition for a load/use hazard
&& !(E_icode in { IMRMOVL, IPOPL }
&& E_dstM in { d_srcA, d_srcB });

## Slide 40: Pipeline Summary
Data Hazards
  Most handled by forwarding
    No performance penalty
  Load/use hazard requires one cycle stall
Control Hazards
  Cancel instructions when detect mispredicted branch
    Two clock cycles wasted
  Stall fetch stage while ret passes through pipeline
    Three clock cycles wasted
Control Combinations
  Must analyze carefully
  First version had subtle bug
    Only arises with unusual instruction combination