## Slide 1: Introduction to Computer Systems
Topics:
  Theme
  Five great realities of computer systems
  How this fits within CS curriculum
CS 213 F ’02
class01a.ppt
15-213
“The Class That Gives CMU Its Zip!”
Randal E. Bryant
August 27, 2002

## Slide 2: Course Theme
  Abstraction is good, but don’t forget reality!
Courses to date emphasize abstraction
  Abstract data types
  Asymptotic analysis
These abstractions have limits
  Especially in the presence of bugs
  Need to understand underlying implementations
Useful outcomes
  Become more effective programmers
    Able to find and eliminate bugs efficiently
    Able to tune program performance
  Prepare for later “systems” classes in CS & ECE
    Compilers, Operating Systems, Networks, Computer Architecture, Embedded Systems

## Slide 3: Great Reality #1
Int’s are not Integers, Float’s are not Reals
Examples
  Is x2 ≥ 0?
    Float’s: Yes!
    Int’s:
      40000 * 40000 --> 1600000000
      50000 * 50000 --> ??
  Is (x + y) + z = x + (y + z)?
    Unsigned & Signed Int’s: Yes!
    Float’s:
      (1e20 + -1e20) + 3.14 --> 3.14
      1e20 + (-1e20 + 3.14) --> ??

## Slide 4: Computer Arithmetic
Does not generate random values
  Arithmetic operations have important mathematical properties
Cannot assume “usual” properties
  Due to finiteness of representations
  Integer operations satisfy “ring” properties
    Commutativity, associativity, distributivity
  Floating point operations satisfy “ordering” properties
    Monotonicity, values of signs
Observation
  Need to understand which abstractions apply in which contexts
  Important issues for compiler writers and serious application programmers

## Slide 5: Great Reality #2
You’ve got to know assembly
Chances are, you’ll never write program in assembly
  Compilers are much better & more patient than you are
Understanding assembly key to machine-level execution model
  Behavior of programs in presence of bugs
    High-level language model breaks down
  Tuning program performance
    Understanding sources of program inefficiency
  Implementing system software
    Compiler has machine code as target
    Operating systems must manage process state

## Slide 6: Assembly Code Example
Time Stamp Counter
  Special 64-bit register in Intel-compatible machines
  Incremented every clock cycle
  Read with rdtsc instruction
Application
  Measure time required by procedure
    In units of clock cycles
  double t;
  start_counter();
  P();
  t = get_counter();
  printf("P required %f clock cycles\n", t);

## Slide 7: Code to Read Counter
  Write small amount of assembly code using GCC’s asm facility
  Inserts assembly code into machine code generated by compiler
static unsigned cyc_hi = 0;
static unsigned cyc_lo = 0;
/* Set *hi and *lo to the high and low order bits
of the cycle counter.
*/
void access_counter(unsigned *hi, unsigned *lo)
{
asm("rdtsc; movl %%edx,%0; movl %%eax,%1"
: "=r" (*hi), "=r" (*lo)
:
: "%edx", "%eax");
}

## Slide 8: Code to Read Counter
/* Record the current value of the cycle counter. */
void start_counter()
{
access_counter(&cyc_hi, &cyc_lo);
}
/* Number of cycles since the last call to start_counter. */
double get_counter()
{
unsigned ncyc_hi, ncyc_lo;
unsigned hi, lo, borrow;
/* Get cycle counter */
access_counter(&ncyc_hi, &ncyc_lo);
/* Do double precision subtraction */
lo = ncyc_lo - cyc_lo;
borrow = lo > ncyc_lo;
hi = ncyc_hi - cyc_hi - borrow;
return (double) hi * (1 << 30) * 4 + lo;
}

## Slide 9: Measuring Time
Trickier than it Might Look
  Many sources of variation
Example
  Sum integers from 1 to n
    n Cycles Cycles/n
    100 961 9.61
    1,000 8,407 8.41
    1,000 8,426 8.43
    10,000 82,861 8.29
    10,000 82,876 8.29
    1,000,000 8,419,907 8.42
    1,000,000 8,425,181 8.43
    1,000,000,000 8,371,2305,591 8.37

## Slide 10: Great Reality #3
Memory Matters
Memory is not unbounded
  It must be allocated and managed
  Many applications are memory dominated
Memory referencing bugs especially pernicious
  Effects are distant in both time and space
Memory performance is not uniform
  Cache and virtual memory effects can greatly affect program performance
  Adapting program to characteristics of memory system can lead to major speed improvements

## Slide 11: Memory Referencing Bug Example
main ()
{
long int a[2];
double d = 3.14;
a[2] = 1073741824; /* Out of bounds reference */
printf("d = %.15g\n", d);
exit(0);
}
A
lph
a
M
I
PS
Linux
-g
5.30498947741318e-315
3.1399998664856
3.14
-O
3.14
3.14
3.14
(Linux version gives correct result, but implementing as separate function gives segmentation fault.)

## Slide 12: Memory Referencing Errors
C and C++ do not provide any memory protection
  Out of bounds array references
  Invalid pointer values
  Abuses of malloc/free
Can lead to nasty bugs
  Whether or not bug has any effect depends on system and compiler
  Action at a distance
    Corrupted object logically unrelated to one being accessed
    Effect of bug may be first observed long after it is generated
How can I deal with this?
  Program in Java, Lisp, or ML
  Understand what possible interactions may occur
  Use or develop tools to detect referencing errors

## Slide 13: Memory Performance Example
Implementations of Matrix Multiplication
  Multiple ways to nest loops
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}

## Slide 14: Matmult Performance (Alpha 21164)
0
20
40
60
80
100
120
140
160
matrix size (n)
ijk
ikj
jik
jki
kij
kji
Too big for L1 Cache
Too big for L2 Cache

## Slide 15: Blocked matmult perf (Alpha 21164)
0
20
40
60
80
100
120
140
160
50
75
100
125
150
175
200
225
250
275
300
325
350
375
400
425
450
475
500
matrix size (n)
bijk
bikj
ijk
ikj

## Slide 16: Great Reality #4
There’s more to performance than asymptotic complexity
Constant factors matter too!
  Easily see 10:1 performance range depending on how code written
  Must optimize at multiple levels: algorithm, data representations, procedures, and loops
Must understand system to optimize performance
  How programs compiled and executed
  How to measure program performance and identify bottlenecks
  How to improve performance without destroying code modularity and generality

## Slide 17: Great Reality #5
Computers do more than execute programs
They need to get data in and out
  I/O system critical to program reliability and performance
They communicate with each other over networks
  Many system-level issues arise in presence of network
    Concurrent operations by autonomous processes
    Coping with unreliable media
    Cross platform compatibility
    Complex performance issues

## Slide 18: Role within Curriculum
Transition from Abstract to Concrete!
  From: high-level language model
  To: underlying implementation
CS 211
Fundamental
Structures
CS 213
Systems
CS 412
Operating
Systems
CS 411
Compilers
Processes
Mem. Mgmt
Machine Code
Optimization
Data Structures
Applications
Programming
CS 212
Execution
Models
CS 441
Networks
Network
Protocols
ECE 347
Architecture
ECE 349
Embedded
Systems
Exec. Model
Memory System
CS 113
C Programming

## Slide 19: Course Perspective
Most Systems Courses are Builder-Centric
  Computer Architecture
    Design pipelined processor in Verilog
  Operating Systems
    Implement large portions of operating system
  Compilers
    Write compiler for simple language
  Networking
    Implement and simulate network protocols

## Slide 20: Course Perspective (Cont.)
Our Course is Programmer-Centric
  Purpose is to show how by knowing more about the underlying system, one can be more effective as a programmer
  Enable you to
    Write programs that are more reliable and efficient
    Incorporate features that require hooks into OS
      E.g., concurrency, signal handlers
  Not just a course for dedicated hackers
    We bring out the hidden hacker in everyone
  Cover material in this course that you won’t see elsewhere