## Slide 1: P6/Linux Memory System Oct. 31, 2002
Topics
  P6 address translation
  Linux memory management
  Linux page fault handling
  memory mapping
class20.ppt
15-213 “The course that gives CMU its Zip!”

## Slide 2: Intel P6
Internal Designation for Successor to Pentium
  Which had internal designation P5
Fundamentally Different from Pentium
  Out-of-order, superscalar operation
  Designed to handle server applications
    Requires high performance memory system
Resulting Processors
  PentiumPro (1996)
  Pentium II (1997)
    Incorporated MMX instructions
      special instructions for parallel processing
    L2 cache on same chip
  Pentium III (1999)
    Incorporated Streaming SIMD Extensions
      More instructions for parallel processing

## Slide 3: P6 Memory System
bus interface unit
DRAM
external system bus (e.g. PCI)
instruction
fetch unit
L1
i-cache
L2
cache
cache bus
L1
d-cache
inst
TLB
data
TLB
processor package
32 bit address space
4 KB page size
L1, L2, and TLBs
  4-way set associative
inst TLB
  32 entries
  8 sets
data TLB
  64 entries
  16 sets
L1 i-cache and d-cache
  16 KB
  32 B line size
  128 sets
L2 cache
  unified
  128 KB -- 2 MB

## Slide 4: Review of Abbreviations
Symbols:
  Components of the virtual address (VA)
    TLBI: TLB index
    TLBT: TLB tag
    VPO: virtual page offset
    VPN: virtual page number
  Components of the physical address (PA)
    PPO: physical page offset (same as VPO)
    PPN: physical page number
    CO: byte offset within cache line
    CI: cache index
    CT: cache tag

## Slide 5: Overview of P6 Address Translation
CPU
VPN
VPO
20
12
TLBT
TLBI
4
16
virtual address (VA)
...
TLB (16 sets, 4 entries/set)
VPN1
VPN2
10
10
PDE
PTE
PDBR
PPN
PPO
20
12
Page tables
TLB
miss
TLB
hit
physical
address (PA)
result
32
...
CT
CO
20
5
CI
7
L2 and DRAM
L1 (128 sets, 4 lines/set)
L1
hit
L1
miss

## Slide 6: P6 2-level Page Table Structure
Page directory
  1024 4-byte page directory entries (PDEs) that point to page tables
  one page directory per process.
  page directory must be in memory when its process is running
  always pointed to by PDBR
Page tables:
  1024 4-byte page table entries (PTEs) that point to pages.
  page tables can be paged in and out.
page directory
...
Up to 1024 page tables
1024
PTEs
1024
PTEs
1024
PTEs
...
1024
PDEs

## Slide 7: P6 Page Directory Entry (PDE)
Page table physical base addr
Avail
G
PS
A
CD
WT
U/S
R/W
P=1
Page table physical base address: 20 most significant bits of physical page table address (forces page tables to be 4KB aligned)
Avail: These bits available for system programmers
G: global page (don’t evict from TLB on task switch)
PS: page size 4K (0) or 4M (1)
A: accessed (set by MMU on reads and writes, cleared by software)
CD: cache disabled (1) or enabled (0)
WT: write-through or write-back cache policy for this page table
U/S: user or supervisor mode access
R/W: read-only or read-write access
P: page table is present in memory (1) or not (0)
31
12
11
9
8
7
6
5
4
3
2
1
0
Available for OS (page table location in secondary storage)
P=0
31
0
1

## Slide 8: P6 Page Table Entry (PTE)
Page physical base address
Avail
G
0
D
A
CD
WT
U/S
R/W
P=1
Page base address: 20 most significant bits of physical page address (forces pages to be 4 KB aligned)
Avail: available for system programmers
G: global page (don’t evict from TLB on task switch)
D: dirty (set by MMU on writes)
A: accessed (set by MMU on reads and writes)
CD: cache disabled or enabled
WT: write-through or write-back cache policy for this page
U/S: user/supervisor
R/W: read/write
P: page is present in physical memory (1) or not (0)
31
12
11
9
8
7
6
5
4
3
2
1
0
Available for OS (page location in secondary storage)
P=0
31
0
1

## Slide 9: How P6 Page Tables Map Virtual Addresses to Physical Ones
PDE
PDBR
physical address
of page table base
(if P=1)
physical
address
of page base
(if P=1)
physical address
of page directory
word offset into
page directory
word offset into
page table
page directory
page table
VPN1
10
VPO
10
12
VPN2
Virtual address
PTE
PPN
PPO
20
12
Physical address
word offset into
physical and virtual
page

## Slide 10: Representation of Virtual Address Space
Simplified Example
  16 page virtual address space
Flags
  P: Is entry in physical memory?
  M: Has this part of VA space been mapped?
Page Directory
PT 3
P=1, M=1
P=1, M=1
P=0, M=0
P=0, M=1
•
•
•
•
P=1, M=1
P=0, M=0
P=1, M=1
P=0, M=1
•
•
•
•
P=1, M=1
P=0, M=0
P=1, M=1
P=0, M=1
•
•
•
•
P=0, M=1
P=0, M=1
P=0, M=0
P=0, M=0
•
•
•
•
PT 2
PT 0
Page 0
Page 1
Page 2
Page 3
Page 4
Page 5
Page 6
Page 7
Page 8
Page 9
Page 10
Page 11
Page 12
Page 13
Page 14
Page 15
Mem Addr
Disk Addr
In Mem
On Disk
Unmapped

## Slide 11: P6 TLB Translation
CPU
VPN
VPO
20
12
TLBT
TLBI
4
16
virtual address (VA)
...
TLB (16 sets, 4 entries/set)
VPN1
VPN2
10
10
PDE
PTE
PDBR
PPN
PPO
20
12
Page tables
TLB
miss
TLB
hit
physical
address (PA)
result
32
...
CT
CO
20
5
CI
7
L2 andDRAM
L1 (128 sets, 4 lines/set)
L1
hit
L1
miss

## Slide 12: P6 TLB
TLB entry (not all documented, so this is speculative):
  V: indicates a valid (1) or invalid (0) TLB entry
  PD: is this entry a PDE (1) or a PTE (0)?
  tag: disambiguates entries cached in the same set
  PDE/PTE: page directory or page table entry
Structure of the data TLB:
  16 sets, 4 entries/set
PDE/PTE
Tag
PD
V
1
1
16
32
entry
entry
entry
entry
entry
entry
entry
entry
entry
entry
entry
entry
entry
entry
entry
entry
...
set 0
set 1
set 2
set 15

## Slide 13: Translating with the P6 TLB
1. Partition VPN into TLBT and TLBI.
2. Is the PTE for VPN cached in set TLBI?
  3. Yes: then build physical address.
4. No: then read PTE (and PDE if not cached) from memory and build physical address.
CPU
VPN
VPO
20
12
TLBT
TLBI
4
16
virtual address
PDE
PTE
...
TLB
miss
TLB
hit
page table translation
PPN
PPO
20
12
physical address
1
2
3
4

## Slide 14: P6 page table translation
CPU
VPN
VPO
20
12
TLBT
TLBI
4
16
virtual address (VA)
...
TLB (16 sets, 4 entries/set)
VPN1
VPN2
10
10
PDE
PTE
PDBR
PPN
PPO
20
12
Page tables
TLB
miss
TLB
hit
physical
address (PA)
result
32
...
CT
CO
20
5
CI
7
L2 andDRAM
L1 (128 sets, 4 lines/set)
L1
hit
L1
miss

## Slide 15: Translating with the P6 Page Tables (case 1/1)
Case 1/1: page table and page present.
MMU Action:
  MMU builds physical address and fetches data word.
OS action
  none
VPN
VPN1
VPN2
PDE
PDBR
PPN
PPO
20
12
20
VPO
12
p=1
PTE
p=1
Data page
data
Page directory
Page table
Mem
Disk

## Slide 16: Translating with the P6 Page Tables (case 1/0)
Case 1/0: page table present but page missing.
MMU Action:
  page fault exception
  handler receives the following args:
    VA that caused fault
    fault caused by non-present page or page-level protection violation
    read/write
    user/supervisor
VPN
VPN1
VPN2
PDE
PDBR
20
VPO
12
p=1
PTE
Page directory
Page table
Mem
Disk
Data page
data
p=0

## Slide 17: Translating with the P6 Page Tables (case 1/0, cont)
OS Action:
  Check for a legal virtual address.
  Read PTE through PDE.
  Find free physical page (swapping out current page if necessary)
  Read virtual page from disk and copy to virtual page
  Restart faulting instruction by returning from exception handler.
VPN
VPN1
VPN2
PDE
PDBR
20
VPO
12
p=1
PTE
p=1
Page directory
Page table
Data page
data
PPN
PPO
20
12
Mem
Disk

## Slide 18: Translating with the P6 Page Tables (case 0/1)
Case 0/1: page table missing but page present.
Introduces consistency issue.
  potentially every page out requires update of disk page table.
Linux disallows this
  if a page table is swapped out, then swap out its data pages too.
VPN
VPN1
VPN2
PDE
PDBR
20
VPO
12
p=0
PTE
p=1
Page directory
Page table
Mem
Disk
Data page
data

## Slide 19: Translating with the P6 Page Tables (case 0/0)
Case 0/0: page table and page missing.
MMU Action:
  page fault exception
VPN
VPN1
VPN2
PDE
PDBR
20
VPO
12
p=0
PTE
Page directory
Page table
Mem
Disk
Data page
data
p=0

## Slide 20: Translating with the P6 Page Tables (case 0/0, cont)
OS action:
  swap in page table.
  restart faulting instruction by returning from handler.
Like case 0/1 from here on.
VPN
VPN1
VPN2
PDE
PDBR
20
VPO
12
p=1
PTE
Page directory
Page table
Mem
Disk
Data page
data
p=0

## Slide 21: P6 L1 Cache Access
CPU
VPN
VPO
20
12
TLBT
TLBI
4
16
virtual address (VA)
...
TLB (16 sets, 4 entries/set)
VPN1
VPN2
10
10
PDE
PTE
PDBR
PPN
PPO
20
12
Page tables
TLB
miss
TLB
hit
physical
address (PA)
result
32
...
CT
CO
20
5
CI
7
L2 andDRAM
L1 (128 sets, 4 lines/set)
L1
hit
L1
miss

## Slide 22: L1 Cache Access
Partition physical address into CO, CI, and CT.
Use CT to determine if line containing word at address PA is cached in set CI.
If no: check L2.
If yes: extract word at byte offset CO and return to processor.
physical
address (PA)
data
32
...
CT
CO
20
5
CI
7
L2 andDRAM
L1 (128 sets, 4 lines/set)
L1
hit
L1
miss

## Slide 23: Speeding Up L1 Access
Observation
  Bits that determine CI identical in virtual and physical address
  Can index into cache while address translation taking place
  Then check with CT from physical address
  “Virtually indexed, physically tagged”
  Cache carefully sized to make this possible
Physical address (PA)
CT
CO
20
5
CI
7
virtual
address (VA)
VPN
VPO
20
12
PPO
PPN
Addr.
Trans.
No
Change
CI
Tag Check

## Slide 24: Linux Organizes VM as Collection of “Areas”
vm_next
vm_next
task_struct
mm_struct
pgd
mm
mmap
vm_area_struct
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_next
vm_start
process virtual memory
text
data
shared libraries
0
0x08048000
0x0804a020
0x40000000
  pgd:
    page directory address
  vm_prot:
    read/write permissions for this area
  vm_flags
    shared with other processes or private to this process
vm_flags
vm_flags
vm_flags

## Slide 25: Linux Page Fault Handling
vm_area_struct
vm_end
r/o
vm_next
vm_start
vm_end
r/w
vm_next
vm_start
vm_end
r/o
vm_next
vm_start
process virtual memory
text
data
shared libraries
0
Is the VA legal?
  i.e. is it in an area defined by a vm_area_struct?
  if not then signal segmentation violation (e.g. (1))
Is the operation legal?
  i.e., can the process read/write this area?
  if not then signal protection violation (e.g., (2))
If OK, handle fault
  e.g., (3)
write
read
read
1
2
3

## Slide 26: Memory Mapping
Creation of new VM area done via “memory mapping”
  create new vm_area_struct and page tables for area
  area can be backed by (i.e., get its initial values from) :
    regular file on disk (e.g., an executable object file)
      initial page bytes come from a section of a file
    nothing (e.g., bss)
      initial page bytes are zeros
  dirty pages are swapped back and forth between a special swap file.
Key point: no virtual pages are copied into physical memory until they are referenced!
  known as “demand paging”
  crucial for time and space efficiency

## Slide 27: User-Level Memory Mapping
void *mmap(void *start, int len,
int prot, int flags, int fd, int offset)
  map len bytes starting at offset offset of the file specified by file description fd, preferably at address start (usually 0 for don’t care).
    prot: MAP_READ, MAP_WRITE
    flags: MAP_PRIVATE, MAP_SHARED
  return a pointer to the mapped area.
  Example: fast file copy
    useful for applications like Web servers that need to quickly copy files.
    mmap allows file transfers without copying into user space.

## Slide 28: mmap() Example: Fast File Copy
#include <unistd.h>
#include <sys/mman.h>
#include <sys/types.h>
#include <sys/stat.h>
#include <fcntl.h>
/*
* mmap.c - a program that uses mmap
* to copy itself to stdout
*/
int main() {
struct stat stat;
int i, fd, size;
char *bufp;
/* open the file & get its size*/
fd = open("./mmap.c", O_RDONLY);
fstat(fd, &stat);
size = stat.st_size;
/* map the file to a new VM area */
bufp = mmap(0, size, PROT_READ,
MAP_PRIVATE, fd, 0);
/* write the VM area to stdout */
write(1, bufp, size);
}

## Slide 29: Exec() Revisited
kernel code/data/stack
Memory mapped region
for shared libraries
runtime heap (via malloc)
program text (.text)
initialized data (.data)
uninitialized data (.bss)
stack
forbidden
0
%esp
process
VM
brk
0xc0
physical memory
same for each process
process-specific data
structures
(page tables,
task and mm structs)
kernel
VM
To run a new program p in the current process using exec():
  free vm_area_struct’s and page tables for old areas.
  create new vm_area_struct’s and page tables for new areas.
    stack, bss, data, text, shared libs.
    text and data backed by ELF executable object file.
    bss and stack initialized to zero.
  set PC to entry point in .text
    Linux will swap in code and data pages as needed.
.data
.text
p
demand-zero
demand-zero
libc.so
.data
.text

## Slide 30: Fork() Revisited
To create a new process using fork():
  make copies of the old process’s mm_struct, vm_area_struct’s, and page tables.
    at this point the two processes are sharing all of their pages.
    How to get separate spaces without copying all the virtual pages from one space to another?
      “copy on write” technique.
  copy-on-write
    make pages of writeable areas read-only
    flag vm_area_struct’s for these areas as private “copy-on-write”.
    writes by either process to these pages will cause page faults.
      fault handler recognizes copy-on-write, makes a copy of the page, and restores write permissions.
  Net result:
    copies are deferred until absolutely necessary (i.e., when one of the processes tries to modify a shared page).

## Slide 31: Memory System Summary
Cache Memory
  Purely a speed-up technique
  Behavior invisible to application programmer and OS
  Implemented totally in hardware
Virtual Memory
  Supports many OS-related functions
    Process creation
      Initial
      Forking children
    Task switching
    Protection
  Combination of hardware & software implementation
    Software management of tables, allocations
    Hardware access of tables
    Hardware caching of table entries (TLB)