## Slide 1
Nirupam Roy
Nakul Garg
Enabling Self-defense in Small Drones
Notes: Hi everyone. my name is Nakul Garg, today I am going to present my paper on enabling self-defense in small drones.
This is a joint work with my advisor Nirupam Roy, and we are from the University of Maryland College Park.
[PAUSE]

## Slide 2
Notes: Drones started their journey as simple toys, today they are being used in serious applications.

## Slide 3
Drones are being used in serious applications
Law Enforcement
Notes: Police and law enforcement are using drones to protect our community and save lives.

## Slide 4
Drones are being used in serious applications
Law Enforcement
Australian Wildfire 2019
Notes: Drones are becoming more and more effective in disaster management.
Recently, they were used in the Australian wildfires to monitor the spread of the fire and save 100s of animals.

## Slide 5
Drones are being used in serious applications
Law Enforcement
Australian Wildfire 2019
Package Delivery in Wuhan, China 2020
Notes: Drones are being considered as a vehicle to carry packages.
Today, in Central-Africa, the majority of the medical supplies are being delivered using drones.
In the ongoing outbreak of Coronavirus, China is using drones to deliver food at the doorsteps of people’s house.

## Slide 6
Drones are being used in serious applications
Law Enforcement
Australian Wildfire 2019
Package Delivery in Wuhan, China 2020
UPS drone delivery service
Notes: And companies like DHL and UPS are ready to begin their drone services in the US.
[PAUSE]
Because of this huge application space, the number of commercial drones are increasing everyday..

## Slide 7
Drones are being used in serious applications
Law Enforcement
Australian Wildfire 2019
Package Delivery in Wuhan, China 2020
7.8 million drones will be sold in 2020
Source : Goldman Sachs
UPS drone delivery service
Notes: and it is been projected that there will be 7.8 million drones by the end of this year.

## Slide 8
Drones can be attacked
Notes: Now when drones are being taken seriously and they are been used in serious applications, we suspect that these drones can be attacked for profit or vandalism.

## Slide 9
Unmanned robots get attacked for profit
Notes: Although it is futuristic, but our past experiences have shown that we are not civilized enough to live with robots.
Whenever some unmanned vehicles were deployed for some tasks, they were attacked for sabotage and profit.
[PAUSE]

## Slide 10
Drones are more vulnerable
They rely on the coordination between its rotors. Slight collision can lead to in-stability.
Notes: And drones are even more vulnerable,
They rely on the coordination between their rotors and sensor and a mid-air collision and disrupt their stability.

## Slide 11
Drones are more vulnerable
They rely on the coordination between its rotors. Slight collision can lead to in-stability.
Collisions can disrupt the sensors and confuse the orientation-tracking algorithms.
Notes: Drones are delicate vehicles and and a collision can confuse it’s orientation tracking system.

## Slide 12
They rely on the coordination between its rotors. Slight collision can lead to in-stability.
Collisions can disrupt the sensors and confuse the orientation-tracking algorithms.
They have fragile structures, any damage can result in a crash.
Drones are more vulnerable
Notes: Because of their fragile structures, any physical damage can result in a crash.

## Slide 13
Notes: And given that the system is so delicate, the attacker doesn’t need a sophisticated weapon to attack the drone, maybe a casual throw of a stone or some other object is enough to take them down.

## Slide 14
Solutions are ready
Advanced RADAR systems.
Directed Infrared Countermeasure (DIRCM) systems.
Large Aircraft Infrared Counter-Measure systems
Notes: However, the problem of detecting incoming attacks, is not new.
For past thirty years, we have built technologies around RADAR, and Infrared countermeasure systems which detect dynamic object very precisely.

## Slide 15
Solutions are ready
Advanced RADAR systems.
Directed Infrared Countermeasure (DIRCM) systems.
Large Aircraft Infrared Counter-Measure systems
Not suitable for drones
Notes: Unfortunately, all these techniques are useless for drones because drones have several constraints. Like

## Slide 16
Low weight carrying capacity
Small form factor
Limited power,
short flight time
(~ 20 mins)
Limited computation resources
Notes: They have very limited weight carrying capacity, (usually around 250grams)
Small form factor
Limited power, and therefore short flight time (around 20 minutes)
And limited computation resources

## Slide 17
Trying to modify them..
LIDAR
RADAR
Depth / Event Cameras
Infrared Sensors
Notes: So when we talk about additional capability of safety in vehicles, we see works which use technologies like
RADAR
LIDAR
And Depth Cameras
What they have tried to do is take existing technologies and tailor them for these kind of resource constrained scenarios.
But essentially, what they all are doing is capturing the image of the environment and then run some object detection algorithms on top of it.

## Slide 18
Trying to modify them..
LIDAR
RADAR
Depth / Event Cameras
Infrared Sensors
consumes lot of power
cameras do not work in dark
limits flight time (~ 5mins)
relies on heavy computing
Notes: Although these technologies work perfectly fine for autonomous cars, they are yet not suitable for resource constrained systems like drones.
These technologies consume a lot of power and relies on heavy computing which limit the flight time of an average drone to just 5 minutes.
Despite advancement in these technologies, we cannot deploy them in real applications.

## Slide 19
We took a different route
Notes: So we decided to take a different route.
Instead of using a sensor which captures the image of the scene and then run object detection algorithm to detect projectiles.

## Slide 20
We took a different route
Event Specific Sensor
Notes: We build a sensor that can DIRECTLY identify a specific event.

## Slide 21
We took a different route
Event Specific Sensor
We do not need
Localization
Scene Imaging
Direction of Arrival
Notes: We do not need to do
Localization
Scene imaging
Or direction of arrival

## Slide 22
We just need to know
Is any moving object going to hit me?
We took a different route
We do not need
Localization
Scene Imaging
Direction of Arrival
Event Specific Sensor
Notes: All we need in this scenario is to know if there is any moving object in the environment
and if it’s going to hit the drone or not?

## Slide 23
We just need to know
Is any moving object going to hit me?
We took a different route
We do not need
Localization
Scene Imaging
Direction of Arrival
Event Specific Sensor
One-bit information is all we need
Notes: It is just a one-bit information

## Slide 24
We just need to know
Is any moving object going to hit me?
We took a different route
We do not need
Localization
Scene Imaging
Direction of Arrival
Event Specific Sensor
One-bit information is all we need
hit or miss?
Notes: Telling a Hit or a Miss

## Slide 25
If we are successful
Notes: IF WE ARE SUCCEFULL,
This lightweight and low power sensing system can enable very small drones, which are as small as honeybees, with self-defense capabilities.
A swarm of tiny drones can employ this mechanism to avoid collision between each other.
Firefighters can use them to chart the building before entering inside and drones can save themselves from flying debris or other obstacles.
There are many opportunities, let us try to understand how we can develop such an event-specific sensor.
We call our system..

## Slide 26
DopplerDodge
Notes: DopplerDodge.
As the name says, here we have used doppler effect to identify if there is any moving object in the environment
And specifically whether that object is going to hit the drone or not.
Before I go to the technique, let me quickly talk about what doppler effect is.

## Slide 27
DopplerDodge
The Doppler Effect
- change in frequency due to relative motion between source and receiver
Notes: Doppler effect simply says that the frequency of a wave changes when there is relative motion between a source and an observer.
It increases if the they are coming towards each other and vice versa.

## Slide 28
Doppler Shift in Reflections
Source signal
Notes: Imagine a set of speaker and microphone where the speaker is transmitting some frequency.
If a flying object is coming towards them,

## Slide 29
Doppler Shift in Reflections
Doppler shift in incident signal
Source signal
Notes: then because of the relative motion between the speaker and the object, we will see that frequency changes.

## Slide 30
Doppler Shift in Reflections
Doppler shift in incident signal
Source signal
Doppler shift in reflected signal
Notes: Interestingly, when the signal is reflected off the object and coming back to the microphone, there will be another level of doppler shift because of the relative motion between the microphone and object.

## Slide 31
Doppler Shift in Reflections
Doppler shift in incident signal
Source signal
Doppler shift in reflected signal
Notes: And basically we will end up with two levels of doppler shift that can be calculated using this equation
This is a simple equation, maybe we have seen in our high school textbooks.
But often this doppler equation misses one point.

## Slide 32
Doppler Shift in Reflections
Source signal
Doppler shift in reflected signal
Doppler shift in incident signal
Notes: What if the object is coming at some angle with the radial direction?
In that case we have to calculate the radial component of the velocity which is v r cos theta.

## Slide 33
Doppler Shift in Reflections
Source signal
Doppler shift in reflected signal
Doppler shift in incident signal
Notes: and our equation becomes

## Slide 34
Doppler Shift in Reflections
Source signal
Doppler shift in reflected signal
Doppler shift in incident signal
radial angle
Notes: Since this component of velocity points towards the radial direction
we call it this angle as radial angle

## Slide 35
Doppler Shift in Reflections
Source signal
Doppler shift in reflected signal
Doppler shift in incident signal
radial velocity
radial angle
Notes: And the velocity as radial velocity

## Slide 36
Time
v.cos 0°
Project Intention : Hit
Doppler Freq
Notes: Now imagine that we put this setup on top of a drone.
And throw a ball such that it’s going to hit the drone.
If we look at this scenario from the top view, it will appear something like this.
The ball will come in a straight line.
Since this ball is moving at some velocity,
the microphone on the drone will observe some finite doppler shift.

## Slide 37
v.cos 0°
v.cos 0°
v.cos 0°
v.cos 0°
Time
Project Intention : Hit
Doppler Freq
Notes: As the ball approaches the drone, notice that radial angle remains constant.

## Slide 38
Time
Project Intention : Hit
Doppler Freq
Constant
radial angle (0°)
v.cos 0°
v.cos 0°
v.cos 0°
v.cos 0°
Notes: As the ball approaches the drone, notice that radial angle remains constant.

## Slide 39
v.cos 0°
v.cos 0°
v.cos 0°
v.cos 0°
Time
Project Intention : Hit
Doppler Freq
Constant
radial angle (0°)
Notes: And if we plot the doppler shift in frequency for this scenario,

## Slide 40
v.cos 0°
v.cos 0°
v.cos 0°
v.cos 0°
Time
Constant
radial angle (0°)
Constant
frequency
Project Intention : Hit
Doppler Freq
Notes: We see that it also remains constant with time.

## Slide 41
Time
v.cos θ1°
Project Intention : Miss
Doppler Freq
Notes: Let us again consider this case,, but this time the ball is not going to hit the drone.
It is going in some other direction, let’s say theta.

## Slide 42
v.cos θ1°
v.cos θ2°
v.cos θ3°
v.cos θ4°
Time
Project Intention : Miss
Doppler Freq
Notes: Now, as the comes toward the drone, the radial increases.

## Slide 43
Time
Project Intention : Miss
Doppler Freq
v.cos θ1°
v.cos θ2°
v.cos θ3°
v.cos θ4°
Increasing
radial angle
Notes: Now, as the comes toward the drone, the radial increases.

## Slide 44
v.cos θ1°
v.cos θ2°
v.cos θ3°
v.cos θ4°
Time
Project Intention : Miss
Doppler Freq
Increasing
radial angle
Notes: Now, if we plot the doppler shift with time, we see that it no longer a straight line.

## Slide 45
v.cos θ1°
v.cos θ2°
v.cos θ3°
v.cos θ4°
Time
Doppler Freq
Increasing
radial angle
Decreasing
frequency
Project Intention : Miss
Notes: It decreases as the angle increases.

## Slide 46
Time
Doppler Freq
Time
Miss
Hit
Doppler Freq
Notes: This is the core intuition of DopplerDodge.
This works very well in theory, how well does it work in practice?
To find out we have done an experiment for which I want to show you a video,

## Slide 48
Hit
Miss
Notes: When we plot the frequencies for both the hit and miss cases over time, we can clearly see that in hit case frequency remains constant but in miss case it is changing just like we thought.

## Slide 49
Hit
Miss
Time
Doppler Freq
Time
Doppler Freq
Notes: If we can track these doppler frequencies, then we can detect if the projectile is going to hit the drone or not.
But tracking doppler frequency in spectrograms is an expensive operation.

## Slide 50
Time
Doppler Freq
Time
Doppler Freq
Hit
Miss
Notes: And in this particular application we don’t need to track the frequencies,

## Slide 51
Hit
Miss
Time
Doppler Freq
Time
Doppler Freq
Notes: but rather if we can break the entire signal into multiple windows, then we can compare them with one another.

## Slide 52
Hit
Miss
Time
Doppler Freq
Time
Doppler Freq
Notes: For example, take these two windows at tie t1 and t2.
We see that in hit case these frequencies have equal values.

## Slide 53
Hit
Miss
Time
Doppler Freq
Time
Doppler Freq
= 1
Notes: And their ratio is equal to one.

## Slide 54
Hit
Miss
Time
Doppler Freq
Time
Doppler Freq
= 1
Notes: but in miss case, if we compare these two frequencies, we see that they are not equal

## Slide 55
Hit
Miss
Time
Doppler Freq
Time
Doppler Freq
= 1
> 1
Notes: the ratio will be greater than 1.

## Slide 56
Hit
Miss
Time
Doppler Freq
Time
Doppler Freq
= 1
> 1
Radial Drift
Notes: We call this ratio Radial Drift, as it tells us the drift in the doppler frequency.

## Slide 57
1. Basic Approach
- Using Fast Fourier Transform
2. Frequency Translation
- Using low power operations
How do we implement this?
Notes: To find out radial drift, we can implement this idea in two different approaches.
The basic approach is to use Fast Fourier Transform and get the frequencies at two different time windows and compare them.
And the second is a low power technique called Frequency Translation.

## Slide 58
1. Basic Approach
- Using Fast Fourier Transform
2. Frequency Translation
- Using low power operations
How do we implement this?
Notes: First let’s see the basic approach.

## Slide 59
FFT based approach
Time
Doppler Freq
Time
Doppler Freq
Notes: We take the time domain signals of the two adjacent block.

## Slide 60
FFT
FFT
Time
Doppler Freq
Time
Doppler Freq
FFT
FFT
FFT based approach
Notes: And apply fast fourier transform on each of them

## Slide 61
FFT
FFT
Time
Doppler Freq
Time
Doppler Freq
FFT
FFT
FFT based approach
Notes: To get the frequencies at their respective times.

## Slide 62
FFT
FFT
Time
Doppler Freq
Time
Doppler Freq
FFT
FFT
FFT based approach
>1 , if Miss
=1 , if Hit
Notes: Then we can simply divide these two values to see if they are equal or not.

## Slide 63
FFT based approach
Notes: We collected some real data and plotted the radial drift for all consecutive samples, to see that for HIT cases the radial drift is close to 1, but for Miss cases it is greater than 1.

## Slide 64
Threshold
FFT based approach
Notes: So we can just use a threshold to classify them.

## Slide 65
Threshold
FFT based approach
However, continuous FFT operations are expensive!
Notes: However, using FFT for this application can be expensive.
Not only does it take too many CPU cycles but also a lot of memory which is not available in small microcontrollers.
(Fix the word available)

## Slide 66
1. Basic Approach
- Using Fast Fourier Transform
2. Frequency Translation
- Using low power operations
How do we implement this?
Notes: So we propose a frequency translation approach which uses low power operation to estimate the radial drift.

## Slide 67
Frequency Translation
Time
Doppler Freq
Time
Doppler Freq
sin(2fA)
sin(2fA+ϕ)
sin(2fA)
sin(2fB+ϕ)
Notes: Again, Consider the time domain signal for these windows in Hit and miss case.

## Slide 68
Frequency Translation
Time
Doppler Freq
Time
Doppler Freq
sin(2fA)
sin(2fA+ϕ)
sin(2fA)
sin(2fB+ϕ)
X
X
Notes: Instead of running FFT, we are simply multiplying these two signals and to get a down-converted signal.
This is a common operation in wireless communication.

## Slide 69
Frequency Translation
Time
Doppler Freq
Time
Doppler Freq
sin(2fA)
sin(2fA+ϕ)
sin(2fA)
sin(2fB+ϕ)
X
X
0.5 cos(22fA))
- 0.5 cos(ϕ)
Notes: In a hit case where these frequencies are equal we get a single frequency output, 2fa

## Slide 70
Frequency Translation
Time
Doppler Freq
Time
Doppler Freq
sin(2fA)
sin(2fA+ϕ)
sin(2fA)
sin(2fB+ϕ)
X
X
0.5 cos(2fA -fB) +ϕ)
- 0.5 cos(2fA+fB) +ϕ)
0.5 cos(22fA))
- 0.5 cos(ϕ)
Notes: But In case of different frequencies, we get two frequency components fa+fb and fa-fb.
If we can keep track of the envelope, that can tell if these are the same frequencies or not.

## Slide 71
Frequency Translation
Time
Doppler Freq
Time
Doppler Freq
sin(2fA)
sin(2fA+ϕ)
sin(2fA)
sin(2fB+ϕ)
X
X
∑
∑
0.5 cos(2fA -fB) +ϕ)
- 0.5 cos(2fA+fB) +ϕ)
0.5 cos(22fA))
- 0.5 cos(ϕ)
Notes: To track the envelope we basically take summation of the entire multiplication block and get the output.

## Slide 72
Frequency Translation
Time
Doppler Freq
Time
Doppler Freq
sin(2fA)
sin(2fA+ϕ)
sin(2fA)
sin(2fB+ϕ)
X
X
∑
∑
∑
…
∑
…
…
∑
…
∑
…
…
0.5 cos(2fA -fB) +ϕ)
- 0.5 cos(2fA+fB) +ϕ)
0.5 cos(22fA))
- 0.5 cos(ϕ)
Notes: Then we keep track of this output over time using a sliding window.

## Slide 73
Frequency Translation
Time
Doppler Freq
Time
Doppler Freq
sin(2fA)
sin(2fA+ϕ)
sin(2fA)
sin(2fB+ϕ)
X
X
∑
∑
∑
…
∑
…
…
∑
…
∑
…
…
0.5 cos(2fA -fB) +ϕ)
- 0.5 cos(2fA+fB) +ϕ)
0.5 cos(22fA))
- 0.5 cos(ϕ)
Notes: The summation of these blocks over time is a constant value for hit case and oscillating for a miss case.

## Slide 74
Frequency Translation
Notes: And if we plot the cumulative sum of this output, … we will still be able to plot the radial drift.
The metric is a little different, the range of the values are a little different, but at the end of the day, we are still able to classify the hit and miss cases with a very low computation.

## Slide 75
Frequency Translation
Threshold

## Slide 76
Evaluation
Throw objects of different sizes from 4meters.
Throw from different angles.
(-40, -20, 0, 20, 40)
Consider it a hit if the ball lands within 10cm from sensor.
For miss cases, we throw objects at different miss distances.
Notes: Now I will talk about the evaluation.
We extensively evaluate DopplerDodge by throwing objects of different shapes and sizes from a distance of 4 meter and different angles.
We consider a projectile as a hit if it lands with 10cm of the sensor otherwise it’s a miss.

## Slide 77
77
Performance Accuracy
Evaluation
Notes: This is the performance accuracy plot. We can see that when the object lands at 0 distance from the sensor we ACCURATELY classify all the events as Hits.
For closer distances like 50cm you can see that there are some misclassifications, some of the events are being classified as Hits although they are Miss.

## Slide 78
78
Performance Accuracy
Evaluation
Biased the sensitivity towards hit
Notes: And this is because we have tuned our system to be more sensitive towards hits.

## Slide 79
79
Latency
Evaluation
Notes: The latency plots shows that our frequency translation approach is 2 to 4 times faster than the basic FFT based approach.

## Slide 80
On-board processing and sensor fusion
High-speed projectiles
Adversarial attacks
Estimating optimal path
Notes: So our current project is a first-step towards a long-term commitment in developing an array of defense mechanism for light weight robotic vehicles.
In near future we have planned to solve a few problem. First of all, we will try to leverage other sensors to improve the accuracy and have a better situational awareness. We will attempt to detect much higher speed of projectiles.
There are some spoofing attacks possible, for active-sensing based mechanism, we are trying to develop some defense mechanism that can prevent us form adversarial attacks.
And finally, while smaller drones are much agile and have lookahead time to move, but heavier drones have higher inertia and it takes longer time for them to move.
We are developing a path estimation technique for them to dodge dynamic objects. If successful, that will give us the power for the drones to plan the path in real time and dodge even a very high-speed dynamic object.

## Slide 81
Lightweight sensing-inferencing modules to enable a way of self-defense in resource-constrained robotic vehicles and drones.
Takeaway

## Slide 82
Lightweight sensing-inferencing modules to enable a way of self-defense in resource-constrained robotic vehicles and drones.
Takeaway
Thank you
Notes: That’s all I have for today. Thank you very much.