## Slide 1: CMSC417
Computer Networks
Prof. Ashok K . Agrawala
© 2019 Ashok Agrawala
September 4, 2018

## Slide 2: Connecting Application Programs
App A
App B
User A
OS
OS
Disk
Server

## Slide 3: Connecting Application Programs
App A
App B
User A
OS
OS
Disk
Server
Internet

## Slide 4: Network Software
  Protocol layers »
  Design issues for the layers »
  Connection-oriented vs. connectionless service »
  Service primitives »
  Relationship of services to protocols »

## Slide 5: Protocol layers
Protocol layering is the main structuring method used to divide up network functionality.
Each protocol instance talks virtually to its peer
Each layer communicates only by using the one below
Lower layer services are accessed by an interface
At bottom, messages are carried by the medium

## Slide 6: Protocol layers
Example: the philosopher-translator-secretary architecture
Each protocol at different layers serves a different purpose

## Slide 7: Protocol layers
Each lower layer adds its own header (with control inform-ation) to the message to transmit and removes it on receive
Layers may also split and join messages, etc.

## Slide 8: Design issues for the layers
Each layer solves a particular problem but must include mechanisms to address a set of recurring design issues
Issue | Example mechanisms at different layers
Reliability despite failures | Codes for error detection/correction (§3.2, 3.3) Routing around failures (§5.2)
Network growth and evolution | Addressing (§5.6) and naming (§7.1) Protocol layering (§1.3)
Allocation of resources like bandwidth | Multiple access (§4.2) Congestion control (§5.3, 6.3)
Security against various threats | Confidentiality of messages (§8.2, 8.6) Authentication of communicating parties (§8.7)

## Slide 9: Connection-oriented vs. connectionless
Service provided by a layer may be kinds of either:
  Connection-oriented, must be set up for ongoing use (and torn down after use), e.g., phone call
  Connectionless, messages are handled separately, e.g., postal delivery

## Slide 10: Service primitives
A service is provided to the layer above as primitives
Hypothetical example of service primitives that may provide a reliably byte stream (connection-oriented) service:

## Slide 11: Service primitives
Hypothetical example of how these primitives may be used for a client-server interaction
Client
Server
LISTEN (0)
ACCEPT
RECEIVE
SEND (4)
DISCONNECT (6)
CONNECT (1)
SEND
RECEIVE
DISCONNECT (5)
Connect request
Accept response
Request for data
Reply
Disconnect
Disconnect
(2)
(3)

## Slide 12: Service primitives
Packets sent in a simple client-server interaction on a connection-oriented network:

## Slide 13: Relationship of services to protocols
A layer provides a service to the one above [vertical]
A layer talks to its peer using a protocol [horizontal]

## Slide 14: Reference models
Reference models describe the layers in a network architecture.
  OSI reference model »
  TCP/IP reference model »
  Model used for this text »

## Slide 15: Reference models
The OSI reference model

## Slide 16: OSI reference model
A principled, international standard, seven layer model to connect different systems.
Provides functions needed by users
Converts different representations
Manages task dialogs
Provides end-to-end delivery
Sends packets over multiple links
Sends frames of information
Sends bits as signals

## Slide 17: The TCP/IP reference model layers
Link layer
Internet layer
Transport layer
Application layer

## Slide 18: TCP/IP reference model
A four layer model derived from experimentation; omits some OSI layers and uses the IP as the network.
IP is the “narrow waist” of the Internet
Protocols are shown in their respective layers

## Slide 19: Comparison of OSI and TCP/IP models

## Slide 20: Reference models

## Slide 21: Model used in this course
It is based on the TCP/IP model but we call out the physical layer and look beyond Internet protocols.

## Slide 22: Network standardization
Who’s Who in the Telecommunications World »
Who’s Who in the International Standards World »
Who’s Who in the Internet Standards World »

## Slide 23: Network standardization
Standards define what is needed for interoperability.
Some of the many standards bodies:
Body | Area | Examples
ITU | Telecommunications | G.992, ADSL H.264, MPEG4
IEEE | Communications | 802.3, Ethernet 802.11, WiFi
IETF | Internet | RFC 2616, HTTP/1.1 RFC 1034/1035, DNS
W3C | Web | HTML5 standard CSS standard

## Slide 24: ITU: International Telecommunications Union
Main sectors
  Radiocommunications
  Telecommunications Standardization
  Development
Classes of Members
  National governments
  Sector members
  Associate members
  Regulatory agencies

## Slide 25: Who’s who in international standards
The 802 working groups. The important ones are marked with *.
The ones marked with  are hibernating. The one marked with † gave up and disbanded itself.

## Slide 26: Who’s who in international standards
The 802 working groups. The important ones are marked with *.
The ones marked with  are hibernating. The one marked with † gave up and disbanded itself.

## Slide 27: Metric units
The main prefix we use:
Prefix | Exp. | prefix | exp.
K(ilo) | 103 | m(illi) | 10-3
M(ega) | 106 | μ(micro) | 10-6
G(iga) | 109 | n(ano) | 10-9
Use powers of 10 for rates, powers of 2 for storage (e. g. 1 Mbps = 1,000,000 bps, 1 KB = 1024 bytes)
B is for bytes, b is for bits

## Slide 28: Metric units
The principle metric prefixes

## Slide 29: Metric units
The principle metric prefixes

## Slide 30: Metric units
The principle metric prefixes