## Slide 1: Sound Propagation and Geometric Acoustics

## Slide 2: Acoustics
The spatial effects on sound

## Slide 3: Why Model Acoustics?
Model acoustics of existing or future architecture (offline)
Increase immersion in Virtual Environments (real-time)

## Slide 4: Affected by Size and Shape of Space

## Slide 5: Also Affected by Material's Stiffness

## Slide 6: Why? Sound is comprised of waves
Similar to light:
Radiates outward from source
Can be absorbed or reflected by surfaces

## Slide 7: Pressure Waves, not EM
Different than light:
Travels much slower
  arrival times
Can cause surfaces to resonate

## Slide 8: Sound -- Coherent Waves
Must consider wave phase
phase cancellation can occur

## Slide 9: Types of Reverberations
Direct - Line of sight sound
Early - Blends with direct (within 50 - 80 ms)
Late - Perceived as separate from direct

## Slide 10: The Wave Equation
∂2p − c2∇2p = f (x, t)
∂t2
How to solve?
Fourier Transform
Very Expensive, often not solved exactly
  requires too much memory & computation

## Slide 11: Why so Expensive?
Solvers require 6-10 samples per wavelength
Audible range: 20 Hz - 22 kHz
Speed of sound is ~350 m / s
  smallest wavelength is ~ 350 m / 22,000 = 15 mm
We must sample at roughly every 2mm!
  That means (500 x 500 x 500) = 125 Million samples per m3!

## Slide 12: Linear Equation -- Superposition
Since wave equation is linear...
We can sum contributions from sources independently
Enables us to calculate an 'Impulse Response' offline to convolve the input audio signal

## Slide 13: Audio Convolution
Sum of Area under curves as you 'slide' two signals past each other

## Slide 14: Simplified Acoustic Model
Only Compute Direct and Early response
  Ignore late
Assume Rigidity of Surfaces
  Ignore resonance
Only Calculate Specular Reflections
  Ignore diffuse reflections, diffraction, transmission...
Piecewise Planar Environment Model
  May have other restrictions: Convexity, etc.

## Slide 15: Image Source Method
Only consider direct paths, create Virtual Sources for specular reflection paths

## Slide 16: Creating Virtual Sources (VS)
Reflect sources across geometry
Must recursively reflect each new Virtual Source
  Bound by order or distance

## Slide 17: Simple Case -- Rectangular Room
Recursively reflect source across room walls
Results in regular lattice of Virtual Sources

## Slide 18: General Case -- Arbitrary Polyhedra
Math:
  d = p - P * n
  R = P + 2dn
Not all Virtual Sources are valid!
  Validity and Visibility!

## Slide 19: Validity Check
Treat walls as 1-sided mirrors
  Only reflect across front face
Toss out invalid sources

## Slide 20: Visibility Check
Most complicated check
Can a specific listener 'see' a source?
Must still reflect 'invisible' sources to create new Virtual Sources

## Slide 21: Visibility Check -- Simple Case
First Order VS:
  Segment between source and receiver intersects reflecting polygon

## Slide 22: Visibility Check -- General Case
Higher Order VS:
  Must check every reflecting surface to ensure visibility

## Slide 23: Obstructions
Must consider if environment is non-convex
  Flag edges as 'obstructing'
  Check these edges for occlusion when adding sound components

## Slide 24: Image Source -- Complexity
| VS | = Nk
N - number of polygons in scene
k - order of VS recursion
Can be precomputed!
Assuming sources don't move

## Slide 25: Ray Tracing -- Just like Graphics!
Treat waves as rays and sum contributions

## Slide 26: Ray Tracing -- Source
Treat sound source as point and uniformly cast finite rays

## Slide 27: Ray Tracing -- Receiver
Treat receivers as spheres
  Impossible for rays to hit points!

## Slide 28: Receiver Size: Design Tradeoff
Too Large:
Creates 'shadows', occluding receivers further away
Too Small:
Unlikely to be hit by rays

## Slide 29: Multiple Reflection Types
Can consider diffuse, specular, transmission, etc.
Can't split, too many rays
Do so stochastically

## Slide 30: Ray Tracing Issues
May miss sound paths!
Can't tell if missing

## Slide 31: Beam Tracing -- Also from Graphics
Replace rays with beams
  have cross sectional area
Replace receiver spheres with points

## Slide 32: Representing a Beam
Set of expanding rays
Share common origin

## Slide 33: Intersecting a Beam
Beams are split on intersection:
Shadowed part becomes transmission beam
Reflection beam created
Remaining section is propagated

## Slide 34: Benefits of Beams over Rays
Ignore tradeoff of receiver size
Finite set of beams can fully cover space

## Slide 35: Recent Work
Realtime Ray and Beam Tracing
Some with GP-GPU acceleration
Inclusion of Diffraction Simulation

## Slide 36: Sources
Image method for efﬁciently simulating small-room acoustics.
J. B. Allen and D. A. Berkley.
The Journal of the Acoustical Society of America, 65(4):943–950, April 1979.
Extension to the image model to arbitrary polyhedra.
J. Borish.
The Journal of the Acoustical Society of America, 75(6):1827–1836, June 1984.
The early history of ray tracing in room acoustics.
P. Svensson.
Reﬂections on sound: In honour of Professor14 Emeritus Asbjørn Krokstad. Norwegian University of Science and Technology, 2008.
A beam tracing approach to acoustic modeling for interactive virtual environments.
T. Funkhouser, I. Carlbom, G. Elko, G. Pingali, M. Sondhi, and J. West.
In Proc. of ACM SIGGRAPH, pages 21–32, 1998.
An Efficient Time-domain Solver for the Acoustic Wave Equation on Graphics Processors
Ravish Mehra, Nikunj Raghuvanshi, Lauri Savioja, Ming C. Lin, and Dinesh Manocha