## Slide 1: COMP768-F16 Course Presentation
Sound Modal Analysis, Synthesis, and Fluid-Structure Interaction
Justin Wilson

## Slide 2: Labeling Conventions
Upper case denotes matrix and lower case denotes vector or scalar
May see damping noted as C or D
  Damping labeled as D or d in this presentation
May see displacement (current position – resting position) as x, r, or u
  3D displacement labeled as u
  1D displacement labeled as x
Rayleigh damping coefficients as η and δ, α and β, or α1 and α2
  Rayleigh damping coefficients labeled as α1 and α2 in this presentation
May see mode space matrix as Φ or U
  Mode space matrix labeled as U in this presentation
May see displacement in mode space as z or q
  Displacement in mode space labeled as q in this presentation
Fluid-Structure Interaction (aka Elasto-Acoustics, aka Solid-Fluid Interface)
Notes: Rayleigh (rey-lee)
η is lowercase eta
δ is lowercase delta
α is lowercase alpha
β is lowercase beta
Φ is uppercase phi

## Slide 3: Discussion topics
Sound modal analysis
  How do we hear sound?
  What properties influence the sound of an object?
  How can we perform sound modal analysis?
Sound modal synthesis
Fluid-Structure Interaction
What causes an object to make a sound when it is struck?

## Slide 4: Sound waves and harmonic motion
When an object is struck, it vibrates and deforms
  The surrounding air rapidly compresses (compression) and expands (rarefaction or decompression) as the object vibrates outward and inward respectively
  As it oscillates periodically, pressure waves are created and air pressure amplitude changes up and down in over time (like a sine wave)
  Although we may not see the vibrations or deformations, our ears hear the variation in air pressure as sound
Harmonic motion (aka harmonic oscillation) is the periodic pattern of compression and rarefaction
Pressure waves
Source: digitalsoundandmusic.com
Notes: Tuning fork vibrates at a single frequency when struck, generating a pure tone
Source: http://digitalsoundandmusic.com/flash/?tutorial=Sound%20Waves%20and%20Harmonic%20Motion
Rarefaction (rair-uh-fak-shuh n)

## Slide 5: A spring-mass system is also a vibration model
Like harmonic motion, a spring mass system also responds in a periodic motion
  Undamped case (d=0)
    mx’’(t) + kx(t) = 0
    Amplitude does not decrease with time
  Damped case (d > 0)
    mx’’(t) + dx’(t) + kx(t) = 0
    Underdamped case (0 < d2 < 4*k*m)
      Amplitude vibrates but eventually stops
      ω =
    Critically damped case (d = 4*k*m)
      Decays to zero without oscillating
    Overdamped case (d > 4*k*m)
      Also decays to zero without oscillating
Source: digitalsoundandmusic.com
Undamped case
Underdamped case
Notes: Then, what properties influence the sound of an object?
ω is lowercase omega

## Slide 6: Sound dynamics equation
Mu’’ + Du’ + Ku = f
  M = mass matrix, where mass is located on the object
  u = vector of the displacement of each element
    vector of all zeros represent object at rest
    n elements for object, then u vector size = 3n (x,y,z position)
  D = viscous damping matrix, how velocity decays over time
  K = stiffness matrix, defines connectivity of the elements
  f = vector of forces, inducing vibrations
Given these parameters, we can simulate the vibration of the solid volume body object in response to an impulse
Then, how do we represent the object and determine its parameter values (M, D, K)?
Source: SIGGRAPH 2016 Course Notes

## Slide 7: Rigid body sound pipeline
Generate volumetric mesh
Construct the stiffness K, mass M, & damping D matrices
Run generalized eigen-decomposition
Construct the decoupled modal vibration equations
Numerically integrate individual modes
Notes: So far, we have learned how to represent an object as a volumetric mesh for sound analysis.
Next, let’s better understand how to construct the object parameters, mass, damping, and stiffness
Eigen (ʌɪɡən)

## Slide 8: Object is a volumetric solid body
Represent surface mesh with a finite element mesh (e.g. tetrahedral)
  Tetrahedral mesh has n nodes where i=1…n
  Xi are the rest positions
  xi(t) is the time-varying displaced position
  ui(t) = (xi(t) – Xi) is the nodal displacement
Mu’’ + Du’ + Ku = f(t)
  High-dimensional equivalent to spring- mass mx’’(t) + dx’(t) + kx(t) = f(t)
M, D, and K are size 3n x 3n sparse matrices
Xi
xi
Pressure waves
Source: digitalsoundandmusic.com
u1x
u1y
u1z
u2x
…
u =
3n x 1 vector of displacement vectors ui of all nodes
=
ui
Single tetrahedron of finite element mesh
Notes: Can use tetgen to convert to tetrahedral mesh.
Tetrahedra (aka simplex), which simply means that ANY 3D volume, regardless of shape or topology, can be meshed with tets

## Slide 9: Rigid body sound pipeline
Generate volumetric mesh
Construct the stiffness K, mass M, & damping D matrices
Run generalized eigen-decomposition
Construct the decoupled modal vibration equations
Numerically integrate individual modes
Notes: So far, we have learned how to represent an object as a volumetric mesh for sound analysis.
Next, let’s better understand how to construct the object parameters, mass, damping, and stiffness

## Slide 10: Stiffness matrix K (parameters)
Stiffness describes element connectivity
If the tetrahedra are small, then can approximate:
  Deformation gradient as a constant value inside of each tetrahedron
    F = [x2 – x1 x3 – x1 x4 – x1][X2 – X1 X3 – X1 X4 – X1] -1
  Strain also as a constant and linearized since the vibration is very tiny
    E = ½ * (F + FT)
Stress tensor S = -C*E (linear constitutive law, aka Hooke’s law)
  Strain tensor E and stiffness tensor C (symmetric 4th order tensor)
  Stiffness tensor C depends on the material; for isotropic materials:
    Cijkl = Kδijδkl + µ(δikδjl + δilδjk − 2/3*δijδkl) where δij is the Kronecker delta function
Given a stress tensor S & direction n, elastic force is Sn
  n1 = effective normal of node 1 = average of three adjacent triangle normals
Source: SIGGRAPH 2016 Course Notes
Single tetrahedron of finite element mesh
Notes: Depending on specific material parameters, the stiffness tensor is symmetric with Cijkl = Cklij = Cjikl = Cijlk
Although strain tensor E is generally nonlinear, approximate as linear since vibration is very tiny
δ is lowercase delta

## Slide 11: Stiffness matrix K (related to force)
Total internal force at node j = fj = ∑ Sinji (summed over i ∈ Tj)
  Tj indicates set of tetrahedral that include node j
  nji is the effective normal n of node j for tetrahedron i
  Si is the constant stiffness tensor S for tetrahedron i
Since nji is a constant direction and Si is linearly related to nodal positions xi, we can express f = Ku (similar to mass-spring kx(t))
  Rewrite Si which is linearly related to nodal position xi with K which is a linear function with respect to the displacement vectors uj
Strain state in a solid medium around some point cannot be described by a single vector
  f stacks internal force vectors of all finite element nodes
  K is a sparse matrix because each node depends only on surrounding tetrahedra
Source: SIGGRAPH 2016 Course Notes
Single tetrahedron of finite element mesh
Notes: ∈ is epsilon

## Slide 12: Stiffness matrix key takeaways
Based on elements of the object’s volumetric mesh & Poisson’s ratio
Poisson’s ratio for most materials range between 0 (cork) and 0.5 (rubber), typically between 0.15 and 0.35
  When a material is compressed in one direction, it usually tends to expand in the other two directions
  Poisson’s ratio ν = (% expansion) / (% compression)
stiffness_ssh “solver” based on UNC (Huai-Ping)
  Inputs
    .ele and .node files generated from Tetgen
    Poisson’s ratio
  Ouput
    Stiffness matrix elements
Poisson’s ratio for different materials
Notes: Poisson’s ratio ν (pronounced nu)

## Slide 13: Mass matrix M
Single tetrahedron contributes a 12 x 12 submatrix to final 3n x 3n mass matrix M |  |  |  |  |  |  |  |  |  |  | 
B11d11 | 0 | 0 | B21d11 | 0 | 0 | B31d11 | 0 | 0 | B41d11 | 0 | 0
0 | B11d22 | 0 | 0 | B21d22 | 0 | 0 | B31d22 | 0 | 0 | B41d22 | 0
0 | 0 | B11d33 | 0 | 0 | B21d33 | 0 | 0 | B31d33 | 0 | 0 | B41d33
B12d11 | 0 | 0 | B22d11 | 0 | 0 | B32d11 | 0 | 0 | B42d11 | 0 | 0
0 | B12d22 | 0 | 0 | B22d22 | 0 | 0 | B32d22 | 0 | 0 | B42d22 | 0
0 | 0 | B12d33 | 0 | 0 | B22d33 | 0 | 0 | B32d33 | 0 | 0 | B42d33
B13d11 | 0 | 0 | B23d11 | 0 | 0 | B33d11 | 0 | 0 | B43d11 | 0 | 0
0 | B13d22 | 0 | 0 | B23d22 | 0 | 0 | B33d22 | 0 | 0 | B43d22 | 0
0 | 0 | B13d33 | 0 | 0 | B23d33 | 0 | 0 | B33d33 | 0 | 0 | B43d33
B14d11 | 0 | 0 | B24d11 | 0 | 0 | B34d11 | 0 | 0 | B44d11 | 0 | 0
0 | B14d22 | 0 | 0 | B24d22 | 0 | 0 | B34d22 | 0 | 0 | B44d22 | 0
0 | 0 | B14d33 | 0 | 0 | B24d33 | 0 | 0 | B34d33 | 0 | 0 | B44d33
12 x 12 submatrix is comprised of 3x3 diagonal matrices Bij making it sparse Bij = (1/20) *pV * (1+δij) * I3x3, i.e. 2nd partial derivative of kinetic energy with respect to nodal velocities |  |  |  |  |  |  |  |  |  |  | 

## Slide 14: Mass matrix key takeaways
Mass matrix construction methods
  Direct Mass Lumping (DML)
  Variational Mass Lumping (VML)
    Consistent Mass Matrix (CMM)
  Template Mass Lumping (TML)
Compute mass matrix using "volumetricMesh“ library [Barbic]
  This library uses consistent mass matrix (CMM) of a tetrahedron
Eigenvectors are mass-normalized

## Slide 15: Damping matrix D (Rayleigh damping)
Rayleigh damping (aka linearly proportional damping) is used to model losses based on mass and stiffness
Rayleigh damping: D = α1M + α2K
  Linear combination of mass (M) and stiffness (K) where α1 and α2 are real-valued parameters
Rayleigh damping is most commonly used because of ease of computation but note the following limitations:
  Rayleigh damping is only a first-order approximation
  Originally chosen for ease of computation, not its physical accuracy
  Only produces normal modes
Other damping models
  Caughey damping
  Generalized proportional damping (GPD)
Notes: Discuss pros/cons of the other damping models
Caughey damping model is more general than Rayleigh
Most general damping model that limits vibration to normal modes is generalized proportional damping (GPD)
Rayleigh (rey-lee)

## Slide 16: Mass, stiffness, and damping “solvers”
Mass (M) and stiffness (K) can be constructed through knowledge of the shape and material properties of the object
  Notably, its density (p), Poisson’s ratio (ν), and Young’s modulus (E)
Damping (D), how do we obtain the Rayleigh coefficients α1 and α2?
  Instead of by hand, researchers1 have established a method to automatically estimate them from recorded audio
Glass for example
  ν = .25, E = 50e09 Pascals, p = 2500 kg/m3
  α1 = 2.0 and α2 = 7.8e-8
1 Example-Guided Physically Based Modal Sound Synthesis [Ren et al]
Notes: For values of Young’s modulus by material, look at https://en.wikipedia.org/wiki/Young%27s_modulus

## Slide 17: Rigid body sound pipeline
Generate volumetric mesh
Construct the stiffness K, mass M, & damping D matrices
Run generalized eigen-decomposition
Construct the decoupled modal vibration equations
Numerically integrate individual modes
Notes: So far, we have learned how to represent an object as a volumetric mesh for sound analysis.
Next, let’s better understand how to construct the object parameters, mass, damping, and stiffness

## Slide 18: Eigendecomposition
Shape and material properties of the object are analyzed to decompose the vibrations into a set of modes of vibration
  Linear combination of normal modes with different amplitudes, frequencies, and phases
We perform generalized eigenvalue decomposition using KU = MUS and displacement vector u = Uq
  U is the modal shape matrix of normal modes, containing the eigenvectors
  S is the diagonal eigenvalue matrix
Mu’’ + Du’ + Ku = f(t), set u = Uq, and multiply by UT
UTMUq’’ + UTDUq’ + UTKUq = UTf(t)
  Simplify by substituting UTMU = I, UTDU = α1I + α2S, and UTKU = S
q’’ + (α1I + α2S)q’ + Sq = UTf(t)
General eigendecomposition solver using Intel MKL (Math Kernel Library) to obtain eigenvalues
Notes: ω is radians per second and f is cycles per second

## Slide 19: Rigid body sound pipeline
Generate volumetric mesh
Construct the stiffness K, mass M, & damping D matrices
Run generalized eigen-decomposition
Construct the decoupled modal vibration equations
Numerically integrate individual modes
Notes: So far, we have learned how to represent an object as a volumetric mesh for sound analysis.
Next, let’s better understand how to construct the object parameters, mass, damping, and stiffness

## Slide 20: Rather than solving a set of coupled equations, we solve n damped vibration independent equations
Matrices UTMU = I, UTDU = α1I + α2S, and UTKU = S are diagonal so equations about q are independent
  So can solve n damped vibration equations independently
  We decouple Mu’’ + Du’ + Ku = f(t) into a set of independent 1D vibration equations mx’’(t) + dx’(t) + kx(t) = 0
q’’ + (α1I + α2S)q’ + Sq = UTf(t)
  Damping di = α1 + α2 * eigenvaluei
  Stiffness ki = eigenvaluei
  UTf(t) is the force vector represented with mode coordinates
  Remember, ωi = 2πfi and mass matrix is mass normalized so m = 1
For the purpose of sound synthesis, we are interested in the vibrational frequencies in our hearing range (20Hz to 20kHz)
  Therefore, we only need to consider modes with vibrational frequencies in this range
ω =
frequency f =
π
Notes: Resulting damping matrix is diagonal only for ideal conditions

## Slide 21: Rigid body sound pipeline
Generate volumetric mesh
Construct the stiffness K, mass M, & damping D matrices
Run generalized eigen-decomposition
Construct the decoupled modal vibration equations
Numerically integrate individual modes
Notes: So far, we have learned how to represent an object as a volumetric mesh for sound analysis.
Next, let’s better understand how to construct the object parameters, mass, damping, and stiffness

## Slide 22: Numeric methods
In general, each natural mode of the system has a different natural frequency
  The physical interpretation of the eigenvalues and eigenvectors which come from solving the system are that they represent the frequencies and corresponding mode shapes
Harmonic Oscillator [Barbic]
  Integrates a single 1D harmonic oscillator; can timestep the following Ordinary Differential Equation: M * q''(t) + D * q'(t) + K * q(t) = f(t)
  Only supports underdamped systems
Modal superposition analysis (aka modal analysis)
Modal expansion thereom
Source: MIT Open Courseware [Vandiver]
Notes: Other numerical methods
To perform modal analysis numerically, the object is represented using a discretized model such as FEM mesh or spring-mass thin-shell
Power iteration: eigenvector computed 1st and then eigenvalue from Rayleigh quotient of the eigenvector
Hermitian matrix Schur decomposition backsubstitution

## Slide 23: Summary of modal analysis steps
Analyze the vibrations of the sounding object (Mu’’ + Du’ + Ku = f(t))
Parameters based on shape and material set of properties
  Stiffness matrix
  Mass matrix
    Using tetrahedral nodes, Poisson’s ratio, Young’s modulus, and density
  Damping model: how vibrations of a modeled object will decay over time
    Rayleigh damping (aka linearly proportional damping of mass and stiffness)
Mode space (q’’ + (α1I + α2S)q’ + Sq = Utf(t))
  Damping di = α1 + α2 * eigenvaluei
  Stiffness ki = eigenvaluei
  UTf(t) converts forces on elements to normal mode amplitudes
  Frequency fi
Dynamically create sounds at runtime with modal synthesis
=
π
Notes: Caughey (K AW - h ee)
Caughey damping
Generalized proportional damping (GPD)

## Slide 24: Modal sound synthesis
Simulate based on a contact point
  Position (x,y,z) of where the object is struck
    ANN (Approximate Nearest Neighbor) [Mount and Arya]
  Impulse direction (x,y,z); e.g. usually striking the object in normal direction to the contact point but could synthesize tangentially to the object like (0,1,0)
Synthesis Toolkit in C++ (STK) [Cook and Scavone]
  C++ open source audio signal processing and algorithmic synthesis
Realtime audio in C++ (RtAudio) [Scavone]
  RtAudio provides a common API for realtime audio input/output

## Slide 25: Real-time sound synthesis
To achieve real-time, these pre-processing steps are performed for a given object and material
  Eigendecomposition is performed and resulting UT and each mode’s damping coefficient d and damped frequency fi are saved
  At run-time, an applied force f is transformed to mode space UTf
  Resulting q vector from UTf contains the amplitudes with which to scale each mode
  Sampled sound equals some of the mode amplitudes
  Resulting damped sinusoids q(t) can be combined and sampled at 44kHz to produce the sound
    Based on Nyquist theorem should sample at double what humans can sense
    For example, if we choose a samping rate of 48kHz, then deltaT = 1.0 / 48kHz ~ 0.00002
Example-Guided Physically Based Modal Sound Synthesis [Ren et al]

## Slide 26: Fluid-Structure Interaction and Elasto-Acoustic coupling
Elasto-acoustic coupling may also be referred to as solid-fluid interface
  It involves the interactions between the vibrations of an elastic structure and the sound field in the surrounding fluid
Weak coupling may be used if the pressure forces of the fluid on the solid are negligible, then a sequential computation can be formed
  Mechanical surface vibrations are calculated first and then used as the input for an acoustic field computation
Strong coupling requires that the mechanical and acoustic field equations including couplings be solved simultaneously

## Slide 27: FSI overview diagram
Two independently Τs and Τf generated triangulations on Ωs and Ωf
Displacement u on Τs
Potential ψ on Tf
Two (d−1)-dimensional grids ∂Τs and ∂Tf on interface boundary ΓI
At the interface ΓI we have to consider the solid - fluid coupling
  n ⋅ (vs – vf) = 0 = n ⋅ u’ + ∂ψ/∂n
  [σ] ⋅ n + pfnψ’ = 0
Τs
Τf
Elasto-Acoustic and Acoustic-Acoustic Coupling on Nonmatching Grids [Flemisch et. al]
ΓI
Notes: Τ is tau
ψ is Psi
σ is lowercase sigma
1. Normal component of mechanical surface velocity of the solid must coincide with the normal component of the acoustic velocity of the fluid
2. Ambient fluid causes a surface force fΓ which acts like a pressure load on the solid

## Slide 28: Displacement vs. potential-based formulation
So we can use standard Lagrangian nodal finite elements in both domains, we use:
  Displacement-based formulation for the solid (u)
  Potential-based formulation for the fluid (ψ)
If both solid and fluid used displacement-based formulations, then would require non-standard discretization by means of Raviart-Thomas
Notes: ψ is Psi
Raviart (ra-vi-art)

## Slide 29: Discretized elasto-coupling dynamics equation
Block diagonal entries Mu, Mψ, Dψ, Ku, Kψ can be assembled locally without needing any information from the opposite grid
  Coupling between the two grids takes place Duψ and DTuψ which realize the boundary integrals
Duψ = [Dpq] = ∈ Rd
Terms defined on next slide
Mu 0
0 -Mψ
u’’
ψ’’
+
0 Duψ
DTuψ -Dψ
u’
ψ’
+
Ku 0
0 -Kψ
u
ψ
=
fu
0
Notes: ψ is Psi

## Slide 30: Algorithm
Duψ = [Dpq] = ∈ Rd
  is scalar basis functions associated with node p on dΤs
  is scalar basis functions associated with node q on dΤf
  pf is the mean density of the fluid
  Γ is the boundary between fluid-structure interface
  Τs and Τf are surface and fluid triangulations respectively
  n is the normal at the boundary point
The key to this equation/algorithm is the determination of the intersection area of two elements from the different grids
    Intersection determined if a vertex lies inside the other surface element en or vice versa
For 3D, complexity order O(n4/3) with n denoting total # of unknowns
    It is possible to do better by incorporating neighbor relations of the surface elements and/or inheritance relations from an underlying geometrical multigrid hierarchy

## Slide 31: Algorithm (continued)
for all slave elements eni, i = 1, …, nn do
  for all master elements emj, j = 1, …, nm do
    determine intersection are enm = eni ∩ emj
    if eij != 0 then
      for all basis function Nm, ɸn with support ∩ eij != 0 do
        add ∫enm Nm ɸn dΓ to M
      end for
    end if
  end for
end for
Elasto-Acoustic and Acoustic-Acoustic Coupling on Nonmatching Grids [Flemisch et. al]

## Slide 32: Research References
Physically Based Sound for Computer Animation and Virtual Environments [ACM SIGGRAPH 2016 Course]
  Modal Vibration
  Acoustic Transfer
Example-Guided Physically Based Modal Sound Synthesis [Ren et al]
Interactive Modal Sound Synthesis Using Generalized Proportional Damping [Sterling et al]
Elasto-Acoustic and Acoustic-Acoustic Coupling on Nonmatching Grids [Flemisch et. al]
Q. Elasto-Acoustics in Formulas of Acoustics [Maysenholder and Mechel]
Fluid-Structure Interaction: Applied Numerical Methods [Morand and Ohayon]

## Slide 33: Software Libraries
Volumetric Mesh library [Barbic]
  Tetgen to volumetric mesh
  Computes mass matrix
Intel MKL (Math Kernel Library)
  General eigendecomposition
Synthesis Toolkit in C++ (STK) [Cook and Scavone]
  Set of open source audio signal processing and algorithmic synthesis C++ classes
Harmonic Oscillator [Barbic]
  Integrates a single 1D harmonic oscillator; can timestep the following Ordinary Differential Equation: M * q''(t) + D * q'(t) + K * q(t) = f(t)
ANN (Approximate Nearest Neighbor) [Mount and Arya]
  Supports exact and approximate nearest neighbor searching in arbitrarily high dimensions

## Slide 34: Thank You and Happy Halloween!
Questions?