## Slide 1
Wireless and Mobile Systems
for the IoT
Nirupam Roy
M-W 2:00-3:15pm
CHM 1224
CMSC 715: Fall 2021
Lecture 1.1: Sensors and DSP Basics

## Slide 2
Abstraction
Computing: Models and Algorithms

## Slide 3
Abstraction
Computing: Models and Algorithms
Data

## Slide 4
Abstraction
Computing: Models and Algorithms
Data
Sensing techniques

## Slide 5
Abstraction
Computing: Models and Algorithms
Data
Sensing techniques

## Slide 6
Abstraction: Traditional view
Computing: Models and Algorithms
Data
Sensing techniques
Data

## Slide 7
Natural language
processing
Computer
vision
Networking
Data packets
Voice recording
Image/video
Abstraction: Traditional view

## Slide 8
Natural language
processing
Computer
vision
Networking
Data packets
Voice recording
Image/video
WiFi signal
Acoustic signal
Light
Abstraction: Traditional view

## Slide 9
Integration of sensing and computing
Notes: Image source: https://www.geospatialworld.net/blogs/5-ways-lidar-is-transforming-the-world-before-our-eyes/
Image source: https://github.com/alvinwan/pc2vid

## Slide 10
Integration of sensing and computing
Notes: Image source: https://searchcustomerexperience.techtarget.com/definition/voice-recognition-speaker-recognition

## Slide 11
Abstraction
Computing: Models and Algorithms
Data
Sensing techniques

## Slide 12
Concept of Sensing

## Slide 13
Gesture/Motion/
Orientation
Vital signs detection
Autonomous vehicle control
Physical environment
(light, sound, speed, geomagnetism, radio waves, …)

## Slide 14
Gesture/Motion/
Orientation
Vital signs detection
Autonomous vehicle control
Physical environment
(light, sound, speed, geomagnetism, radio waves, …)

## Slide 15
Gesture/Motion/
Orientation
Vital signs detection
Autonomous vehicle control
Physical environment
(light, sound, speed, geomagnetism, radio waves, …)
Signal

## Slide 16
Sensors
- Definitions
- Generic working principle
2. Signals
- Digital abstraction
- Mathematical model

## Slide 17
What is a sensor?

## Slide 18
What is a sensor?
Is there a common principle?
Notes: Image source: https://www.electronicshub.org/different-types-sensors/

## Slide 19
1. How does a sound sensor (microphone) work?

## Slide 20
2. How does a gas sensor work?

## Slide 21
3. How does a light sensor work?

## Slide 22
4. How does a temperature sensor work?
Circuit sensitive to capacitance change
Voltage signal

## Slide 23
4. How does a temperature sensor work?
MEMS (Micro-Electro Mechanical Systems)

## Slide 24
Air flow
Electrical fluctuations
proportional to the
speed/volume of air-flow
Mapping
Mapping
10 Miles per hour
Fundamental principle of sensors

## Slide 25
A physical phenomenon
We want to measure
A structure or material
that reacts to the physical phenomenon
A circuit that converts the reaction to measurable electrical signal (e.g. voltage)
Interpretation of the signal, storing the data
SENSOR

## Slide 26
Temperature
Thermo-couple
Time
Voltage
Time
Temp.
Mapping
At time t
40° F
(a scalar value)
Fundamental principle of sensors

## Slide 27
Scalar vs. Vector Output

## Slide 28
X
Y
Scalar and vector output
Global coordinate system

## Slide 29
X
Y
Coordinate system

## Slide 30
X
Y
Local coordinate system
Coordinate system

## Slide 31
X
Y
VX
Vy
Local coordinate system
Coordinate system

## Slide 32
X
Y
VX
Vy
Local coordinate system
Output = <Vx, Vy>
Coordinate system

## Slide 33
X
Y
Vx
Vy
Local coordinate system
Coordinate system
Output at time t
<Vx (t), Vy(t)>
for a 2-axis sensor

## Slide 34
X
Y
Vx
Vy
Local coordinate system
Coordinate system
Output at time t
<Vx (t), Vy(t), Vz(t)>
for a 3-axis sensor
Z

## Slide 35
Coordinate system

## Slide 36
North
East
Global coordinate system
Coordinate system
Local coordinate system
X
Y
Z

## Slide 37
Mapping
Sensor data
Time
Sensor data
Scalar
Vector
Time
Sensor data
Sensor

## Slide 38
Mapping
Sensor data
Time
Sensor data
Scalar
Vector
Time
Sensor data
Sensor
Output at time t
<Vx (t), Vy(t), Vz(t)>

## Slide 39
Properties of a signal
Frequency, Amplitude, and Phase

## Slide 40
What is frequency?

## Slide 41
Definition of Frequency
Frequency is the number of occurrences of a repeating event per unit of time.

## Slide 42
Frequency, Amplitude, and Phase

## Slide 43
Time
Frequency, Amplitude, and Phase

## Slide 44
Time
Frequency, Amplitude, and Phase

## Slide 45
Frequency, Amplitude, and Phase
Time
Amplitude
One cycle
A
+A
-A
0

## Slide 46
𝚹
A
time = t second
Frequency, Amplitude, and Phase

## Slide 47
𝚹
A
time = t second
Frequency, Amplitude, and Phase
Phase

## Slide 48
𝚹
A
time = t second
Frequency, Amplitude, and Phase
Phase
-- with initial/additional phase ϕ

## Slide 49
Frequency, Amplitude, and Phase

## Slide 50
Frequency, Amplitude, and Phase

## Slide 51
𝚹
A
time = t second
Frequency, Amplitude, and Phase

## Slide 52
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Frequency: 2Hz
Frequency, Amplitude, and Phase
Notes: 1) Two common terms related to signals are amplitude and frequency. Frequency is the number of repetition of the signal per second.

## Slide 53
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Frequency: 4Hz
Frequency: 2Hz
Frequency, Amplitude, and Phase

## Slide 54
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Frequency: 2Hz
Frequencies of an arbitrary signal

## Slide 55
Frequencies of an arbitrary signal

## Slide 56
Frequencies of an arbitrary signal

## Slide 57
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
The concept of the Fourier series

## Slide 58
Time Domain and Frequency Domain
Approx. square wave

## Slide 59
Time Domain and Frequency Domain
Time domain view
Frequency domain view

## Slide 60
Analogy: Food coloring chart
Basis for food colors
Notes: Emphasize basis and coefficient using Color analogy

## Slide 61
Analogy: Food coloring chart
Basis for food colors
Notes: Emphasize basis and coefficient using Color analogy

## Slide 62
Analogy: Food coloring chart
Basis for food colors
Notes: Emphasize basis and coefficient using Color analogy

## Slide 63
Analogy: Food coloring chart
Basis for food colors
Notes: Emphasize basis and coefficient using Color analogy

## Slide 64
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Time Domain and Frequency Domain

## Slide 65
Time Domain and Frequency Domain
Amplitude
0.25
0.50
Time
0.00
Amplitude
4
Frequency (Hz)
0
6
8
2
IFFT
FFT
Fourier Transform
Time domain
Frequency domain
FFT = Fast Fourier Transform
IFFT = Inverse Fast Fourier Transform

## Slide 66
Frequency band
Amplitude
4
Frequency (kHz)
0
6
8
2
A 4 kHz frequency band starting at 2 kHz
What is bandwidth?
What is baseband?

## Slide 67
Spectrogram
U
M
D

## Slide 68
Spectrogram
U
M
D
[
[
[
[
FFT
FFT
FFT
FFT
FFT of overlapping windows
of samples
(Spectrogram)

## Slide 69
Spectrogram
U
M
D