## Slide 1: RF-IDraw: Virtual Touch Screen in the Air
Deepak Vasisht
Jue Wang, Dina Katabi

## Slide 2: How Do We Get Virtual Touch Screens?

## Slide 3: How Do We Get Virtual Touch Screens?
Use RF-localization to track the RFIDs
But … accuracy is not enough …

## Slide 4: How Do We Get Virtual Touch Screens?

## Slide 5: Localization with Antenna Arrays
Wireless
Source
Antenna Array Receiver

## Slide 6: Localization with Antenna Arrays
Array’s beam points to source
Antenna Array Receiver

## Slide 7: Localization with Antenna Arrays
çç

## Slide 8: Localization with Antenna Arrays
Location Uncertainty

## Slide 9: Localization with Antenna Arrays
More Antennas
 Less uncertainty

## Slide 10: Localization with Antenna Arrays

## Slide 11: Localization with Antenna Arrays
Not practical!

## Slide 12: RF-IDraw
Enables virtual touch screens in the air
Motion tracking to within 3.7cm
Rich interface that recognizes words written in the air
Works with standard RFIDs and RFID readers

## Slide 13: How Does it Work?

## Slide 14: Ambiguity-Resolution Tradeoff

## Slide 15: Ambiguity-Resolution Tradeoff
Antenna spacing is λ/2,
λ is the wavelength

## Slide 16: Ambiguity-Resolution Tradeoff
Spacing is λ
Ambiguity
Higher resolution

## Slide 17: Ambiguity-Resolution Tradeoff
8 λ

## Slide 18: Ambiguity-Resolution Tradeoff
Ambiguity in position
Low resolution
High resolution
No ambiguity

## Slide 19: RF-IDraw: Multi-Resolution Array
8 λ
λ/2
Narrowly spaced and widely spaced antennas create an overlay of multi-resolution beams.
Use fewer antennas, but place them smartly

## Slide 20: Localization

## Slide 21: Localization
Are we done?

## Slide 22: Let’s Try
Accuracy ~ 15cm
Errors are random and don’t preserve the shape of the trajectory.

## Slide 23: Noiseless Scenario

## Slide 24: Noiseless Scenario

## Slide 25: Noiseless Scenario

## Slide 26: Impact of Noise
Incorrect beams
Mistaken location

## Slide 27: Impact of Noise
Want errors to be systematic –i.e., they may move the trajectory but preserve its shape

## Slide 28: Idea: Stick with your choices

## Slide 29: Idea: Stick with your choices
Incorrect beams
Mistaken location
Sticking with a beam, even if it is not in the exact location, causes systematic errors

## Slide 30: Performance Results

## Slide 31: Implementation
ThingMagic RFID Readers
  Reader has 4 antennas
  Used two readers
Alien Squiggle RFID Tags
Baseline: 2 Antenna arrays with 4 antennas each

## Slide 32: Setup
Ground Truth: VICON motion capture system
Notes: Of course, we need a ground truth for the location of the source. For that we use the Vicon motion capture system. It is half a million dollar system of infra-red camera mounted on a celing. The good thing, however, about this system is that it can track motion to few milimeters.
Animate for distance

## Slide 33: Example

## Slide 34: Examples
“Jue”
“Clear”
4 cm wide

## Slide 35: Metric: Absolute Positioning Error
Ground truth

## Slide 36: Absolute Positioning Error
Chart: 
RF-IDraw
Antenna Arrays
Positioning error (in m)
CDF
19cm
42cm

## Slide 37: Metric: Trajectory Error
Ground truth

## Slide 38: Trajectory Error
Chart: 
Antenna Arrays
RF-IDraw
40.8cm
3.7cm
Trajectory Error (in m)
CDF

## Slide 39: Virtual Touch Screen Application
5 users wrote 150 words
Words used as touch gestures on Android using MonkeyRunner API
Word recognition using MyScript Stylus app

## Slide 40: Example
Antenna Arrays
RF-IDraw

## Slide 41: Character Recognition Rate
Chart: 
| 2m | 3m | 5m
RF-IDraw | 0.98 | 0.976 | 0.973
Antenna Arrays | 0.042 | 0.037 | 0.004
Distance from Source (in m)
Character Recognition Rate(%)
RF-IDraw delivers accurate virtual touch screens

## Slide 42: Related Work
RF-based localization
  Witrack [NSDI,14], WiSee [Mobicom’14], ArrayTrack [NSDI’13], PinPoint [NSDI’13], PinIt [SIGCOMM’13], Zee [MobiCom’12], PinLoc [MobySys’12], FM-based [MobySys’12], EZ [MobiCom’10], ….
Kinect and vision-based gesture recognition
  Zhang et al [IEEE Multimedia’13], Murata et al [IJDSN’14] , Yin et al [IEEE VL/HCC’14]

## Slide 43: Conclusion
RF-IDraw the first wireless system that enables virtual touch screens on the air
It focuses on trajectory tracking as opposed to point-by-point localization
It introduces the concept of multi-resolution arrays
Its design applies beyond RFIDs to other wireless technologies – e.g., WiFi

## Slide 45
FingerIO: Using Active Sonar for Fine Grained Finger Tracking
Rajalakshmi Nandakumar, Vikram Iyer
Shyam Gollakota, Desney Tan

## Slide 46
Can we achieve finger tracking for near device interaction with no finger instrumentation and no line of sight?

## Slide 47
Application 1: Make anything an input surface

## Slide 48
Application 2: Move beyond tiny screens

## Slide 49
Application 3: Interaction with occlusions

## Slide 50
Complex processing
RF travels at the speed of light→ need GHz of bandwidth
Mobile devices have limited processing capabilities
Existing Approaches: Doppler Radar
Custom hardware
Requires yet another radio on mobile devices
Consumes additional power and area on devices

## Slide 51
Track a finger with no instrumentation and no line of sight
Introduce algorithms and techniques for active sonar without custom hardware
Achieve 0.8 —1.2 cm accuracy on a Galaxy S4 and smartwatch prototype
FingerIO

## Slide 52
Transform mobile devices into active sonar systems
Achieve sub-centimeter level tracking accuracy
Challenges

## Slide 53
Key Idea: Transform the Device into Active Sonar
Sound waves transmitted by the phone speaker reflect off of the finger

## Slide 54
Mic 2
Mic 1
Key Idea: Transform the Device into Active Sonar
Echo from finger is recorded by 2 microphones

## Slide 55
Key Idea: Transform the Device into Active Sonar
Time for the echo to arrive back at the phone changes as the finger moves

## Slide 56
Accuracy Depends on Time Measurement
Sampling at 48kHz, 1 sample → 0.7cm
t1
t2
Mic 2
Mic 1

## Slide 57
Transform mobile devices into active sonar systems
Achieve sub-centimeter tracking accuracy
Challenges

## Slide 58
How can we measure arrival time?
Transmit chirp signals and use autocorrelation to determine arrival times
Chirp
Correlation Profile

## Slide 59
First Order Solution: Correlation
We use the closest moving echo to achieve finger tracking
t1
t2
Moving Finger Echo
Correlation Profile

## Slide 60
Correlation in Practice
How to get the exact arrival time of the echoes?
Estimate echo arrival with 2-3 sample error
→ tracking accuracy of 3 cm

## Slide 61
Inspiration from WiFi Networks
Transmitters and receivers do not share a common, synchronized clock
Receivers need to determine the start of a message to successfully decode

## Slide 62
WiFi’s Solution: OFDM
Timing Errors Create FFT Phase Offsets
FFT Phase
Compute inverse FFT to generate N sample OFDM symbol
Append the first S samples to create a cyclic suffix
 Creates a periodic signal
We leverage this phase to get exact echo arrival time

## Slide 63
Putting it All Together
Transmit 18-20 kHz OFDM symbols every 5.92 ms
Use correlation to get a coarse timing estimate within 2-3 samples
Correct error using phase properties of OFDM to achieve < 1 cm accuracy
5.92 ms
t

## Slide 64
Evaluation

## Slide 65: How accurate is FingerIO?
Random user drawings
10 Users
3 Repetitions
30 Total measurements
0.8 cm accuracy
50 x 100 cm2 around phone
FingerIO Phone
Reference Phone

## Slide 66: How accurate is FingerIO?
10
8
6
4
2
0

## Slide 67: Smartwatch Tracking Accuracy
10 Participants
3 Drawings
30 Total measurements
1.2 cm accuracy
25 x 50 cm2 on one side
40mm
40mm
Mic 1
Mic 2
Speaker

## Slide 68: Addressing unintended motion
10 users
1 min random motion
10 min of motion
0 false detection (watch)
2 false detection (phone)
5 cm
Start-Stop Gesture

## Slide 69
Track a finger with no instrumentation and no line of sight
Introduce algorithms and techniques for active sonar without custom hardware
Enable exciting new directions for finger tracking research
Conclusion

## Slide 70
FingerIO: Using Active Sonar for Fine Grained Finger Tracking
Rajalakshmi Nandakumar, Vikram Iyer
Shyam Gollakota, Desney Tan