## Slide 1
Machine Learning for Physical Sensing & Perception
Nirupam Roy
Tu-Th 3:30 – 4:45pm
IRB 1207
CMSC 818V : Fall 2025
Lecture 1_4: Frequency in Learning

## Slide 2
Announcement - 1
Due tonight!

## Slide 3
Announcement - 2
You have been added to Zaratan cluster for
818v assignments.
Get familiar with “Zaratan Primer”
https://www.cs.umd.edu/class/fall2022/cmsc416/zaratan.shtml
Stay tuned for more information.

## Slide 4
2
m = 0
3
4
1
N-1
N-2
…
+
-
+
-
-
+
Frequency
The Curious Case of “Negative frequency”

## Slide 5
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
The Curious Case of “Negative frequency”

## Slide 6
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
The Curious Case of “Negative frequency”
Real signal’s magnitude spectrum is symmetric.
Why?
Magnitude
|zm|
2
2j

## Slide 7
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
The Curious Case of “Negative frequency”
Complex signal’s magnitude spectrum may or may not be symmetric.
Why?
Magnitude
|zm|

## Slide 8
From “# of Cycles” to “the real-world frequencies”
Sampling frequency = fs (i.e., fs samples per second)
Slowest frequency ( radians per step) = N samples per rotation
= (N/ fs) seconds per rotation
Therefore, the slowest frequency = (fs /N) Hz
Higher frequencies are integer multiple of (fs /N) Hz
0, , , , … , ,

## Slide 9
Estimating the real-world frequencies
Sampling frequency = fs (i.e., fs samples per second)
Slowest frequency ( radians per step) = N samples per rotation
= (N/ fs) seconds per rotation
Therefore, the slowest frequency = (fs /N) Hz
Higher frequencies are integer multiple of (fs /N) Hz
0, , , , … , ,
- , - , - , … , , -

## Slide 10
The resolution and the highest frequency
Resolution
= minimum observable frequency difference =
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
Magnitude/Phase of zm
What if the actual frequency falls in between two frequency bins?

## Slide 11
The resolution and the highest frequency
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
Magnitude/Phase of zm
Highest frequency =

## Slide 12
The resolution and the highest frequency
How can we increase the resolution?
How can we increase the range of the spectrum?
,
=

## Slide 13
Time resolution v/s Frequency resolution

## Slide 14
Time resolution v/s Frequency resolution
Uncertainty principle:
“You cannot simultaneously know a signal’s exact time location and its exact frequency content.”

## Slide 15
U
M
D
[
[
DFT
DFT
How can we increase the frequency resolution?
=
How can we increase the time resolution?
Time resolution v/s Frequency resolution

## Slide 16
Sampling Theorem

## Slide 17
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Sampling theorem

## Slide 18
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Aliasing: Two signals become indistinguishable
after sampling
Sampling theorem

## Slide 19
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Aliasing

## Slide 20
Aliasing

## Slide 21
How to find a good sample rate?
Suppose you sample a signal in some way. If you can exactly reconstruct the signal from the samples, then you have done a proper sampling and captured the key signal information
Notes: [Reference slides] http://terrano.ucsd.edu/jorge/teaching/mae143a/lectures/8sampling.pdf

## Slide 22
How to find a good sample rate?
Suppose you sample a signal in some way. If you can exactly reconstruct the signal from the samples, then you have done a proper sampling and captured the key signal information
The sampling frequency fs , is the number of samples per second. This is to be compared with the signal cyclic frequencies
Notes: [Reference slides] http://terrano.ucsd.edu/jorge/teaching/mae143a/lectures/8sampling.pdf

## Slide 23
11.1 samples/cycle
3.2 samples/cycle
1.05
samples/cycle
How to find a good sample rate?

## Slide 24
How to find a good sample rate?
Nyquist-Shannon sampling theorem:
In order to uniquely represent a signal F(t) by a set of samples, the sampling rate must be more than twice the highest frequency component present in F(t).
If sample rate is fs and maximum frequency we want to
record is fmax , then
fs > 2fmax

## Slide 25
Nyquist frequency = Maximum alias-free frequency
for a given sample rate.
Nyquist rate = Lower bound of sample rate for a
signal.
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
(fs / 2)
(2fmax)

## Slide 26
Aliasing
Amplitude
8
Frequency (Hz)
0
12
16
4
fmax = 12 Hz

## Slide 27
Commonly, the maximum frequency in human voice is 4 kHz, what sample rate will you use in your audio recorder?
Is there any limit on the maximum sample rate you can use?

## Slide 28
Aliasing

## Slide 29
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Aliasing: Two signals become indistinguishable after sampling
Sampling theorem

## Slide 30
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
4
Frequency (Hz)
0
6
8
2
Frequency domain
-6
-4
-2
Time domain samples
FFT

## Slide 31
Aliasing: Different frequencies, same name!!
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
Magnitude/Phase of zm
Assume, Sample rate = 8 Hz
For a COMPLEX signal, what value will we see if the actual frequency is:
a) 3 Hz
b) -2 Hz
c) 6 Hz
d) -5 Hz
e) 4 Hz and -4Hz

## Slide 32
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
Magnitude/Phase of zm
6
7
8
5

## Slide 33
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
Magnitude/Phase of zm
6
7
8
5

## Slide 34
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
Magnitude/Phase of zm
Fs/4
- Fs/4
0
Fs/2

## Slide 35
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
Magnitude/Phase of zm
2
- 2
0
1
3
4
-4
-3
-1

## Slide 36
Aliasing: Different frequencies, same name!!
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
Magnitude/Phase of zm
Assume, Sample rate = 8 Hz
For a COMPLEX signal, what value will we see if the actual frequency is:
a) 3 Hz
b) -2 Hz
c) 6 Hz
d) -5 Hz
e) 4 Hz and -4Hz

## Slide 37
Aliasing: Different frequencies, same name!!
2
m = 0
3
4
1
-3
-2
-1
-4
Frequency
Magnitude/Phase of zm
Assume, Sample rate = 8 Hz
For a REAL signal, what value will we see if the actual frequency is:
a) 3 Hz
b) -2 Hz
c) 6 Hz
d) -5 Hz
e) 4 Hz and -4Hz

## Slide 38
Aliasing: Spectrogram of increasing frequency

## Slide 39
Amplitude
4
Frequency (Hz)
0
6
8
2
Sampling frequency = 10Hz
Nyquist frequency = 5Hz
Calculating the aliased frequency value for real signals

## Slide 40
Amplitude
4
Frequency (Hz)
0
6
8
2
Sampling frequency = 10Hz
Amplitude
4
Frequency (Hz)
0
6
8
2
Nyquist frequency = 5Hz
Received
signal
Calculating the aliased frequency value for real signals

## Slide 41
Calculating the aliased frequency value for real signals
Amplitude
4
Frequency (Hz)
0
6
8
2
Sampling frequency = 10Hz
Amplitude
4
Frequency (Hz)
0
6
8
2
Nyquist frequency = 5Hz
Received
signal
fs = Sampling frequency
f = Target frequency
fa = Aliased(perceived) frequency
K = Non-negative integer
fa = min(abs(K*fs - f))

## Slide 42
10k
20k
30k
40k
50k
60k
70k
80k
90k
100k
Frequency spectrum
Amplitude
Nyquist frequency
Aliasing: A real life scenario
Notes: to amplify the signal power …
Now, this signal typically contains many more frequencies than the sampling system can handle …

## Slide 43
10k
20k
30k
40k
50k
60k
70k
80k
90k
100k
Frequency spectrum
Amplitude
Nyquist frequency
Aliasing: A real life scenario
Notes: to amplify the signal power …
Now, this signal typically contains many more frequencies than the sampling system can handle …

## Slide 44
Frequency spectrum
Nyquist frequency
10k
20k
30k
40k
50k
60k
70k
80k
90k
100k
Amplitude
We need a “Low-pass filter”
to remove unwanted high frequency signals
Aliasing: A real life scenario
Notes: to amplify the signal power …
Now, this signal typically contains many more frequencies than the sampling system can handle …

## Slide 45
10k
20k
30k
40k
50k
60k
70k
80k
90k
100k
Frequency spectrum
Sensor
ADC
Amplitude
Anti-aliasing
Filter
Anti-aliasing filter
Nyquist frequency
Notes: to amplify the signal power …
Now, this signal typically contains many more frequencies than the sampling system can handle …

## Slide 46
10k
20k
30k
40k
50k
60k
70k
80k
90k
100k
ADC
Amplitude
Sensor
Frequency spectrum
Anti-aliasing
Filter
Anti-aliasing filter
Nyquist frequency
Notes: Hence, a low pass filter…

## Slide 47
Anti-aliasing
filter
10k
20k
30k
40k
50k
60k
70k
80k
90k
100k
Anti-aliasing
Filter
ADC
Amplitude
Sensor
Frequency spectrum
Anti-aliasing filter
Notes: removes the unwanted frequencies above 24 kHz …
And ultimately, this filtered signal is sampled by an ADC to generate digital sound samples

## Slide 48
What limitations of FFT or STFT bother you?
Fixed frequency locations for a given sample rate and time window.

## Slide 49
Paper: https://arxiv.org/pdf/2101.08596
ICLR 2021
Questioning the standards

## Slide 50
Classifier
Classifier
“Dog”
“Dog”
Application: Classification

## Slide 51
Audio Classification Steps

## Slide 52
Zero-Crossing Rate (ZCR) – counts how often the signal crosses zero.
Short-Time Energy – total signal energy in a frame (loudness).
RMS Amplitude – average signal power measure.
Autocorrelation – detects periodicity and pitch.
Temporal Moments – mean/variance/skewness of waveform shape.
AMDF – pitch estimation via average magnitude differences.
Rise/Attack/Decay Times – capture onset and offset dynamics.
Temporal Centroid – center of gravity of signal energy in time.
Envelope Features – smoothed amplitude curve of signal.
Cepstrum (time-domain view) – captures pitch and vocal tract characteristics.
Spectral Centroid – weighted average frequency (brightness)
Spectral Bandwidth – spread of spectrum around the centroid
Spectral Rolloff – frequency below which most energy lies
Spectral Flux – frame-to-frame change in the spectrum
Spectral Flatness – how noise-like vs. tone-like the spectrum is
Spectral Contrast – difference between peaks and valleys across bands
Fundamental Frequency (F0) – lowest frequency, perceived as pitch
Harmonic-to-Noise Ratio – balance between harmonic and noise energy
Formant Frequencies – resonant peaks in speech/instrument sounds
MFCCs – compressed spectral features modeled after human hearing
Time domain features
Freq. domain features

## Slide 53
Zero-Crossing Rate (ZCR) – counts how often the signal crosses zero.
Short-Time Energy – total signal energy in a frame (loudness).
RMS Amplitude – average signal power measure.
Autocorrelation – detects periodicity and pitch.
Temporal Moments – mean/variance/skewness of waveform shape.
AMDF – pitch estimation via average magnitude differences.
Rise/Attack/Decay Times – capture onset and offset dynamics.
Temporal Centroid – center of gravity of signal energy in time.
Envelope Features – smoothed amplitude curve of signal.
Cepstrum (time-domain view) – captures pitch and vocal tract characteristics.
Spectral Centroid – weighted average frequency (brightness)
Spectral Bandwidth – spread of spectrum around the centroid
Spectral Rolloff – frequency below which most energy lies
Spectral Flux – frame-to-frame change in the spectrum
Spectral Flatness – how noise-like vs. tone-like the spectrum is
Spectral Contrast – difference between peaks and valleys across bands
Fundamental Frequency (F0) – lowest frequency, perceived as pitch
Harmonic-to-Noise Ratio – balance between harmonic and noise energy
Formant Frequencies – resonant peaks in speech/instrument sounds
MFCCs – compressed spectral features modeled after human hearing
Time domain features
Freq. domain features

## Slide 54
Short-Time Fourier Transform (STFT)
Spectrogram
Notes: MFCC: https://medium.com/@MuhyEddin/feature-extraction-is-one-of-the-most-important-steps-in-developing-any-machine-learning-or-deep-94cf33a5dd46

## Slide 55
Mel-Frequency Cepstral Coefficients (MFCC)
(1) The human ear doesn’t perceive frequency linearly.
(2) We are more sensitive to low-frequency changes (e.g., distinguishing
500 Hz vs. 600 Hz) than to high-frequency changes (e.g., 5000 Hz vs.
5100 Hz).
(3) This comes from the basilar membrane in the cochlea, where spacing
of hair cells produces a nonlinear frequency resolution.
Mel == Melody
Notes: MFCC: https://medium.com/@MuhyEddin/feature-extraction-is-one-of-the-most-important-steps-in-developing-any-machine-learning-or-deep-94cf33a5dd46

## Slide 56
Mel-Frequency Cepstral Coefficients (MFCC)

## Slide 57
Evolution of Classification Architecture

## Slide 59
= one-dimensional waveform of T samples
sampling frequency Fs
= Replaces MFCC
= The main model (e.g., classifier)
LEAF: A LEarnable Audio Frontend

## Slide 60
Learnable modules

## Slide 61
LEAF: A LEarnable Audio Frontend

## Slide 66
Extra Slides

## Slide 69
Fourier series
2

## Slide 70
Fourier series

## Slide 76
Discrete Fourier Transform formula
Discrete version:

## Slide 77
Discrete Fourier Transform formula
Discrete version: