## Slide 1
Machine Learning for Physical Sensing & Perception
CMSC 818V : Fall 2026
Nirupam Roy
Tu-Th 12:30 – 1:45pm
IRB 2107
Lecture 2: Signals as Measurements of Physical Phenomena

## Slide 2
The Forward Measurement Model
Assembling x, θ, F, and n
24

## Slide 3
What is a forward model?
44
y = F (x ; θ ) + n
A model of the physical process that maps the state of the world to the measurements produced by a sensor.
F maps the latent physical state x into the expected sensor measurement y, given system/environment parameters θ.
Notice what F does not have to be: it does not need to be the physical state itself, or the measurement itself — it is the mapping between them.

## Slide 4
A forward model doesn't have to be exact
45
F can take many forms:
Derived from physics
Simulated numerically
Approximated
Partly learned from data
Completely learned
The test:
“If I gave you the true physical state, could your model predict what the sensor would measure?” If yes — you have a forward model.

## Slide 5
The forward question vs. the inverse question
46
The forward question
“If I know where the target is, what signal should the radar receive?”
The inverse question
“Given the received signal, where is the target?”
An instance — a target at distance d:
y (t) = α s (t − 2 x /c) + n(t)
x → y
forward model
y → x̂
inverse problem
46
y (t) = α s (t − 2 τ) + n(t)

## Slide 6
The forward model, across sensing systems
47
In every system, the forward model predicts the measurement from the physical state.
System | Physical state x | Forward model predicts
Camera | 3D scene, materials, lighting | Pixel intensities
Microphone | Sound source + room | Recorded waveform
Radar | Target position / velocity | RF echo / IQ samples
LiDAR | Surface geometry | Return times / intensities
IMU | Body motion | Acceleration and gyro readings
CT | Internal attenuation map | X-ray projections

## Slide 7
θ: what does it actually mean?
48
y = F (x ; θ ) + n
Parameters describing the sensing system, environment, and propagation conditions that determine the forward process.
θ is not what we are trying to infer — it is what the forward model needs to know to relate x to y.
θ is a parameter of the model, not a label — some θ are known and chosen, others are unknown and must be estimated alongside x.

## Slide 8
θ: what does it actually mean?

## Slide 9
θ across five sensing systems
49
System | x — quantity of interest | θ — forward-model parameters
Camera | Object geometry / pose | Illumination, camera pose, focal length, exposure
Microphone array | Source location | Room geometry/materials, mic locations, speed of sound
Radar | Target position / velocity | Antenna geometry, carrier frequency, transmitted waveform
WiFi localization | User location | AP position, room geometry, furniture, antenna response
IMU | Motion / trajectory | Sensor bias, scale factor, orientation, gravity

## Slide 10
The x / θ boundary depends on the task, not the quantity
50
Task: speaker localization
x = speaker location
θ = room geometry / materials
Task: room reconstruction
x = room geometry / materials
θ = everything else (source signal, mic array geometry, …)
The same physical quantity — room geometry — is θ in one task and x in the other. The split is set by what you are trying to infer, not by the physics itself.

## Slide 11
Clean terminology for the whole pipeline
51
x
physical state of interest
θ
system/environment parameters governing measurement formation
F
forward model
y
sensor measurement
n
measurement noise / unmodeled effects
x
what we want
y
what we measure
F
θ

## Slide 12
F vs. θ: model structure vs. instantiation
52
F specifies the structure of the forward model; θ specifies the parameters that instantiate it for a particular system or environment.
y (t) = (1/r) s (t − r/c) + n(t)
x = r (distance) θ = c (propagation speed)
For a richer room-acoustic model:
θ = { room geometry, wall reflection coefficients, microphone positions, c, … }
F
model structure / physical laws
θ
parameters that instantiate that model
x
physical state we want to infer

## Slide 13
Why not just call θ "nuisance parameters"?
53
Some θ are known, deliberately chosen design parameters:
Antenna spacing
Radar carrier frequency
Camera focal length
Others are genuinely unknown nuisance parameters:
Room materials — and other unmodeled environmental conditions
θ mixes both known design choices and unknown nuisances — so "nuisance parameters" is too narrow a name for what it actually captures.
A nuisance parameter is a parameter that affects the sensor measurement but is not the quantity you actually want to estimate.

## Slide 14
θ: nuisance / environment parameters
27
Room geometry
Materials
Illumination
Temperature
Sensor gain
Microphone response
Antenna configuration
θ is not what we usually want to estimate — but it shapes F, so ignoring it silently biases our inference of x.
27

## Slide 15
F and n: process and uncertainty
28
F: the forward model
The known — or partially known — physical process transforming x into measurements. Sometimes physics-based, sometimes learned, often both.
n: measurement noise
The measurement uncertainty not captured by the deterministic part of the model — sensor electronics, thermal noise, unmodeled effects.
28

## Slide 16
From a deterministic map to a probabilistic model
29
Once we admit noise, y is no longer a deterministic function of x — it is a random variable given x.
p ( y | x)
the probabilistic measurement model
Bayesian inference (later lectures) are built on this model.
29

## Slide 17
Deterministic Model vs.
Stochastic Measurement
Why y = F(x) is almost never literally true
30

## Slide 18
Gaussian noise

## Slide 19
The Central Limit Theorem (CLT) (roughly):
When many independent random contributions are added together, their sum tends to
have a Gaussian (normal) distribution, even if the individual contributions are not Gaussian.
Why Gaussian?
Galton board

## Slide 20
Why y = F(x) is almost never literally true
31
Instead, we write y = F(x) + n. For Gaussian noise:
n ~ 𝒩 (0, σ 2 )
p (y |x ) ∝ exp [ −‖y−F (x)‖2 / 2σ 2 ]
This is the origin of a very common pattern in estimation: under Gaussian measurement noise, maximizing p(y|x) becomes minimizing squared measurement error.
We will not derive it in detail today — just recognize the shape when it returns in Lecture 3.
31

## Slide 21
What Information Is Lost During Sensing?
From forward models to inverse problems
54

## Slide 22
What information is lost during sensing?
55
A sensor does not capture the complete physical state of the world.
The forward process transforms, mixes, compresses, and often irreversibly discards information before producing the measurement.
y = F (x ; θ ) + n
even with no noise:
y = F (x ; θ )
We generally cannot uniquely recover x from y.

## Slide 23
1. Dimensionality reduction
56
The physical world often has many more degrees of freedom than the measurement — the clearest example is a camera.
3D world
2D image
projection
A pixel tells us where something projects onto the image plane, but not its depth.
u = fX/Z v = fY/Z
Many 3D points can produce the same (u, v) — e.g. (X, Y, Z) and (2X, 2Y, 2Z) project to the same image location.
Depth information has been partially lost through projection.

## Slide 24
2. Multiple causes, one measurement
57
Suppose a camera measures a dark pixel. Why is it dark?
Dark material
Weak illumination
Surface orientation
Shadow
y ∝ illumination × reflectance
Illumination is governed by θ; reflectance depends on x (and sometimes θ too).
x₁ ≠ x₂ but F (x₁; θ₁) = F (x₂; θ₂)
Different combinations of physical quantities can give the same y — the fundamental many-to-one nature of many forward models.

## Slide 25
3. The sensor is an information bottleneck

## Slide 26
3. The sensor is an information bottleneck
58
Every sensor has limited sensitivity.
L(λ) ⟶ (R, G, B )
A rich electromagnetic spectrum is reduced to approximately three channels.
Two different spectral distributions can therefore produce the same RGB values.
Similarly, a microphone measures pressure variation over a limited frequency range — it does not capture every property of the acoustic field.
The sensor itself acts as an information bottleneck.

## Slide 27
4. Finite resolution destroys detail
59
If two objects are closer than the radar's range resolution, their reflections may merge into one return.
continuous scene → finite samples
x (t) → x [n]
Fine-scale spatial or temporal information can disappear.

## Slide 28
5. Occlusion: some states are never measured
60
A camera observes the front surface of a box, but not the back.
complete 3D object → visible-surface projection
No amount of processing of a single image can directly recover measurements that were never acquired. Any reconstruction of the back must come from assumptions or prior knowledge.
The same issue occurs in radar shadowing, ultrasound, LiDAR, and many other sensing systems.

## Slide 29
6. Mixing: contributions become entangled
61
y(t) = s(t) ∗ h(t) + n(t)
A microphone measurement contains both the source s(t) and the environment h(t) — they are not separately observed.
Likewise, wireless CSI may contain the superposition of many propagation paths:
H(f) = Σₖ αₖ exp(−j2πfτₖ)
The receiver measures the combined channel, not necessarily each individual reflector/path.
Information may not be completely absent — it may be entangled.
lost information ≠ mixed/latent information — a sophisticated inverse method can sometimes disentangle the latter.

## Slide 30
7. Noise limits distinguishability (Signal-to-noise ratio or SNR)
62
y = F (x ; θ ) + n
Suppose two physical states produce slightly different ideal measurements:
F(x₁) ≈ F(x₂)
If the difference is smaller than the measurement noise, the sensor may not be able to distinguish them.
Even a theoretically invertible mapping may be practically unrecoverable.

## Slide 31
Three concepts this motivates
63
Ambiguity
Can different physical states explain the same measurement?
Identifiability
Can the physical state of interest be uniquely determined from the available measurements?
Observability
Do the measurements contain enough information about the state to recover it?
Especially important for dynamical systems, later in the course.
x₁ ≠ x₂, F(x₁) ≈ F(x₂)
For Lecture 1 we emphasize ambiguity and identifiability, and only briefly mention observability — formal observability fits better with state estimation.

## Slide 32
Where does the lost information go?
64
x
F(⋅; θ)
y
3D → 2D
projection loss
continuous → sampled
resolution loss
many wavelengths → RGB
spectral loss
multiple paths → one signal
mixing
hidden surfaces → no measurement
occlusion
ideal signal → noisy signal
uncertainty
If the forward process loses information, how can we recover the physical state?

## Slide 33
What information was lost?
36
The sensor gives us y. We actually want x.
How do we get from y back to x?
36
Notes: That is the question Lectures 2–4 will progressively answer.

## Slide 34
The bridge to inverse problems
65
Measurements + Physics + Priors + Learning
⟶ Physical inference
Much of physical sensing ML exists because the measurement alone is insufficient.
We use physical structure, multiple measurements, priors, and learned regularities to resolve what the forward process made ambiguous.

## Slide 35
How does information about the physical world become
encoded in “Signals” ?
(amplitude, time, frequency, and phase)
2

## Slide 36
1. What is a signal?
5

## Slide 37
Modeling a Signal
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00

## Slide 38
A signal is any physical quantity that varies with one or more independent variables (such as time, space, or both) and conveys information about a system or phenomenon.
Define “Signal”

## Slide 39
A signal is any physical quantity that varies with one or more independent variables (such as time, space, or both) and conveys information about a system or phenomenon.
Define “Signal”
A signal is a mathematical function of one or more independent variables (like time or space).

## Slide 40
A signal is any physical quantity that varies with one or more independent variables (such as time, space, or both) and conveys information about a system or phenomenon.
Define “Signal”
A signal is a mathematical function of one or more independent variables (like time or space).
where:
= domain: what variables index the signal;
= value space (often loosely called the range): what value the signal takes at each domain point.

## Slide 41
The number of independent variable of the function.
Define “Dimension” of a signal
1D signals:
Audio waveform x(t) -- (time).
Stock price x[n] -- (discrete index).
2D signals:
Grayscale image x(m,n) -- (row, column)
3D signals:
Video x(m,n,t) (space + time)

## Slide 42
The number of independent variable of the function.
Define “Dimension” of a signal
1D signals:
Audio waveform x(t) -- (time).
Stock price x[n] -- (discrete index).
2D signals:
Grayscale image x(m,n) -- (row, column)
3D signals:
Video x(m,n,t) (space + time)
What about a color image?

## Slide 43
Scalar-valued vs. Vector-valued
Output of a Sensor

## Slide 44
Mapping
Sensor data
Time
Sensor data
Scalar
Vector
Time
Sensor data
Sensor

## Slide 45
Mapping
Sensor data
Time
Sensor data
Scalar
Vector
Time
Sensor data
Sensor
Output at time t
<Vx (t), Vy(t), Vz(t)>

## Slide 46
X
Y
Vx
Vy
Output at time t
<ax (t), ay(t), az(t)>
3-axis accelerometer sensor
Z

## Slide 47
domain=1, value space=3
domain=2, value space=3
domain=3, value space=3
domain=2, value space=3

## Slide 48
Sensor data
Is an image a multi-dimensional signal?

## Slide 49
Sensor data
Is a gray-scale image a scalar-valued or a vector-valued signal?

## Slide 50
Scalar and Vector fields
Temperature distribution (scalar field)

## Slide 51
Magnetic field (vector field)
Scalar and Vector fields
Particle flow
(vector field)

## Slide 52
2. How Signals ”encodes” physical
information
Amplitude, Frequency, and Phase

## Slide 53
Amplitude: how strongly did the world interact with the signal?
7

## Slide 54
Path-loss model
8
y(t) = A s(t)
What determines A ?
propagation distance
absorption
reflectivity
scattering strength
source strength
sensor gain
Acoustic example — ideal spherical spreading
Amplitude contains physical information — but it is usually confounded.
A weak radar return could mean: a distant target · a poorly reflecting target · propagation loss · antenna orientation.

## Slide 55
What is frequency?

## Slide 56
Definition of Frequency
Frequency is the number of occurrences of a repeating event per unit time (independent variable).

## Slide 57
1D function
2D function

## Slide 58
What can be a simple repeating
“function” == signal?

## Slide 59
Frequency, Amplitude, and Phase

## Slide 60
Model for a signal (frequency, amplitude, and phase)

## Slide 61
Time
Frequencies of an arbitrary signal

## Slide 62
Frequency, Amplitude, and Phase

## Slide 63
Model for a signal (frequency, amplitude, and phase)

## Slide 64
Model for a signal (frequency, amplitude, and phase)

## Slide 65
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Frequency: 2Hz
Frequency, Amplitude, and Phase
Notes: 1) Two common terms related to signals are amplitude and frequency. Frequency is the number of repetition of the signal per second.

## Slide 66
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Frequency: 4Hz
Frequency: 2Hz
Frequency, Amplitude, and Phase

## Slide 67
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Frequency: 2Hz
Frequencies of an arbitrary signal

## Slide 68
Time
Frequencies of an arbitrary signal

## Slide 69
Time
Frequencies of an arbitrary signal

## Slide 70
Frequencies of an arbitrary signal

## Slide 71
Frequencies of an arbitrary signal

## Slide 72
Frequencies of an arbitrary signal

## Slide 73
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
The concept of the Fourier series
The key idea: Any function can be written as the sum of sinusoidal functions.

## Slide 74
Time Domain and Frequency Domain
Approx. square wave

## Slide 75
Analogy: Food coloring chart
Basis for food colors
Notes: Emphasize basis and coefficient using Color analogy

## Slide 76
Analogy: Food coloring chart
Basis for food colors
Notes: Emphasize basis and coefficient using Color analogy

## Slide 77
Analogy: Food coloring chart
Basis for food colors
Notes: Emphasize basis and coefficient using Color analogy

## Slide 78
Analogy: Food coloring chart
Basis for food colors
Notes: Emphasize basis and coefficient using Color analogy

## Slide 79
Time Domain and Frequency Domain
Time domain view
Frequency domain view

## Slide 80
Why do we need
the frequency domain view?

## Slide 81
Why do we need the frequency domain view?
Sound
Sound + Noise
Time
domain
Freq.
domain

## Slide 82
Time
Model for a signal (frequency, amplitude, and phase)

## Slide 83
Time
Model for a signal (frequency, amplitude, and phase)

## Slide 84
Time
Amplitude
One cycle
A
+A
-A
0
Model for a signal (frequency, amplitude, and phase)

## Slide 85
𝚹
A
time = t second
Model for a signal (frequency, amplitude, and phase)

## Slide 86
𝚹
A
time = t second
Phase
Model for a signal (frequency, amplitude, and phase)

## Slide 87
𝚹
A
time = t second
Phase
-- with initial/additional phase ϕ
Model for a signal (frequency, amplitude, and phase)

## Slide 88
𝚹
1
Model for a signal (frequency, amplitude, and phase)

## Slide 89
Projections on sinusoids

## Slide 90
Projections on sinusoids
Notes: Talk about cos() is an even function and sin() is odd. The even component of the function f() is captured by the cos() and odd is by sin().
Odd fn X Odd fn = Even fn.
Even X Odd = Odd
Eve X Eve = Even
Integration of an odd function between –a to a, is zero.

## Slide 91
Complex numbers
Imaginary

## Slide 92
Complex numbers and Natural exponential
j
j

## Slide 93
…
…
…
Complex numbers and Natural exponential
Euler’s formula

## Slide 94
Complex numbers and Natural exponential

## Slide 95
Model for a signal (frequency, amplitude, and phase)

## Slide 96
Model for a signal (frequency, amplitude, and phase)

## Slide 98
Visualizing Transient Frequencies

## Slide 99
Visualizing transient frequencies
U
M
D

## Slide 100
Spectrogram
U
M
D

## Slide 101
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Frequency components change over time
FFT
A set of
frequencies

## Slide 102
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Frequency components change over time
FFT

## Slide 103
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Frequency components change over time
FFT
FFT

## Slide 104
U
M
D
Frequency components change over time

## Slide 105
Spectrogram
U
M
D
[
[
[
[
FFT
FFT
FFT
FFT
FFT of overlapping windows
of samples
(Spectrogram)

## Slide 106
Spectrogram
U
M
D

## Slide 107
Physical signal
(voice)
Time varying voltage
signal
Spectrogram plot
on computer
FFT
A collection of numbers
Analog
Digital

## Slide 108
Sampling

## Slide 109
A physical phenomenon
We want to measure
A structure or material
That reacts to the physical phenomenon
A circuit that converts the reaction to measurable electrical signal (e.g. voltage)
Interpretation of the signal, storing the data
SENSOR
Digital
Analog
Analog

## Slide 110
Physical signal
(voice)
Time varying voltage
signal
Spectrogram plot
on computer
FFT
A collection of numbers
Analog
Digital
?

## Slide 111
Physical signal
(voice)
Time varying voltage
signal
Spectrogram plot
on computer
FFT
A collection of numbers
Analog
Digital
ADC
Analog-to-Digital Converter

## Slide 112
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Sampling

## Slide 113
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
[ 0.34 0.22 0.09 0.21 0.30 0.08 0.09 ]
Sampling
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00

## Slide 114
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Clock
T = Sampling interval
fs= 1/T = Sample rate (or sampling frequency)
Sampling

## Slide 115
1-dimensional sampling

## Slide 116
1-dimensional sampling
(we sample the domain
of the function, not the
value-sapce)
X
Y
Vx
Vy

## Slide 117
1-dimensional sampling
2-dimensional sampling

## Slide 118
1-dimensional sampling
2-dimensional sampling
3-dimensional sampling

## Slide 119
Physical signal
(voice)
Time varying voltage
signal
Spectrogram plot
on computer
FFT
A collection of numbers
Analog
Digital
ADC
Analog-to-Digital Converter

## Slide 120
Digitization process (What is inside an ADC)

## Slide 121
Digitization process (What is inside an ADC)

## Slide 122
Digitization process (What is inside an ADC)
Sample and hold

## Slide 123
Digitization process (What is inside an ADC)
Notes: [PC] https://panoradio-sdr.de/analog-digital-conversion/

## Slide 124
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
[ 0.34 0.22 0.09 0.21 0.30 0.08 0.09 ]
Discrete in time and in amplitude
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00

## Slide 125
Digitization process (What is inside an ADC)
Notes: [PC] https://panoradio-sdr.de/analog-digital-conversion/

## Slide 126
Quantization level and Bit resolution of an ADC
Notes: [PC] https://en.wikipedia.org/wiki/Quantization_%28signal_processing%29

## Slide 127
Digitization process (What is inside an ADC)
Sample and hold
Quantized

## Slide 128
Digitization process (What is inside an ADC)

## Slide 129
Gliding over
the Sampling Theorem

## Slide 130
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Sampling theorem

## Slide 131
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Aliasing: Two signals become indistinguishable
after sampling
Sampling theorem

## Slide 132
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Aliasing

## Slide 133
Aliasing

## Slide 134
Moiré patterns
Location: Ground level, near Gannon Auditorium and across from the large screen.
Photos may be used for websites, professional purposes, your LinkedIn profile, etc. For best results, please avoid fine stripes, checks, bright colors or busy patterns.

## Slide 135
How to find a good sample rate?
Suppose you sample a signal in some way. If you can exactly reconstruct the signal from the samples, then you have done a proper sampling and captured the key signal information
Notes: [Reference slides] http://terrano.ucsd.edu/jorge/teaching/mae143a/lectures/8sampling.pdf

## Slide 136
How to find a good sample rate?
Suppose you sample a signal in some way. If you can exactly reconstruct the signal from the samples, then you have done a proper sampling and captured the key signal information
The sampling frequency fs , is the number of samples per second. This is to be compared with the signal cyclic frequencies
Notes: [Reference slides] http://terrano.ucsd.edu/jorge/teaching/mae143a/lectures/8sampling.pdf

## Slide 137
11.1 samples/cycle
3.2 samples/cycle
1.05
samples/cycle
How to find a good sample rate?

## Slide 138
How to find a good sample rate?
Nyquist-Shannon sampling theorem:
In order to uniquely represent a signal F(t) by a set of samples, the sampling rate must be more than twice the highest frequency component present in F(t).
If sample rate is fs and maximum frequency we want to
record is fmax , then
fs > 2fmax

## Slide 139
Nyquist frequency = Maximum alias-free frequency
for a given sample rate.
Nyquist rate = Lower bound of sample rate for a
signal.
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
(fs / 2)
(2fmax)

## Slide 140
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
[ 0.34 0.22 0.09 0.21 0.30 0.08 0.09 ]
Samples of the physical phenomena
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00

## Slide 141
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
[ 0.34 0.22 0.09 0.21 0.30 0.08 0.09 ]
Samples of the physical phenomena
A point in the N-dimensional space

## Slide 142
Signal as a point in a N-dimensional space

## Slide 143
Projection and Dot product of vectors

## Slide 144
Change of basis

## Slide 145
“Change of basis” to Frequency domain

## Slide 146
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Recall from past…
The key idea: Any function can be written as the sum of sinusoidal functions.

## Slide 147
Time Domain and Frequency Domain
Time domain view
Frequency domain view

## Slide 148
“Change of basis” to Frequency domain

## Slide 149
“Change of basis” to Frequency domain
Fourier Basis

## Slide 150
Finding good basis: Orthogonality

## Slide 151
Finding good basis: Orthogonality
What makes two signals orthogonal?
The formal definition for orthogonal signals is that their inner product
(also called the dot product) is zero: