## Slide 1: Public investment and electric vehicle design: a model-based market analysis framework [1]
Benjamin M. Knisely
Department of Mechanical Engineering, University of Maryland

## Slide 2: Overview
Electric vehicles (EVs) could provide social and environmental benefits through reduction of GHG emissions, but struggles with widespread adoption
Government regulation and investment influences adoption
Ancillary services also influence adoption
  E.g. Vehicle charging stations (CS)

## Slide 3: Overview
A game-theoretic optimization framework analyzing public policy’s effect on the EV market is proposed
Government
Manufacturer
Charge Station Operator

## Slide 4: Background – Public Policy and EV Market
Primary barriers to adoption:
  Price
  Social preference
  “Range Anxiety”
Policy can influence:
  Consumer choices
  Manufacturer decisions
  Charge station design

## Slide 5: Background – EV Engineering Design
Powertrain governs fuel economy and emissions
  Battery, motor, engine size
  Final drive ratio
Battery EV Drivetrain
Plug-in Hybrid EV Drivetrain

## Slide 6: Background – Design for Market Systems
Maximizes expected value of product, as opposed to engineering performance
Demand model used to estimate profit
Consumer Demand = f(Design Attribute A)
Design Attribute A = f(Design Variables X)

## Slide 7: Background – Design for Market Systems
Design for Market Systems Framework

## Slide 8: Background – Design for Market Systems
Design for Market Systems Framework [2]

## Slide 9: Key Assumptions
Subsidy-related policies only
Time independent
Market consists of 2 manufacturers:
  BEV and PHEV producer
  Conventional vehicle producer
Study focuses on 2 markets (Central Beijing and Ann Arbor, MI) suited well for charger installation

## Slide 10: Key Assumptions
Greenhouse gas emissions estimated based on CO2 emission from gas consumption and electricity production
Baseline tax and plate fees for all vehicles equal
Gas prices
  Ann Arbor: $2.51/gal
  Beijing: $4.77/gal

## Slide 11: Stakeholder Decisions
Government
  Public policies
Manufacturer
  Battery design
  Powertrain design
  Vehicle price
CS Operator
  # of stations
  Charging price

## Slide 12: Optimization Models

## Slide 13: Variable Overview
EM: Emissions
D: Demand
P: Price
A: Vehicle Attributes
I: Government Investment
C: Cost
Π: Profit

## Slide 14: Optimization Models

## Slide 15: Decision-Making Framework

## Slide 16: Policy Model
US Policy Model

## Slide 17: Engineering Model
1 BEV and 1 PHEV
Vehicles simulated with AMESim

## Slide 18: Engineering Model

## Slide 19: Charging Service Model

## Slide 20: Charging Service Model
Optimal Locations = min distance to each EV user on map
  Assumes uniform distribution of users

## Slide 21: Charging Service Model
Every charger should serve 12 users/day

## Slide 22: Market Model

## Slide 23: Optimization Model

## Slide 24: Results

## Slide 28: Conclusions
Collaboration is the clear winning strategy
Increasing budget has diminishing returns for EV adoption
High vehicle price combined with low EV acceptance and high sensitivity to price is a adoption bottleneck + inefficient
BEV-investments are most cost-effective
Gas price changes have a significant impact on vehicle demand

## Slide 29: References
[1] Kang, N., Ren, Y., Feinberg, F. M., and Papalambros, P. Y., 2016, “Public Investment and Electric Vehicle Design: A Model-Based Market Analysis Framework with Application to a USA–China Comparison Study,” Design Science, 2.
[2] Michalek, J. J., Papalambros, P. Y., and Skerlos, S. J., 2005, “A Study of Fuel Efficiency and Emission Policy Impact on Optimal Vehicle Design Decisions,” J. Mech. Des, 126(6), pp. 1062–1070.

## Slide 30
Thank You