## Slide 1
Lecture 3.1
Acoustics for IoT
CMSC 818W : Spring 2019
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2118
Feb. 14th 2019

## Slide 2
Waves

## Slide 3
Waves: Transfer of energy, not mass

## Slide 4
Sound
WiFi signal
Physical vibrations
Visible light
Ripples in water
Infrared
…
…

## Slide 5
Mechanical Wave
Electromagnetic Wave
Sound
WiFi signal
Physical vibrations
Visible light
Ripples in water
Infrared
…
…

## Slide 6
Mechanical waves
Transverse wave

## Slide 7
Mechanical waves
Transverse wave

## Slide 8
Mechanical waves
Transverse wave
Longitudinal wave

## Slide 9
Mechanical waves
Transverse wave
Longitudinal wave

## Slide 10
Mechanical waves

## Slide 11
Mechanical waves

## Slide 12
Mechanical waves

## Slide 13
Amplitude
0.25
0.50
0.75
1.00
Distance (meters)
0.00
Mechanical waves: Time and space

## Slide 14
Amplitude
0.25
0.50
0.75
1.00
Distance (meters)
0.00
Phase of the signal changes over distance/space
Mechanical waves: Time and space

## Slide 15
Amplitude
0.25
0.50
0.75
1.00
Distance (meters)
0.00
Wavelength = λ meters
Mechanical waves: Time and space

## Slide 16
Mechanical waves: Time and space

## Slide 17
Wavelength = λ meters
Mechanical waves: Time and space

## Slide 18
Sound wave observed over time at a point in space
Mechanical waves: Time and space

## Slide 19
Sound wave observed over time at a point in space
Amplitude
0.50
1.00
1.50
2.00
Time (sec)
0.00
Mechanical waves: Time and space
Cycles per sec = frequency = f Hz

## Slide 20
Time and space
Cycles per sec = frequency = f Hz

## Slide 21
Time and space
Cycles per sec = frequency = f Hz
Distance per cycle = wavelength = λ meters

## Slide 22
Time and space
Cycles per sec = frequency = f Hz
Distance per second = speed = C meters/sec
Distance per cycle = wavelength = λ meters

## Slide 23
Time and space
Cycles per sec = frequency = f Hz
Distance per second = speed = C meters/sec
Distance per cycle = wavelength = λ meters
C = f . λ

## Slide 24
Time and space
Cycles per sec = frequency = f Hz
Distance per second = speed = C meters/sec
Distance per cycle = wavelength = λ meters
C = f . λ
Speed of sound in air: 343 m/s
Speed of sound in water: 1493 m/s
Speed of sound in iron: 5130 m/s
Speed of electromagnetic waves: 3*108 m/s
(~ a million times faster than sound)

## Slide 25
Time and space

## Slide 26
Time and space

## Slide 27
Time and space
Distance = d meter

## Slide 28
Time and space
Distance = d meter
Sound is delayed by = d/C sec

## Slide 29
Distance = d meter
Time and space
Sound is delayed by = d/C sec
= (d/C).f cycles

## Slide 30
Distance = d meter
Time and space
Sound is delayed by = d/C sec
= (d/C).f cycles

## Slide 31
Distance = d meter
Time and space
Sound is delayed by = d/C sec
= (d/C).f cycles

## Slide 32
Sound is delayed by = d/C sec
= (d/C).f cycles
Distance = d meter
Time and space

## Slide 33
𝚹
A
time = t second
Frequency, Amplitude, and Phase

## Slide 34
Sound is delayed by = d/C sec
= (d/C).f cycles
Distance = d meter
Time and space

## Slide 35
Distance = d meter
Sound is delayed by = d/C sec
= (d/C).f cycles
d meter
Time and space

## Slide 36
Distance = d meter
Sound is delayed by = d/C sec
= (d/C).f cycles
d meter
Time and space

## Slide 37
Distance = d meter
Sound is delayed by = d/C sec
= (d/C).f cycles
d meter
Equation of the sine wave in time and space:
F(x,t) =
Time and space

## Slide 38
Time and space

## Slide 39
X meter
Time and space

## Slide 40
X meter
Time and space

## Slide 41
X meter
X.sin()
Time and space

## Slide 42
d = X.sin()
X meter
Time and space

## Slide 43
d = X.sin()
X meter
Time and space

## Slide 44
Reflection of sound

## Slide 45
Reflection

## Slide 46
Reflection

## Slide 47
d1
d2
Reflection

## Slide 48
Time = t1
Reflection

## Slide 49
Time = t1
Absorption
+
Reflection
Reflection

## Slide 50
t2
Time = t1
echo
Absorption
+
Reflection
Reflection

## Slide 51
Sound travelled (2d) distance
d
t2
Time = t1
echo
Absorption
+
Reflection
Reflection

## Slide 52
Sound travelled (2d) distance
d
t2
Time = t1
C(t2-t1) = 2d
echo
Absorption
+
Reflection
Reflection

## Slide 53
Sound travelled (2d) distance
d
t2
Time = t1
C(t2-t1) = 2d
echo
Echolocation
Absorption
+
Reflection
Reflection

## Slide 54
Echolocation in nature
Bat

## Slide 55
Echolocation in nature
Beluga whale

## Slide 56
Acoustic imaging

## Slide 57
Acoustic imaging
Sonogram

## Slide 58
Acoustic imaging
Sonogram

## Slide 59
Multipath

## Slide 60
Multipath

## Slide 61
Multipath: Convolution
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00

## Slide 62
Multipath: Convolution
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Direct path

## Slide 63
Multipath: Convolution
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Direct path
Echo

## Slide 64
Multipath: Convolution
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Direct path
Echo

## Slide 65
Multipath: Convolution
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Direct path
Echo

## Slide 66
Multipath: Convolution
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00
Amplitude
0.25
0.50
0.75
1.00
1.25
Time (sec)
0.00

## Slide 67
Amplitude
0.25
0.50
Time (sec)
0.00
Impulse
Impulse response

## Slide 68
Room’s acoustic environment (reflections, absorption etc.)
Amplitude
0.25
0.50
Time (sec)
0.00
Impulse
Impulse response

## Slide 69
Amplitude
0.25
0.50
Time (sec)
0.00
Impulse
Room’s acoustic environment (reflections, absorption etc.)
Impulse Response
Impulse response

## Slide 70
Impulse response

## Slide 71
SYSTEM
Impulse Response
Impulse
Impulse response

## Slide 72
SYSTEM
Impulse Response
Input
Input
X
Impulse response

## Slide 73
SYSTEM
Impulse Response
Input
Input
X
Impulse response
Convolution

## Slide 74
Sound production and recording

## Slide 75
Sound
Sound recording with microphone

## Slide 76
Sound
Analog signal (voltage)
ADC
Sound recording with microphone
ADC = Analog-to-Digital Converter

## Slide 77
Sound
Analog signal (voltage)
ADC
Audio Sample Buffer
S6 S5 S4 S3 S2 S1 S0
Sound recording with microphone
ADC = Analog-to-Digital Converter

## Slide 78
Audio Sample Buffer
S6 S5 S4 S3 S2 S1 S0
Sound production with speaker

## Slide 79
Audio Sample Buffer
S6 S5 S4 S3 S2 S1 S0
DAC
Analog signal (voltage)
Sound production with speaker
DAC = Digital-to-Analog Converter

## Slide 80
Audio Sample Buffer
S6 S5 S4 S3 S2 S1 S0
DAC
Analog signal (voltage)
Sound
Sound production with speaker
DAC = Digital-to-Analog Converter

## Slide 81
Human hearing

## Slide 82
10
100
1000
10,000
100,000
Frequency (log scale)
0
20Hz – 20kHz (Human hearing range)
Human hearing

## Slide 83
10
100
1000
10,000
100,000
Frequency (log scale)
0
20Hz – 20kHz (Human hearing range)
Infra-sound
Ultrasound
Audible sound
Human hearing

## Slide 84
10
100
1000
10,000
100,000
Frequency (log scale)
0
20Hz – 20kHz (Human hearing range)
Infra-sound
Ultrasound
Audible sound
Dog /Cat
(45/65kHz)
Bat/Dolphin
(120/150kHz)
Human hearing

## Slide 85
60k
40k
Amplitude
20k
Frequency
Audible
Inaudible Ultrasound
Near-ultrasound

## Slide 86
60k
40k
Amplitude
20k
Frequency
Near-ultrasound
Audible
Inaudible Ultrasound
Near-ultrasound

## Slide 87
Acoustic ranging: Case study
BeepBeep – SenSys 2007

## Slide 88
Device A
Device B
Distance = d

## Slide 89
Device A
Device B
Distance = d
Time = t1

## Slide 90
Device A
Device B
Distance = d
Time = t1
Time = t2

## Slide 91
Device A
Device B
Distance = d
Time = t1
Time = t2
Time = t1
Bluetooth/WiFi

## Slide 92
Device A
Device B
Distance = d
Time = t1
Time = t2
Time = t1
Bluetooth/WiFi
d = C . (t2-t1)

## Slide 93
Device A
Device B
Distance = d
Time = t1
Time = t2
Time = t1
Bluetooth/WiFi
d = C . (t2-t1)
Problem: Clock synchronization

## Slide 94: The root cause of inaccuracy – three uncertainties
Clock synchronization uncertainty
time

## Slide 95: The root cause of inaccuracy – three uncertainties
Clock synchronization uncertainty
Sending uncertainty
time

## Slide 96: The root cause of inaccuracy – three uncertainties
Clock synchronization uncertainty
Sending uncertainty
time
...
t0 = wall_clock();
write(sound_dev, signal);
...
software issuing command

## Slide 97: The root cause of inaccuracy – three uncertainties
Clock synchronization uncertainty
Sending uncertainty
time
...
t0 = wall_clock();
write(sound_dev, signal);
...
software issuing command
sound leaves
speaker
unknown delays (software, system, driver, hardware, …) ?

## Slide 98: The root cause of inaccuracy – three uncertainties
Clock synchronization uncertainty
Sending uncertainty
time
...
t0 = wall_clock();
write(sound_dev, signal);
...
software issuing command
sound leaves
speaker
unknown delays (software, system, driver, hardware, …) ?
Receiving uncertainty

## Slide 99: The root cause of inaccuracy – three uncertainties
Clock synchronization uncertainty
Sending uncertainty
time
...
t0 = wall_clock();
write(sound_dev, signal);
...
software issuing command
sound leaves
speaker
unknown delays (software, system, driver, hardware, …) ?
sound
reaches mic
Receiving uncertainty

## Slide 100: The root cause of inaccuracy – three uncertainties
Clock synchronization uncertainty
Sending uncertainty
time
...
t0 = wall_clock();
write(sound_dev, signal);
...
software issuing command
sound leaves
speaker
unknown delays (software, system, driver, hardware, …) ?
sound
reaches mic
unknown delays (hardware, interrupt, driver, scheduling, …) ?
Receiving uncertainty

## Slide 101: The root cause of inaccuracy – three uncertainties
Clock synchronization uncertainty
Sending uncertainty
time
...
t0 = wall_clock();
write(sound_dev, signal);
...
software issuing command
sound leaves
speaker
unknown delays (software, system, driver, hardware, …) ?
...
read(sound_dev, signal);
t1 = wall_clock();
...
software aware of arrival
sound
reaches mic
unknown delays (hardware, interrupt, driver, scheduling, …) ?
Receiving uncertainty

## Slide 102: Beepbeep’s basic procedure
Device A
Device B
DAB=|ETOAA-ETOAB|/2
A’s recording
B’s recording
ETOAA
ETOAB
Device A emits a beep while both recording
Device B emits another beep while both continue recording
Both devices detect TOA of the two beeps and obtain respective ETOAs
Exchange ETOAs and calculate the distance

## Slide 103: Timeline
Device A
Device B

## Slide 104: Timeline
Device A
Device B
1st Beep
tA0

## Slide 105: Timeline
Device A
Device B
1st Beep
tA0
tB1
tA1

## Slide 106: Timeline
Device A
Device B
1st Beep
tA0
tB1
tA1
2nd Beep
tB2

## Slide 107: Timeline
Device A
Device B
1st Beep
tA0
tB1
tA1
2nd Beep
tB2
tA3
tB3

## Slide 108: Timeline
Device A
Device B
1st Beep
tA0
tB1
tA1
2nd Beep
tB2
tA3
tB3
ETOAA

## Slide 109: Timeline
Device A
Device B
1st Beep
tA0
tB1
tA1
2nd Beep
tB2
tA3
tB3
ETOAA
ETOAB

## Slide 110: Timeline
tA3
2nd Beep
tB3
tB2
1st Beep
tB1
tA0
tA1
ETOAA
ETOAB
P
Device A
Device B

## Slide 111: Timeline
tA3
2nd Beep
tB3
tB2
1st Beep
tB1
tA0
tA1
ETOAA
ETOAB
P
P
Device A
Device B

## Slide 112: Timeline
tA3
2nd Beep
tB3
tB2
1st Beep
tB1
tA0
tA1
ETOAA
ETOAB
P
P
Q
Device A
Device B

## Slide 113: Timeline
tA3
2nd Beep
tB3
tB2
1st Beep
tB1
tA0
tA1
ETOAA
ETOAB
P
P
Q
|ETOAA-ETOAB|
= (P+Q+P) – (Q)
Device A
Device B

## Slide 114: Timeline
tA3
2nd Beep
tB3
tB2
1st Beep
tB1
tA0
tA1
ETOAA
ETOAB
P
P
Q
|ETOAA-ETOAB|
= (P+Q+P) – (Q)
= 2P
= 2 (time of flight)
Device A
Device B

## Slide 115
Project ideas: Inertial motion sensing
1. Car location in multistory parking lot.
2. Driver-passenger detection using smartphone
4. WiFi AP hand-off based on the motion pattern
3. Driver’s / Biker’s driving pattern detection, dangerous
driving/biking alert
5. 3D image by combining video and motion info.