## Slide 1
GPS, Differential GPS, and Applications
to Drones

## Slide 2
Tremendous excitement with drones

## Slide 3
Despite the excitement …

## Slide 4
Drones still not ready for public places

## Slide 5
Several instances of crashes and failure …
Notes: Drone accidents are very common .. Severely threateninig life and property

## Slide 6
Why do drones crash?

## Slide 7
Drone Stabilization
Inertial Measurement Unit (IMU) crucial for tracking 3D orientation  stabilization, control
Accelerometer
Gyroscope
Magnetometer
IMU

## Slide 8
IMU can fail
However, rotor vibration and magnetic interference derails
the sensors … causing correlated failures
Inertial Measurement Unit (IMU) crucial for tracking 3D orientation  stabilization, control
Accelerometer
Gyroscope
Magnetometer
IMU

## Slide 9
45% of drone crashes due to IMU failures [DJI Drone Survey 2015]
We ask: can we design a Plan-B for IMU failure?
Drones already use GPS for localization …
recent drones using multiple GPS for reliability
Can we leverage multiple GPS receivers to compute
3D orientation (i.e., a backup for IMU sensor failure)

## Slide 10: Use multiple GPS to compute 3D orientation

## Slide 11: Use multiple GPS to compute 3D orientation

## Slide 12: Use multiple GPS to compute 3D orientation

## Slide 13: Use multiple GPS to compute 3D orientation

## Slide 14: Use multiple GPS to compute 3D orientation

## Slide 15: Use multiple GPS to compute 3D orientation
Translate Relative Positions into 3D Orientation
To match IMU accuracy (~2 deg.)
Relative vector estimates have to be ~2cm

## Slide 16
To match IMU, we require <2cm error for each 3D vector
Basic GPS  3m absolute position error
Opportunity:
We do not care about absolute location …
we only need relative
Differential GPS  relative 15cm error
We bring additional spatio-temporal information fusion techniques …
for these small sized drones
3D vector
Parkinson et al, GPS 96, Cohen et al, Journal of Satellite Communication 96
Hedgecock et al, Mobisys 13, Sensys 14

## Slide 17
Basic satellite trilateration: 300km error
GPS Localization (phones): 1-3m error
Differential GPS (airplanes): 15cm error
For drone orientation (< ): ~2cm error
Some background on GPS

## Slide 18
A brief review of GPS literature
(300 km to 15 cm)

## Slide 19
GPS Signal
.
Basic GPS Localization

## Slide 20
GPS Signal
.
Basic GPS Localization
However, 3D location needs 3 equations … hence, use 3 satellites

## Slide 21
GPS Signal
.
Basic GPS Localization
However, 3D location needs 3 equations … hence, use 3 satellites

## Slide 22
GPS Signal
.
Basic GPS Localization
=
.
Satellite
Geometry
Matrix
However, 3D location needs 3 equations … hence, use 3 satellites
300 Km of error
due to unsynchronized clocks

## Slide 23
GPS Signal
.
Basic GPS Localization
=
Satellite Geometry Matrix
1-3m error
New unknown … use 4th satellite and estimate both location and

## Slide 24
1-3m error acceptable to smartphones, car GPS
Differential GPS
using phase of the signals
Drone orientation warrants cm level accuracy

## Slide 25
Differential GPS (using carrier phase)

## Slide 26
GPS Carrier Phase
GPS Carrier Wave
Phase
True Range
Possible to measure precisely
(2-5 mm error)
However, difficult to
estimate N
GPS Receiver
GPS Satellite

## Slide 27
GPS Carrier Phase
GPS Carrier Wave
Phase
True Range
Real systems more difficult:
However, since we only care about relative distances …
Possible to eliminate some errors by subtracting phase equations
across receivers, satellites, time, etc.
For example …
GPS Receiver
GPS Satellite

## Slide 28
(I) Single Differential Across Receivers – Cancelling Satellite Errors
Range =
Range =
1
Relative Position (Baseline)
S
2
Clock Errors can be eliminated further

## Slide 29
(II) Satellite Double Differential: Cancel Receiver Errors
S
K
R12 = Relative vector (BaseLine) between two GPSs
However, integer ambiguity remains
1
2
Can be translated into Orientation

## Slide 30
Differential GPS community has exploited such techniques to achieve orientation estimation on big planes, ships
For a small drone we need very high accuracy
Need to handle dynamic errors

## Slide 31
(III) Time Double Differentials
No Integer Ambiguity
Change in orientation
S

## Slide 32
Change in Orientation, but unpolluted by Integer Ambiguity
Two Observations on Orientation
Satellite Double Differentials
Time Double Differential
Drone Absolute Orientation, but polluted by Integer Ambiguity
Naturally amenable to a process filtering model

## Slide 33
Bayesian Filtering Approach
q
q
q
Transition
Measurement
pitch, roll, yaw
pitch, roll, yaw
pitch, roll, yaw
Notes: We can model orientation as states that evolve in time and by using the two different perspectives, we can derive suitable transition and emission models as follows ..

## Slide 34
Measurement Model
q
q
q
Trans.
Meas.
Satellite Double
Differentials

## Slide 35
Measurement Model
q
q
q
Trans.
Meas.
Integer Ambiguity ?
Satellite Double
Differentials

## Slide 36
Transition Model
q
q
q
Trans.
Meas.
36
Time Double
Differentials

## Slide 37
Bayesian Filtering Approach
q
q
q
Trans.
Meas.
37
Time Double
Differentials

## Slide 38
Bayesian Filtering Approach
q
q
q
Trans.
Meas.
38
Integer Ambiguity ?
Time Double
Differentials
Satellite Double
Differentials

## Slide 39
Integer Ambiguity Resolution depends on Flight Aggressiveness
Two regimes of aggressiveness
Low Dynamic Flights
Highly Aggressive flights
Kalman Filter
Particle Filter

## Slide 40
Pitch, Roll, Yaw
[]
Pitch, Roll, Yaw
[]
Pitch, Roll, Yaw
[]
Orientation Estimation - Low Dynamic flights
Static Drone
Trans.
Meas.
Kalman Filter
known

## Slide 41
Pitch, Roll, Yaw
[]
Pitch, Roll, Yaw
[]
Pitch, Roll, Yaw
[]
Highly Aggressive Flights: Cycle Slips
Trans.
Kalman Filter
Cycle Slips
Kalman filter derailed
Meas.
known
Static Drone

## Slide 42
Divergence due to cycle slips
Cycle Slips trigger divergence
Several Cycle Slips during flight

## Slide 43
Handling Aggressive Flights and Cycle Slips

## Slide 44
Kalman Filters are optimal under Gaussian error
  When estimates of N incorrect, error no longer Gaussian
We need 2 solutions:
Identify when estimates of N are poor
Correct estimates in real time to prevent divergence
Main Question

## Slide 45
Correct Orientation 
Measurement Model
1. Identifying Poor Estimates of N

## Slide 46
2. Correcting N via Particle Filters
~
~
1
High Conf.
<
1
Low
Conf.
v
v
.
.
.
v
Keep doing
Kalman
v
v
v
v
Trigger Particle Filter
v
v
v
~
~
1
v
v
~
~
1
~
~
1
Back to
Kalman

## Slide 47
Simple Particle Converges slowly

## Slide 48
Measurement (q)
Initial
Particles
Simple Particle Filter
Weigh and Propagate

## Slide 49
Combine Trans. And Meas. like Kalman Filter
Initial
Particles
Adjusted Particle Filter
Provides near optimal combining for correct particles
Accelerates convergence with few particles
Propagate the Adjusted State
Measurement (q)

## Slide 50
Adjusted Particle Tracks Well

## Slide 51
Adjusted Particle Tracks Well

## Slide 52
GPS
GoPro
IMU
Pi
Evaluation Platform

## Slide 53
Performance
Vision Ground Truth
GPS vs IMU

## Slide 54: SafetyNet can track aggressive turns
Sharp Angles
(Truth)
Tilt Orientation (degree)

## Slide 55
Sharp Angles
SafetyNet can track aggressive turns

## Slide 56: Comparison with IMU
Only 30% worse than IMU

## Slide 57: Comparison with IMU
4x better than IMU

## Slide 58
Conclusion
Despite Excitement, poor relability is the show stopper for disruptive drone applications
We propose an orthogonal approach for drone state estimation using carrier phase GPS
We developed a Particle filter do systematically combine carrier phase data for orientation
Real Extensive flight tests achieve an accuracy comparable to IMU

## Slide 59
Not Completely Solved Yet …
Fusion of Carrier Phases with IMU can achieve better accuracy
Multipath decoupling can enable flying between buildings at low altitude
Orientation Estimation of Self Driving Cars can add to reliability
Cannot tolerate Jamming Attacks

## Slide 60
Thoughts?