## Slide 1: Location Determination
Framework and Technologies

## Slide 2: Meaning of Location
Three Dimensional Space
Reference Coordinate System
  Global – GPS
  Local
  Application Specific
Multiple References
  Ability to Map
Notation

## Slide 3: Location Uses
All levels of accuracies have applications
Outdoors
  Navigation
    Automobiles/ Road Vehicles
    Aircrafts
    Boats/Ships
    Personal – walking/jogging/running
  Targetting
  Finding Hospitals/Gas Stations….
Indoors
  Advertising
  Finding …
System based vs. device based

## Slide 4: How
Benchmarks
  Known locations (Accuracy?)
  Unknown Location WRT the location of Benchmarks
What Form ??
  Physical, marked locations
  Location of devices
What do I measure??
  Proximity
  Distance
  Some function of distance
  Direction
  Some function of direction
How many measurements
  3
  4
Use Geometry
  Triangulation
  Trilateration

## Slide 5: Desirable Features
In Doors and Out Doors operation
Independent of GPS
Rapidly Deployable
Agnostic to Frequency Band or Protocol
Accurate
Scalable
…

## Slide 6: Proximity
Detect the presence close to a known location
RFID
  Passive
    Read by putting in a field of RF and reading the scatter pattern
    Inventory Control
    EZPass
  Active
    iBeacon
      Using low power Bluetooth
    Estimotes
    ….
How does Passive RFID approach compare with barcodes?
FingerPrinting Based approach in WiFi Field

## Slide 7: RF Field Based - WiFi
AP – Generate Beacons 100 ms
Can measure signal Strength
  RSSI – Received Signal Strength Indicator
  Included in spec to support handovers.
RSSI – Relative scale or dbm
  Most devices now report dbm
  Range (-50 to -90 dbm)
  Integer values only

## Slide 8: Problem Formulation
K Access Points
Signal Field
Where S is k dimensional vector and X is the location vector.
Problem – The signal strength of K APs is measured by a device as signal vector S. Determine the location X where the device is
Issues:
  Is S an invertible function?
  Does S have a closed form?
  Is S deterministic or do the measurements vary with time

## Slide 9: Signal Function
Closed Form
  Maxwell Equations
  Affected by
    Decay
    Reflections
    Refraction
    Diffusion
    Scattering
  Some Approximations have been attempted
  Outdoor – Cellular Phone
    Accuracies ~200 meters
  Indoor – WiFi
    Accuracies 5-10 meters
What should be K, the number of signal generators – APs.
Most WiFi deployment is for supporting networking access and not for location.
At a location one can only hear a small number of APs.
  There are ~4500 APs on campus. How do we efficiently handle this 4500 dimensional function?

## Slide 10: Stochastic nature of Signals
Repeated measurements vary when nothing has changed
There is some correlation among samples
Signal Vector has to be treated as a stochastic vector
As it is reasonable to assume that all APs operate independently the signals from them can be treated as independent random variables.
Analytical models require the modeling of the randomness

## Slide 11: FingerPrinting
We can estimate the joint probability distribution of the signal vector
  by empirical measurements
  Discretize X and make measurements of S at known locations – a grid in X space
  Treat the measurement points as benchmark points
  Find the benchmark point closest to the device signal vector in signal space
May refine the location by determining a few closest benchmark points and interpolating

## Slide 12: Horus: A WLAN-Based Indoor Location Determination System
Moustafa Youssef
H
O
R
U
S
H
O
R
U
S

## Slide 13: WLAN Location Determination (Cont’d)
Signal strength= f(distance)
Does not follow free space loss
Use lookup table  Radio map
Radio Map: signal strength characteristics at selected locations

## Slide 14: WLAN Location Determination (Cont’d)
Offline phase
  Build radio map
  Radar system: average signal strength
Online phase
  Get user location
  Nearest location in signal strength space (Euclidian distance)
(xi, yi)
(x, y)
[-53, -56]
[-50, -60]
[-58, -68]
5
13

## Slide 15: Horus Goals
High accuracy
  Wider range of applications
Energy efficiency
  Energy constrained devices
Scalability
  Number of supported users
  Coverage area

## Slide 16: Sampling Process
Active scanning
  Send a probe request
  Receive a probe response

## Slide 17: Signal Strength Characteristics
Temporal variations
  One access point
  Multiple access points
Spatial variations
  Large scale
  Small scale

## Slide 18: Temporal Variations

## Slide 19: Temporal Variations

## Slide 20: Temporal Variations: Correlation

## Slide 21: Spatial Variations: Large-Scale

## Slide 22: Spatial Variations: Small-Scale

## Slide 23: Testbeds
A.V. William’s
  4th floor, AVW
  224 feet by 85.1 feet
  UMD net (Cisco APs)
  21 APs (6 on avg.)
  172 locations
  5 feet apart
  Windows XP Prof.
FLA
  3rd floor, 8400 Baltimore Ave
  39 feet by 118 feet
  LinkSys/Cisco APs
  6 APs (4 on avg.)
  110 locations
  7 feet apart
  Linux (kernel 2.5.7)
Orinoco/Compaq cards

## Slide 24: Horus Components
Basic algorithm [Percom03]
Correlation handler [InfoCom04]
Continuous space estimator [Under]
Locations clustering [Percom03]
Small-scale compensator [WCNC03]

## Slide 25: Basic Algorithm: Mathematical Formulation
x: Position vector
s: Signal strength vector
  One entry for each access point
s(x) is a stochastic process
P[s(x), t]: probability of receiving s at x at time t
s(x) is a stationary process
  P[s(x)] is the histogram of signal strength at x

## Slide 26: Basic Algorithm: Mathematical Formulation

## Slide 27: Basic Algorithm: Mathematical Formulation
Argmaxx[P(x/s)]
Using Bayesian inversion
  Argmaxx[P(s/x).P(x)/P(s)]
  Argmaxx[P(s/x).P(x)]
P(x): User history

## Slide 28: Basic Algorithm
Offline phase
  Radio map: signal strength histograms
Online phase
  Bayesian based inference

## Slide 29: WLAN Location Determination (Cont’d)
(xi, yi)
(x, y)
-40 -60 -80
-40 -60 -80
[-53]
P(-53/L1)=0.55
P(-53/L2)=0.08

## Slide 30
Basic Algorithm: Signal Strength Distributions

## Slide 31
Basic Algorithm: Results
Accuracy of 5 feet 90% of the time
Slight advantage of parametric over non-parametric method
  Smoothing of distribution shape

## Slide 32: Correlation Handler
Need to average multiple samples to increase accuracy
Independence assumption is wrong

## Slide 33: Correlation Handler: Autoregressive Model
s(t+1)=.s(t)+(1- ).v(t)
: correlation degree
E[v(t)]=E[s(t)]
Var[v(t)]= (1+ )/(1- ) Var[s(t)]

## Slide 34: Correlation Handler: Averaging Process
s(t+1)= .s(t)+(1- ).v(t)
s ~ N(0, m)
v ~ N(0, r)
A=1/n (s1+s2+...+sn)
E[A(t)]=E[s(t)]=0
Var[A(t)]= m2/n2 { [(1-  n)/(1- )]2 + n+ 1-  2 *(1-  2(n-1))/(1-  2) }

## Slide 35: Correlation Handler: Averaging

## Slide 36
Correlation Handler: Results
Independence assumption: performance degrades as n increases
Two factors affecting accuracy
  Increasing n
  Deviation from the actual distribution

## Slide 37: Continuous Space Estimator
Enhance the discrete radio map space estimator
Two techniques
  Center of mass of the top ranked locations
  Time averaging window

## Slide 38
Center of Mass: Results
N = 1 is the discrete-space estimator
Accuracy enhanced by more than 13%

## Slide 39
Time Averaging Window: Results
N = 1 is the discrete-space estimator
Accuracy enhanced by more than 24%

## Slide 40: Horus Components
Basic algorithm
Correlation handler
Continuous space estimator
Small-scale compensator
Locations clustering

## Slide 41: Small-scale Compensator
Multi-path effect
Hard to capture by radio map (size/time)

## Slide 42: Small-scale Compensator: Small-scale Variations
AP1
AP2
Variations up to 10 dBm in 3 inches
Variations proportional to average signal strength

## Slide 43: Small-scale Compensator: Perturbation Technique
Detect small-scale variations
  Using previous user location
Perturb signal strength vector
  (s1, s2, …, sn)  (s1d1, s2d2, …, sndn)
  Typically, n=3-4
di is chosen relative to the received signal strength

## Slide 44
Small-scale Compensator: Results
Perturbation technique is not sensitive to the number of APs perturbed
Better by more than 25%

## Slide 45: Horus Components
Basic algorithm
Correlation handler
Continuous space estimator
Small-scale compensator
Locations clustering

## Slide 46: Locations Clustering
Reduce computational requirements
Two techniques
  Explicit
  Implicit

## Slide 47: Locations Clustering: Explicit Clustering
Use access points that cover each location
Use the q strongest access points
S=[-60, -45, -80, -86, -70]
S=[-45, -60, -70, -80, -86]
q=3

## Slide 48
Locations Clustering: Results- Explicit Clustering
An order of magnitude enhancement in avg. num. of oper. /location estimate
As q increases, accuracy slightly increases

## Slide 49: Locations Clustering: Implicit Clustering
Use the access points incrementally
Implicit multi-level clustering
S=[-60, -45, -80, -86, -70]
S=(-45, -60, -70, -80, -86)
S=[-45, -60, -70, -80, -86]

## Slide 50
Locations Clustering: Results- Implicit Clustering
Avg. num. of oper. /location estimate better than explicit clustering
Accuracy increases with Threshold

## Slide 51
Horus Components

## Slide 52
Horus-Radar Comparison

## Slide 53
Training Time
15 seconds training time per location

## Slide 54
Radio map Spacing
Average distance error increase by as much as 100% (20 feet)
14 feet gives good accuracy

## Slide 55
Radar with Horus Techniques
Average distance error enhanced by more than 58%
Worst case error decreased by more than 76%

## Slide 56: Conclusions
The Horus system achieves its goals
High accuracy
  Through a probabilistic location determination technique
  Smoothing signal strength distributions by Gaussian approximation
  Using a continuous-space estimator
  Handling the high correlation between samples from the same access point
  The perturbation technique to handle small-scale variations
Low computational requirements
  Through the use of clustering techniques

## Slide 57: Conclusions (Cont’d)
Scalability in terms of the coverage area
  Through the use of clustering techniques
Scalability in terms of the number of users
  Through the distributed implementation
Training time of 15 seconds per location is enough to construct the radio-map
Radio map spacing of 14 feet
Horus vs. Radar
  More accurate by more than 11 feet, on the average
  More than an order of magnitude savings in number of operations required per location estimate
Horus vs. Ekahau

## Slide 58: Conclusions (Cont’d)
Modules can be applied to other WLAN location determination systems
  Correlation handling, continuous-space estimator, clustering, and small-scale compensator
Applied to Radar
  Average distance error enhanced by more than 58%
  Worst case error decreased by more than 76%
Techniques presented thesis are applicable to other RF-technologies
  802.11a, 802.11g, HiperLAN, and BlueTooth, …

## Slide 59: Locus
Indoor location anywhere on College Park Campus
Based on Wi-Fi RSSI
~ 4500 Access Points
Floor accuracy >95%
Location Accurate to the room
Being integrated with M-Urgency

## Slide 60: Flying Turtle
Locating indoors

## Slide 61: Flying Squirrel – NRL Project
Goal
  Real-time discovery, analysis, and mapping of IEEE 802.11a/b/g/n wireless networks
  Use passive listeners
  Extensive analytics

## Slide 62: Flying Turtle
20 sensors on 4100 wing of AVW - compose approx. 20 ft, 20 ft grid points.

## Slide 63: Initial Observations

## Slide 64: Our Approach
Dynamic Fingerprinting/Radio Map
With passive listeners
  Can we provide accurate localization from measured signal strengths ?

## Slide 65: Time Based Location
Ashok K. Agrawala
Director, MIND Lab
Professor, Computer Science
University of Maryland

## Slide 66: Topics
Location Determination
    Horus and Locus
    PinPoint
Clock Synchronization
    With Absolute Real Time

## Slide 67: GeoLocation
RSSI Based – Horus and Locus
Accurate Time Stamping
GeoLocation with accuracy in inches
Clock Synchronization
  Mapping Function Timing Protocol
  Synchronization with Absolute Time
Flying Turtle - testbed

## Slide 68: PinPoint Technology - Basis
Use a clock model
Determine node to node distance by measuring time of flight of the signal

## Slide 69: Clock Model
The clock at a node is assumed to have drift stable over short periods.
Hence clock time t is related to the real time t by
where
  a and b remain constant for the measurement phase.
  b, the drift rate of the clock is no worse than 100 parts per million
  t is measured with a nanosecond resolution

## Slide 70: Measurements for node pair A and B
Let
  a1, b1: tx and rx ts of first A msg
  b2, a2: tx and rx ts of first B msg
  a3, b3: tx and rx ts of second A msg
  a4, b4: tx and rx ts of second B msg

## Slide 71: Calculations for node pair A and B
Drift ratio
Propagation delay
Remote clock reading

## Slide 72: Accurate Time-stamping
Accuracy of distance measurement is directly related to the accuracy of timestamping
Collaboration with Austrian Academy of Sciences
  SMiLE 3 board

## Slide 73: Block Diagram of SMiLE

## Slide 74: SMiLE Details
Altera FPGA Cyclone III
Max 2830 WiFi chip
Sampling Rate = 44 MHz (22.75 ns Tick)
Discretization 256 levels (22.75/256 = 88.77 ps)

## Slide 75: Measurement Results
Time Stamping
  Tick time 88.77 ps (~2.66 cm)
  Standard Deviation of Error – 0.97 ticks
  Stable
Clocks
  Have variable drifts ~ (0.119 to 0.364 ppm)

## Slide 76: Clock Drift (Skew)

## Slide 77: Distance Measurements
Configuration

## Slide 78: Distance Measurements
Configuration
  Outdoors
Experiment
  Nodes take turn is sending messages
  10ms interval

## Slide 79: Distance Statistics
stats | path | in ticks | in feet |  | 
mean | 12 | 1200.3790 | 104.8188 |  | 
 | 13 | 1169.8708 | 102.1548 |  | 
 | 14 | 1170.1178 | 102.1764 |  | 
 | 15 | 1182.3626 | 103.2456 |  | 
 | 23 | 1681.8644 | 146.8628 |  | 
 | 34 | 1603.9611 | 140.0602 |  | 
 | 45 | 1656.1120 | 144.6141 |  | 
 | 52 | 1639.8012 | 143.1898 |  | 
 | 24 | 2352.6710 | 205.4386 |  | 
 | 35 | 2313.8754 | 202.0509 |  | 
 | path | in ticks | in feet | in cms | in inches
std | 12 | 2.5491 | 0.2226 | 6.7845 | 2.6711
 | 13 | 2.4626 | 0.2150 | 6.5544 | 2.5805
 | 14 | 3.4353 | 0.3000 | 9.1433 | 3.5997
 | 15 | 4.0475 | 0.3534 | 10.7725 | 4.2412
 | 23 | 8.9180 | 0.7787 | 23.7358 | 9.3448
 | 34 | 15.0450 | 1.3138 | 40.0432 | 15.7651
 | 45 | 11.0574 | 0.9655 | 29.4299 | 11.5866
 | 52 | 12.2881 | 1.0730 | 32.7055 | 12.8762
 | 24 | 3.9620 | 0.3460 | 10.5451 | 4.1516
 | 35 | 25.5180 | 2.2283 | 67.9175 | 26.7392

## Slide 80: Distance
Chart: Distance in clock Ticks Nodes 3-4
Chart: Distance in Clock Ticks Nodes 1-2

## Slide 81: Implication
ASIC Based Technique with accuracy in inches with sub second latencies
Indoor Location
  Multipath Effects need addressing

## Slide 82: Clock Synchronization
Mapping Function Based
With Absolute Time

## Slide 83: Mapping Function Based Synchronization
Normal approach
  Exchange signals
  Determine corrections
  Correct the local clock
Our Approach
  Use a free running local clock
  Exchange messages to determine a mapping function
  When time information is needed
    Read time from local clock
    Map it using a mapping function

## Slide 84: Mapping Function
Two nodes, a and b
φa(t) = ta
ψa(ta) = t
  Example
φab(tb) = ta
ψab(ta) = tb

## Slide 85: Approach
Linear model of clock works well over short periods of time
When exchanging messages, Time instants ta(2) and tb(2) are the same time instants in real time.
Calculate and use a piecewise linear mapping function

## Slide 86: Synchronization tolerance
How far is the time at a node compared to the mapped time?

## Slide 87: Synchronization Tolerance
3 nodes 4 ft apart
Average ~ 80 ps, STD ~ 60 ps

## Slide 88: Synchronization Tolerance
Five Nodes – 123451 path

## Slide 89: Synchronization with Absolute time
Note that
If we can measure d accurately we can determine b the drift rate with respect to real time

## Slide 90: Two Approaches
Over the air
  The term d is a function of distance and the speed of light.
    We can keep nodes at fixed distance
    Speed of light through air changes as a function of temperature, pressure and humidity
    Monitoring these we can determine the speed of light with an accuracy of one part in 109
    As these parameters change slowly we can have a stable reference during a mission.
Using a communications means with known delay
  Fiber with measured delay