## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 1115
CMSC 417 : Spring 2020
Topic: Intra- and Inter-AS routing (BGP) – Part 2
(Textbook chapter 4)

## Slide 2: A dive into the BGP policies

## Slide 3: Nontransit vs. Transit ASes
ISP 1
ISP 2
Nontransit AS
might be a corporate
or campus network.
Could be a “content
provider”
NET A
Traffic NEVER
flows from ISP 1
through NET A to ISP 2
(At least not intentionally!)
IP traffic
Internet Service
providers (often)
have transit
networks

## Slide 4: Selective Transit
NET B
NET C
NET A provides transit
between NET B and NET C
and between NET D
and NET C
NET A
NET D
NET A DOES NOT
provide transit
Between NET D
and NET B
Most transit networks transit in a selective manner…
IP traffic

## Slide 5: Customers and Providers
Customer pays provider for access to the Internet
provider
customer
IP traffic
provider
customer

## Slide 6: Customers Don’t Always Need BGP
provider
customer
Nail up default routes 0.0.0.0/0
pointing to provider.
Nail up routes 192.0.2.0/24
pointing to customer
192.0.2.0/24
Static routing is the most common way of connecting an
autonomous routing domain to the Internet.
This helps explain why BGP is a mystery to many …

## Slide 7: Customer-Provider Hierarchy
IP traffic
provider
customer

## Slide 8: The Peering Relationship
peer
peer
customer
provider
Peers provide transit between
their respective customers
Peers do not provide transit
between peers
Peers (often) do not exchange $$$
traffic
allowed
traffic NOT
allowed

## Slide 9: Peering Provides Shortcuts
Peering also allows connectivity between
the customers of “Tier 1” providers.
peer
peer
customer
provider

## Slide 10: BGP-4
BGP = Border Gateway Protocol
Is a Policy-Based routing protocol
Is the de facto EGP of today’s global Internet
Relatively simple protocol, but configuration is complex and the entire world can see, and be impacted by, your mistakes.
1989 : BGP-1 [RFC 1105]
  Replacement for EGP (1984, RFC 904)
1990 : BGP-2 [RFC 1163]
1991 : BGP-3 [RFC 1267]
1995 : BGP-4 [RFC 1771]
  Support for Classless Interdomain Routing (CIDR)

## Slide 11: BGP Operations (Simplified)
Establish session on
TCP port 179
Exchange all
active routes
Exchange incremental
updates
AS1
AS2
While connection
is ALIVE exchange
route UPDATE messages
BGP session

## Slide 12: Four Types of BGP Messages
Open : Establish a peering session.
Keep Alive : Handshake at regular intervals.
Notification : Shuts down a peering session.
Update : Announcing new routes or withdrawing previously announced routes.
announcement
=
prefix + attributes values

## Slide 13: BGP Attributes
Value Code Reference
----- --------------------------------- ---------
1 ORIGIN [RFC1771]
2 AS_PATH [RFC1771]
3 NEXT_HOP [RFC1771]
4 MULTI_EXIT_DISC [RFC1771]
5 LOCAL_PREF [RFC1771]
6 ATOMIC_AGGREGATE [RFC1771]
7 AGGREGATOR [RFC1771]
8 COMMUNITY [RFC1997]
9 ORIGINATOR_ID [RFC2796]
10 CLUSTER_LIST [RFC2796]
11 DPA [Chen]
12 ADVERTISER [RFC1863]
13 RCID_PATH / CLUSTER_ID [RFC1863]
14 MP_REACH_NLRI [RFC2283]
15 MP_UNREACH_NLRI [RFC2283]
16 EXTENDED COMMUNITIES [Rosen]
...
255 reserved for development
From IANA: http://www.iana.org/assignments/bgp-parameters
Most important attributes
Not all attributes
need to be present in
every announcement

## Slide 14: Attributes are Used to Select Best Routes
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
Given multiple
routes to the same
prefix, a BGP speaker
must pick at most
one best route
(Note: it could reject
them all!)

## Slide 15: BGP Next Hop Attribute
Every time a route announcement crosses an AS boundary, the Next Hop attribute is changed to the IP address of the border router that announced the route.
AS 6431
AT&T Research
135.207.0.0/16
Next Hop = 12.125.133.90
AS 7018
AT&T
AS 12654
RIPE NCC
RIS project
12.125.133.90
135.207.0.0/16
Next Hop = 12.127.0.121
12.127.0.121

## Slide 16: Join EGP with IGP For Connectivity
Forwarding Table
Forwarding Table
AS 1
AS 2
192.0.2.1
135.207.0.0/16
10.10.10.10
EGP
192.0.2.1
135.207.0.0/16
destination
next hop
10.10.10.10
192.0.2.0/30
destination
next hop
135.207.0.0/16
Next Hop = 192.0.2.1
192.0.2.0/30
135.207.0.0/16
destination
next hop
10.10.10.10
+
192.0.2.0/30
10.10.10.10

## Slide 17: Implementing Customer/Provider and Peer/Peer relationships
Enforce transit relationships
  Outbound route filtering
Enforce order of route preference
  provider < peer < customer
Two parts:

## Slide 18: Import Routes
From
peer
From
peer
From
provider
From
provider
From
customer
From
customer
provider route
customer route
peer route
ISP route

## Slide 19: Export Routes
To
peer
To
peer
To
customer
To
customer
To
provider
From
provider
provider route
customer route
peer route
ISP route
filters
block

## Slide 20: How Can Routes be Colored? BGP Communities!
A community value is 32 bits
By convention,
first 16 bits is
ASN indicating
who is giving it
an interpretation
community
number
Very powerful
BECAUSE it
has no (predefined) meaning
Community Attribute = a list of community values.
(So one route can belong to multiple communities)
RFC 1997 (August 1996)
Used for signalling
within and between
ASes
Two reserved communities
no_advertise 0xFFFFFF02: don’t pass to BGP neighbors
  no_export = 0xFFFFFF01: don’t export out of AS

## Slide 21: Tweak Tweak Tweak
For inbound traffic
  Filter outbound routes
  Tweak attributes on outbound routes in the hope of influencing your neighbor’s best route selection
For outbound traffic
  Filter inbound routes
  Tweak attributes on inbound routes to influence best route selection
outbound
routes
inbound
routes
inbound
traffic
outbound
traffic
In general, an AS has more
control over outbound traffic

## Slide 22: Route Selection Summary
Highest Local Preference
Shortest ASPATH
Lowest MED
i-BGP < e-BGP
Lowest IGP cost
to BGP egress
Lowest router ID
traffic engineering
Enforce relationships
Throw up hands and
break ties

## Slide 23: Back to Frank …
AS 1
AS 2
AS 4
AS 3
13.13.0.0/16
peer
peer
customer
provider
local pref = 80
local pref = 100
local pref = 90
Higher Local
preference values
are more preferred
Local preference only used in iBGP

## Slide 24: Implementing Backup Links with Local Preference (Outbound Traffic)
Forces outbound traffic to take primary link, unless link is down.
AS 1
primary link
backup link
Set Local Pref = 100
for all routes from AS 1
AS 65000
Set Local Pref = 50
for all routes from AS 1
We’ll talk about inbound traffic soon …

## Slide 25: Multihomed Backups (Outbound Traffic)
Forces outbound traffic to take primary link, unless link is down.
AS 1
primary link
backup link
Set Local Pref = 100
for all routes from AS 1
AS 2
Set Local Pref = 50
for all routes from AS 3
AS 3
provider
provider

## Slide 26: ASPATH Attribute
AS7018
135.207.0.0/16
AS Path = 6341
AS 1239
Sprint
AS 1755
Ebone
AT&T
AS 3549
Global Crossing
135.207.0.0/16
AS Path = 7018 6341
135.207.0.0/16
AS Path = 3549 7018 6341
AS 6341
135.207.0.0/16
AT&T Research
Prefix Originated
AS 12654
RIPE NCC
RIS project
AS 1129
Global Access
135.207.0.0/16
AS Path = 7018 6341
135.207.0.0/16
AS Path = 1239 7018 6341
135.207.0.0/16
AS Path = 1755 1239 7018 6341
135.207.0.0/16
AS Path = 1129 1755 1239 7018 6341

## Slide 27: Interdomain Loop Prevention
BGP at AS YYY will never accept a route with ASPATH containing YYY.
AS 7018
12.22.0.0/16
ASPATH = 1 333 7018 877
Don’t Accept!
AS 1

## Slide 28: Traffic Often Follows ASPATH
AS 4
AS 3
AS 2
AS 1
135.207.0.0/16
135.207.0.0/16
ASPATH = 3 2 1
IP Packet
Dest =
135.207.44.66

## Slide 29: … But It Might Not
AS 4
AS 3
AS 2
AS 1
135.207.0.0/16
135.207.0.0/16
ASPATH = 3 2 1
IP Packet
Dest =
135.207.44.66
AS 5
135.207.44.0/25
ASPATH = 5
135.207.44.0/25
AS 2 filters all
subnets with masks
longer than /24
135.207.0.0/16
ASPATH = 1
From AS 4, it
may look like this
packet will take
path 3 2 1, but it
actually takes
path 3 2 5

## Slide 30: Shorter Doesn’t Always Mean Shorter
In fairness:
could you do
this “right” and
still scale?
Exporting internal
state would
dramatically
increase global
instability and
amount of routing
state
AS 4
AS 3
AS 2
AS 1
Mr. BGP says that
path 4 1 is better
than path 3 2 1
Duh!

## Slide 31: Shedding Inbound Traffic with ASPATH Padding Hack
Padding will (usually)
force inbound
traffic from AS 1
to take primary link
AS 1
192.0.2.0/24
ASPATH = 2 2 2
customer
AS 2
provider
192.0.2.0/24
backup
primary
192.0.2.0/24
ASPATH = 2

## Slide 32: Padding May Not Shut Off All Traffic
AS 1
192.0.2.0/24
ASPATH = 2 2 2 2 2 2 2 2 2 2 2 2 2 2
customer
AS 2
provider
192.0.2.0/24
192.0.2.0/24
ASPATH = 2
AS 3
provider
AS 3 will send
traffic on “backup”
link because it prefers
customer routes and local
preference is considered
before ASPATH length!
Padding in this way is often
used as a form of load
balancing
backup
primary

## Slide 33: COMMUNITY Attribute to the Rescue!
AS 1
customer
AS 2
provider
192.0.2.0/24
192.0.2.0/24
ASPATH = 2
AS 3
provider
backup
primary
192.0.2.0/24
ASPATH = 2
COMMUNITY = 3:70
Customer import policy at AS 3:
If 3:90 in COMMUNITY then
set local preference to 90
If 3:80 in COMMUNITY then
set local preference to 80
If 3:70 in COMMUNITY then
set local preference to 70
AS 3: normal
customer local
pref is 100,
peer local pref is 90

## Slide 34: Hot Potato Routing: Go for the Closest Egress Point
192.44.78.0/24
15
56
IGP distances
egress 1
egress 2
This Router has two BGP routes to 192.44.78.0/24.
Hot potato: get traffic off of your network as
Soon as possible. Go for egress 1!

## Slide 35: Getting Burned by the Hot Potato
15
56
17
2865
High bandwidth
Provider backbone
Low bandwidth
customer backbone
Heavy
Content
Web Farm
Many customers want
their provider to
carry the bits!
tiny http request
huge http reply
SFO
NYC
San Diego

## Slide 36: Cold Potato Routing with MEDs (Multi-Exit Discriminator Attribute)
15
56
17
2865
Heavy
Content
Web Farm
192.44.78.0/24
192.44.78.0/24
MED = 15
192.44.78.0/24
MED = 56
This means that MEDs must be considered BEFORE
IGP distance!
Prefer lower
MED values
Note1 : some providers will not listen to MEDs
Note2 : MEDs need not be tied to IGP distance

## Slide 37: Route Selection Summary
Highest Local Preference
Shortest ASPATH
Lowest MED
i-BGP < e-BGP
Lowest IGP cost
to BGP egress
Lowest router ID
traffic engineering
Enforce relationships
Throw up hands and
break ties