## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 1115
CMSC 417 : Spring 2022
Topic: Internetworking: ARP, ICMP, VPN
(Textbook chapter 3)

## Slide 2: Network address vs LAN address

## Slide 3
Destination
Source
Router
Two perspectives of addresses:
(1)Network-to-network & (2)machine-to-machine

## Slide 4
Source
Router
application
transport
network
link
physical

## Slide 5
Source
Router
network
link
physical
application
transport
network
link
physical

## Slide 6
Router
Hierarchical address for addressing networks
(IP address)
network
link
physical

## Slide 7
Source
Router
application
transport
network
link
physical
network
link
physical

## Slide 8
Source
Router
application
transport
network
link
physical
network
link
physical
Flat address for addressing machines at the link-layer
(MAC address)

## Slide 9: Address Resolution Protocol (ARP)

## Slide 10: MAC addresses and ARP
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  e.g.: 1A-2F-BB-76-09-AD
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)

## Slide 11: MAC addresses and ARP
each adapter on LAN has unique LAN addr. or MAC addr.
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 12: MAC addresses (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address not portable
  address depends on IP subnet to which node is attached

## Slide 13: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 14: ARP Packet Format
  HardwareType: type of physical network (e.g., Ethernet)
  ProtocolType: type of higher layer protocol (e.g., IP)
  HLEN & PLEN: length of physical and protocol addresses
  Operation: request or response
  Source/Target Physical/Protocol addresses

## Slide 15: ARP protocol: same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF (Link layer broadcast address)
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 16: Address Translation Protocol (ARP)
Map IP addresses into physical addresses
  destination host
  next hop router
Techniques
  encode physical address in host part of IP address
  table-based
ARP (Address Resolution Protocol)
  table of IP to physical address bindings
  broadcast request if IP address not in table
  target machine responds with its physical address
  table entries are discarded if not refreshed
  Query message include the physical address of the sending host. Why?

## Slide 17: Internet Control Message Protocol (ICMP)

## Slide 18: Internet Control Message Protocol (ICMP)
Defines a collection of error messages that are sent back to the source host whenever a router or host is unable to process an IP datagram successfully
  Destination host unreachable due to link /node failure
  Reassembly process failed
  TTL had reached 0 (so datagrams don't cycle forever)
  IP header checksum failed
ICMP-Redirect
  From router to a source host
  With a better route information

## Slide 19
ICMP message types

## Slide 20
Ping example

## Slide 21
Traceroute : An unintuitive application using ICMP

## Slide 22
Traceroute example

## Slide 23
Traceroute : An unintuitive application

## Slide 24: Virtual Networks and Tunnels

## Slide 28
Why do we need virtual networks or tunnels?
1. Security
2. Special capabilities between routers (e.g., multicast)
3. Supporting heterogeneity
Disadvantages:
1. Increases packet length
a) Wastage of bandwidth
b) More processing
c) Fragmentation
2. Increases management cost

## Slide 29
A note on the “subnet mask”

## Slide 30
inet 10.104.216.101  00001010.01101000.11011000.01100101
netmask ff:ff:f0:00  11111111.11111111.11110000.00000000
broadcast 10.104.223.255 
00001010.01101000.11011111.11111111