## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 1115
CMSC 417 : Spring 2020
Topic: BGP attacks and Application Layer Protocols
(Textbook chapters 4 and 9)

## Slide 2: BGP Attacks

## Slide 3: Prefix Hijacking
1
2
3
4
5
6
7
12.34.0.0/16
12.34.0.0/16
Originating someone else’s prefix
  What fraction of the Internet believes it?

## Slide 4: Prefix highjack
http://queue.acm.org/detail.cfm?id=2668966

## Slide 5: Sub-Prefix Hijacking
Originating a more-specific prefix
  Every AS picks the bogus route for that prefix
  Traffic follows the longest matching prefix
1
2
3
4
5
6
7
12.34.0.0/16
12.34.158.0/24

## Slide 6: Sub-prefix hijack
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
  February 2008 : Pakistan Telecom hijacks YouTube
Notes: -level of autonomous systems
-e.g., YouTube, AT&T, pakistan telecom
-routing is done on IP addresses, so when someone wants to go to YouTube they get YouTube’s IP address and YouTube announces to the world that they have the ip address and traffic is forwarded towards them. So here multinet would route to it’s provider pakistan telecom that then forwards the traffic on to youtube.
-these networks chosen for a specific reason which is that there was an incident in february 2008 pakistan telecom actually high jacked traffic going to youtube (misconfiguration).
-they announced to the world that they’re youtube and traffic destined to youtube was routed to them
-youtube was unavailable for a couple of hours as operators phone each other to figure out what was going on.

## Slide 7: Pakistan Telecom: Sub-prefix hijack
  Here’s what should have happened….
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
X
Hijack + drop packets going to YouTube
  Block your own customers.

## Slide 8: Pakistan Telecom: Sub-prefix hijack
  But here’s what Pakistan ended up doing…
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
Pakistan
Telecom
No, I’m YouTube!
IP 208.65.153.0 / 24
Notes: Our works focuses on attacks of this flavor..

## Slide 9: Bogus AS Paths to Hide Hijacking
Adds AS hop(s) at the end of the path
  E.g., turns “701 88” into “701 88 3”
Motivations
  Evade detection for a bogus route
  E.g., by adding the legitimate AS to the end
Hard to tell that the AS path is bogus…
  Even if other ASes filter based on prefix ownership
701
88
3
18.0.0.0/8
18.0.0.0/8

## Slide 10: Path-Shortening Attacks
Remove ASes from the AS path
  E.g., turn “701 3715 88” into “701 88”
Motivations
  Make the AS path look shorter than it is
  Attract sources that normally try to avoid AS 3715
  Help AS 88 look like it is closer to the Internet’s core
Who can tell that this AS path is a lie?
  Maybe AS 88 *does* connect to AS 701 directly
701
88
3715
?

## Slide 11: Attacks that Add a Bogus AS Hop
Add ASes to the path
  E.g., turn “701 88” into “701 3715 88”
Motivations
  Trigger loop detection in AS 3715
    Denial-of-service attack on AS 3715
    Or, blocking unwanted traffic coming from AS 3715!
  Make your AS look like is has richer connectivity
Who can tell the AS path is a lie?
  AS 3715 could, if it could see the route
  AS 88 could, but would it really care as long as it received data traffic meant for it?
701
88

## Slide 12: Violating “Consistent Export” to Peers
Peers require consistent export
  Prefix advertised at all peering points
  Prefix advertised with same AS path length
Reasons for violating the policy
  Trick neighbor into “cold potato”
  Configuration mistake
Main defense
  Analyzing BGP updates
  … or data traffic
  … for signs of inconsistency
src
dest
Bad AS
data
BGP

## Slide 13: Other Attacks
Attacks on BGP sessions
  Confidentiality of BGP messages
  Denial-of-service on BGP session
  Inserting, deleting, modifying, or replaying messages
Resource exhaustion attacks
  Too many IP prefixes (e.g., BGP “512K Day”)
  Too many BGP update messages
Data-plane attacks
  Announce one BGP routes, but use another

## Slide 14: Solution Techniques
Protective filtering
  Know your neighbors
Anomaly detection
  Suspect the unexpected
Checking against registries
  Establish ground truth for prefix origination
Signing and verifying
  Prevent bogus AS PATHs
Data-plane verification
  Ensure the path is actually followed

## Slide 15: Application Layer Protocols

## Slide 16
application
transport
network
link
physical
Application Layer

## Slide 17: Application Layer
Our Goal:
Conceptual, implementation aspects of network application protocols
  Transport-layer service models
  Client-server paradigm
  Peer-to-peer paradigm
  Content distribution networks
Learn about protocols by examining popular application-level protocols
  HTTP
  SMTP / POP3 / IMAP
  DNS

## Slide 18: Outline
  Principles of network applications
  Web and HTTP
  Electronic Mail (SMTP, POP3, IMAP)
  DNS

## Slide 19: Creating a network app
Write programs that:
run on (different) end systems
communicate over network
e.g., web server software communicates with browser software
No need to write software for network-core devices
network-core devices do not run user applications
applications on end systems allows for rapid app development, propagation
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 20: Application architectures
Possible structure of applications:
Client-server
Peer-to-peer (P2P)
Hybrid

## Slide 21: Client-server architecture
server: always-on host
permanent IP address
data centers for scaling
clients:
communicate with server
may be intermittently connected
may have dynamic IP addresses
do not communicate directly with each other
client/server

## Slide 22: P2P architecture
no always-on server
arbitrary end systems directly communicate
peers request service from other peers, provide service in return to other peers
  self scalability – new peers bring new service capacity, as well as new service demands
peer-peer

## Slide 23: P2P architecture
Game Server
no always-on server
arbitrary end systems directly communicate
peers request service from other peers, provide service in return to other peers
  self scalability – new peers bring new service capacity, as well as new service demands

## Slide 24: P2P architecture
no always-on server
arbitrary end systems directly communicate
peers request service from other peers, provide service in return to other peers
  self scalability – new peers bring new service capacity, as well as new service demands
Peers are intermittently connected and change IP addresses
  Complex Management

## Slide 25: Hybrid of client-server and P2P
Skype
  Internet telephony app
  Finding address of remote party: centralized server(s)
  Client-client connection is direct (not through server)
Instant messaging
  Chatting between two users is P2P
  Presence detection/location centralized:
    User registers its IP address with central server when it comes online
    User contacts central server to find IP addresses of buddies

## Slide 26: App-layer protocol defines
types of messages exchanged,
  e.g., request, response
message syntax:
  what fields in messages & how fields are delineated
message semantics
  meaning of information in fields
rules for when and how processes send & respond to messages
open protocols:
defined in RFCs
allows for interoperability
e.g., HTTP, SMTP
proprietary protocols:
e.g., Skype

## Slide 27: What transport service does an app need?
data loss
some apps (e.g., file transfer, web transactions) require 100% reliable data transfer
other apps (e.g., audio) can tolerate some loss
timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
throughput
some apps (e.g., multimedia) require minimum amount of throughput to be “effective”
other apps (“elastic apps”) make use of whatever throughput they get
Why is bandwidth different from
timing constraints?

## Slide 28: Transport service requirements: common apps
application
file transfer
e-mail
Web documents
real-time audio/video
stored audio/video
interactive games
text messaging
data loss
no loss
no loss
no loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
throughput
elastic
elastic
elastic
audio: 5kbps-1Mbps
video:10kbps-5Mbps
same as above
few kbps up
elastic
time sensitive
no
no
no
yes, 100’s msec
yes, few secs
yes, 100’s ms
yes and no
no

## Slide 29: Internet transport protocols services
TCP service:
reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
does not provide: timing, minimum throughput guarantee, security
connection-oriented: setup required between client and server processes
UDP service:
unreliable data transfer between sending and receiving process
does not provide: reliability, flow control, congestion control, timing, throughput guarantee, security, or connection setup,
Q: why bother? Why is there a UDP?
Notes: FedEx vs USPS

## Slide 30: Internet apps: application, transport protocols
application
e-mail
remote terminal access
Web
file transfer
streaming multimedia
Internet telephony
naming
application
layer protocol
SMTP [RFC 2821]
Telnet [RFC 854], SSH
HTTP [RFC 2616]
FTP [RFC 959]
HTTP (e.g., YouTube), RTP [RFC 1889]
SIP, RTP, proprietary
(e.g., Skype)
DNS
underlying
transport protocol
TCP
TCP
TCP
TCP
TCP or UDP
TCP or UDP
UDP (and TCP)

## Slide 31: Outline
  Principles of network applications
  Socket Programming with UDP and TCP
  Web and HTTP
  Electronic Mail (SMTP, POP3, IMAP)
  DNS

## Slide 32: Socket programming
goal: learn how to build client/server applications that communicate using sockets
socket: door between application process and end-end-transport protocol
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 33: Socket programming
goal: learn how to build client/server applications that communicate using sockets
socket: door between application process and end-end-transport protocol
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket
  Two socket types for two transport services:
  UDP: unreliable datagram (User Datagram Protocol)
  TCP: reliable, byte stream-oriented (Transmission Control Protocol)

## Slide 34: Outline
  Principles of network applications
  Web and HTTP
  Electronic Mail (SMTP, POP3, IMAP)
  DNS

## Slide 35: Web and HTTP
First, a review…
web page consists of objects
object can be HTML file, JPEG image, Java applet, audio file,…
web page consists of base HTML-file which includes several referenced objects
each object is addressable by a URL, e.g.,
www.someschool.edu/someDept/pic.gif
host name
path name

## Slide 36: HTTP overview
HTTP: hypertext transfer protocol
Web’s application layer protocol
client/server model
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
PC running
Firefox browser
server
running
Apache Web
server
iPhone running
Safari browser
HTTP request
HTTP response
HTTP request
HTTP response

## Slide 37: HTTP overview
Uses TCP:
client initiates TCP connection (creates socket) to server, port 80
server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
HTTP is “stateless”
server maintains no information about past client requests
protocols that maintain “state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 38: HTTP connections
non-persistent HTTP
at most one object sent over TCP connection
  connection then closed
downloading multiple objects required multiple connections
persistent HTTP
multiple objects can be sent over single TCP connection between client, server

## Slide 39: Non-persistent HTTP
suppose user enters URL:
1a. HTTP client initiates TCP connection to HTTP server (process) at www.someSchool.edu on port 80
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket. Message indicates that client wants object someDepartment/home.index
1b. HTTP server at host www.someSchool.edu waiting for TCP connection at port 80. “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object, and sends message into its socket
time
(contains text, references to 10 jpeg images)
www.someSchool.edu/someDepartment/home.index
5. HTTP client receives response message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects
6. Steps 1-5 repeated for each of 10 jpeg objects
4. HTTP server closes TCP connection.

## Slide 40: Non-persistent HTTP: response time
RTT (Round Trip Time): time for a small packet to travel from client to server and back
HTTP response time:
one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return
file transmission time
non-persistent HTTP response time
  = 2RTT+ file transmission time
time to
transmit
file
initiate TCP
connection
RTT
request
file
RTT
file
received
time
time

## Slide 41: Persistent HTTP
Persistent HTTP:
server leaves connection open after sending response
subsequent HTTP messages between same client/server sent over open connection
client sends requests as soon as it encounters a referenced object
as little as one RTT for all the referenced objects
initiate TCP
connection
RTT
RTT
request
new file
request
file
time
time
Notes: Breakdown of layering

## Slide 42: Other optimizations
Pipelining
  Send several requests at once
initiate TCP
connection
RTT
RTT
request
new files
request
file
time
time

## Slide 43: Other optimizations
Pipelining
  Send several requests at once
HTTP/2
  Push resources
initiate TCP
connection
RTT
RTT
request
file
send
file
push
objects
time
time

## Slide 44: Other optimizations
Pipelining
  Send several requests at once
HTTP/2
  Push resources
QUIC
  Eliminate first RTT
initiate QUIC
connection
RTT
time
time
request
file
send
file
push
objects

## Slide 45: HTTP request message
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
request line
(GET, POST,
HEAD commands)
header
lines
carriage return,
line feed at start
of line indicates
end of header lines
GET /index.html HTTP/1.1\r\n
Host: www-net.cs.umass.edu\r\n
User-Agent: Firefox/3.6.10\r\n
Accept: text/html,application/xhtml+xml\r\n
Accept-Language: en-us,en;q=0.5\r\n
Accept-Encoding: gzip,deflate\r\n
Accept-Charset: ISO-8859-1,utf-8;q=0.7\r\n
Keep-Alive: 115\r\n
Connection: keep-alive\r\n
\r\n
carriage return character
line-feed character

## Slide 46: HTTP request message: general format
request
line
header
lines
body
method
sp
sp
cr
lf
version
URL
cr
lf
value
header field name
cr
lf
value
header field name
~
~
~
~
cr
lf
entity body
~
~
~
~
:
:

## Slide 47: Uploading form input
POST method:
web page often includes form input
input is uploaded to server in entity body
URL method:
uses GET method
input is uploaded in URL field of request line:
www.somesite.com/animalsearch?monkeys&banana

## Slide 48: Method types
HTTP/1.0:
GET
POST
HEAD
  asks server to leave requested object out of response
HTTP/1.1:
GET, POST, HEAD
PUT
  uploads file in entity body to path specified in URL field
DELETE
  deletes file specified in the URL field

## Slide 49: HTTP response message
status line
(protocol
status code
status phrase)
header
lines
data, e.g.,
requested
HTML file
HTTP/1.1 200 OK\r\n
Date: Sun, 26 Sep 2010 20:09:20 GMT\r\n
Server: Apache/2.0.52 (CentOS)\r\n
Last-Modified: Tue, 30 Oct 2007 17:00:02 GMT\r\n
ETag: "17dc6-a5c-bf716880"\r\n
Accept-Ranges: bytes\r\n
Content-Length: 2652\r\n
Keep-Alive: timeout=10, max=100\r\n
Connection: Keep-Alive\r\n
Content-Type: text/html; charset=ISO-8859-1\r\n
\r\n
data data data data data ...

## Slide 50: HTTP response status codes
200 OK
  request succeeded, requested object later in this msg
301 Moved Permanently
  requested object moved, new location specified later in this msg (Location:)
400 Bad Request
  request msg not understood by server
404 Not Found
  requested document not found on this server
505 HTTP Version Not Supported
status code appears in 1st line in server-to-client response message.
some sample codes:
Notes: cats

## Slide 51: Trying out HTTP (client side) for yourself
1. Telnet to your favorite Web server:
opens TCP connection to port 80
(default HTTP server port)
at gaia.cs.umass. edu.
anything typed in will be sent
to port 80 at gaia.cs.umass.edu
telnet gaia.cs.umass.edu 80
2. type in a GET HTTP request:
GET /kurose_ross/interactive/index.php HTTP/1.1
Host: gaia.cs.umass.edu
by typing this in (hit carriage
return twice), you send
this minimal (but complete)
GET request to HTTP server
3. look at response message sent by HTTP server!
(or use Wireshark to look at captured HTTP request/response)