## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 1115
CMSC 417 : Spring 2022
Topic: Overview of networks – Part 2
(Textbook chapter 1)

## Slide 2
Network interface controller
(NIC)

## Slide 3
Point-to-point connection

## Slide 5
MOOCs
Online Content
Search Engines
Notes: So building networks is hard
But unfortunately, computer networks are becoming increasingly critical to our daily lives
You know all the standard uses of computers…
Social networking
Gaming
But there’s a lot you may not thinki about
Financial sector – trillions of dollars –
Critical infrastructures – power grid, water delibvery systems – now all managed and operated with IP networks
911 communication services
…
Remote medicine
Brakes of your car
Power grid and critical infrastructure
Financial and trading networks – move billions of dollars per day over computer netowrks
Computer networks are no longer just for fun and games
People’s lives every day depend on the availability and functioning of computer netowrks
Makign it very important that we build them well, and protect them from adversaries,

## Slide 6
All pair Point-to-point connection

## Slide 7
All pair Point-to-point connection
Is this scalable?

## Slide 8
Shared channel
Multiple access

## Slide 9
Shared channel
Multiple access
How to direct the flow of data at these points?

## Slide 10
Multiplexing multiple logical flows over a single physical link
Switching

## Slide 11: Circuit Switching
end-end resources allocated to, reserved for “call” between source & destination:
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
commonly used in traditional telephone networks

## Slide 12: Alternative core: Circuit Switching

## Slide 13: Circuit Switching: FDM versus TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 14: Circuit Switching
end-end resources allocated to, reserved for “call” between source & destination:
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
commonly used in traditional telephone networks
Circuit segment idle if there is not enough data

## Slide 15: Packet Switching

## Slide 16: Packet Switching
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link

## Slide 17: Switch vs Router
Switches
Routers

## Slide 18: Chapter 1: Roadmap
  What is the Internet?
  Network edge
  Network core
  Delay, Loss, Throughput in networks
  Protocol layers, service models
  History

## Slide 19
What’s the Internet?
Notes: Associate press: an Internet vs the Internet

## Slide 20: Chapter 1: Roadmap
  What is the Internet?
  Network edge
  Network core
  Delay, Loss, Throughput in networks
  Protocol layers, service models
  History

## Slide 21
Network Edge
Notes: So building networks is hard
But unfortunately, computer networks are becoming increasingly critical to our daily lives
You know all the standard uses of computers…
Social networking
Gaming
But there’s a lot you may not thinki about
Financial sector – trillions of dollars –
Critical infrastructures – power grid, water delibvery systems – now all managed and operated with IP networks
911 communication services
…
Remote medicine
Brakes of your car
Power grid and critical infrastructure
Financial and trading networks – move billions of dollars per day over computer netowrks
Computer networks are no longer just for fun and games
People’s lives every day depend on the availability and functioning of computer netowrks
Makign it very important that we build them well, and protect them from adversaries,

## Slide 22
Network Edge

## Slide 23: A closer look at network structure:
Network edge:
  hosts: clients and servers
  servers often in data centers
  access networks, physical media: wired, wireless communication links

## Slide 24
Access Network: Home Network
to/from headend or central office
cable or DSL modem
(DSL=Digital Subscriber Line)
router, firewall
wired Ethernet (1 Gbps)
wireless access
point (54 Mbps)
wireless
devices
often combined
in single box

## Slide 25
Access Network: Home Network

## Slide 26: Enterprise Access Networks (Ethernet)
Typically used in companies, universities, etc.
  10 Mbps, 100Mbps, 1Gbps, 10Gbps transmission rates
  Today, end systems typically connect into Ethernet switch
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)

## Slide 27: Wireless Access Networks
Shared wireless access network connects end system to router
  via base station aka “access point”
Wireless LANs:
  within building (100 ft.)
  802.11b/g/n (WiFi): 11, 54, 450 Mbps transmission rate
Wide-area wireless access
  provided by telco (cellular) operator, 10’s km
  between 1 and 10 Mbps
  3G, 4G: LTE
to Internet
to Internet

## Slide 28: Chapter 1: Roadmap
  What is the Internet?
  Network edge
  Network core
  Delay, Loss, Throughput in networks
  Protocol layers, service models
  History

## Slide 29
MOOCs
Online Content
Search Engines
Network Core
Notes: So building networks is hard
But unfortunately, computer networks are becoming increasingly critical to our daily lives
You know all the standard uses of computers…
Social networking
Gaming
But there’s a lot you may not thinki about
Financial sector – trillions of dollars –
Critical infrastructures – power grid, water delibvery systems – now all managed and operated with IP networks
911 communication services
…
Remote medicine
Brakes of your car
Power grid and critical infrastructure
Financial and trading networks – move billions of dollars per day over computer netowrks
Computer networks are no longer just for fun and games
People’s lives every day depend on the availability and functioning of computer netowrks
Makign it very important that we build them well, and protect them from adversaries,

## Slide 30: The Network Core
Mesh of interconnected routers
Packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity

## Slide 31: Two key network-core functions
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
destination address in arriving
packet’s header

## Slide 32: Packet-switching: Store-and-Forward
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)

## Slide 33: Internet Structure: Network of Networks
End systems connect to Internet via access ISPs (Internet Service Providers)
  residential, company and university ISPs
Access ISPs in turn must be interconnected.
  so that any two hosts can send packets to each other
Resulting network of networks is very complex
  evolution was driven by economics and national policies
Let’s take a stepwise approach to describe current Internet structure

## Slide 34
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Internet Structure: Network of Networks

## Slide 35
Option: connect each access ISP to every other access ISP?
access
net
access
net
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
access
net
access
net
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…
Internet Structure: Network of Networks

## Slide 36
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to one global transit ISP?
Customer and provider ISPs have economic agreement.
global ISP
Internet Structure: Network of Networks

## Slide 37
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
Internet Structure: Network of Networks
But if one global ISP is viable business, there will be competitors ….

## Slide 38
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
But if one global ISP is viable business, there will be competitors …. which must be interconnected
IXP
peering link
Internet exchange point
IXP
Internet Structure: Network of Networks

## Slide 39
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
… and regional networks may arise to connect access nets to ISPs
Internet Structure: Network of Networks

## Slide 40
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
Content provider/distribution network
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users
Internet Structure: Network of Networks

## Slide 41
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider/distribution network (e.g., Google, Akamai): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
IXP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
Regional ISP
Regional ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Internet Structure: Network of Networks

## Slide 42: Chapter 1: Roadmap
  What is the Internet?
  Network edge
  Network core
  Delay, Loss, Throughput in networks
  Protocol layers, service models
  History

## Slide 43: How do loss and delay occur?
A
B
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 44: Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 45
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
v: propagation speed
dprop = d/v
dtrans and dprop
very different
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
Four sources of packet delay
Notes: 45

## Slide 46: Packet Loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)

## Slide 47: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)

## Slide 48: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 49: Throughput: Internet scenario
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R

## Slide 50: Bandwidth
Bits transmitted at a particular bandwidth can be regarded as having some width:
(a) bits transmitted at 1Mbps (each bit 1 μs wide);
(b) bits transmitted at 2Mbps (each bit 0.5 μs wide).

## Slide 51: Delay X Bandwidth
We think the channel between a pair of processes as a hollow pipe
Latency (delay) length of the pipe and bandwidth the width of the pipe
Delay of 50 ms and bandwidth of 45 Mbps
50 x 10-3 seconds x 45 x 106 bits/second
2.25 x 106 bits = 280 KB data.
Network as a pipe

## Slide 52: Delay X Bandwidth
Relative importance of bandwidth and latency depends on application
  For large file transfer, bandwidth is critical
  For small messages (HTTP, NFS, etc.), latency is critical
  Variance in latency (jitter) can also affect some applications (e.g., audio/video conferencing)

## Slide 53: Delay X Bandwidth
  How many bits the sender must transmit before the first bit arrives at the receiver if the sender keeps the pipe full
  Takes another one-way latency to receive a response from the receiver
  If the sender does not fill the pipe—send a whole delay × bandwidth product’s worth of data before it stops to wait for a signal—the sender will not fully utilize the network

## Slide 54: Delay X Bandwidth
Infinite bandwidth
  RTT dominates
  Throughput = TransferSize / TransferTime
  TransferTime = RTT + 1/Bandwidth x TransferSize
Its all relative
  1-MB file to 1-Gbps link looks like a 1-KB packet to 1-Mbps link

## Slide 55: Relationship between bandwidth and latency
A 1-MB file would fill the 1-Mbps link 80 times,
but only fill the 1-Gbps link 1/12 of one time

## Slide 56: Chapter 1: Roadmap
  What is the Internet?
  Network edge
  Network core
  Delay, Loss, Throughput in networks
  Protocol layers, service models

## Slide 57: Protocol “Layers”
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing structure of network?
…. or at least our discussion of networks?

## Slide 58: Protocol “Layers”
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing structure of network?
…. or at least our discussion of networks?

## Slide 59: Organization of air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 60: Layering of airline functionality
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing

## Slide 61: Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 62: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of packets from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 63: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 64
The OSI 7-layer Model
OSI – Open Systems Interconnection
OSI Architecture

## Slide 65: Description of Layers
Physical Layer
  Handles the transmission of raw bits over a communication link
Data Link Layer
  Collects a stream of bits into a larger aggregate called a frame
  Network adaptor along with device driver in OS implement the protocol in this layer
  Frames are actually delivered to hosts
Network Layer
  Handles routing among nodes within a packet-switched network
  Unit of data exchanged between nodes in this layer is called a packet
  The lower three layers are implemented on all network nodes

## Slide 66: Description of Layers
Transport Layer
  Implements a process-to-process channel
  Unit of data exchanges in this layer is called a message
Session Layer
  Provides a name space that is used to tie together the potentially different transport streams that are part of a single application
Presentation Layer
  Concerned about the format of data exchanged between peers
Application Layer
  Standardize common type of exchanges
  The transport layer and the higher layers typically run only on end-hosts and not on the intermediate switches and routers

## Slide 67: Network Architecture
Example of a layered network system

## Slide 68: Internet Architecture
Internet Protocol Graph
Alternative view of the Internet architecture. The “Network” layer shown here is sometimes referred to as the “sub-network” or “link” layer.

## Slide 69
This course: Top-Down or Bottom-up?
1
2
3
4