## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 1115
CMSC 417 : Spring 2020
Topic: Internetworking
(Textbook chapter 3)

## Slide 2
One topic continued from the last lecture (overview of networks)

## Slide 3: Chapter 1: Roadmap
  What is the Internet?
  Network edge
  Network core
  Delay, Loss, Throughput in networks
  Protocol layers, service models

## Slide 4: Protocol “Layers”
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing structure of network?
…. or at least our discussion of networks?

## Slide 5: Layering of airline functionality
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing

## Slide 6: Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 7: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of packets from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 8: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 9
The OSI 7-layer Model
OSI – Open Systems Interconnection
OSI Architecture

## Slide 10: Description of Layers
Physical Layer
  Handles the transmission of raw bits over a communication link
Data Link Layer
  Collects a stream of bits into a larger aggregate called a frame
  Network adaptor along with device driver in OS implement the protocol in this layer
  Frames are actually delivered to hosts
Network Layer
  Handles routing among nodes within a packet-switched network
  Unit of data exchanged between nodes in this layer is called a packet
  The lower three layers are implemented on all network nodes

## Slide 11: Description of Layers
Transport Layer
  Implements a process-to-process channel
  Unit of data exchanges in this layer is called a message
Session Layer
  Provides a name space that is used to tie together the potentially different transport streams that are part of a single application.
Presentation Layer
  Concerned about the format of data exchanged between peers (data formats, data encryption)
Application Layer
  Standardize common type of exchanges
  The transport layer and the higher layers typically run only on end-hosts and not on the intermediate switches and routers

## Slide 12: Network Architecture
Example of a layered network system

## Slide 13: Internet Architecture
Internet Protocol Graph
Alternative view of the Internet architecture. The “Network” layer shown here is sometimes referred to as the “sub-network” or “link” layer.

## Slide 14
This course: Top-Down or Bottom-up?
1
2
3
4

## Slide 15
Internetworking

## Slide 16
Connection between hosts
1. Addressing
– Unique identifier for global addressing
– Link name for neighbors
2. Forwarding
-- Switching packets between links
3. Routing
-- Determining paths between hosts

## Slide 17
Connection between hosts

## Slide 18
Connection between hosts
1. Addressing
– Unique identifier for global addressing
– Link name for neighbors
2. Forwarding
-- Switching packets between links
3. Routing
-- Determining paths between hosts

## Slide 19: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets will traverse in going from given initial source host to given final destination host
“good”: least “cost”, “fastest”, “least congested”

## Slide 20: Graph abstraction of the network
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
aside: graph abstraction is useful in other network contexts, e.g.,
P2P, where N is set of peers and E is set of TCP connections

## Slide 21: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or related to congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path

## Slide 22: Routing
  For a simple network, we can calculate all shortest paths and load them into some nonvolatile storage on each node.
  Such a static approach has several shortcomings
    It does not deal with node or link failures
    It does not consider the addition of new nodes or links
    It implies that edge costs cannot change
  What is the solution?
    Need a distributed and dynamic protocol
    Two main classes of protocols
      Distance Vector
      Link State

## Slide 23
Distance Vector Routing

## Slide 24: Distance Vector
Each node constructs a one dimensional array (a vector) containing the “distances” (costs) to all other nodes and distributes that vector to its immediate neighbors
Starting assumption is that each node knows the cost of the link to each of its directly connected neighbors

## Slide 25
A
B
D
C
E
7
11
4
15
5
13
19
Distance Vector Routing: An example

## Slide 26
A
B
D
C
E
7
11
4
15
5
13
19
Dest | Cost | N. Hop
Routing table at Node A
Distance Vector Routing: An example

## Slide 27
A
B
D
C
E
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Routing table at Node A
Distance Vector Routing: An example
Know thy neighbors !!
How?

## Slide 28
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | ∞ | --
B | ∞ | --
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | ∞ | --
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 0
7
11
4
15
5
13
19

## Slide 29
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | ∞ | --
B | ∞ | --
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | ∞ | --
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 0
7
11
4
15
5
13
19
Let your neighbors know what you know!!

## Slide 30
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | ∞ | --
B | ∞ | --
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | ∞ | --
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19
Update your routing table, if required!!

## Slide 31
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19

## Slide 32
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19

## Slide 33
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19

## Slide 34
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19

## Slide 35
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19

## Slide 36
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 1
7
11
4
15
5
13
19
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
When will a node send routing updates to its neighbors?

## Slide 37: Routing updates
Two circumstances when a node sends out routing advertisements:
Periodic update: Automatically after some time. Why?
2) Triggered update: Whenever an event makes a node to change its routing table (e.g., link fail or a new message from a neighbor).

## Slide 38
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 2
7
11
4
15
5
13
19
Node A: No Updates
Node B: No Updates
Node C: No Updates
Node D: No Updates
Node E: No Updates
Convergence

## Slide 39: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
v
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y

## Slide 40: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum is next
hop in shortest path, used in forwarding table
B-F equation says:

## Slide 41: Distance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 42: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)

## Slide 43: Distance vector algorithm
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
each node: