## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2023
Topic: Internetworking: ARP, ICMP, VPN
(Textbook chapter 3)

## Slide 2: Internet Control Message Protocol (ICMP)

## Slide 3: Internet Control Message Protocol (ICMP)
Defines a collection of error messages that are sent back to the source host whenever a router or host is unable to process an IP datagram successfully
  Destination host unreachable due to link /node failure
  Reassembly process failed
  TTL had reached 0 (so datagrams don't cycle forever)
  IP header checksum failed
ICMP-Redirect
  From router to a source host
  With a better route information

## Slide 4
ICMP message types

## Slide 5
Ping example

## Slide 6
Traceroute : An unintuitive application using ICMP

## Slide 7
Traceroute example

## Slide 8
Traceroute : An unintuitive application

## Slide 9: Virtual Networks and Tunnels

## Slide 10
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Untrusted/Shared network

## Slide 11
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
Untrusted/Shared network

## Slide 12
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
New IP Header Source: Gateway-A Dest: Gateway-A
IP Header
Data
Encapsulation
Untrusted/Shared network

## Slide 13
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
New IP Header Source: Gateway-A Dest: Gateway-A
IP Header
Data
Decapsulation
New IP Header Source: Gateway-A Dest: Gateway-A
IP Header
Data
Untrusted/Shared network

## Slide 14
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
IP Header
Data
Untrusted/Shared network

## Slide 15
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
New IP Header Source: Gateway-A Dest: Gateway-A
IP Header
Data
New IP Header Source: Gateway-A Dest: Gateway-A
IP Header
Data
Encryption/Decryption
Untrusted/Shared network

## Slide 16
Trusted network (Site A)
Trusted network (Site B)
Untrusted/Shared network
Gateway A
Gateway B
Virtual Tunnel
Virtual Private Network
(VPN)

## Slide 17
Why do we need virtual networks or tunnels?
1. Security
2. Special capabilities between routers (e.g., multicast)
3. Supporting heterogeneity

## Slide 18
Why do we need virtual networks or tunnels?
1. Security
2. Special capabilities between routers (e.g., multicast)
3. Supporting heterogeneity
Disadvantages:
1. Increases packet length
a) Wastage of bandwidth
b) More processing
c) Fragmentation
2. Increases management cost

## Slide 19: IPv6
1) Address and packet format
2) Unicast, Multicast, Anycast addressing
3) IPV4 and IPV6 coexistence

## Slide 20: IPv6: Address and packet format
Pic courtesy: https://techhub.hpe.com

## Slide 21: IPv6: Unicast, Multicast, Anycast addressing

## Slide 22: IPv6: Unicast, Multicast, Anycast addressing
IP: Anycast example

## Slide 23: IPv4 and IPv6 Co-existence

## Slide 24: IPv4 and IPv6 Co-existence

## Slide 25
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2023
Topic: Transport Layer Protocols (UDP, TCP)
(Textbook chapter 5)

## Slide 27
Transport layer: Two perspective
(1) Abstraction of clients. (machines/networks/processes)
(2) Abstraction of services.

## Slide 28
(1) Abstraction of clients

## Slide 29
Connection between processes

## Slide 30
Implementation of networking algorithms

## Slide 31: Transport Protocols
Logical communication between processes
  Sender divides a message into segments
  Receiver reassembles segments into message
Transport services
  (De)multiplexing packets
  Detecting corrupted data
  Optionally: reliable delivery, flow control, …

## Slide 32: Two Basic Transport Features
Demultiplexing: port numbers
Error detection: checksums
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
OS
Client
IP
payload
detect corruption

## Slide 33: Multiplexing/demultiplexing
application
transport
network
link
physical
P1
application
transport
network
link
physical
application
transport
network
link
physical
P2
P3
P4
P1
host 1
host 2
host 3
= process
= socket
delivering received segments
to correct socket
Demultiplexing at rcv host:
gathering data from multiple
sockets, enveloping data with
header (later used for
demultiplexing)
Multiplexing at send host:

## Slide 34: How demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries 1 transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format
Analogous to airport shuttles
Shuttles MUX passengers and take them
to downtown -- DeMUX at different locations

## Slide 35
Connection-less mux/demux:
- User Datagram Protocol (UDP)
Connection-oriented mux/demux:
- Transmission Control Protocol (TCP)

## Slide 36: Connectionless demultiplexing
Create sockets with port numbers:
DatagramSocket mySocket1 = new DatagramSocket(99111);
DatagramSocket mySocket2 = new DatagramSocket(99222);
UDP socket identified by two-tuple:
(dest IP address, dest port number)
When host receives UDP segment:
  checks destination port number in segment
  directs UDP segment to socket with that port number
IP datagrams with different source IP addresses and/or source port numbers directed to same socket

## Slide 37: Connectionless demux (cont)
DatagramSocket serverSocket = new DatagramSocket(6428);
Client
IP:B
P2
client
IP: A
P1
P1
P3
server
IP: C
SP: 6428
DP: 9157
SP: 9157
DP: 6428
SP: 6428
DP: 5775
SP: 5775
DP: 6428
SP provides “return address”

## Slide 38: Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
recv host uses all four values to direct segment to appropriate socket
Server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
Web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request

## Slide 39: Connection-oriented demux (cont)
Client
IP:B
P1
client
IP: A
P1
P2
P4
server
IP: C
SP: 9157
DP: 80
SP: 9157
DP: 80
P5
P6
P3
D-IP:C
S-IP: A
D-IP:C
S-IP: B
SP: 5775
DP: 80
D-IP:C
S-IP: B
= process
= socket

## Slide 40: Connection-oriented demux: Threaded Web Server
Client
IP:B
P1
client
IP: A
P1
P2
server
IP: C
SP: 9157
DP: 80
SP: 9157
DP: 80
P4
P3
D-IP:C
S-IP: A
D-IP:C
S-IP: B
SP: 5775
DP: 80
D-IP:C
S-IP: B
= process
= socket

## Slide 41
(2) Abstraction of services

## Slide 42: IP Protocol Stack: Key Abstractions
Transport layer is where we “pay the piper”
  Provide applications with good abstractions
  Without support or feedback from the network
Best-effort local packet delivery
Best-effort global packet delivery
Reliable streams
Applications
Messages
Link
Network
Transport
Application

## Slide 43: End-to-end Protocols
Common properties that a transport protocol can be expected to provide
  Guarantees message delivery
  Delivers messages in the same order they were sent
  Delivers at most one copy of each message
  Supports arbitrarily large messages
  Supports synchronization between the sender and the receiver
  Allows the receiver to apply flow control to the sender
  Supports multiple application processes on each host

## Slide 44: End-to-end Protocols
Typical limitations of the network on which transport protocol will operate
  Drop messages/Packet loss
  Reorder messages/Out of order delivery
  Deliver duplicate copies of a given message
  Limit messages to some finite size
  Deliver messages after an arbitrarily long delay

## Slide 45: End-to-end Protocols
Challenge for Transport Protocols
  Develop algorithms that turn the less-than-desirable properties of the underlying network into the high level of service required by application programs

## Slide 48: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out of order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
Why is there a UDP?
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small segment header
no congestion control: UDP can blast away as fast as desired

## Slide 49: UDP: more
often used for streaming multimedia apps
  loss tolerant
  rate sensitive
other UDP uses
  DNS
  SNMP
reliable transfer over UDP: add reliability at application layer
  application-specific error recovery!
source port #
dest port #
32 bits
Application
data
(message)
UDP segment format
length
checksum
Length, in
bytes of UDP
segment,
including
header

## Slide 50: UDP checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later ….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment

## Slide 51: User Datagram Protocol (UDP)
Datagram messaging service
  Demultiplexing: port numbers
  Detecting corruption: checksum
Lightweight communication between processes
  Send and receive messages
  Avoid overhead of ordered, reliable delivery
SRC port
DST port
checksum
length
DATA

## Slide 52
Recall encapsulation

## Slide 53: Advantages of UDP
Fine-grain control
  UDP sends as soon as the application writes
No connection set-up delay
  UDP sends without establishing a connection
No connection state
  No buffers, parameters, sequence #s, etc.
Small header overhead
  UDP header is only eight-bytes long

## Slide 54: Popular Applications That Use UDP
Multimedia streaming
  Retransmitting packets is not always worthwhile
  E.g., phone calls, video conferencing, gaming, IPTV
Simple query-response protocols
  Overhead of connection establishment is overkill
  E.g., Domain Name System (DNS), DHCP, etc.
“Address for www.cnn.com?”
“12.3.4.15”

## Slide 55
What are the features of a ‘best effort’ network?
Packet loss
Out of order delivery
Multiple copies
Delay variations
A non-zero probability of packet delivery

## Slide 56
What are the expectations from a reliable packet delivery system?
Guaranteed delivery
Ordered delivery
At-most one copy of the message
(any or all of the above)