## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2023
Topics:
A) TCP details (Textbook chapter 6)
B) Link layer: Introduction, Ethernet (Textbook chapter 2)

## Slide 2
TCP Congestion Control
Should TCP increment CWND during Dup-ACKs?

## Slide 3: Revisiting Dup ACKs
13
14
15
16
17
18
X
14
14
14
14
14
19
STHRES
CWND
TX
RX
<Open>
19
20
6
6
N/A
14
21
Notes: After FR/FR, when CA is entered, cwnd is half of the window when lost was detected.
So the effect of lost is halving the window.
[Source: RFC 2581, Fall & Floyd, “Simulation based Comparison of Tahoe, Reno, and SACK TCP”]

## Slide 4: Revisiting Dup ACKs
13
14
15
16
17
18
X
14
14
14
14
?
STHRES
CWND
TX
RX
<Open>
6
6
N/A
What if there are multiple losses in an RTT?
X
19
20
14
21
Notes: After FR/FR, when CA is entered, cwnd is half of the window when lost was detected.
So the effect of lost is halving the window.
[Source: RFC 2581, Fall & Floyd, “Simulation based Comparison of Tahoe, Reno, and SACK TCP”]

## Slide 5
TCP Selective ACK (SACK): RFC 2018
https://www.rfc-editor.org/rfc/rfc2018

## Slide 6
Slides courtesy: https://cseweb.ucsd.edu/classes/wi01/cse222/lectures/attack-18.pdf

## Slide 20
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2023
Topic: Link layer
(Textbook chapter 2)

## Slide 21
Protocol Layers
Notes: Picture Courtesy : https://microchipdeveloper.com/tcpip:tcp-ip-five-layer-model

## Slide 22: Link = Medium + Adapters

## Slide 23: What is a Link?
Communication Medium
Network Adapter

## Slide 24
Ripple: Communicating through Physical Vibrations
NSDI 2015
Vibration as medium

## Slide 26
Motion sensor
(accelerometer)
Vibration motor
Notes: Now, what could be the “RECEIVER” for such vibrations?
Observe that almost all mobile devices today have a motion sensor called … ACCELEROMETERS

## Slide 27
Motion sensor
(accelerometer)
Vibration motor
Notes: Thus, if the vibrating transmitter comes in CONTACT with the accelerometer … by literally TOUCHING the accelerometer … then the accelerometer can SENSE the vibrations and DECODE the data bits from it.
We have built such vibratory transmitters inside smartwatches and finger rings.
When the human finger touches the accelerometer … the vibration flows the the finger bone … and the data is transferred.
Of course, the human does not feel anything at all …

## Slide 28
Light as medium: LiFi

## Slide 29: Adaptors Communicating
Sending side
  Encapsulates packet in a frame
  Adds error checking bits, flow control, etc.
Receiving side
  Looks for errors, flow control, etc.
  Extracts datagram and passes to receiving node
sending
node
frame
receiving
node
packet
frame
adapter
adapter
link layer protocol
packet

## Slide 32: Link Layer Addresses (Recap) (Discussed earlier in the context of ARP)

## Slide 33: ARP protocol
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 34: As an Aside: Promiscuous Mode
Normal adapter: receives frames sent to
  The local MAC address
  Broadcast address FF-FF-FF-FF-FF-FF
Promiscuous mode
  Receive everything, independent of destination MAC
Useful for packet sniffing
  Network monitoring
  E.g., wireshark, tcpdump

## Slide 35: Why Not Just Use IP Addresses?
Links can support any network protocol
  Not just for IP (e.g., IPX, Appletalk, X.25, …)
  Different addresses on different kinds of links
An adapter may move to a new location
  So, cannot simply assign a static IP address
  Instead, must reconfigure the adapter’s IP address
Must identify the adapter during bootstrap
  Need to talk to the adapter to assign it an IP address

## Slide 37: Collisions
Single shared broadcast channel
  Avoid having multiple nodes speaking at once
  Otherwise, collisions lead to garbled data
71-65-F7-2B-08-53
1A-2F-BB-76-09-AD
0C-C4-11-6F-E3-98

## Slide 38: Multi-Access Protocol
Divide the channel into pieces
  In time
  In frequency

## Slide 39: Multi-Access Protocol
Time Division Multiple Access
Frequency Division Multiple Access
Code Division Multiple Access

## Slide 40: Multi-Access Protocol
Divide the channel into pieces
  In time
  In frequency
Take turns
  Pass a token for the right to transmit
Defer action
  Let collisions happen
  … and detect and recover from them
Carrier Sense Multiple Access

## Slide 41: Like Human Conversation…
Carrier sense
  Listen before speaking
  …and don’t interrupt!
Collision detection
  Detect simultaneous talking
  … and shut up!
Random access
  Wait for a random period of time
  … before trying to talk again!

## Slide 42: Carrier Sense Multiple Access (CSMA)

## Slide 43: Carrier Sense Multiple Access (CSMA)
Listen for other senders
  Then transmit your data
Collisions can still occur
  Propagation delay
  Wasted transmission

## Slide 44
CSMA: The time-space graph of collision

## Slide 45
CSMA: The time-space graph of collision

## Slide 46: CSMA: The time-space graph of collision

## Slide 47: CSMA: The time-space graph of collision
The time-space region of collision

## Slide 48: Comparing the Three Approaches
Divide the channel into pieces
  In time
  In frequency
Take turns
  Pass a token for the right to transmit
Punt
  Let collisions happen
  … and detect and recover from them
Carrier Sense Multiple Access

## Slide 49: Comparing the Three Approaches
Channel partitioning
  Efficient and fair at high load
  Inefficient at low load
“Taking turns”
  Eliminates empty slots without collisions
  Vulnerable to failures (e.g. lost token)
Random access
  Efficient at low load
  Collision overhead at high load

## Slide 50
Automatic Repeat request
Flow control
Not implemented in wired LAN (e.g. Ethernet)

## Slide 51: Ethernet

## Slide 52: Ethernet
Dominant wired LAN technology
First widely used LAN technology
Kept up with speed race: 10 Mbps – 40 Gbps
Metcalfe’s
Ethernet
sketch

## Slide 54: Ethernet Uses CSMA/CD
Carrier Sense: wait for link to be idle
  Channel idle: start transmitting
  Channel busy: wait until idle
  A strategy is p-persistent if, after waiting for the line to clear, the sender sends with probability p≤1.
Collision Detection: listen while transmitting
  No collision: transmission is complete
  Collision: abort transmission, and send jam signal
Random Access: exponential back-off
  After collision, wait random time before trying again
  After mth collision, choose K randomly from {0, …, 2m-1}
  … and wait for K*512 bit times before trying again

## Slide 55: CSMA/CD Collision Detection
Detect collision
  Abort transmission
  Jam the link
Wait random time
  Transmit again
Hard in wireless
  Must receive data while transmitting

## Slide 56: CSMA/CD Collision Detection
Without collision detection
With collision detection and abort

## Slide 58
Collision does not happen like this. :-D

## Slide 59
Collision happens when both packet overlaps at the receiver.

## Slide 60
Preparing for the worst-case scenario of collision
Collision happens when both packet overlaps at the receiver.

## Slide 61
Preparing for the worst-case scenario of collision

## Slide 62
Preparing for the worst-case scenario of collision

## Slide 63
Preparing for the worst-case scenario of collision

## Slide 64
Preparing for the worst-case scenario of collision
The packet should be at least for 2d seconds long so that the sender can get the notification of the collision (through the jamming signal)

## Slide 65
Preparing for the worst-case scenario of collision
The packet should be at least for 2d seconds long so that the sender can get the notification of the collision (through the jamming signal)
Transmission time >= 2*propagation time

## Slide 66
Preparing for the worst-case scenario of collision
Formula for minimum packet size (P) or maximum length (L)