## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2023
Topic: Link layer: WiFi, Mobility, BGP
(Textbook chapter 2, 4)

## Slide 2: WiFi: IEEE 802.11 Wireless LANs
LAN Architecture
MAC protocol
Frame structure
Advanced features

## Slide 3: CSMA: Carrier Sense, Multiple Access
Multiple access: channel is shared medium
  Station: wireless host or access point
  Multiple stations may want to transmit at same time
Carrier sense: sense channel before sending
  Station doesn’t send when channel is busy
  To prevent collisions with ongoing transfers
  But, detecting ongoing transfers isn’t always possible
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 4: CSMA/CA: Collision Avoidance (CA), Not Collision Detection (CD)
Collision detection in wired Ethernet
  Station listens while transmitting
  Detects collision with other transmission
  Aborts transmission and tries sending again

## Slide 5: CSMA/CA: Collision Avoidance (CA), Not Collision Detection (CD)
Collision detection in wired Ethernet
  Station listens while transmitting
  Detects collision with other transmission
  Aborts transmission and tries sending again
Problem #1: cannot detect all collisions
  Hidden terminal problem
  Fading

## Slide 6: CSMA/CA: Collision Avoidance, Not Detection
Collision detection in wired Ethernet
  Station listens while transmitting
  Detects collision with other transmission
  Aborts transmission and tries sending again
Problem #1: cannot detect all collisions
  Hidden terminal problem
  Fading
Problem #2: Can not listen while sending
  Strength of received signal is much smaller
  Expensive to build hardware that detects collisions
So, 802.11 does collision avoidance, not detection

## Slide 7: Hidden Terminal Problem
A and C can’t see each other, both send to B
Occurs since 802.11 relies on physical carrier sensing, which is susceptible to hidden terminal problem
C
B
A

## Slide 8: Virtual carrier sensing
First exchange control frames before transmitting data
  Sender issues “Request to Send” (RTS), incl. length of data
  Receiver responds with “Clear to Send” (CTS)
If sender sees CTS, transmits data (of specified length)
If other node sees CTS, will idle for specified period
If other node sees RTS but not CTS, free to send

## Slide 9: Hidden Terminal Problem
A and C can’t see each other, both send to B
RTS/CTS can help
  Both A and C would send RTS that B would see first
  B only responds with one CTS (say, echo’ing A’s RTS)
  C detects that CTS doesn’t match and won’t send
C
B
A

## Slide 10
Virtual carrier sensing (RTS-CTS)
A
B
C
D

## Slide 11
Virtual carrier sensing (RTS-CTS)

## Slide 12: Exposed Terminal Problem
B sending to A, C wants to send to D
As C receives B’s packets, carrier sense would prevent it from sending to D, even though wouldn’t interfere
RTS/CTS can help
  C hears RTS from B, but not CTS from A
  C knows it’s transmission will not interfere with A
  C is safe to transmit to D
C
B
A
D

## Slide 13: Impact on Higher-Layer Protocols
Wireless and mobility change path properties
  Wireless: higher packet loss, not from congestion
  Mobility: transient disruptions, and changes in RTT
Logically, impact should be minimal …
  Best-effort service model remains unchanged
  TCP and UDP can (and do) run over wireless, mobile
But, performance definitely is affected
  TCP treats packet loss as a sign of congestion
  TCP tries to estimate the RTT to drive retransmissions
  TCP does not perform well under out-of-order packets
Internet not designed with these issues in mind

## Slide 14: WiFi: IEEE 802.11 Wireless LANs
LAN Architecture
MAC protocol
Frame structure
Advanced features

## Slide 15
WiFi: IEEE 802.11 Frame
Notes: Address 4 is used for Ad-hoc mode.

## Slide 16
802.11 Frame: The secret of Address-3

## Slide 17
802.11 Frame: The secret of Address-3
Case 1: Router R1 send data to host H1

## Slide 18
802.11 Frame: The secret of Address-3
Case 1: Router R1 send data to host H1
(1) R1 knows H1’s IP addr, runs ARP to get the MAC addr.

## Slide 19
802.11 Frame: The secret of Address-3
Case 1: Router R1 send data to host H1
(2) R1 encapsulates the data in Ethernet frame.
Source addr: R1’s MAC addr
Dest. addr: H1’s MAC addr

## Slide 20
802.11 Frame: The secret of Address-3
Case 1: Router R1 send data to host H1
(3) AP converts the Ethernet (802.3) frame to WiFi frame (802.11).
Addr 1: H1’s MAC addr
Addr 2: AP’s MAC addr
Addr 3: R1’s MAC addr

## Slide 21
802.11 Frame: The secret of Address-3
Case 1: Router R1 send data to host H1
(4) H1 can determine that the frame has come from R1 by checking Addr-3 field.

## Slide 22
802.11 Frame: The secret of Address-3
Case 2: Host H1 responds by sending packet to Router R1

## Slide 23
802.11 Frame: The secret of Address-3
Case 2: Host H1 responds by sending packet to Router R1
H1 creates a WiFi frame.
Addr 1: AP’s MAC addr
Addr 2: H1’s MAC addr
Addr 3: R1’s MAC addr

## Slide 24
802.11 Frame: The secret of Address-3
Case 2: Host H1 responds by sending packet to Router R1
(2) AP can determine that the frame should be forwarded to R1 by checking Addr-3 field.

## Slide 25
802.11 Frame: The secret of Address-3
Case 2: Host H1 responds by sending packet to Router R1
(3) AP converts the WiFi (802.11) frame to Ethernet frame (802.3).
Source addr : H1’s MAC addr
Dest. addr : R1’s MAC addr

## Slide 26: WiFi: IEEE 802.11 Wireless LANs
LAN Architecture
MAC protocol
Frame structure
Advanced features

## Slide 27: WiFi: Advanced features
1) Rate adaptation
2) Power management

## Slide 28
Award # 2125526

## Slide 29
Notes: Separate systems: donor’s system is not accessible by guest
Speed – donor’s speed should not be affected by the donation

## Slide 30
Cellular Networks

## Slide 31
Mobile
Switching
Center
Public telephone
network
Mobile
Switching
Center
Components of cellular network architecture
connects cells to wired tel. net.
manages call setup
handles mobility
MSC
covers geographical region
base station (BS) analogous to 802.11 AP
mobile users attach to network through BS
air-interface: physical and link layer protocol between mobile and BS
cell
wired network

## Slide 32: Cellular networks: the first hop
Two techniques for sharing mobile-to-BS radio spectrum
combined FDMA/TDMA: divide spectrum in frequency channels, divide each channel into time slots
CDMA: code division multiple access
frequency
bands
time slots

## Slide 33
Picture1: https://www.brandsynario.com/the-evolution-of-gs-generation-networks/
Notes: Picture from: https://www.brandsynario.com/the-evolution-of-gs-generation-networks/

## Slide 34
Picture1: https://www.brandsynario.com/the-evolution-of-gs-generation-networks/
Picture2: http://kaaale.blogspot.com/2019/02/the-evolution-of-cellular-mobile.html
Notes: Picture from: https://www.brandsynario.com/the-evolution-of-gs-generation-networks/

## Slide 35
2G (voice) network architecture

## Slide 36
3G (voice+data) network architecture
Key insight: new cellular data
network operates in parallel
(except at edge) with existing
cellular voice network
voice network unchanged in core
data network operates in parallel

## Slide 37
3G (voice+data) network architecture

## Slide 38
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Public
Internet
G
3G versus 4G LTE network architecture
GGSN
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
Evolved Packet Core
(EPC)
MME
Public
Internet
P-GW
G
S-GW
G
HSS
3G
4G-LTE

## Slide 39
4G: differences from 3G
all IP core: IP packets tunneled (through core IP network) from base station to gateway
no separation between voice and data – all traffic carried over IP core to gateway
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
Evolved Packet Core
(EPC)
Public
Internet
P-GW
G
S-GW
G
UE
(user element)
eNodeB
(base station)
Packet data
network
Gateway
(P-GW)
Serving
Gateway
(S-GW)
data
MME
HSS
Mobility
Management
Entity (MME)
control
Home Subscriber
Server(HSS)
(like HLR+VLR)

## Slide 40
5G cellular networks

## Slide 41: Mobility in Wireless Networks

## Slide 42: What is mobility?
spectrum of mobility, from the network perspective:
no mobility
high mobility
mobile wireless user,
using same access
point
mobile user, passing through multiple access point while maintaining ongoing connections (like cell phone)
mobile user, connecting/ disconnecting from network using DHCP.

## Slide 43: Mobility: vocabulary
wide area network
home network: “home” of mobile
(e.g., 128.119.40/24)
permanent address: address in home network, can always be used to reach mobile
e.g., 128.119.40.186
home agent: entity that will perform mobility functions on behalf of mobile, when mobile is remote

## Slide 44: Mobility: more vocabulary
wide area network
care-of-address: address in visited network.
(e.g., 79,129.13.2)
visited network: network in which mobile currently resides (e.g., 79.129.13/24)
permanent address: remains constant (e.g., 128.119.40.186)
foreign agent: entity in visited network that performs mobility functions on behalf of mobile.
correspondent: wants to communicate with mobile

## Slide 45: Mobility: approaches
let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
let end-systems handle it:
  indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  direct routing: correspondent gets foreign address of mobile, sends directly to mobile

## Slide 46: Mobility: approaches
let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
let end-systems handle it:
  indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  direct routing: correspondent gets foreign address of mobile, sends directly to mobile
not
scalable
to millions of
mobiles

## Slide 47: Mobility: registration
wide area network
end result:
foreign agent knows about mobile
home agent knows location of mobile
home network
visited network
1
mobile contacts foreign agent on entering visited network
2
foreign agent contacts home agent home: “this mobile is resident in my network”

## Slide 48: Mobility via indirect routing
wide area network
home
network
visited
network
3
2
1
correspondent addresses packets using home address of mobile
home agent intercepts packets, forwards to foreign agent
foreign agent receives packets, forwards to mobile

## Slide 49
Packet encapsulation

## Slide 50: Mobility via indirect routing
wide area network
home
network
visited
network
3
2
4
1
correspondent addresses packets using home address of mobile
home agent intercepts packets, forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 51: Indirect Routing: comments
mobile uses two addresses:
  permanent address: used by correspondent (hence mobile location is transparent to correspondent)
  care-of-address: used by home agent to forward datagrams to mobile
foreign agent functions may be done by mobile itself
triangle routing: correspondent-home-network-mobile
  inefficient when
  correspondent, mobile
  are in same network

## Slide 52: Mobility via direct routing
1
2
3
4
home
network
visited
network
correspondent requests, receives foreign address of mobile
correspondent forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 53
Mobility through multiple foreign networks

## Slide 54: Inter-domain routing

## Slide 55
Our (improved) view of the Internet

## Slide 56: Making routing scalable
scale: with billions of destinations:
Can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice

## Slide 57: Autonomous Routing Domains
A collection of physical networks glued together
using IP, that have a unified administrative
routing policy.
Campus networks
Corporate networks
ISP Internal networks
…

## Slide 58: Autonomous Systems (ASes)
An autonomous system is an autonomous routing domain
that has been assigned an Autonomous System Number (ASN).
RFC 1930: Guidelines for creation, selection,
and registration of an Autonomous System
… the administration of an AS appears to other ASes to
have a single coherent interior routing plan and presents a
consistent picture of what networks are reachable through it.

## Slide 59: AS Numbers (ASNs)
ASNs are 16 and 32 bit values.
64512 through 65535 are “private”
Genuity: 1
MIT: 3
Harvard: 11
UC San Diego: 7377
AT&T: 7018, 6341, 5074, …
UUNET: 701, 702, 284, 12199, …
Sprint: 1239, 1240, 6211, 6242, …
…
ASNs represent units of routing policy
Currently over 11,000 in use.

## Slide 60: Interdomain routing = routing between autonomous systems
AS 701
AS 1239
AS 7018
UUNet
AT&T
Common Backbone
Sprint
Fidelity Investments
AT&T Research
207.104.168.0/24
AS 6431
AS 11040
192.223.184.0/21
134.244.0.0/16

## Slide 61: Internet approach to scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
inter-AS routing
routing among AS’es
gateways perform inter-domain routing (as well as intra-domain routing)
intra-AS routing
routing among hosts, routers in same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocol
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es

## Slide 62: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations

## Slide 63
Intra-AS Routing

## Slide 64: Intra-AS Routing
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary for decades, until 2016)

## Slide 65: OSPF (Open Shortest Path First)
“open”: publicly available
uses link-state algorithm
  link state packet dissemination
  topology map at each node
  route computation using Dijkstra’s algorithm
router floods OSPF link-state advertisements to all other routers in entire AS
  carried in OSPF messages directly over IP (rather than TCP or UDP
  link state: for each attached link

## Slide 66: OSPF “advanced” features
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different ToS (e.g., satellite link cost set low for best effort ToS; high for real-time ToS)
integrated uni- and multi-cast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.

## Slide 67: Hierarchical OSPF
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers

## Slide 68: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’es.

## Slide 69: Inter-AS tasks
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

## Slide 70
Inter-AS Routing

## Slide 71: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy
allows subnet to advertise its existence to rest of Internet: “I am here”

## Slide 72: eBGP, iBGP connections
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
gateway routers run both eBGP and iBGP protocols

## Slide 73: BGP basics
when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X

## Slide 74: BGP basics
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1

## Slide 75: BGP basics
when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection.
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X

## Slide 76: Path attributes and BGP routes
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
Policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other other neighboring ASes

## Slide 77: BGP path advertisement
Based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
Based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c

## Slide 78: BGP path advertisement
AS1 gateway router 1c learns path AS2,AS3,X from 2a
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
Based on policy, AS1 gateway router 1c chooses path AS3,X, and advertises path within AS1 via iBGP

## Slide 79: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 80: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1d learn about dest X via iBGP from 1c: “path to X goes through 1c”
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
AS3,X
Q: how does router set forwarding table entry to distant prefix?
1
2
1
2
dest
interface
…
…
X
…
…
1
physical link
local link interfaces
at 1a, 1d

## Slide 81: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1d learn about dest X via iBGP from 1c: “path to X goes through 1c”
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
Q: how does router set forwarding table entry to distant prefix?
dest
interface
…
…
X
…
…
2
1a: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 2
1
2

## Slide 82: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 83: Hot Potato Routing
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS1,AS3,X
OSPF link weights
201
152
112
263

## Slide 84: A dive into the BGP policies

## Slide 85: Nontransit vs. Transit ASes
ISP 1
ISP 2
Nontransit AS
might be a corporate
or campus network.
Could be a “content
provider”
NET A
Traffic NEVER
flows from ISP 1
through NET A to ISP 2
(At least not intentionally!)
IP traffic
Internet Service
providers (often)
have transit
networks