## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2023
Topic: Internetworking
(Textbook chapter 3)

## Slide 2: Chapter 1: Roadmap (cont…)
  What is the Internet?
  Network edge
  Network core
  Delay, Loss, Throughput in networks
  Protocol layers, service models

## Slide 3: Protocol “Layers”
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing structure of network?
…. or at least our discussion of networks?

## Slide 4: Layering of airline functionality
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing

## Slide 5: Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
Can layering be harmful? Give an example.

## Slide 6: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of packets from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 7
The OSI 7-layer Model
OSI – Open Systems Interconnection
OSI Architecture

## Slide 8: Description of Layers
Physical Layer
  Handles the transmission of raw bits over a communication link
Data Link Layer
  Collects a stream of bits into a larger aggregate called a frame
  Network adaptor along with device driver in OS implement the protocol in this layer
  Frames are actually delivered to hosts
Network Layer
  Handles routing among nodes within a packet-switched network
  Unit of data exchanged between nodes in this layer is called a packet
  The lower three layers are implemented on all network nodes

## Slide 9: Description of Layers
Transport Layer
  Implements a process-to-process channel
  Unit of data exchanges in this layer is called a message
Session Layer
  Provides a name space that is used to tie together the potentially different transport streams that are part of a single application.
Presentation Layer
  Concerned about the format of data exchanged between peers (data formats, data encryption)
Application Layer
  Standardize common type of exchanges
  The transport layer and the higher layers typically run only on end-hosts and not on the intermediate switches and routers

## Slide 10: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 11: Network Architecture
Example of a layered network system

## Slide 12: Internet Architecture
Internet Protocol Graph
Alternative view of the Internet architecture. The “Network” layer shown here is sometimes referred to as the “sub-network” or “link” layer.

## Slide 13
This course: Top-Down or Bottom-up?
1
2
3
4

## Slide 14
Internetworking

## Slide 15
Connection between hosts
1. Addressing
– Unique identifier for global addressing
– Link name for neighbors
2. Forwarding
-- Switching packets between links
3. Routing
-- Determining paths between hosts

## Slide 16
Connection between hosts

## Slide 17
Connection between hosts
1. Addressing
– Unique identifier for global addressing
– Link name for neighbors
2. Forwarding
-- Switching packets between links
3. Routing
-- Determining paths between hosts

## Slide 18: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets will traverse in going from given initial source host to given final destination host
“good”: least “cost”, “fastest”, “least congested”

## Slide 19: Graph abstraction of the network
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
aside: graph abstraction is useful in other network contexts, e.g.,
P2P, where N is set of peers and E is set of TCP connections

## Slide 20: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or related to congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path

## Slide 21: Routing
  For a simple network, we can calculate all shortest paths and load them into some nonvolatile storage on each node.
  Such a static approach has several shortcomings
    It does not deal with node or link failures
    It does not consider the addition of new nodes or links
    It implies that edge costs cannot change
  What is the solution?
    Need a distributed and dynamic protocol
    Two main classes of protocols
      Distance Vector
      Link State

## Slide 22
Distance Vector Routing

## Slide 23: Distance Vector
Each node constructs a one-dimensional array (a vector) containing the “distances” (costs) to all other nodes and distributes that vector to its immediate neighbors
Starting assumption is that each node knows the cost of the link to each of its directly connected neighbors

## Slide 24
Advertise:
A router transmits its distance vector to each of its neighbors in a
routing packet.
2. Each router receives and saves the most recently received
distance vector from each of its neighbors.
3. Update:
A router recalculates its distance vector when:
  It receives a distance vector from a neighbor containing
  different information than before.
  b) It discovers that a link to a neighbor has gone down
  (or the cost has changed).
Distance Vector Routing protocol

## Slide 25
A
B
D
C
E
7
11
4
15
5
13
19
Distance Vector Routing: An example

## Slide 26
A
B
D
C
E
7
11
4
15
5
13
19
Dest | Cost | N. Hop
Routing table at Node A
Distance Vector Routing: An example

## Slide 27
A
B
D
C
E
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Routing table at Node A
Distance Vector Routing: An example
Know thy neighbors !!
How?

## Slide 28
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | ∞ | --
B | ∞ | --
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | ∞ | --
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 0
7
11
4
15
5
13
19

## Slide 29
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | ∞ | --
B | ∞ | --
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | ∞ | --
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 0
7
11
4
15
5
13
19
Let your neighbors know what you know!!

## Slide 30
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | ∞ | --
B | ∞ | --
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | ∞ | --
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 1
7
11
4
15
5
13
19
Update your routing table, if required!!

## Slide 31
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Round: 1
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Let’s consider updates at node A

## Slide 32
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19

## Slide 33
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Round: 1
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Let’s consider updates at node A

## Slide 34
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Round: 1
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Let’s consider updates at node A

## Slide 35
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Round: 1
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Let’s consider updates at node A

## Slide 36
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19

## Slide 37
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19
When will a node send routing advertisements to its neighbors?

## Slide 38
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 1
7
11
4
15
5
13
19
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
When will a node send routing advertisements to its neighbors?

## Slide 39: Routing advertisements
Two circumstances when a node sends out routing advertisements:
Periodic: Automatically after some time. Why?
2) Triggered: Whenever an event makes a node to change its routing table (e.g., link fail or a new message from a neighbor).

## Slide 40
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 2
7
11
4
15
5
13
19
Node A: No Updates
Node B: No Updates
Node C: No Updates
Node D: No Updates
Node E: No Updates
Convergence

## Slide 41: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
v
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y

## Slide 42: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum is next
hop in shortest path, used in forwarding table
B-F equation says:

## Slide 43
Distance vector algorithm
Putting together…
Notes: The code is taken from: https://www.javatpoint.com/distance-vector-routing-algorithm

## Slide 44: Distance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]
Putting together…

## Slide 45: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)

## Slide 46: Distance vector algorithm
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
each node: