## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2023
Topic: Internetworking : IP
(Textbook chapter 3)

## Slide 2
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Example: IP Fragmentation
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packer Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Original Packet
Frag. Pkt #1
Frag. Pkt #2
Frag. Pkt #3

## Slide 3
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Example: IP Reassembly
Data buffer
Header buffer
Data from fgmt 1
Data from fgmt 2
Data from fgmt 3

## Slide 4
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Data buffer
Header buffer
Header from
fgmt 1
(will be updated later)
Example: IP Reassembly
Data from fgmt 1
Data from fgmt 2
Data from fgmt 3

## Slide 5
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Data from fgmt 1
0
64
128
Data from fgmt 2
Data from fgmt 3
Data buffer
Header buffer
Example: IP Reassembly
What if assembly is not possible?
Header from
fgmt 1
(will be updated later)
Data from fgmt 1
Data from fgmt 2
Data from fgmt 3

## Slide 6
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Data buffer
Header buffer
Header from
fgmt 1
(will be updated later)
Example: IP Reassembly
Data from fgmt 1
Data from fgmt 2
Data from fgmt 3
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
Which header fields will be updated
during reassembly?

## Slide 7: Network Addresses

## Slide 8: IP Address (IPv4)
A unique 32-bit number
Identifies an interface (on a host, on a router, …)
Represented in dotted-quad notation
00001100
00100010
10011110
00000101
12
34
158
5
12:34:158:5

## Slide 9: Grouping Related Hosts
The Internet is an “inter-network”
  Used to connect networks together, not hosts
  Need to address a network (i.e., group of hosts)
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
LAN = Local Area Network
WAN = Wide Area Network

## Slide 10: Scalability Challenge
Suppose hosts had arbitrary addresses
  Then every router would need a lot of information
  …to know how to direct packets toward every host
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
5.6.7.8
2.4.6.8
1.2.3.5
5.6.7.9
2.4.6.9
1.2.3.4
1.2.3.5
forwarding table

## Slide 11: Hierarchical Addressing in U.S. Mail
Addressing in the U.S. mail
  Zip code: 08540
  Building: 35 Olden Street
  Room in building: 306
  Name of occupant: Jennifer Rexford
Forwarding the U.S. mail
  Deliver to the post office in the zip code
  Assign to mailman covering the building
  Drop letter into mailbox for building/room
  Give letter to the appropriate person
???

## Slide 12: Hierarchical Addressing: IP Prefixes
Network and host portions (left and right)
00001100
00100010
10011110
00000101
Network (24 bits)
Host (8 bits)
12
34
158
5
(N bits)
(32-N bits)

## Slide 13: Easy to Add New Hosts
No need to update the routers
  E.g., adding a new host 5.6.7.213 on the right
  Doesn’t require adding a new forwarding-table entry
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table
host
5.6.7.213

## Slide 14: Hierarchical Addressing: IP Prefixes
Network and host portions (left and right)
00001100
00100010
10011110
00000101
Network (24 bits)
Host (8 bits)
12
34
158
5
(N bits)
(32-N bits)
N = ?

## Slide 15: “Classes” of networks
The sizes of networks can be different
host
host
host
LAN 1
...
host
host
LAN 2
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
1.2.3.0/24
5.6.7.0/24
forwarding table
Large networks (many hosts)
Fewer such networks exist
Small networks (fewer hosts)
Many such networks exist

## Slide 16: Class-full addressing

## Slide 17
Picture courtesy: https://www.geeksforgeeks.org/introduction-of-classful-ip-addressing/
How can you tell network class from the IP address?

## Slide 18
Picture courtesy: https://www.ictshore.com/free-ccna-course/network-layer-ipv4-addressing/attachment/1013-05-classful_addressing/
What percentage of addresses and allocated to each class?

## Slide 19: Global Addresses
Properties
  globally unique
  hierarchical: network + host
  4 Billion IP address, half are A type, ¼ is B type, and 1/8 is C type
Format
Dot notation
  10.3.2.4
  128.96.33.81
  192.12.69.77

## Slide 20
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Let’s assume we have 4-bit address (instead of 32 bit)
Class A (Half of all possible addresses)
Class B (1/4 of all possible addresses)
Class C (1/8 of all possible addresses)

## Slide 21
0000
0001
0010
0011
0100
0101
0110
0111
Let’s assume we have 4-bit address (instead of 32 bit)
Class A (Half of all possible addresses)
Say, 1 bit for network part = 2 different networks
Say, 2 bits for host part = 4 hosts per network

## Slide 22: Global Addresses
Properties
  globally unique
  hierarchical: network + host
  4 Billion IP address, half are A type, ¼ is B type, and 1/8 is C type
Format
Dot notation
  10.3.2.4
  128.96.33.81
  192.12.69.77

## Slide 23: Classful Addressing
In the olden days, only fixed allocation sizes
  Class A: 0*
    Very large /8 blocks (e.g., MIT has 18.0.0.0/8)
    There can be 126 different class A networks (0 and 127 values are reserved) and (224-2) different hosts (2 values are reserved)
  Class B: 10*
    Large /16 blocks (e.g,. Princeton has 128.112.0.0/16)
  Class C: 110*
    Small /24 blocks (e.g., AT&T Labs has 192.20.225.0/24)
    221 different networks possible, 254 hosts (255 is reserved for broadcast and 0 is reserved)
  Class D: 1110* for multicast groups
  Class E: 11110* reserved for future use
This is why folks use dotted-quad notation!

## Slide 24: IP Datagram Forwarding
Strategy
  every datagram contains destination's address
  if directly connected to destination network, then forward to host
  if not directly connected to destination network, then forward to some router
  forwarding table maps network number into next hop
  each host has a default router
  each router maintains a forwarding table
Example (router R2)

## Slide 25: IP Datagram Forwarding
Algorithm
if (NetworkNum of destination = NetworkNum of one of my interfaces) then
deliver packet to destination over that interface
else
if (NetworkNum of destination is in my forwarding table) then
deliver packet to NextHop router
else
deliver packet to default router
First: find the NetworkNum. How?

## Slide 26: IP Datagram Forwarding
Algorithm
if (NetworkNum of destination = NetworkNum of one of my interfaces) then
deliver packet to destination over that interface
else
if (NetworkNum of destination is in my forwarding table) then
deliver packet to NextHop router
else
deliver packet to default router
For a host with only one interface and only a default router in its forwarding table, this simplifies to
if (NetworkNum of destination = my NetworkNum)then
deliver packet to destination directly
else
deliver packet to default router

## Slide 27: Obtaining a Block of Addresses
Internet Corporation for Assigned Names and Numbers (ICANN)
  Allocates large blocks to Regional Internet Registries
Regional Internet Registries (RIRs)
  E.g., ARIN (American Registry for Internet Numbers)
  Allocates to ISPs and large institutions
Internet Service Providers (ISPs)
  Allocate address blocks to their customers
  Who may, in turn, allocate to their customers…

## Slide 28
Obtaining a Block of Addresses
Your organization: XYZ
Maximum # of hosts is estimated to be 10 millions.
What class of IP address will you request for?
Maximum # of hosts is estimated to be 64K ?
Maximum # of hosts is estimated to be 250?
Maximum # of hosts is estimated to be 100?
Maximum # of hosts is estimated to be 20?
Maximum # of hosts is estimated to be 300?
Maximum # of hosts is estimated to be 66K?

## Slide 29
Problems with the classes of addresses
Wastage of addresses
Bigger tables to look up at routers

## Slide 30: Pre-CIDR (1988-1994): Steep Growth
Growth faster than improvements in equipment capability

## Slide 31: Subnetting

## Slide 32
Router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
223.1.1.6
ISP
The ISP provided the network address space: 223.1.1.X

## Slide 33
Router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
223.1.1.6
ISP
The ISP provided the network address space: 223.1.1.X
223.1.2.X
223.1.3.X

## Slide 34
Router
The ISP provided the network address space: 223.1.1.X
Two separate networks are needed. How can we assign addresses to these “sub” networks?

## Slide 35
Router
The ISP provided the network address space: 223.1.1.X

## Slide 36
Router
The ISP provided the network address space: 223.1.1.X
Use subnetting

## Slide 37
Router
The ISP provided the network address space: 223.1.1.X
11011111.00000001.00000001.XXXXXXX
Use part of the host bits to identify separate subnets.

## Slide 38
Router
The ISP provided the network address space: 223.1.1.X
11011111.00000001.00000001.XXXXXXX
Use part of the host bits to identify separate subnets.
11011111.00000001.00000001.0XXXXXX
11011111.00000001.00000001.1XXXXXX
Subnet mask = 11111111. 11111111. 11111111.10000000

## Slide 39: Subnetting
Add another level to address/routing hierarchy: subnet
Subnet masks define variable partition of host part of class A and B addresses
Subnets visible only within site
“Bitwise and”

## Slide 40: Subnetting
Forwarding Table at Router R1

## Slide 41: Subnetting
Forwarding Table at Router R1
Forwarding Algorithm
D = destination IP address
for each entry < SubnetNum, SubnetMask, NextHop>
  D1 = SubnetMask & D
  if D1 = SubnetNum
    if NextHop is an interface
    deliver datagram directly to destination
    else
    deliver datagram to NextHop (a router)

## Slide 42: Subnetting
Notes
Would use a default router if nothing matches
Not necessary for all ones in subnet mask to be contiguous
Can put multiple subnets on one physical network
Subnets not visible from the rest of the Internet

## Slide 43
Subnets “toy” example

## Slide 44
Address space assigned to you:

## Slide 48: Class-less addressing: CIDR

## Slide 49: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
200.23.16.0–200.23.17.255

## Slide 50: Classless Inter-Domain Routing (CIDR)
IP Address : 12.4.0.0 IP Mask: 255.254.0.0
00001100
00000100
00000000
00000000
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network.
Network number = IP address + Mask
Written as 12.4.0.0/15

## Slide 51: Hierarchical Address Allocation
Hierarchy is key to scalability
  Address allocated in contiguous chunks (prefixes)
  Today, the Internet has about 400,000 prefixes
12.0.0.0/8
12.0.0.0/16
12.254.0.0/16
12.1.0.0/16
12.2.0.0/16
12.3.0.0/16
:
:
:
12.3.0.0/24
12.3.1.0/24
:
:
12.3.254.0/24
12.253.0.0/19
12.253.32.0/19
12.253.160.0/19
:
:
:
:
:

## Slide 52: Classless Addressing
Route aggregation with CIDR

## Slide 53: Separate Forwarding Entry Per Prefix
Prefix-based forwarding
  Map the destination address to matching prefix
  Forward to the outgoing interface
host
host
host
LAN 1
...
host
host
host
LAN
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 54: CIDR Makes Packet Forwarding Harder
Forwarding table may have many matches
  E.g., entries for 201.10.0.0/21 and 201.10.6.0/23
  The IP address 201.10.6.17 would match both!
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2

## Slide 55: Longest Prefix Match Forwarding
Destination-based forwarding
  Packet has a destination address
  Router identifies longest-matching prefix
  Cute algorithmic problem: very fast lookups
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
201.10.6.17
destination
forwarding table
Serial0/0.1
outgoing link

## Slide 56: Pre-CIDR (1988-1994): Steep Growth
Growth faster than improvements in equipment capability

## Slide 57: CIDR (1994-1996): Much Flatter
Efforts to aggregate

## Slide 58: CIDR Growth (1996-1998): Roughly Linear
Good use of aggregation, and peer pressure!

## Slide 59: DotCom Boom (1998-2001): Steep Growth
Internet boom and increased multi-homing

## Slide 60: Long Term (1989-2005): Post-Boom
Today we are up to ~400,000 prefixes

## Slide 61: Getting an IP address: DHCP

## Slide 62: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/…
DHCP: Dynamic Host Configuration Protocol: dynamically get address from a server
  “plug-and-play”

## Slide 63: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network

## Slide 64: DHCP: Dynamic Host Configuration Protocol
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 65: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 66
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 67: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 68: Dynamic Host Configuration Protocol (DHCP)
DHCP server is responsible for providing configuration information to hosts
DHCP server maintains a pool of available addresses
There is at least one DHCP server for an administrative domain (a server or a relay agent per subnet)

## Slide 69: DHCP
Newly booted or attached host sends DHCPDISCOVER message to a special IP address (255.255.255.255)
DHCP relay agent unicasts the message to DHCP server and waits for the response