## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2024
Topic: BGP
(Textbook chapter 4)
April 30th, 2024

## Slide 2
1) A4 assignment: Mark your group/partner on gradescope.
2) Final project: Form groups of four.

## Slide 3: Inter-domain routing

## Slide 4
Our (improved) view of the Internet

## Slide 5: Making routing scalable
scale: with billions of destinations:
Can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice

## Slide 6: Autonomous Routing Domains
A collection of physical networks glued together
using IP, that have a unified administrative
routing policy.
Campus networks
Corporate networks
ISP Internal networks
…

## Slide 7: Autonomous Systems (ASes)
An autonomous system is an autonomous routing domain
that has been assigned an Autonomous System Number (ASN).
RFC 1930: Guidelines for creation, selection,
and registration of an Autonomous System
… the administration of an AS appears to other ASes to
have a single coherent interior routing plan and presents a
consistent picture of what networks are reachable through it.

## Slide 8: AS Numbers (ASNs)
ASNs are 16 and 32 bit values.
64512 through 65535 are “private”
Genuity: 1
MIT: 3
Harvard: 11
UC San Diego: 7377
AT&T: 7018, 6341, 5074, …
UUNET: 701, 702, 284, 12199, …
Sprint: 1239, 1240, 6211, 6242, …
…
ASNs represent units of routing policy
Currently over 11,000 in use.

## Slide 9: Interdomain routing = routing between autonomous systems
AS 701
AS 1239
AS 7018
UUNet
AT&T
Common Backbone
Sprint
Fidelity Investments
AT&T Research
207.104.168.0/24
AS 6431
AS 11040
192.223.184.0/21
134.244.0.0/16

## Slide 10: Internet approach to scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
inter-AS routing
routing among AS’es
gateways perform inter-domain routing (as well as intra-domain routing)
intra-AS routing
routing among hosts, routers in same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocol
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es

## Slide 11: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations

## Slide 12
Intra-AS Routing

## Slide 13: Intra-AS Routing
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary for decades, until 2016)

## Slide 14: OSPF (Open Shortest Path First)
“open”: publicly available
uses link-state algorithm
  link state packet dissemination
  topology map at each node
  route computation using Dijkstra’s algorithm
router floods OSPF link-state advertisements to all other routers in entire AS
  carried in OSPF messages directly over IP (rather than TCP or UDP
  link state: for each attached link

## Slide 15: OSPF “advanced” features
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different ToS (e.g., satellite link cost set low for best effort ToS; high for real-time ToS)
integrated uni- and multi-cast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.

## Slide 16: Hierarchical OSPF
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers

## Slide 17: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’es.

## Slide 18: Inter-AS tasks
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

## Slide 19
Inter-AS Routing

## Slide 20: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy
allows subnet to advertise its existence to rest of Internet: “I am here”

## Slide 21: eBGP, iBGP connections
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
gateway routers run both eBGP and iBGP protocols

## Slide 22: BGP basics
when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X

## Slide 23
Acronym nightmares
Routing protocols
Exterior Gateway Routing Protocol
(EGP)
Interior Gateway Routing Protocol
(IGP)
e.g., OSPF, RIP
(recall LS and DV routing)
e.g., BGP
External Border
Gateway Protocol (e-BGP)
Internal Border
Gateway Protocol (i-BGP)

## Slide 24: BGP basics
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1

## Slide 25: BGP basics
when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection.
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X

## Slide 26: Path attributes and BGP routes
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
Policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other other neighboring ASes

## Slide 27: BGP path advertisement
Based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
Based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c

## Slide 28: BGP path advertisement
AS1 gateway router 1c learns path AS2,AS3,X from 2a
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
Based on policy, AS1 gateway router 1c chooses path AS3,X, and advertises path within AS1 via iBGP

## Slide 29: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 30: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1d learn about dest X via iBGP from 1c: “path to X goes through 1c”
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
AS3,X
Q: how does router set forwarding table entry to distant prefix?
1
2
1
2
dest
interface
…
…
X
…
…
1
physical link
local link interfaces
at 1a, 1d

## Slide 31
recall: 1a, 1b, 1d learn about dest X via iBGP from 1c: “path to X goes through 1c”
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
dest
interface
…
…
X
…
…
2
1a: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 2
1
2
BGP, OSPF, forwarding table entries
Q: how does router set forwarding table entry to distant prefix?

## Slide 32: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 33: Hot Potato Routing
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS1,AS3,X
OSPF link weights
201
152
112
263

## Slide 34: A dive into the BGP policies

## Slide 35: Nontransit vs. Transit ASes
ISP 1
ISP 2
Nontransit AS
might be a corporate
or campus network.
Could be a “content
provider”
NET A
Traffic NEVER
flows from ISP 1
through NET A to ISP 2
(At least not intentionally!)
IP traffic
Internet Service
providers (often)
have transit
networks

## Slide 36: Selective Transit
NET B
NET C
NET A provides transit
between NET B and NET C
and between NET D
and NET C
NET A
NET D
NET A DOES NOT
provide transit
Between NET D
and NET B
Most transit networks transit in a selective manner…
IP traffic

## Slide 37: Customers and Providers
Customer pays provider for access to the Internet
provider
customer
IP traffic
provider
customer

## Slide 38: Customers Don’t Always Need BGP
provider
customer
Nail up default routes 0.0.0.0/0
pointing to provider.
Nail up routes 192.0.2.0/24
pointing to customer
192.0.2.0/24
Static routing is the most common way of connecting an
autonomous routing domain to the Internet.
This helps explain why BGP is a mystery to many …

## Slide 39: Customer-Provider Hierarchy
IP traffic
provider
customer

## Slide 40: The Peering Relationship
peer
peer
customer
provider
Peers provide transit between
their respective customers
Peers do not provide transit
between peers
Peers (often) do not exchange $$$
traffic
allowed
traffic NOT
allowed

## Slide 41: Peering Provides Shortcuts
Peering also allows connectivity between
the customers of “Tier 1” providers.
peer
peer
customer
provider

## Slide 42: BGP-4
BGP = Border Gateway Protocol
Is a Policy-Based routing protocol
Is the de facto EGP of today’s global Internet
Relatively simple protocol, but configuration is complex and the entire world can see, and be impacted by, your mistakes.
1989 : BGP-1 [RFC 1105]
  Replacement for EGP (1984, RFC 904)
1990 : BGP-2 [RFC 1163]
1991 : BGP-3 [RFC 1267]
1995 : BGP-4 [RFC 1771]
  Support for Classless Interdomain Routing (CIDR)

## Slide 43: BGP Operations (Simplified)
Establish session on
TCP port 179
Exchange all
active routes
Exchange incremental
updates
AS1
AS2
While connection
is ALIVE exchange
route UPDATE messages
BGP session

## Slide 44: Four Types of BGP Messages
Open : Establish a peering session.
Keep Alive : Handshake at regular intervals.
Notification : Shuts down a peering session.
Update : Announcing new routes or withdrawing previously announced routes.
announcement
=
prefix + attributes values

## Slide 45: BGP Attributes
Value Code Reference
----- --------------------------------- ---------
1 ORIGIN [RFC1771]
2 AS_PATH [RFC1771]
3 NEXT_HOP [RFC1771]
4 MULTI_EXIT_DISC [RFC1771]
5 LOCAL_PREF [RFC1771]
6 ATOMIC_AGGREGATE [RFC1771]
7 AGGREGATOR [RFC1771]
8 COMMUNITY [RFC1997]
9 ORIGINATOR_ID [RFC2796]
10 CLUSTER_LIST [RFC2796]
11 DPA [Chen]
12 ADVERTISER [RFC1863]
13 RCID_PATH / CLUSTER_ID [RFC1863]
14 MP_REACH_NLRI [RFC2283]
15 MP_UNREACH_NLRI [RFC2283]
16 EXTENDED COMMUNITIES [Rosen]
...
255 reserved for development
From IANA: http://www.iana.org/assignments/bgp-parameters
Most important attributes
Not all attributes
need to be present in
every announcement

## Slide 46: Attributes are Used to Select Best Routes
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
Given multiple
routes to the same
prefix, a BGP speaker
must pick at most
one best route
(Note: it could reject
them all!)

## Slide 47: BGP Next Hop Attribute
Every time a route announcement crosses an AS boundary, the Next Hop attribute is changed to the IP address of the border router that announced the route.
AS 6431
AT&T Research
135.207.0.0/16
Next Hop = 12.125.133.90
AS 7018
AT&T
AS 12654
RIPE NCC
RIS project
12.125.133.90
135.207.0.0/16
Next Hop = 12.127.0.121
12.127.0.121

## Slide 48: Join EGP with IGP For Connectivity
Forwarding Table
Forwarding Table
AS 1
AS 2
192.0.2.1
135.207.0.0/16
10.10.10.10
EGP
192.0.2.1
135.207.0.0/16
destination
next hop
10.10.10.10
192.0.2.0/30
destination
next hop
135.207.0.0/16
Next Hop = 192.0.2.1
192.0.2.0/30
135.207.0.0/16
destination
next hop
10.10.10.10
+
192.0.2.0/30
10.10.10.10

## Slide 49: Implementing Customer/Provider and Peer/Peer relationships
Enforce transit relationships
  Outbound route filtering
Enforce order of route preference
  provider < peer < customer
Two parts:

## Slide 50: Import Routes
From
peer
From
peer
From
provider
From
provider
From
customer
From
customer
provider route
customer route
peer route
ISP route

## Slide 51: Export Routes
To
peer
To
peer
To
customer
To
customer
To
provider
From
provider
provider route
customer route
peer route
ISP route
filters
block

## Slide 52: How Can Routes be Colored? BGP Communities!
A community value is 32 bits
By convention,
first 16 bits is
ASN indicating
who is giving it
an interpretation
community
number
Very powerful
BECAUSE it
has no (predefined) meaning
Community Attribute = a list of community values.
(So one route can belong to multiple communities)
RFC 1997 (August 1996)
Used for signalling
within and between
ASes
Two reserved communities
no_advertise 0xFFFFFF02: don’t pass to BGP neighbors
  no_export = 0xFFFFFF01: don’t export out of AS

## Slide 53
BGP Community attribute: Example

## Slide 54: Tweak Tweak Tweak
For inbound traffic
  Filter outbound routes
  Tweak attributes on outbound routes in the hope of influencing your neighbor’s best route selection
For outbound traffic
  Filter inbound routes
  Tweak attributes on inbound routes to influence best route selection
outbound
routes
inbound
routes
inbound
traffic
outbound
traffic
In general, an AS has more
control over outbound traffic

## Slide 55: Route Selection Summary
Highest Local Preference
Shortest ASPATH
Lowest MED
i-BGP < e-BGP
Lowest IGP cost
to BGP egress
Lowest router ID
traffic engineering
Enforce relationships
Throw up hands and
break ties

## Slide 56: Back to Frank …
AS 1
AS 2
AS 4
AS 3
13.13.0.0/16
peer
peer
customer
provider
local pref = 80
local pref = 100
local pref = 90
Higher Local
preference values
are more preferred
Local preference only used in iBGP

## Slide 57: Implementing Backup Links with Local Preference (Outbound Traffic)
Forces outbound traffic to take primary link, unless link is down.
AS 1
primary link
backup link
Set Local Pref = 100
for all routes from AS 1
AS 65000
Set Local Pref = 50
for all routes from AS 1

## Slide 58: Multihomed Backups (Outbound Traffic)
Forces outbound traffic to take primary link, unless link is down.
AS 1
primary link
backup link
Set Local Pref = 100
for all routes from AS 1
AS 2
Set Local Pref = 50
for all routes from AS 3
AS 3
provider
provider

## Slide 59: ASPATH Attribute
AS7018
135.207.0.0/16
AS Path = 6341
AS 1239
Sprint
AS 1755
Ebone
AT&T
AS 3549
Global Crossing
135.207.0.0/16
AS Path = 7018 6341
135.207.0.0/16
AS Path = 3549 7018 6341
AS 6341
135.207.0.0/16
AT&T Research
Prefix Originated
AS 12654
RIPE NCC
RIS project
AS 1129
Global Access
135.207.0.0/16
AS Path = 7018 6341
135.207.0.0/16
AS Path = 1239 7018 6341
135.207.0.0/16
AS Path = 1755 1239 7018 6341
135.207.0.0/16
AS Path = 1129 1755 1239 7018 6341

## Slide 60: Interdomain Loop Prevention
BGP at AS YYY will never accept a route with ASPATH containing YYY.
AS 7018
12.22.0.0/16
ASPATH = 1 333 7018 877
Don’t Accept!
AS 1

## Slide 61: Traffic Often Follows ASPATH
AS 4
AS 3
AS 2
AS 1
135.207.0.0/16
135.207.0.0/16
ASPATH = 3 2 1
IP Packet
Dest =
135.207.44.66

## Slide 62: … But It Might Not
AS 4
AS 3
AS 2
AS 1
135.207.0.0/16
135.207.0.0/16
ASPATH = 3 2 1
IP Packet
Dest =
135.207.44.66
AS 5
135.207.44.0/25
ASPATH = 5
135.207.44.0/25
AS 2 filters all
subnets with masks
longer than /24
135.207.0.0/16
ASPATH = 1
From AS 4, it
may look like this
packet will take
path 3 2 1, but it
actually takes
path 3 2 5

## Slide 63: Shorter Doesn’t Always Mean Shorter
In fairness:
could you do
this “right” and
still scale?
Exporting internal
state would
dramatically
increase global
instability and
amount of routing
state
AS 4
AS 3
AS 2
AS 1
Mr. BGP says that
path 4 1 is better
than path 3 2 1
Duh!

## Slide 64: Shedding Inbound Traffic with ASPATH Padding Hack
Padding will (usually)
force inbound
traffic from AS 1
to take primary link
AS 1
192.0.2.0/24
ASPATH = 2 2 2
customer
AS 2
provider
192.0.2.0/24
backup
primary
192.0.2.0/24
ASPATH = 2

## Slide 65: Padding May Not Shut Off All Traffic
AS 1
192.0.2.0/24
ASPATH = 2 2 2 2 2 2 2 2 2 2 2 2 2 2
customer
AS 2
provider
192.0.2.0/24
192.0.2.0/24
ASPATH = 2
AS 3
provider
AS 3 will send
traffic on “backup”
link because it prefers
customer routes and local
preference is considered
before ASPATH length!
Padding in this way is often
used as a form of load
balancing
backup
primary

## Slide 66: COMMUNITY Attribute to the Rescue!
AS 1
customer
AS 2
provider
192.0.2.0/24
192.0.2.0/24
ASPATH = 2
AS 3
provider
backup
primary
192.0.2.0/24
ASPATH = 2
COMMUNITY = 3:70
Customer import policy at AS 3:
If 3:90 in COMMUNITY then
set local preference to 90
If 3:80 in COMMUNITY then
set local preference to 80
If 3:70 in COMMUNITY then
set local preference to 70
AS 3: normal
customer local
pref is 100,
peer local pref is 90

## Slide 67: Hot Potato Routing: Go for the Closest Egress Point
192.44.78.0/24
15
56
IGP distances
egress 1
egress 2
This Router has two BGP routes to 192.44.78.0/24.
Hot potato: get traffic off of your network as
Soon as possible. Go for egress 1!

## Slide 68: Getting Burned by the Hot Potato
15
56
17
2865
High bandwidth
Provider backbone
Low bandwidth
customer backbone
Heavy
Content
Web Farm
Many customers want
their provider to
carry the bits!
tiny http request
huge http reply
SFO
NYC
San Diego

## Slide 69: Cold Potato Routing with MEDs (Multi-Exit Discriminator Attribute)
15
56
17
2865
Heavy
Content
Web Farm
192.44.78.0/24
192.44.78.0/24
MED = 15
192.44.78.0/24
MED = 56
This means that MEDs must be considered BEFORE
IGP distance!
Prefer lower
MED values
Note1 : some providers will not listen to MEDs
Note2 : MEDs need not be tied to IGP distance

## Slide 70: Route Selection Summary
Highest Local Preference
Shortest ASPATH
Lowest MED
i-BGP < e-BGP
Lowest IGP cost
to BGP egress
Lowest router ID
traffic engineering
Enforce relationships
Throw up hands and
break ties

## Slide 71: BGP Attacks

## Slide 72: Prefix Hijacking
1
2
3
4
5
6
7
12.34.0.0/16
12.34.0.0/16
Originating someone else’s prefix
  What fraction of the Internet believes it?

## Slide 73: Prefix highjack
http://queue.acm.org/detail.cfm?id=2668966

## Slide 74: Sub-Prefix Hijacking
Originating a more-specific prefix
  Every AS picks the bogus route for that prefix
  Traffic follows the longest matching prefix
1
2
3
4
5
6
7
12.34.0.0/16
12.34.158.0/24

## Slide 75: Sub-prefix hijack
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
  February 2008 : Pakistan Telecom hijacks YouTube
Notes: -level of autonomous systems
-e.g., YouTube, AT&T, pakistan telecom
-routing is done on IP addresses, so when someone wants to go to YouTube they get YouTube’s IP address and YouTube announces to the world that they have the ip address and traffic is forwarded towards them. So here multinet would route to it’s provider pakistan telecom that then forwards the traffic on to youtube.
-these networks chosen for a specific reason which is that there was an incident in february 2008 pakistan telecom actually high jacked traffic going to youtube (misconfiguration).
-they announced to the world that they’re youtube and traffic destined to youtube was routed to them
-youtube was unavailable for a couple of hours as operators phone each other to figure out what was going on.

## Slide 76: Pakistan Telecom: Sub-prefix hijack
  Here’s what should have happened….
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
X
Hijack + drop packets going to YouTube
  Block your own customers.

## Slide 77: Pakistan Telecom: Sub-prefix hijack
  But here’s what Pakistan ended up doing…
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
Pakistan
Telecom
No, I’m YouTube!
IP 208.65.153.0 / 24
Notes: Our works focuses on attacks of this flavor..

## Slide 78: Bogus AS Paths to Hide Hijacking
Adds AS hop(s) at the end of the path
  E.g., turns “701 88” into “701 88 3”
Motivations
  Evade detection for a bogus route
  E.g., by adding the legitimate AS to the end
Hard to tell that the AS path is bogus…
  Even if other ASes filter based on prefix ownership
701
88
3
18.0.0.0/8
18.0.0.0/8

## Slide 79: Path-Shortening Attacks
Remove ASes from the AS path
  E.g., turn “701 3715 88” into “701 88”
Motivations
  Make the AS path look shorter than it is
  Attract sources that normally try to avoid AS 3715
  Help AS 88 look like it is closer to the Internet’s core
Who can tell that this AS path is a lie?
  Maybe AS 88 *does* connect to AS 701 directly
701
88
3715
?

## Slide 80: Attacks that Add a Bogus AS Hop
Add ASes to the path
  E.g., turn “701 88” into “701 3715 88”
Motivations
  Trigger loop detection in AS 3715
    Denial-of-service attack on AS 3715
    Or, blocking unwanted traffic coming from AS 3715!
  Make your AS look like is has richer connectivity
Who can tell the AS path is a lie?
  AS 3715 could, if it could see the route
  AS 88 could, but would it really care as long as it received data traffic meant for it?
701
88

## Slide 81: Violating “Consistent Export” to Peers
Peers require consistent export
  Prefix advertised at all peering points
  Prefix advertised with same AS path length
Reasons for violating the policy
  Trick neighbor into “cold potato”
  Configuration mistake
Main defense
  Analyzing BGP updates
  … or data traffic
  … for signs of inconsistency
src
dest
Bad AS
data
BGP

## Slide 82: Other Attacks
Attacks on BGP sessions
  Confidentiality of BGP messages
  Denial-of-service on BGP session
  Inserting, deleting, modifying, or replaying messages
Resource exhaustion attacks
  Too many IP prefixes (e.g., BGP “512K Day”)
  Too many BGP update messages
Data-plane attacks
  Announce one BGP routes, but use another

## Slide 83: Solution Techniques
Protective filtering
  Know your neighbors
Anomaly detection
  Suspect the unexpected
Checking against registries
  Establish ground truth for prefix origination
Signing and verifying
  Prevent bogus AS PATHs
Data-plane verification
  Ensure the path is actually followed