## Slide 1
CMSC 417: Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
Spring 2024
Topic: Overview of networks (cont…)
(Textbook chapter 1)
& Internetworking
(Textbook chapter 3)
Feb 1st, 2024

## Slide 2: Chapter 1: Roadmap
  What is the Internet?
  Network edge
  Network core
  Delay, Loss, Throughput in networks
  Protocol layers, service models
  History

## Slide 3: How do loss and delay occur?
A
B
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 4: Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dtotal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 5
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
v: propagation speed
dprop = d/v
dtrans and dprop
very different
propagation
nodal
processing
queueing
dtotal = dproc + dqueue + dtrans + dprop
A
B
transmission
Four sources of packet delay
Notes: 5

## Slide 6: Packet Loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)

## Slide 7: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)

## Slide 8: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 9: Throughput: Internet scenario
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R

## Slide 10: Bandwidth
Bits transmitted at a particular bandwidth can be regarded as having some width:
(a) bits transmitted at 1Mbps (each bit 1 μs wide);
(b) bits transmitted at 2Mbps (each bit 0.5 μs wide).

## Slide 11: Chapter 1: Roadmap (cont…)
  What is the Internet?
  Network edge
  Network core
  Delay, Loss, Throughput in networks
  Protocol layers, service models

## Slide 12: Protocol “Layers”
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing structure of network?
…. or at least our discussion of networks?

## Slide 13: Layering of airline functionality
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing

## Slide 14: Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
Can layering be harmful? Give an example.

## Slide 15: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of packets from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 16
The OSI 7-layer Model
OSI – Open Systems Interconnection
(by International Organization for Standardization, ISO)
OSI Architecture

## Slide 17: Description of Layers
Physical Layer
  Handles the transmission of raw bits over a communication link
Data Link Layer
  Collects a stream of bits into a larger aggregate called a frame
  Network adaptor along with device driver in OS implement the protocol in this layer
  Frames are actually delivered to hosts
Network Layer
  Handles routing among nodes within a packet-switched network
  Unit of data exchanged between nodes in this layer is called a packet
  The lower three layers are implemented on all network nodes

## Slide 18: Description of Layers
Transport Layer
  Implements a process-to-process channel
  Unit of data exchanges in this layer is called a message
Session Layer
  Provides a name space that is used to tie together the potentially different transport streams that are part of a single application.
Presentation Layer
  Concerned about the format of data exchanged between peers (data formats, data encryption)
Application Layer
  Standardize common type of exchanges
  The transport layer and the higher layers typically run only on end-hosts and not on the intermediate switches and routers

## Slide 19: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 20: Network Architecture
Example of a layered network system

## Slide 21: Internet Architecture
Internet Protocol Graph
Alternative view of the Internet architecture. The “Network” layer shown here is sometimes referred to as the “sub-network” or “link” layer.

## Slide 22
This course: Top-Down or Bottom-up?
1
2
3
4

## Slide 23
Internetworking

## Slide 24
Connection between hosts
1. Addressing
– Unique identifier for global addressing
– Link name for neighbors
2. Forwarding
-- Switching packets between links
3. Routing
-- Determining paths between hosts

## Slide 25
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
Internet Structure: Network of Networks
But if one global ISP is viable business, there will be competitors ….
Routers

## Slide 26
Connection between hosts

## Slide 27
Connection between hosts
Using network to maintain network.
Behaves like Applications. Uses TCP/UDP packets

## Slide 28
Connection between hosts
1. Addressing
– Unique identifier for global addressing
– Link name for neighbors
2. Forwarding
-- Switching packets between links
3. Routing
-- Determining paths between hosts

## Slide 29: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets will traverse in going from given initial source host to given final destination host
“good”: least “cost”, “fastest”, “least congested”

## Slide 30: Graph abstraction of the network
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
aside: graph abstraction is useful in other network contexts, e.g.,
P2P, where N is set of peers and E is set of TCP connections

## Slide 31: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or related to congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path

## Slide 32: Routing
  For a simple network, we can calculate all shortest paths and load them into some nonvolatile storage on each node.
  Such a static approach has several shortcomings
    It does not deal with node or link failures
    It does not consider the addition of new nodes or links
    It implies that edge costs cannot change
  What is the solution?
    Need a distributed and dynamic protocol
    Two main classes of protocols
      Distance Vector
      Link State

## Slide 33
Distance Vector Routing

## Slide 34: Distance Vector
Each node constructs a one-dimensional array (a vector) containing the “distances” (costs) to all other nodes and distributes that vector to its immediate neighbors
Starting assumption is that each node knows the cost of the link to each of its directly connected neighbors

## Slide 35
Advertise:
A router transmits its distance vector to each of its neighbors in a
routing packet.
2. Each router receives and saves the most recently received
distance vector from each of its neighbors.
3. Update:
A router recalculates its distance vector when:
  It receives a distance vector from a neighbor containing
  different information than before.
  b) It discovers that a link to a neighbor has gone down
  (or the cost has changed).
Distance Vector Routing protocol

## Slide 36
Thank you

## Slide 39
A
B
D
C
E
7
11
4
15
5
13
19
Distance Vector Routing: An example

## Slide 40
A
B
D
C
E
7
11
4
15
5
13
19
Dest | Cost | N. Hop
Routing table at Node A
Distance Vector Routing: An example

## Slide 41
A
B
D
C
E
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Routing table at Node A
Distance Vector Routing: An example
Know thy neighbors !!
How?

## Slide 42
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | ∞ | --
B | ∞ | --
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | ∞ | --
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 0
7
11
4
15
5
13
19

## Slide 43
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | ∞ | --
B | ∞ | --
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | ∞ | --
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 0
7
11
4
15
5
13
19
Let your neighbors know what you know!!

## Slide 44
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | ∞ | --
B | ∞ | --
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | ∞ | --
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 1
7
11
4
15
5
13
19
Update your routing table, if required!!

## Slide 45
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Round: 1
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Let’s consider updates at node A

## Slide 46
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19

## Slide 47
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Round: 1
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Let’s consider updates at node A

## Slide 48
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Round: 1
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Let’s consider updates at node A

## Slide 49
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Round: 1
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Let’s consider updates at node A

## Slide 50
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19

## Slide 51
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19
When will a node send routing advertisements to its neighbors?

## Slide 52
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 1
7
11
4
15
5
13
19
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
When will a node send routing advertisements to its neighbors?

## Slide 53: Routing advertisements
Two circumstances when a node sends out routing advertisements:
Periodic: Automatically after some time. Why?
2) Triggered: Whenever an event makes a node to change its routing table (e.g., link fail or a new message from a neighbor).

## Slide 54
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 2
7
11
4
15
5
13
19
Node A: No Updates
Node B: No Updates
Node C: No Updates
Node D: No Updates
Node E: No Updates
Convergence

## Slide 55: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
v
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y

## Slide 56: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum is next
hop in shortest path, used in forwarding table
B-F equation says:

## Slide 57
Distance vector algorithm
Putting together…
Notes: The code is taken from: https://www.javatpoint.com/distance-vector-routing-algorithm

## Slide 58: Distance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]
Putting together…

## Slide 59: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)

## Slide 60: Distance vector algorithm
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
each node:

## Slide 61
Advertise:
A router transmits its distance vector to each of its neighbors in a
routing packet.
2. Each router receives and saves the most recently received
distance vector from each of its neighbors.
3. Update:
A router recalculates its distance vector when:
  It receives a distance vector from a neighbor containing
  different information than before.
  b) It discovers that a link to a neighbor has gone down
  (or the cost has changed).
Distance Vector Routing protocol (Recap)

## Slide 62: Routing updates (Recap)
Two circumstances when a node sends out routing advertisements:
Periodic: Automatically after some time.
2) Triggered: Whenever an event makes a node to change its routing table (e.g., link fail or a new message from a neighbor).

## Slide 63
Distance Vector Routing: Link failure

## Slide 64
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 2
7
11
4
15
5
13
19

## Slide 65
A
B
D
C
E
Dest | Cost | N. Hop
A | ∞ | --
B | 0 | B
C | ∞ | --
D | 4 | D
E | ∞ | --
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | ∞ | --
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 3
7
11
4
15
5
13
19
Node A: No Updates
Node B: No Updates
Node C: No Updates
Node D: No Updates
Node E: No Updates

## Slide 66
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 19 | D
D | 4 | D
E | 17 | D
Dest | Cost | N. Hop
A | 0 | A
B | ∞ | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 19 | D
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 17 | D
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 3
7
11
4
15
5
13
19
Node A: Updates for B
Node B: Updates for A,C,E
Node C: Updates for B
Node D: No Updates
Node E: Updates for B
Cost update

## Slide 67
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 19 | D
D | 4 | D
E | 17 | D
Dest | Cost | N. Hop
A | 0 | A
B | ∞ | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 19 | D
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 17 | D
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 4
7
11
4
15
5
13
19
Node A: Updates for B
Node B: No Updates
Node C: No Updates
Node D: No Updates
Node E: No Updates

## Slide 68
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 19 | D
D | 4 | D
E | 17 | D
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 19 | D
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 17 | D
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 5
7
11
4
15
5
13
19

## Slide 69: Distance vector: link cost changes
link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
x
z
1
4
50
y
1

## Slide 70
Distance vector: link cost “decreases”
node Y
node Z
Dest | Cost | Hop
X | 4 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 1 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 1 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 1 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 2 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 2 | Y
Y | 1 | Y
Z | 0 | Z
T1
Cost change
T2
T3
T4
Bellman-Ford algo.
considered the route
through Z (cost=51).

## Slide 71
Distance vector: link cost “increases”
node Y
node Z
Dest | Cost | Hop
X | 4 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 8 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
T1
Cost change
T2
T3
T4
Bellman-Ford algo.
considers two routes from the
saved advertisements.
<X, 60, X> -- direct link
<X, 5, Z> + dZ(X) – Cost 6 link via Z
60

## Slide 72
Distance vector: link cost “increases”
node Y
node Z
Dest | Cost | Hop
X | 4 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 8 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
T1
Cost change
T2
T3
T4
Bellman-Ford algo.
considers two routes from the
saved advertisements.
<X, 60, X> -- direct link
<X, 5, Z> + dZ(X) – Cost 6 link via Z
60
When will this looped update stop (converge)?

## Slide 73
Distance vector: link cost “increases”
node Y
node Z
Dest | Cost | Hop
X | 4 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 8 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
T1
Cost change
T2
T3
T4
Bellman-Ford algo.
considers two routes from the
saved advertisements.
<X, 60, X> -- direct link
<X, 5, Z> + dZ(X) – Cost 6 link via Z
60
“Count-to-infinity” problem

## Slide 74: Count-to-infinity Problem: Solutions-1
Use some relatively small number as an approximation of infinity
For instance, in the Routing Information Protocol (RIP)—that implements DV routing-- the maximum number of hops is typically set to 15 with 16 hops considered as infinity. If a network destination is more than 15 hops away, it is considered unreachable.

## Slide 75
Use some relatively small number as an approximation of infinity
Maximum possible hops
Count-to-infinity Problem: Solutions-1

## Slide 76
Use some relatively small number as an approximation of infinity
Maximum possible hops
“Thus, when considering even the most distant Facebook user in the Siberian tundra or the Peruvian rainforest, a friend of your friend probably knows a friend of their friend,” -- Facebook
(1) https://research.facebook.com/blog/2016/2/three-and-a-half-degrees-of-separation/
(2) Six degrees of separation: https://en.wikipedia.org/wiki/Six_degrees_of_separation
Count-to-infinity Problem: Solutions-1

## Slide 77
Technique to improve the time to stabilize routing is called
split horizon
  When a node sends a routing update to its neighbors, it does not send those routes it learned from each neighbor back to that neighbor
  For example, if Z has the route (X, 5, Y) in its table, then it knows it must have learned this route from Y, and so whenever Z sends a routing update to Y, it does not include the route (X, 5) in that update
Count-to-infinity Problem: Solutions-2

## Slide 78
Distance vector: link cost “increases”
node Y
node Z
Dest | Cost | Hop
X | 4 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 8 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
T1
Cost change
T2
T3
T4
Bellman-Ford algo.
considers two routes from the
saved advertisements.
<X, 60, X> -- direct link
<X, 5, Z> + dZ(X) – Cost 6 link via Z
60
Case: Split horizon

## Slide 79: Count-to-infinity Problem: Solutions-3
In a stronger version of split horizon, called split horizon with poison reverse
  B actually sends that back route to A, but it puts negative information in the route to ensure that A will not eventually use B to get to E
  For example, B sends the route (E, ∞) to A

## Slide 80
Distance vector: link cost “increases”
node Y
node Z
Dest | Cost | Hop
X | 4 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 8 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
T1
Cost change
T2
T3
T4
Bellman-Ford algo.
considers two routes from the
saved advertisements.
<X, 60, X> -- direct link
<X, ♾, Z> + dZ(X) – Cost 6 link via Z
60
Case: Split horizon
with poisoned reverse

## Slide 81
Distance vector: Poisoned reverse
Does poison reverse solve the general count-to-infinity problem?
It does not. It may be possible that loops involving three or more nodes (rather than simply two immediately neighboring nodes, as we shown in last example) will not be detected by the poison reverse technique.

## Slide 82: DV Implementation: Routing Information Protocol (RIP)
  Example Network
  running RIP RIPv2 Packet Format

## Slide 83
Limitations of DV routing
Notes: What is RFC: https://www.techtarget.com/whatis/definition/Request-for-Comments-RFC