## Slide 1
CMSC 417: Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
Spring 2024
Topic: Internetworking
(Textbook chapter 3)
Feb 6th, 2024

## Slide 2
A
B
D
C
E
7
11
4
15
5
13
19
Distance Vector Routing: An example

## Slide 3
A
B
D
C
E
7
11
4
15
5
13
19
Dest | Cost | N. Hop
Routing table at Node A
Distance Vector Routing: An example

## Slide 4
A
B
D
C
E
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Routing table at Node A
Distance Vector Routing: An example
Know thy neighbors !!
How?

## Slide 5
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | ∞ | --
B | ∞ | --
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | ∞ | --
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 0
7
11
4
15
5
13
19

## Slide 6
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | ∞ | --
B | ∞ | --
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | ∞ | --
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 0
7
11
4
15
5
13
19
Let your neighbors know what you know!!

## Slide 7
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | ∞ | --
B | ∞ | --
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | ∞ | --
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 1
7
11
4
15
5
13
19
Update your routing table, if required!!

## Slide 8
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Round: 1
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Let’s consider updates at node A

## Slide 9
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19

## Slide 10
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Round: 1
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Let’s consider updates at node A

## Slide 11
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | ∞ | --
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Round: 1
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Let’s consider updates at node A

## Slide 12
A
B
D
C
E
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | ∞ | --
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Round: 1
7
11
4
15
5
13
19
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 11 | C
D | 4 | D
E | ∞ | --
Let’s consider updates at node A

## Slide 13
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19

## Slide 14
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
Round: 1
7
11
4
15
5
13
19
When will a node send routing advertisements to its neighbors?

## Slide 15
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 1
7
11
4
15
5
13
19
Node A: Updates for B,D,E
Node B: Updates for A, E
Node C: No Updates
Node D: Updates for A
Node E: Updates for A, B
When will a node send routing advertisements to its neighbors?

## Slide 16: Routing advertisements
Two circumstances when a node sends out routing advertisements:
Periodic: Automatically after some time. Why?
2) Triggered: Whenever an event makes a node to change its routing table (e.g., link fail or a new message from a neighbor).

## Slide 17
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 2
7
11
4
15
5
13
19
Node A: No Updates
Node B: No Updates
Node C: No Updates
Node D: No Updates
Node E: No Updates
Convergence

## Slide 18: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
v
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y

## Slide 19: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum is next
hop in shortest path, used in forwarding table
B-F equation says:

## Slide 20
Distance vector algorithm
Putting together…
Notes: The code is taken from: https://www.javatpoint.com/distance-vector-routing-algorithm

## Slide 21: Distance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]
Putting together…

## Slide 22: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)

## Slide 23: Distance vector algorithm
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
each node:

## Slide 24
Advertise:
A router transmits its distance vector to each of its neighbors in a
routing packet.
2. Each router receives and saves the most recently received
distance vector from each of its neighbors.
3. Update:
A router recalculates its distance vector when:
  It receives a distance vector from a neighbor containing
  different information than before.
  b) It discovers that a link to a neighbor has gone down
  (or the cost has changed).
Distance Vector Routing protocol (Recap)

## Slide 25: Routing updates (Recap)
Two circumstances when a node sends out routing advertisements:
Periodic: Automatically after some time. [typically 30 sec.]
2) Triggered: Whenever an event makes a node to change its routing table (e.g., link fail or a new message from a neighbor).

## Slide 26
Distance Vector Routing: Link failure

## Slide 27
A
B
D
C
E
Dest | Cost | N. Hop
A | 18 | C
B | 0 | B
C | 11 | C
D | 4 | D
E | 16 | C
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 11 | B
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 2
7
11
4
15
5
13
19

## Slide 28
A
B
D
C
E
Dest | Cost | N. Hop
A | ∞ | --
B | 0 | B
C | ∞ | --
D | 4 | D
E | ∞ | --
Dest | Cost | N. Hop
A | 0 | A
B | 18 | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | ∞ | --
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 16 | C
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 3
7
11
4
15
5
13
19
Node A: No Updates
Node B: No Updates
Node C: No Updates
Node D: No Updates
Node E: No Updates

## Slide 29
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 19 | D
D | 4 | D
E | 17 | D
Dest | Cost | N. Hop
A | 0 | A
B | ∞ | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 19 | D
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 17 | D
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 3
7
11
4
15
5
13
19
Node A: Updates for B
Node B: Updates for A,C,E
Node C: Updates for B
Node D: No Updates
Node E: Updates for B
Cost update

## Slide 30
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 19 | D
D | 4 | D
E | 17 | D
Dest | Cost | N. Hop
A | 0 | A
B | ∞ | C
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 19 | D
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 17 | D
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 4
7
11
4
15
5
13
19
Node A: Updates for B
Node B: No Updates
Node C: No Updates
Node D: No Updates
Node E: No Updates

## Slide 31
A
B
D
C
E
Dest | Cost | N. Hop
A | 19 | A
B | 0 | B
C | 19 | D
D | 4 | D
E | 17 | D
Dest | Cost | N. Hop
A | 0 | A
B | 19 | B
C | 7 | C
D | 22 | C
E | 12 | C
Dest | Cost | N. Hop
A | 7 | A
B | 19 | D
C | 0 | C
D | 15 | D
E | 5 | E
Dest | Cost | N. Hop
A | 12 | C
B | 17 | D
C | 5 | C
D | 13 | D
E | 0 | E
Dest | Cost | N. Hop
A | 22 | C
B | 4 | B
C | 15 | C
D | 0 | D
E | 13 | E
Round: 5
7
11
4
15
5
13
19

## Slide 32: Distance vector: link cost changes
link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
x
z
1
4
50
y
1

## Slide 33
Distance vector: link cost “decreases”
node Y
node Z
Dest | Cost | Hop
X | 4 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 1 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 1 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 1 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 2 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 2 | Y
Y | 1 | Y
Z | 0 | Z
T1
Cost change
T2
T3
T4
Bellman-Ford algo.
considered the route
through Z (cost=51).

## Slide 34
Distance vector: link cost “increases”
node Y
node Z
Dest | Cost | Hop
X | 4 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 8 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
T1
Cost change
T2
T3
T4
Bellman-Ford algo.
considers two routes from the
saved advertisements.
<X, 60, X> -- direct link
<X, 5, Z> + dZ(X) – Cost 6 link via Z
60

## Slide 35
Distance vector: link cost “increases”
node Y
node Z
Dest | Cost | Hop
X | 4 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 8 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
T1
Cost change
T2
T3
T4
Bellman-Ford algo.
considers two routes from the
saved advertisements.
<X, 60, X> -- direct link
<X, 5, Z> + dZ(X) – Cost 6 link via Z
60
When will this looped update stop (converge)?

## Slide 36
Distance vector: link cost “increases”
node Y
node Z
Dest | Cost | Hop
X | 4 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 8 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
T1
Cost change
T2
T3
T4
Bellman-Ford algo.
considers two routes from the
saved advertisements.
<X, 60, X> -- direct link
<X, 5, Z> + dZ(X) – Cost 6 link via Z
60
“Count-to-infinity” problem

## Slide 37
Distance vector: link cost “increases”
node Y
node Z
Dest | Cost | Hop
X | 4 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 8 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
T1
Cost change
T2
T3
T4
Bellman-Ford algo.
considers two routes from the
saved advertisements.
<X, 60, X> -- direct link
<X, 5, Z> + dZ(X) – Cost 6 link via Z
60
When will this looped update stop (converge)?

## Slide 38
“Count-to-infinity” problem: Another scenario
A
B
C
D
E
X
Small number for infinity
Triggered update and hold time
Avoiding loop while advertising
1
1
1
1

## Slide 39: Count-to-infinity Problem: Solutions-1
Use some relatively small number as an approximation of infinity
For instance, in the Routing Information Protocol (RIP)—that implements DV routing-- the maximum number of hops is typically set to 15 with 16 hops considered as infinity. If a network destination is more than 15 hops away, it is considered unreachable.

## Slide 40
Use some relatively small number as an approximation of infinity
Maximum possible hops
Count-to-infinity Problem: Solutions-1

## Slide 41
Use some relatively small number as an approximation of infinity
Maximum possible hops
“Thus, when considering even the most distant Facebook user in the Siberian tundra or the Peruvian rainforest, a friend of your friend probably knows a friend of their friend,” -- Facebook
(1) https://research.facebook.com/blog/2016/2/three-and-a-half-degrees-of-separation/
(2) Six degrees of separation: https://en.wikipedia.org/wiki/Six_degrees_of_separation
Count-to-infinity Problem: Solutions-1

## Slide 42
Technique to improve the time to stabilize routing is called
split horizon
  When a node sends a routing update to its neighbors, it does not send those routes it learned from each neighbor back to that neighbor
  For example, if Z has the route (X, 5, Y) in its table, then it knows it must have learned this route from Y, and so whenever Z sends a routing update to Y, it does not include the route (X, 5) in that update
Count-to-infinity Problem: Solutions-2

## Slide 43
Thank you

## Slide 46
Distance vector: link cost “increases”
node Y
node Z
Dest | Cost | Hop
X | 4 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 8 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
T1
Cost change
T2
T3
T4
Bellman-Ford algo.
considers two routes from the
saved advertisements.
<X, 60, X> -- direct link
<X, 5, Z> + dZ(X) – Cost 6 link via Z
60
Case: Split horizon

## Slide 47: Count-to-infinity Problem: Solutions-3
In a stronger version of split horizon, called split horizon with poison reverse
  B actually sends that back route to A, but it puts negative information in the route to ensure that A will not eventually use B to get to E
  For example, B sends the route (E, ∞) to A

## Slide 48
Distance vector: link cost “increases”
node Y
node Z
Dest | Cost | Hop
X | 4 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 6 | Z
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 8 | X
Y | 0 | Y
Z | 1 | Z
Dest | Cost | Hop
X | 5 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
Dest | Cost | Hop
X | 7 | Y
Y | 1 | Y
Z | 0 | Z
T1
Cost change
T2
T3
T4
Bellman-Ford algo.
considers two routes from the
saved advertisements.
<X, 60, X> -- direct link
<X, ♾, Z> + dZ(X) – Cost 6 link via Z
60
Case: Split horizon
with poisoned reverse

## Slide 49
Distance vector: Poisoned reverse
Does poison reverse solve the general count-to-infinity problem?
It does not. It may be possible that loops involving three or more nodes (rather than simply two immediately neighboring nodes, as we shown in last example) will not be detected by the poison reverse technique.

## Slide 50: DV Implementation: Routing Information Protocol (RIP)
  Example Network
  running RIP RIPv2 Packet Format

## Slide 51
Limitations of DV routing
Notes: What is RFC: https://www.techtarget.com/whatis/definition/Request-for-Comments-RFC

## Slide 52
What is RFC?
Request for Comments (RFC):
A peer reviewed publication in a series from the
principal technical development and standards-setting
bodies for the Internet, most prominently
the Internet Engineering Task Force (IETF).
How to Read an RFC: https://www.ietf.org/blog/how-read-rfc/
[ref] https://www.ietf.org/standards/rfcs/

## Slide 53
Link State Routing

## Slide 54: Link State Routing
Strategy:
Send to all nodes (not just neighbors) information about neighbors (not connection to all nodes).
All nodes will know the link-state information of all other nodes

## Slide 55: Link State Routing
Link State Packet (LSP):
  The ID of the node that created the LSP
  (2) Costs of links to each directly connected neighbor
  (3) A sequence number (SEQNO)
  [To distinguish a newer LSP from the old ones]
  [Smaller number == older LSP]
  (4) A Time-To-Live (TTL) for this packet
  [To make sure old information is eventually removed
  from the network]
Strategy:
Send to all nodes (not just neighbors) information about neighbors (not connection to all nodes).
What is the unit of the “Time-to-Live”?

## Slide 56
Link State Routing
(1) Reliable flooding
[Makes sure all nodes in the network get a copy of LSP from all other nodes]
(2) Route calculation
(Dijkstra’s shortest path algorithm)
[Calculates the shortest path from each node to all other nodes and the corresponding next-hop]

## Slide 57
Link State Routing: Reliable flooding
  Store most recent LSP from each node
  Forward LSP to all nodes but one that sent it
  Generate new LSP periodically; increment SEQNO
  Start SEQNO at 0 when reboot
  Decrement TTL before flooding it to neighbors.
  Also age the stored LSP (decrement TTL)
  Discard when TTL=0.
Goals:
Flood in minimum time
Minimize total routing traffic

## Slide 58: Link State
Reliable Flooding
Flooding of link-state packets. (a) LSP arrives at node X; (b) X floods LSP to A and C; (c) A and C flood LSP to B (but not X); (d) flooding is complete
Gets two identical copies of LSP.
Accepts the one arrived first

## Slide 59: Link State
Reliable Flooding
Flooding of link-state packets. (a) LSP arrives at node X; (b) X floods LSP to A and C; (c) A and C flood LSP to B (but not X); (d) flooding is complete
If B receives LSP from A first, will B send the second copy received from A to C?

## Slide 60
LSP processing

## Slide 61
A
B
D
C
E
7
11
4
15
5
13
19
C
11
15
5
A
7
19
B
4
19
D
4
13
E
5
13
After flooding every node will have the following information:
B
C
A
D
B
D
E
B
E
D
C
Consider this network:
Each node has complete knowledge of the network topology
Apply shortest path algorithm to find routes

## Slide 62: Shortest Path Routing
Dijkstra’s Algorithm - Assume non-negative link weights
  N: set of nodes in the graph
  l((i, j): the non-negative cost associated with the edge between nodes i, j N and l(i, j) =  if no edge connects i and j
  Let s N be the starting node which executes the algorithm to find shortest paths to all other nodes in N
  Two variables used by the algorithm
    M: set of nodes incorporated so far by the algorithm
    C(n) : the cost of the path from s to each node n
    The algorithm
      M = {s}
      For each n in N – {s}
        C(n) = l(s, n)
      while ( N  M)
        M = M  {w} such that C(w) is the minimum
        for all w in (N-M)
        For each n in (N-M)
        C(n) = MIN (C(n), C(w) + l(w, n))

## Slide 63: Shortest Path Routing
In practice, each switch computes its routing table directly from the LSP’s it has collected using a realization of Dijkstra’s algorithm called the forward search algorithm
Specifically each switch maintains two lists, known as Tentative and Confirmed
Each of these lists contains a set of entries of the form (Destination, Cost, NextHop)

## Slide 64
A
B
D
C
E
7
11
4
15
5
13
19
C
11
15
5
A
7
19
B
4
19
D
4
13
E
5
13
After flooding every node will have the following information:
B
C
A
D
B
D
E
B
E
D
C
Consider this network:

## Slide 65
>

## Slide 66
A
7
19
B
C
>

## Slide 67
A
7
19
B
C
>

## Slide 68
A
7
19
B
C
>
Unvisited nodes
Confirmed nodes
Tentative nodes

## Slide 69
A
7
19
B
C
>

## Slide 70
A
7
19
B
C
>

## Slide 71
A
7
19
B
C
>
C
11
15
5
B
D
E
7

## Slide 72
A
7
19
B
C
>
C
11
15
5
B
D
E
Update costs
7

## Slide 73
A
7
19
B
C
>
C
18
22
12
B
D
E
Update costs
7

## Slide 74
22
12
D
E
A
7
18
B
C
C
18
22
12
B
D
E
Update costs
7
>

## Slide 75
22
12
D
E
A
7
18
B
C
>

## Slide 76
22
12
D
E
A
7
C
18
B
>
E
5
13
D
C

## Slide 77
E
5
13
25
D
C
No update.
X
22
12
D
E
A
7
C
18
B
>

## Slide 78
22
12
D
E
A
7
C
18
B
>
B
4
19
A
D
X
18
No update.

## Slide 79
B
4
19
A
D
22
12
D
E
A
7
C
18
B
X
18
22
No update.
>

## Slide 80
22
12
D
E
A
7
C
18
B
>
B
4
19
A
D
X
18
22
No update.

## Slide 81
D
4
13
B
E
X
No update.
X
22
12
D
E
A
7
C
18
B
>

## Slide 82
22
12
D
E
A
7
C
18
B
>
D
4
13
B
E
X
No update.
X

## Slide 83
A
B
D
C
E
7
11
4
15
5
13
19
Consider this network:
22
12
D
E
A
7
C
18
B

## Slide 84: Shortest Path Routing

## Slide 85: Shortest Path Routing

## Slide 86: Shortest Path Routing
Dijkstra’s Algorithm
M = {s}
      For each n in N – {s}
        C(n) = l(s, n)
      while ( N  M)
        M = M  {w} such that C(w) is the minimum
        for all w in (N-M)
        For each n in (N-M)
        C(n) = MIN (C(n), C(w) + l(w, n))
Confirmed list
Tentative list
Newly added member to the confirmed list

## Slide 87: Shortest Path Routing
The algorithm
  Initialize the Confirmed list with an entry for myself; this entry has a cost of 0
  For the node just added to the Confirmed list in the previous step, call it node Next, select its LSP
  For each neighbor (Neighbor) of Next, calculate the cost (Cost) to reach this Neighbor as the sum of the cost from myself to Next and from Next to Neighbor
    If Neighbor is currently on neither the Confirmed nor the Tentative list, then add (Neighbor, Cost, Nexthop) to the Tentative list, where Nexthop is the direction I go to reach Next
    If Neighbor is currently on the Tentative list, and the Cost is less than the currently listed cost for the Neighbor, then replace the current entry with (Neighbor, Cost, Nexthop) where Nexthop is the direction I go to reach Next
  If the Tentative list is empty, stop. Otherwise, pick the entry from the Tentative list with the lowest cost, move it to the Confirmed list, and return to Step 2.

## Slide 88: Open Shortest Path First (OSPF)
  OSPF Header Format OSPF Link State Advertisement

## Slide 89: Comparison of LS and DV algorithms
message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time varies
speed of convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network

## Slide 90: Comparison of LS and DV algorithms
message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time varies
speed of convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network