## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2025
Topic: CIDR, DHCP, NAT, ARP, ICMP
(Textbook chapter 3)
March 5th, 2025

## Slide 2: Class-less Interdomain Routing (CIDR)
Generalizes the ideas of subnetting

## Slide 3
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0

## Slide 4
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
223.1.1.128
223.1.1.192
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0

## Slide 5
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
223.1.1.128
223.1.1.192
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Lesson 1:
Address classes are not needed. Mask can define the number of bits for the network part.
Lesson 2:
Network hierarchies can be hidden from the outside world.
Network addresses can be aggregated/summarized/combined

## Slide 6: CIDR: Classless address

## Slide 7
CIDR: Classless InterDomain Routing
  Network portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
200.23.16.0–200.23.17.255
IP addressing: CIDR
This X bit network part is often called Prefix or Network-prefix

## Slide 8
IP addressing: CIDR
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
forwarding table
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address

## Slide 9: CIDR: Super-netting/ Route aggregation

## Slide 10
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Forwarding tab.
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.0.0/16

## Slide 11
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Forwarding tab.
223.1.0.0/16
223.1.0.0/16

## Slide 12
200.20.0.0/24
200.20.1.0/24
200.20.2.0/24

## Slide 13
200.20.0.0/24
200.20.1.0/24
200.20.2.0/24

## Slide 14
200.20.0.0/24
200.20.1.0/24
200.20.2.0/24
Route aggregation

## Slide 15
Route aggregation with CIDR

## Slide 16: Classless Inter-Domain Routing (CIDR)
IP Address : 12.4.0.0 IP Mask: 255.254.0.0
00001100
00000100
00000000
00000000
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network.
Network number = IP address + Mask
Written as 12.4.0.0/15

## Slide 17: Hierarchical Address Allocation
Hierarchy is key to scalability
  Address allocated in contiguous chunks (prefixes)
  Today, the Internet has about 1,132,452 prefixes
12.0.0.0/8
12.0.0.0/16
12.254.0.0/16
12.1.0.0/16
12.2.0.0/16
12.3.0.0/16
:
:
:
12.3.0.0/24
12.3.1.0/24
:
:
12.3.254.0/24
12.253.0.0/19
12.253.32.0/19
12.253.160.0/19
:
:
:
:
:
  (March 4, 2025. Source: https://ipv4.bgp.he.net/report/netstats)

## Slide 18: Separate Forwarding Entry Per Prefix
Prefix-based forwarding
  Map the destination address to matching prefix
  Forward to the outgoing interface
host
host
host
LAN 1
...
host
host
host
LAN
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 19
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1

## Slide 20
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homing

## Slide 21
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homing
Forwarding tab.

## Slide 22
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homing
Forwarding tab.
201.10.0.0/21
201.10.6.0/23

## Slide 23
11001001.00001010.00000000.00000000/21
11001001.00001010.00000110.00000000/23
11001001.00001010.00000110.00010001
A packet with dest. Addr.: 201.10.6.17
201.10.0.0/21
201.10.6.0/23
CIDR Makes Packet Forwarding Harder
Forwarding table

## Slide 24: CIDR Makes Packet Forwarding Harder
Forwarding table may have many matches
  E.g., entries for 201.10.0.0/21 and 201.10.6.0/23
  The IP address 201.10.6.17 would match both!
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2

## Slide 25: Longest Prefix Match Forwarding
Destination-based forwarding
  Packet has a destination address
  Router identifies longest-matching prefix
  Cute algorithmic problem: very fast lookups
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
201.10.6.17
destination
forwarding table
outgoing link

## Slide 26: Getting an IP address: DHCP Protocol

## Slide 27: IP addresses: how to get one?
Q: How does a host get its IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/…
DHCP: Dynamic Host Configuration Protocol: dynamically get address from a server
  “plug-and-play”

## Slide 28: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network

## Slide 29: DHCP: Dynamic Host Configuration Protocol
DHCP overview:
  host broadcasts “DHCP discover” msg
  DHCP server responds with “DHCP offer” msg
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 30: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 31
<Discover>
Broadcast: is there a DHCP server out there?

## Slide 32
A note on the “broadcast address”

## Slide 33
inet 10.104.216.101  00001010.01101000.11011000.01100101
netmask ff:ff:f0:00  11111111.11111111.11110000.00000000
broadcast 10.104.223.255 
00001010.01101000.11011111.11111111

## Slide 34
Which protocol would you use to exchange these DHCP protocol messages?
<Discover>
Broadcast: is there a DHCP server out there?
Notes: It operates on UDP (User Datagram Protocol) and typically uses port 67 for DHCP servers and port 68 for DHCP clients.

## Slide 35
<Discover>
Broadcast: is there a DHCP server out there?

## Slide 36
<Discover>
Broadcast: is there a DHCP server out there?

## Slide 37
<Discover>
Broadcast: is there a DHCP server out there?

## Slide 38
<Discover>
Broadcast: is there a DHCP server out there?

## Slide 39
<Discover>
Broadcast: is there a DHCP server out there?
yiaddr (“your” IP address)
Used by the server.

## Slide 40
<Discover>
Broadcast: is there a DHCP server out there?
XId (transaction ID)
A random ID set by the client to keep track of the “question-answer” pair.

## Slide 41
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use

## Slide 42
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use

## Slide 43
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use

## Slide 44
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use

## Slide 45
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use

## Slide 46
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use
<Request>
Broadcast: OK. I’ll take that IP address! Can I ?

## Slide 47
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use
<Request>
Broadcast: OK. I’ll take that IP address! Can I ?
Notes: It is broadcast so that other DHCP servers can get a notification. The behavior is different for first time aquiring address vs renewing the lease of the address.

## Slide 48
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use
<Request> Broadcast: OK. I’ll take that IP address! Can I ?

## Slide 49
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use
<Request> Broadcast: OK. I’ll take that IP address! Can I ?
<Ack>
Broadcast: OK. You’ve got that IP address!

## Slide 50
<Discover>
Broadcast: is there a DHCP server out there?
<Offer>
Broadcast: I’m a DHCP server! Here’s an IP address you can use
<Request> Broadcast: OK. I’ll take that IP address! Can I ?
<Ack>
Broadcast: OK. You’ve got that IP address!
Discussion Point 1: The transaction ID (xid). RFC 2131
Discussion Point 2: Broadcast address. (Limited/Directed broadcast)
Notes: RFC 2131, Page [39]: The DHCP client broadcasts DHCPDISCOVER, DHCPREQUEST and DHCPINFORM messages, unless the client knows the address of a DHCP server. The client unicasts DHCPRELEASE messages to the server.
DHCP is not intended for use in configuring routers.

## Slide 51: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 52: Dynamic Host Configuration Protocol (DHCP)
DHCP server is responsible for providing configuration information to hosts
DHCP server maintains a pool of available addresses
There is at least one DHCP server for an administrative domain (a server or a relay agent per subnet)

## Slide 53: DHCP relay
Newly booted or attached host sends DHCPDISCOVER message to a special IP address (255.255.255.255)
DHCP relay agent unicasts the message to DHCP server and waits for the response

## Slide 54
DHCP relay

## Slide 55
PC: http://www.tcpipguide.com/free/t_BOOTPRelayAgentsForwardingAgents-3.htm

## Slide 56
Check your IP addresses
(ifconfig/ipconfig)

## Slide 57
Check your IP addresses
(ifconfig/ipconfig)

## Slide 58: Private Address Space & NAT

## Slide 60: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers

## Slide 61: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 62: NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 63: NAT: network address translation
implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 64: NAT: network address translation
implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 65: NAT: network address translation
16-bit port-number field:
  Over 60,000 simultaneous connections with a single LAN-side address!
NAT challenges:
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  NAT traversal: what if client wants to connect to server behind NAT?

## Slide 66: Network-specific address (IP address) vs LAN-specific address (HW address)

## Slide 67
Destination
Source
Router
Two perspectives of addresses:
(1)Network-to-network & (2)machine-to-machine

## Slide 68
Source
Router
application
transport
network
link
physical

## Slide 69
Source
Router
network
link
physical
application
transport
network
link
physical

## Slide 70
Router
Hierarchical address for addressing networks
(IP address)
network
link
physical

## Slide 71
Source
Router
application
transport
network
link
physical
network
link
physical

## Slide 72
Source
Router
application
transport
network
link
physical
network
link
physical
Flat address for addressing machines at the link-layer
(MAC address)

## Slide 73: Address Resolution Protocol (ARP)

## Slide 74: MAC addresses and ARP
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  e.g.: 1A-2F-BB-76-09-AD
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)

## Slide 75: MAC addresses and ARP
each adapter on LAN has unique LAN addr. or MAC addr.
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 76: MAC addresses (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address not portable
  address depends on IP subnet to which node is attached

## Slide 77: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 78: ARP protocol: same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 79: Address Translation Protocol (ARP)
Map IP addresses into physical addresses
  destination host
  next hop router
Techniques
  encode physical address in host part of IP address
  table-based
ARP (Address Resolution Protocol)
  table of IP to physical address bindings
  broadcast request if IP address not in table
  target machine responds with its physical address
  table entries are discarded if not refreshed
  Query message include the physical address of the sending host. Why?

## Slide 80: ARP Packet Format
  HardwareType: type of physical network (e.g., Ethernet)
  ProtocolType: type of higher layer protocol (e.g., IP)
  HLEN & PLEN: length of physical and protocol addresses
  Operation: request or response
  Source/Target Physical/Protocol addresses