## Slide 1
Computer Networks
Nirupam Roy
M-W 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2025
Topic: Advanced Internetworking and BGP
(Textbook chapter 4)
April 30th, 2025

## Slide 2: BGP Next Hop Attribute
Every time a route announcement crosses an AS boundary, the Next Hop attribute is changed to the IP address of the border router that announced the route.
AS 6431
AT&T Research
135.207.0.0/16
Next Hop = 12.125.133.90
AS 7018
AT&T
AS 12654
RIPE NCC
RIS project
12.125.133.90
135.207.0.0/16
Next Hop = 12.127.0.121
12.127.0.121

## Slide 3: Join EGP with IGP For Connectivity
Forwarding Table
Forwarding Table
AS 1
AS 2
192.0.2.1
135.207.0.0/16
10.10.10.10
EGP
192.0.2.1
135.207.0.0/16
destination
next hop
10.10.10.10
192.0.2.0/30
destination
next hop
135.207.0.0/16
Next Hop = 192.0.2.1
192.0.2.0/30
135.207.0.0/16
destination
next hop
10.10.10.10
+
192.0.2.0/30
10.10.10.10

## Slide 4: A dive into the BGP policies

## Slide 5: Nontransit vs. Transit ASes
ISP 1
ISP 2
Nontransit AS
might be a corporate
or campus network.
Could be a “content
provider”
NET A
Traffic NEVER
flows from ISP 1
through NET A to ISP 2
(At least not intentionally!)
IP traffic
Internet Service
providers (often)
have transit
networks

## Slide 6: Selective Transit
NET B
NET C
NET A provides transit
between NET B and NET C
and between NET D
and NET C
NET A
NET D
NET A DOES NOT
provide transit
Between NET D
and NET B
Most transit networks transit in a selective manner…
IP traffic

## Slide 7: Customers and Providers
Customer pays provider for access to the Internet
provider
customer
IP traffic
provider
customer

## Slide 8: Customers Don’t Always Need BGP
provider
customer
Nail up default routes 0.0.0.0/0
pointing to provider.
Nail up routes 192.0.2.0/24
pointing to customer
192.0.2.0/24
Static routing is the most common way of connecting an
autonomous routing domain to the Internet.
This helps explain why BGP is a mystery to many …

## Slide 9: Customer-Provider Hierarchy
IP traffic
provider
customer

## Slide 10: The Peering Relationship
peer
peer
customer
provider
Peers provide transit between
their respective customers
Peers do not provide transit
between peers
Peers (often) do not exchange $$$
traffic
allowed
traffic NOT
allowed

## Slide 11: Peering Provides Shortcuts
Peering also allows connectivity between
the customers of “Tier 1” providers.
peer
peer
customer
provider

## Slide 12: BGP-4
BGP = Border Gateway Protocol
Is a Policy-Based routing protocol
Is the de facto EGP of today’s global Internet
Relatively simple protocol, but configuration is complex and the entire world can see, and be impacted by, your mistakes.
1989 : BGP-1 [RFC 1105]
  Replacement for EGP (1984, RFC 904)
1990 : BGP-2 [RFC 1163]
1991 : BGP-3 [RFC 1267]
1995 : BGP-4 [RFC 1771]
  Support for Classless Interdomain Routing (CIDR)

## Slide 13: BGP Operations (Simplified)
Establish session on
TCP port 179
Exchange all
active routes
Exchange incremental
updates
AS1
AS2
While connection
is ALIVE exchange
route UPDATE messages
BGP session

## Slide 14: Four Types of BGP Messages
Open : Establish a peering session.
Keep Alive : Handshake at regular intervals.
Notification : Shuts down a peering session.
Update : Announcing new routes or withdrawing previously announced routes.
announcement
=
prefix + attributes values

## Slide 15: BGP Attributes
Value Code Reference
----- --------------------------------- ---------
1 ORIGIN [RFC1771]
2 AS_PATH [RFC1771]
3 NEXT_HOP [RFC1771]
4 MULTI_EXIT_DISC [RFC1771]
5 LOCAL_PREF [RFC1771]
6 ATOMIC_AGGREGATE [RFC1771]
7 AGGREGATOR [RFC1771]
8 COMMUNITY [RFC1997]
9 ORIGINATOR_ID [RFC2796]
10 CLUSTER_LIST [RFC2796]
11 DPA [Chen]
12 ADVERTISER [RFC1863]
13 RCID_PATH / CLUSTER_ID [RFC1863]
14 MP_REACH_NLRI [RFC2283]
15 MP_UNREACH_NLRI [RFC2283]
16 EXTENDED COMMUNITIES [Rosen]
...
255 reserved for development
From IANA: http://www.iana.org/assignments/bgp-parameters
Most important attributes
Not all attributes
need to be present in
every announcement
Notes: In BGP, the treat-as-withdraw path attribute is used to effectively rescind a path, meaning it removes a prefix from the BGP routing table if a specific path attribute is matched.

## Slide 16: Attributes are Used to Select Best Routes
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
Given multiple
routes to the same
prefix, a BGP speaker
must pick at most
one best route
(Note: it could reject
them all!)

## Slide 17: BGP Next Hop Attribute
Every time a route announcement crosses an AS boundary, the Next Hop attribute is changed to the IP address of the border router that announced the route.
AS 6431
AT&T Research
135.207.0.0/16
Next Hop = 12.125.133.90
AS 7018
AT&T
AS 12654
RIPE NCC
RIS project
12.125.133.90
135.207.0.0/16
Next Hop = 12.127.0.121
12.127.0.121

## Slide 18: Join EGP with IGP For Connectivity
Forwarding Table
Forwarding Table
AS 1
AS 2
192.0.2.1
135.207.0.0/16
10.10.10.10
EGP
192.0.2.1
135.207.0.0/16
destination
next hop
10.10.10.10
192.0.2.0/30
destination
next hop
135.207.0.0/16
Next Hop = 192.0.2.1
192.0.2.0/30
135.207.0.0/16
destination
next hop
10.10.10.10
+
192.0.2.0/30
10.10.10.10

## Slide 19: Implementing Customer/Provider and Peer/Peer relationships
Enforce transit relationships
  Outbound route filtering
Enforce order of route preference
  provider < peer < customer
Two parts:

## Slide 20: Import Routes
From
peer
From
peer
From
provider
From
provider
From
customer
From
customer
provider route
customer route
peer route
AS-219

## Slide 21: Import Routes
From
peer
From
peer
From
provider
From
provider
From
customer
From
customer
provider route
customer route
peer route

## Slide 22: Export Routes
To
peer
To
peer
To
customer
To
customer
To
provider
From
provider
provider route
customer route
peer route
ISP route
filters
block
?
?
?
?
?
?
provider route
customer route
peer route

## Slide 23: Export Routes
To
peer
To
peer
To
customer
To
customer
To
provider
From
provider
provider route
customer route
peer route
ISP route
filters
block
provider route
customer route
peer route

## Slide 24: Export Routes
To
peer
To
peer
To
customer
To
customer
To
provider
From
provider
provider route
customer route
peer route
ISP route
filters
block
provider route
customer route
peer route

## Slide 25: Export Routes
To
peer
To
peer
To
customer
To
customer
To
provider
From
provider
provider route
customer route
peer route
ISP route
filters
block
provider route
customer route
peer route

## Slide 26: How Can Routes be Colored? BGP Communities!
A community value is 32 bits
By convention,
first 16 bits is
ASN indicating
who is giving it
an interpretation
community
number
Very powerful
BECAUSE it
has no (predefined) meaning
Community Attribute = a list of community values.
(So one route can belong to multiple communities)
RFC 1997 (August 1996)
Used for signalling
within and between
ASes
Two reserved communities
no_advertise 0xFFFFFF02: don’t pass to BGP neighbors
  no_export = 0xFFFFFF01: don’t export out of AS

## Slide 27
BGP Communities examples
Notes: no-exportDon’t advertise this route to external (eBGP) peers.no-advertiseDon’t advertise this route to any peers (iBGP or eBGP).local-ASDon’t advertise this route outside the local AS, even within confederations.

## Slide 28
Tag customer routes with 64512:100.
Instruct Router B to only advertise routes with 64512:100.

## Slide 29
Instruct Router B to only advertise routes with 64512:100.
Tag customer routes with 64512:100. (on Router A)

## Slide 30
BGP Community attribute: Example

## Slide 31: Tweak Tweak Tweak
For inbound traffic
  Filter outbound routes
  Tweak attributes on outbound routes in the hope of influencing your neighbor’s best route selection
For outbound traffic
  Filter inbound routes
  Tweak attributes on inbound routes to influence best route selection
outbound
routes
inbound
routes
inbound
traffic
outbound
traffic
In general, an AS has more
control over outbound traffic

## Slide 32: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 33: Route Selection Summary
Highest Local Preference
Shortest ASPATH
Lowest MED
i-BGP < e-BGP
Lowest IGP cost
to BGP egress
Lowest router ID
traffic engineering
Enforce relationships
Throw up hands and
break ties

## Slide 34: Hot Potato Routing
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS1,AS3,X
OSPF link weights
201
152
112
263

## Slide 35: Back to Frank …
AS 1
AS 2
AS 4
AS 3
13.13.0.0/16
peer
peer
customer
provider
local pref = 80
local pref = 100
local pref = 90
Higher Local
preference values
are more preferred
Local preference only used in iBGP

## Slide 36: Implementing Backup Links with Local Preference (Outbound Traffic)
Forces outbound traffic to take primary link, unless link is down.
AS 1
primary link
backup link
Set Local Pref = 100
for all routes from AS 1
AS 65000
Set Local Pref = 50
for all routes from AS 1

## Slide 37: Multihomed Backups (Outbound Traffic)
Forces outbound traffic to take primary link, unless link is down.
AS 1
primary link
backup link
Set Local Pref = 100
for all routes from AS 1
AS 2
Set Local Pref = 50
for all routes from AS 3
AS 3
provider
provider

## Slide 38: ASPATH Attribute
AS7018
135.207.0.0/16
AS Path = 6341
AS 1239
Sprint
AS 1755
Ebone
AT&T
AS 3549
Global Crossing
135.207.0.0/16
AS Path = 7018 6341
135.207.0.0/16
AS Path = 3549 7018 6341
AS 6341
135.207.0.0/16
AT&T Research
Prefix Originated
AS 12654
RIPE NCC
RIS project
AS 1129
Global Access
135.207.0.0/16
AS Path = 7018 6341
135.207.0.0/16
AS Path = 1239 7018 6341
135.207.0.0/16
AS Path = 1755 1239 7018 6341
135.207.0.0/16
AS Path = 1129 1755 1239 7018 6341

## Slide 39: Interdomain Loop Prevention
BGP at AS YYY will never accept a route with ASPATH containing YYY.
AS 7018
12.22.0.0/16
ASPATH = 1 333 7018 877
Don’t Accept!
AS 1

## Slide 40: Traffic Often Follows ASPATH
AS 4
AS 3
AS 2
AS 1
135.207.0.0/16
135.207.0.0/16
ASPATH = 3 2 1
IP Packet
Dest =
135.207.44.66

## Slide 41: … But It Might Not
AS 4
AS 3
AS 2
AS 1
135.207.0.0/16
135.207.0.0/16
ASPATH = 3 2 1
IP Packet
Dest =
135.207.44.66
AS 5
135.207.44.0/25
ASPATH = 5
135.207.44.0/25
AS 2 filters all
subnets with masks
longer than /24
135.207.0.0/16
ASPATH = 1
From AS 4, it
may look like this
packet will take
path 3 2 1, but it
actually takes
path 3 2 5

## Slide 42: Shorter Doesn’t Always Mean Shorter
In fairness:
could you do
this “right” and
still scale?
Exporting internal
state would
dramatically
increase global
instability and
amount of routing
state
AS 4
AS 3
AS 2
AS 1
Mr. BGP says that
path 4 1 is better
than path 3 2 1
Duh!

## Slide 43: Shedding Inbound Traffic with ASPATH Padding Hack
Padding will (usually)
force inbound
traffic from AS 1
to take primary link
AS 1
192.0.2.0/24
ASPATH = 2 2 2
customer
AS 2
provider
192.0.2.0/24
backup
primary
192.0.2.0/24
ASPATH = 2

## Slide 44: Padding May Not Shut Off All Traffic
AS 1
192.0.2.0/24
ASPATH = 2 2 2 2 2 2 2 2 2 2 2 2 2 2
customer
AS 2
provider
192.0.2.0/24
192.0.2.0/24
ASPATH = 2
AS 3
provider
AS 3 will send
traffic on “backup”
link because it prefers
customer routes and local
preference is considered
before ASPATH length!
Padding in this way is often
used as a form of load
balancing
backup
primary

## Slide 45: COMMUNITY Attribute to the Rescue!
AS 1
customer
AS 2
provider
192.0.2.0/24
192.0.2.0/24
ASPATH = 2
AS 3
provider
backup
primary
192.0.2.0/24
ASPATH = 2
COMMUNITY = 3:70
Customer import policy at AS 3:
If 3:90 in COMMUNITY then
set local preference to 90
If 3:80 in COMMUNITY then
set local preference to 80
If 3:70 in COMMUNITY then
set local preference to 70
AS 3: normal
customer local
pref is 100,
peer local pref is 90

## Slide 46: Hot Potato Routing: Go for the Closest Egress Point
192.44.78.0/24
15
56
IGP distances
egress 1
egress 2
This Router has two BGP routes to 192.44.78.0/24.
Hot potato: get traffic off of your network as
Soon as possible. Go for egress 1!

## Slide 47: Getting Burned by the Hot Potato
15
56
17
2865
High bandwidth
Provider backbone
Low bandwidth
customer backbone
Heavy
Content
Web Farm
Many customers want
their provider to
carry the bits!
tiny http request
huge http reply
SFO
NYC
San Diego

## Slide 48: Cold Potato Routing with MEDs (Multi-Exit Discriminator Attribute)
15
56
17
2865
Heavy
Content
Web Farm
192.44.78.0/24
192.44.78.0/24
MED = 15
192.44.78.0/24
MED = 56
This means that MEDs must be considered BEFORE
IGP distance!
Prefer lower
MED values
Note1 : some providers will not listen to MEDs
Note2 : MEDs need not be tied to IGP distance

## Slide 49: Route Selection Summary
Highest Local Preference
Shortest ASPATH
Lowest MED
i-BGP < e-BGP
Lowest IGP cost
to BGP egress
Lowest router ID
traffic engineering
Enforce relationships
Throw up hands and
break ties

## Slide 50: BGP Attacks

## Slide 51: Prefix Hijacking
1
2
3
4
5
6
7
12.34.0.0/16
12.34.0.0/16
Originating someone else’s prefix
  What fraction of the Internet believes it?

## Slide 52: Prefix highjack
http://queue.acm.org/detail.cfm?id=2668966

## Slide 53: Sub-Prefix Hijacking
Originating a more-specific prefix
  Every AS picks the bogus route for that prefix
  Traffic follows the longest matching prefix
1
2
3
4
5
6
7
12.34.0.0/16
12.34.158.0/24

## Slide 54: Sub-prefix hijack
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
  February 2008 : Pakistan Telecom hijacks YouTube
Notes: -level of autonomous systems
-e.g., YouTube, AT&T, pakistan telecom
-routing is done on IP addresses, so when someone wants to go to YouTube they get YouTube’s IP address and YouTube announces to the world that they have the ip address and traffic is forwarded towards them. So here multinet would route to it’s provider pakistan telecom that then forwards the traffic on to youtube.
-these networks chosen for a specific reason which is that there was an incident in february 2008 pakistan telecom actually high jacked traffic going to youtube (misconfiguration).
-they announced to the world that they’re youtube and traffic destined to youtube was routed to them
-youtube was unavailable for a couple of hours as operators phone each other to figure out what was going on.

## Slide 55: Pakistan Telecom: Sub-prefix hijack
  Here’s what should have happened….
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
X
Hijack + drop packets going to YouTube
  Block your own customers.

## Slide 56: Pakistan Telecom: Sub-prefix hijack
  But here’s what Pakistan ended up doing…
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
No, I’m YouTube!
IP 208.65.153.0 / 24
Notes: Our works focuses on attacks of this flavor..

## Slide 57: Bogus AS Paths to Hide Hijacking
Adds AS hop(s) at the end of the path
  E.g., turns “701 88” into “701 88 3”
Motivations
  Evade detection for a bogus route
  E.g., by adding the legitimate AS to the end
Hard to tell that the AS path is bogus…
  Even if other ASes filter based on prefix ownership
701
88
3
18.0.0.0/8
18.0.0.0/8

## Slide 58: Path-Shortening Attacks
Remove ASes from the AS path
  E.g., turn “701 3715 88” into “701 88”
Motivations
  Make the AS path look shorter than it is
  Attract sources that normally try to avoid AS 3715
  Help AS 88 look like it is closer to the Internet’s core
Who can tell that this AS path is a lie?
  Maybe AS 88 *does* connect to AS 701 directly
701
88
3715
?

## Slide 59: Attacks that Add a Bogus AS Hop
Add ASes to the path
  E.g., turn “701 88” into “701 3715 88”
Motivations
  Trigger loop detection in AS 3715
    Denial-of-service attack on AS 3715
    Or, blocking unwanted traffic coming from AS 3715!
  Make your AS look like is has richer connectivity
Who can tell the AS path is a lie?
  AS 3715 could, if it could see the route
  AS 88 could, but would it really care as long as it received data traffic meant for it?
701
88

## Slide 60: Violating “Consistent Export” to Peers
Peers require consistent export
  Prefix advertised at all peering points
  Prefix advertised with same AS path length
Reasons for violating the policy
  Trick neighbor into “cold potato”
  Configuration mistake
Main defense
  Analyzing BGP updates
  … or data traffic
  … for signs of inconsistency
src
dest
Bad AS
data
BGP

## Slide 61: Other Attacks
Attacks on BGP sessions
  Confidentiality of BGP messages
  Denial-of-service on BGP session
  Inserting, deleting, modifying, or replaying messages
Resource exhaustion attacks
  Too many IP prefixes (e.g., BGP “512K Day”)
  Too many BGP update messages
Data-plane attacks
  Announce one BGP routes, but use another

## Slide 62: Solution Techniques
Protective filtering
  Know your neighbors
Anomaly detection
  Suspect the unexpected
Checking against registries
  Establish ground truth for prefix origination
Signing and verifying
  Prevent bogus AS PATHs
Data-plane verification
  Ensure the path is actually followed