## Slide 1
CMSC 417: Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
Spring 2025
Topic: Overview of networks Part-2
(Textbook chapter 1)
Jan 29th, 2025

## Slide 2
Our Goal:
Get “feel” and terminology
More depth, detail later in course
Approach:
  Use Internet as example

## Slide 3: Roadmap
  What is the Internet?
  Network edge
  Network core
  Delay, Loss, Throughput in networks
  Protocol layers, service models

## Slide 4: What is the Internet ?

## Slide 5
internet == The network of networks

## Slide 6
internet == The network of networks
The Internet?

## Slide 7
MOOCs
Online Content
Search Engines
Abstraction
Notes: So building networks is hard
But unfortunately, computer networks are becoming increasingly critical to our daily lives
You know all the standard uses of computers…
Social networking
Gaming
But there’s a lot you may not thinki about
Financial sector – trillions of dollars –
Critical infrastructures – power grid, water delibvery systems – now all managed and operated with IP networks
911 communication services
…
Remote medicine
Brakes of your car
Power grid and critical infrastructure
Financial and trading networks – move billions of dollars per day over computer netowrks
Computer networks are no longer just for fun and games
People’s lives every day depend on the availability and functioning of computer netowrks
Makign it very important that we build them well, and protect them from adversaries,

## Slide 8: What’s the Internet: Components View
Billions of connected computing devices:
  hosts = end systems
  running network apps
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
smartphone
PC
server
wireless
laptop
mobile network
global ISP
regional ISP
home
network
institutional
network
Notes: 8

## Slide 9
Internet: “network of networks”
  Interconnected ISPs
Protocols control sending, receiving of messages
  e.g., TCP, IP, HTTP, Skype, 802.11
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
  (also ISO, IEEE)
mobile network
global ISP
regional ISP
home
network
institutional
network
What’s the Internet: Protocols View
Notes: Associate press: an Internet vs the Internet

## Slide 10: What’s a protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
… specific messages sent
… specific actions taken when messages received, or other events
Network protocols:
Machines rather than humans
All communication activity in Internet governed by protocols
Protocols define format, order of messages sent and received among network entities, and actions taken on message transmission, receipt

## Slide 11
A human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
What’s a protocol?
client
server

## Slide 12: What’s the Internet: A Service View
Infrastructure that provides services to applications:
  Web, VoIP, email, games, e-commerce, social nets, …
Provides programming interface to apps
  hooks that allow sending and receiving app programs to “connect” to Internet
  provides service options, analogous to postal service
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 13
Circuit-Switching / Packet-Switching
How to connect computers in a network?

## Slide 14
Point-to-point connection

## Slide 16
MOOCs
Online Content
Search Engines
Notes: So building networks is hard
But unfortunately, computer networks are becoming increasingly critical to our daily lives
You know all the standard uses of computers…
Social networking
Gaming
But there’s a lot you may not thinki about
Financial sector – trillions of dollars –
Critical infrastructures – power grid, water delibvery systems – now all managed and operated with IP networks
911 communication services
…
Remote medicine
Brakes of your car
Power grid and critical infrastructure
Financial and trading networks – move billions of dollars per day over computer netowrks
Computer networks are no longer just for fun and games
People’s lives every day depend on the availability and functioning of computer netowrks
Makign it very important that we build them well, and protect them from adversaries,

## Slide 17
All pair Point-to-point connection
Notes: It is a viable solution (for small networks, like home networks, access networks—ethernet, USB hub that is also a network by its own merits…it addresses protocols etc.). Only question is that is this connection topology suitable for the Internet?

## Slide 18
All pair Point-to-point connection
Is this scalable?

## Slide 19
Shared channel
Multiple access

## Slide 20
Shared channel
Multiple access
How to direct the flow of data at these points?

## Slide 21
Multiplexing multiple logical flows over a single physical link
Switching

## Slide 22: Circuit Switching
end-end resources allocated to, reserved for “call” between source & destination:
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
commonly used in traditional telephone networks

## Slide 23: Circuit Switching: Telephone (voice)

## Slide 24
Circuit Switching: Telephone (data)

## Slide 25: Circuit Switching
end-end resources allocated to, reserved for “call” between source & destination:
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
commonly used in traditional telephone networks
Circuit segment idle if there is not enough data

## Slide 26: Packet Switching: What is a packet (packet/datagram/frame)

## Slide 27
Data packets: A format for organizing data
Analogy: JPEG file format

## Slide 28: Packet Switching: What is a packet (packet/datagram/frame)

## Slide 29: Packet Switching
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link

## Slide 30: Switch vs Router
Switches
Routers

## Slide 31
What’s the Internet?
Notes: Associate press: an Internet vs the Internet

## Slide 32: Chapter 1: Roadmap
  What is the Internet?
  Network edge
  Network core
  Delay, Loss, Throughput in networks
  Protocol layers, service models
  History

## Slide 33
Network Edge
Notes: So building networks is hard
But unfortunately, computer networks are becoming increasingly critical to our daily lives
You know all the standard uses of computers…
Social networking
Gaming
But there’s a lot you may not thinki about
Financial sector – trillions of dollars –
Critical infrastructures – power grid, water delibvery systems – now all managed and operated with IP networks
911 communication services
…
Remote medicine
Brakes of your car
Power grid and critical infrastructure
Financial and trading networks – move billions of dollars per day over computer netowrks
Computer networks are no longer just for fun and games
People’s lives every day depend on the availability and functioning of computer netowrks
Makign it very important that we build them well, and protect them from adversaries,

## Slide 34
Network Edge

## Slide 35: A closer look at network structure:
Network edge:
  hosts: clients and servers
  servers often in data centers
  access networks, physical media: wired, wireless communication links

## Slide 36
Access Network: Home Network
to/from headend or central office
cable or DSL modem
(DSL=Digital Subscriber Line)
router, firewall
wired Ethernet
wireless access
point
wireless
devices
often combined
in single box

## Slide 37
Access Network: Home Network

## Slide 38: Enterprise Access Networks (Ethernet)
Typically used in companies, universities, etc.
  10 Mbps, 100Mbps, 1Gbps, 10Gbps transmission rates
  Today, end systems typically connect into Ethernet switch
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)

## Slide 39: Wireless Access Networks
Shared wireless access network connects end system to router
  via base station aka “access point”
Wireless LANs:
  within building (100 ft.)
  802.11b/g/n (WiFi): 11, 54, 450 Mbps transmission rate
Wide-area wireless access
  provided by telco (cellular) operator, 10’s km
  between 1 and 10 Mbps
  3G, 4G: LTE, 5G,…
to Internet
to Internet

## Slide 40: Chapter 1: Roadmap
  What is the Internet?
  Network edge
  Network core
  Delay, Loss, Throughput in networks
  Protocol layers, service models
  History

## Slide 41
MOOCs
Online Content
Search Engines
Network Core
Notes: So building networks is hard
But unfortunately, computer networks are becoming increasingly critical to our daily lives
You know all the standard uses of computers…
Social networking
Gaming
But there’s a lot you may not thinki about
Financial sector – trillions of dollars –
Critical infrastructures – power grid, water delibvery systems – now all managed and operated with IP networks
911 communication services
…
Remote medicine
Brakes of your car
Power grid and critical infrastructure
Financial and trading networks – move billions of dollars per day over computer netowrks
Computer networks are no longer just for fun and games
People’s lives every day depend on the availability and functioning of computer netowrks
Makign it very important that we build them well, and protect them from adversaries,

## Slide 42: The Network Core
Mesh of interconnected routers
Packet-switching:
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity

## Slide 43: Two key network-core functions
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
destination address in arriving
packet’s header

## Slide 44: Why is routing challenging?
1
2
3
No central control in a distributed system.

## Slide 45: Packet-switching: Store-and-Forward
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)

## Slide 46
Organization of the
“Network of networks”

## Slide 47: Internet Structure: Network of Networks
End systems connect to Internet via access ISPs (Internet Service Providers)
  residential, company and university ISPs
Access ISPs in turn must be interconnected.
  so that any two hosts can send packets to each other
Resulting network of networks is very complex
  evolution was driven by economics and national policies
Let’s take a stepwise approach to describe current Internet structure

## Slide 48
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Internet Structure: Network of Networks

## Slide 49
Option: connect each access ISP to every other access ISP?
access
net
access
net
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
access
net
access
net
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…
Internet Structure: Network of Networks

## Slide 50
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to one global transit ISP?
Customer and provider ISPs have economic agreement.
global ISP
Internet Structure: Network of Networks

## Slide 51
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
Internet Structure: Network of Networks
But if one global ISP is viable business, there will be competitors ….

## Slide 52
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
But if one global ISP is viable business, there will be competitors …. which must be interconnected
IXP
peering link
Internet exchange point
IXP
Internet Structure: Network of Networks

## Slide 53
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
… and regional networks may arise to connect access nets to ISPs
Internet Structure: Network of Networks
regional net

## Slide 54
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
Content provider/distribution network
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users
Internet Structure: Network of Networks
regional net

## Slide 55
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider/distribution network (e.g., Google, Akamai): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
IXP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
Regional ISP
Regional ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Internet Structure: Network of Networks

## Slide 56: Chapter 1: Roadmap
  What is the Internet?
  Network edge
  Network core
  Delay, Loss, Throughput in networks
  Protocol layers, service models
  History

## Slide 57: How do loss and delay occur?
A
B
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 58
Thank you