## Slide 1
CMSC 417: Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
Spring 2025
Topic: Internetworking (LS routing + IP)
(Textbook chapter 3)
Feb 17th, 2025

## Slide 2
Link State Routing
Routing by rumor
Consistent
view of topology

## Slide 3: Link State Routing
Strategy:
Send to all nodes (not just neighbors) information about neighbors (not connection to all nodes).
All nodes will know the link-state information of all other nodes

## Slide 4: Link State Routing
Link State Packet (LSP):
  The ID of the node that created the LSP
  (2) Costs of links to each directly connected neighbor
  (3) A sequence number (SEQNO)
  [To distinguish a newer LSP from the old ones]
  [Smaller number == older LSP]
  (4) A Time-To-Live (TTL) for this packet
  [To make sure old information is eventually removed
  from the network]
Strategy:
Send to all nodes (not just neighbors) information about neighbors (not connection to all nodes).
What is the unit of the “Time-to-Live”?

## Slide 5
Link State Routing
(1) Reliable flooding
[Makes sure all nodes in the network get a copy of LSP from all other nodes]
(2) Route calculation
(Dijkstra’s shortest path algorithm)
[Calculates the shortest path from each node to all other nodes and the corresponding next-hop]

## Slide 6
Link State Routing: Reliable flooding
  Store most recent LSP from each node
  Forward LSP to all nodes but one that sent it
  Generate new LSP periodically; increment SEQNO
  Start SEQNO at 0 when reboot
  Decrement TTL before flooding it to neighbors.
  Also age the stored LSP (decrement TTL)
  Discard when TTL=0.
Goals:
0) Ensure all nodes get LSPs from all other
Flood in minimum time
Minimize total routing traffic

## Slide 7: Link State
Reliable Flooding
Flooding of link-state packets. (a) LSP arrives at node X; (b) X floods LSP to A and C; (c) A and C flood LSP to B (but not X); (d) flooding is complete
Gets two identical copies of LSP.
Accepts the one arrived first

## Slide 8: Link State
Reliable Flooding
Flooding of link-state packets. (a) LSP arrives at node X; (b) X floods LSP to A and C; (c) A and C flood LSP to B (but not X); (d) flooding is complete
If B receives this LSP from A first, will B send the second copy received from C to A?
This copy is not added to database.
But will ‘B’ flood it?

## Slide 9
LSP processing

## Slide 10
LSP processing flow
LSP available
Exists in
Database?
Flood LSP
Add to database
Run shortest path
algorithm
End
Ignore
Is it
a newer LSP?
(seq. #)
Yes
No
No
Yes

## Slide 11
A
B
D
C
E
7
11
4
15
5
13
19
C
11
15
5
A
7
19
B
4
19
D
4
13
E
5
13
After flooding every node will have the following information:
B
C
A
D
B
D
E
B
E
D
C
Consider this network:
Each node has complete knowledge of the network topology
Apply shortest path algorithm to find routes

## Slide 12
A
B
D
C
E
7
11
4
15
5
13
19
Consider this network:

## Slide 13
A
B
D
C
E
7
11
4
15
5
13
19
C
11
15
5
A
7
19
B
4
19
D
4
13
E
5
13
After flooding every node will have the following information:
B
C
A
D
B
D
E
B
E
D
C
Consider this network:
C
15
A
7
C
11

## Slide 14
A
B
D
C
E
7
11
4
15
5
13
19
C
11
15
5
A
7
19
B
4
19
D
4
13
E
5
13
After flooding every node will have the following information:
B
C
A
D
B
D
E
B
E
D
C
Consider this network:
C
15
A
7
C
11
Each node has complete knowledge of the network topology
Apply shortest path algorithm to find routes

## Slide 15: Shortest Path Routing
Dijkstra’s Algorithm - Assume non-negative link weights
  N: set of nodes in the graph
  l((i, j): the non-negative cost associated with the edge between nodes i, j N and l(i, j) =  if no edge connects i and j
  Let s N be the starting node which executes the algorithm to find shortest paths to all other nodes in N
  Two variables used by the algorithm
    M: set of nodes incorporated so far by the algorithm
    C(n) : the cost of the path from s to each node n
    The algorithm
      M = {s}
      For each n in N – {s}
        C(n) = l(s, n)
      while ( N  M)
        M = M  {w} such that C(w) is the minimum
        for all w in (N-M)
        For each n in (N-M)
        C(n) = MIN (C(n), C(w) + l(w, n))

## Slide 16: Shortest Path Routing
In practice, each switch computes its routing table directly from the LSP’s it has collected using a realization of Dijkstra’s algorithm called the forward search algorithm
Specifically, each switch maintains two lists, known as Tentative and Confirmed
Each of these lists contains a set of entries of the form (Destination, Cost, NextHop)

## Slide 17
A
B
D
C
E
7
11
4
15
5
13
19
C
11
15
5
A
7
19
B
4
19
D
4
13
E
5
13
After flooding every node will have the following information:
B
C
A
D
B
D
E
B
E
D
C
Consider this network:
C
15
A
7
C
11

## Slide 18
>

## Slide 19
A
7
19
B
C
>

## Slide 20
A
7
19
B
C
>

## Slide 21
A
7
19
B
C
>
Unvisited nodes
Confirmed nodes
Tentative nodes

## Slide 22
A
7
19
B
C
>
Unvisited nodes
Confirmed nodes
Tentative nodes

## Slide 23
A
7
19
B
C
>
‘Confirm’ the lowest cost nodes
from the list of ‘tentative’ nodes.

## Slide 24
A
7
19
B
C
>
C
11
15
5
B
D
E
7
A
X
X
= Ignore the confirmed nodes
‘Confirm’ the lowest cost nodes
from the list of ‘tentative’ nodes.
… and find out this newly ‘confirmed’
node’s LSP (i.e., C’s LSP).

## Slide 25
A
7
19
B
C
>
C
11
15
5
B
D
E
Update costs
7
A
X
By adding the cost
to reach ‘C’.

## Slide 26
A
7
19
B
C
>
C
18
22
12
B
D
E
Costs updated
7
A
X

## Slide 27
22
12
D
E
A
7
18
B
C
C
18
22
12
B
D
E
>
7
A
X
Join with minimum link costs
Costs updated
Note that B’s link is updated.

## Slide 28
22
12
D
E
A
7
18
B
C
>

## Slide 29
22
12
D
E
A
7
C
18
B
>
E
5
13
D
C
‘Confirm’ the lowest cost nodes
from the list of ‘tentative’ nodes.
… and find out this newly ‘confirmed’
node’s LSP.

## Slide 30
E
5
13
25
D
C
No addition to the topology as the links are already at minimum costs.
X
22
12
D
E
A
7
C
18
B
>

## Slide 31
22
12
D
E
A
7
C
18
B
>
B
4
19
A
D
X
18
C
11
X
‘Confirm’ the lowest cost nodes
from the list of ‘tentative’ nodes.
… and find out this newly ‘confirmed’
node’s LSP (this time B’s LSP).

## Slide 32
B
4
19
A
D
22
12
D
E
A
7
C
18
X
18
22
>
B
C
11
X
No addition to the topology as the links are already at minimum costs.

## Slide 33
22
12
D
E
A
7
C
18
B
>
D
4
13
B
E
X
X
C
15
X
No addition to the topology as the links are already at minimum costs.
‘Confirm’ the lowest cost nodes
from the list of ‘tentative’ nodes.
… and find out this newly ‘confirmed’
node’s LSP (this time D’s LSP).

## Slide 34
A
B
D
C
E
7
11
4
15
5
13
19
22
12
D
E
A
7
C
18
B

## Slide 35: Shortest Path Routing
Dijkstra’s Algorithm
M = {s}
      For each n in N – {s}
        C(n) = l(s, n)
      while ( N  M)
        M = M  {w} such that C(w) is the minimum
        for all w in (N-M)
        For each n in (N-M)
        C(n) = MIN (C(n), C(w) + l(w, n))
Confirmed list
Tentative list
Newly added member to the confirmed list

## Slide 36: Open Shortest Path First (OSPF)
  OSPF Header Format OSPF Link State Advertisement
OSPF runs over IPv4 and IPv6 (does not use a transport protocol such
as UDP or TCP).
It encapsulates its data directly in IP packets with protocol number 89.

## Slide 37: Comparison of LS and DV algorithms
message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time varies
speed of convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network

## Slide 38
 | Distance Vector routing | Link State routing
Convergence time/Latency |  | ✅
Robustness to Loop |  | ✅
Processing overhead | ✅ | 
Bandwidth requirement (for control plane) | ✅ | 
Scalability (and robustness to complex topology and changes) |  | ✅

## Slide 39
Internet Protocol

## Slide 40: The Internet network layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 41: Internetworking
What is IP
  IP stands for Internet Protocol
  Key tool used today to build scalable, heterogeneous internetworks
  It runs on all the nodes in a collection of networks and defines the infrastructure that allows these nodes and networks to function as a single logical internetwork
  A simple internetwork showing the protocol layers

## Slide 42
Pic courtesy: https://www.are.na/block/881873

## Slide 43: IP Service Model
Packet Delivery Model
  Connectionless model for data delivery
  Best-effort delivery (unreliable service)
    packets are lost
    packets are delivered out of order
    duplicate copies of a packet are delivered
    packets can be delayed for a long time
Global Addressing Scheme
  Provides a way to identify all hosts in the network

## Slide 44
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP datagram format (i.e., Packet format)
Variable size header.
(20 bytes default
without options)
Variable size data.
Data size =
(Datagram Len – Header Len)

## Slide 45: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version number
(4 bits)
header length
in # of 4-bytes (4 bits)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
(real-time, non-real-time etc.)
max number remaining hops
(decremented at each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit, Min-MTU
discovery
for
fragmentation/
reassembly
Why header only?

## Slide 46
Thank you