## Slide 1
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2025
Topic: Internetworking: CIDR, DHCP, NAT, ARP
(Textbook chapter 3)
Feb 26th, 2025

## Slide 2
Announcement: Yibo is a new TA for 417

## Slide 3: Subnetting

## Slide 4
Router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
223.1.1.6
ISP
The ISP provided the network address space: 223.1.1.X

## Slide 5
Router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
223.1.1.6
ISP
The ISP provided the network address space: 223.1.1.X
223.1.2.X
223.1.3.X

## Slide 6
Router
The ISP provided the network address space: 223.1.1.X
Two separate networks are needed. How can we assign addresses to these “sub” networks?

## Slide 7
Router
The ISP provided the network address space: 223.1.1.X

## Slide 8
Router
The ISP provided the network address space: 223.1.1.X
Use subnetting

## Slide 9
Router
The ISP provided the network address space: 223.1.1.X
11011111.00000001.00000001.XXXXXXX
Use part of the host bits to identify separate subnets.

## Slide 10
Router
The ISP provided the network address space: 223.1.1.X
11011111.00000001.00000001.XXXXXXX
Use part of the host bits to identify separate subnets.
11011111.00000001.00000001.0XXXXXX
11011111.00000001.00000001.1XXXXXX
Subnet mask = 11111111. 11111111. 11111111.10000000

## Slide 11: Subnetting
Add another level to address/routing hierarchy: subnet
Subnet masks define variable partition of host part of class A and B addresses
Subnets visible only within site
“Bitwise and”

## Slide 12: Subnetting
Forwarding Table at Router R1

## Slide 13: Subnetting
Forwarding Table at Router R1
Forwarding Algorithm
D = destination IP address
for each entry < SubnetNum, SubnetMask, NextHop>
  D1 = SubnetMask & D
  if D1 = SubnetNum
    if NextHop is an interface
    deliver datagram directly to destination
    else
    deliver datagram to NextHop (a router)

## Slide 14: Subnetting
Notes
Would use a default router if nothing matches
Not necessary for all ones in subnet mask to be contiguous
Can put multiple subnets on one physical network
Subnets not visible from the rest of the Internet

## Slide 15
Subnets “toy” example

## Slide 16
Address space assigned to you:

## Slide 17
30 hosts max.
22 hosts max.
18 hosts max.

## Slide 20
Announcements
In-class Midterm-1 exam: March 3rd.
Syllabus: Until “Subnetting”.

## Slide 21
It is the question format from the last year for reference. Expect changes.

## Slide 22
It is the question format from the last year for reference. Expect changes.

## Slide 23
It is the question format from the last year for reference. Expect changes.

## Slide 24: Class-less Interdomain Routing (CIDR)
Generalizes the ideas of subnetting

## Slide 25
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0

## Slide 26
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
223.1.1.128
223.1.1.192
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0

## Slide 27
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
223.1.1.128
223.1.1.192
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Lesson 1:
Address classes are not needed. Mask can define the number of bits for the network part.
Lesson 2:
Network hierarchies can be hidden from the outside world.
Network addresses can be aggregated/summarized/combined

## Slide 28: CIDR: Classless address

## Slide 29
CIDR: Classless InterDomain Routing
  Network portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
200.23.16.0–200.23.17.255
IP addressing: CIDR
This X bit network part is often called Prefix or Network-prefix

## Slide 30
IP addressing: CIDR
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
forwarding table
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address

## Slide 31: CIDR: Super-netting/ Route aggregation

## Slide 32
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Forwarding tab.
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.0.0/16

## Slide 33
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Forwarding tab.
223.1.0.0/16
223.1.0.0/16

## Slide 34
Thank you

## Slide 37
200.20.0.0/24
200.20.1.0/24
200.20.2.0/24

## Slide 38
200.20.0.0/24
200.20.1.0/24
200.20.2.0/24

## Slide 39
200.20.0.0/24
200.20.1.0/24
200.20.2.0/24
Route aggregation

## Slide 40
Route aggregation with CIDR

## Slide 41: Classless Inter-Domain Routing (CIDR)
IP Address : 12.4.0.0 IP Mask: 255.254.0.0
00001100
00000100
00000000
00000000
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network.
Network number = IP address + Mask
Written as 12.4.0.0/15

## Slide 42: Hierarchical Address Allocation
Hierarchy is key to scalability
  Address allocated in contiguous chunks (prefixes)
  Today, the Internet has about 400,000 prefixes
12.0.0.0/8
12.0.0.0/16
12.254.0.0/16
12.1.0.0/16
12.2.0.0/16
12.3.0.0/16
:
:
:
12.3.0.0/24
12.3.1.0/24
:
:
12.3.254.0/24
12.253.0.0/19
12.253.32.0/19
12.253.160.0/19
:
:
:
:
:

## Slide 43: Separate Forwarding Entry Per Prefix
Prefix-based forwarding
  Map the destination address to matching prefix
  Forward to the outgoing interface
host
host
host
LAN 1
...
host
host
host
LAN
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 44
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1

## Slide 45
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homing

## Slide 46
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homing
Forwarding tab.

## Slide 47
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homing
Forwarding tab.
201.10.0.0/21
201.10.6.0/23

## Slide 48
11001001.00001010.00000000.00000000/21
11001001.00001010.00000110.00000000/23
11001001.00001010.00000110.00010001
A packet with dest. Addr.: 201.10.6.17
201.10.0.0/21
201.10.6.0/23
CIDR Makes Packet Forwarding Harder
Forwarding table

## Slide 49: CIDR Makes Packet Forwarding Harder
Forwarding table may have many matches
  E.g., entries for 201.10.0.0/21 and 201.10.6.0/23
  The IP address 201.10.6.17 would match both!
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2

## Slide 50: Longest Prefix Match Forwarding
Destination-based forwarding
  Packet has a destination address
  Router identifies longest-matching prefix
  Cute algorithmic problem: very fast lookups
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
201.10.6.17
destination
forwarding table
outgoing link

## Slide 51: Getting an IP address: DHCP Protocol

## Slide 52: IP addresses: how to get one?
Q: How does a host get its IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/…
DHCP: Dynamic Host Configuration Protocol: dynamically get address from a server
  “plug-and-play”

## Slide 53: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network

## Slide 54: DHCP: Dynamic Host Configuration Protocol
DHCP overview:
  host broadcasts “DHCP discover” msg
  DHCP server responds with “DHCP offer” msg
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 55: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 56
Broadcast: is there a DHCP server out there?

## Slide 57
A note on the “broadcast address”

## Slide 58
inet 10.104.216.101  00001010.01101000.11011000.01100101
netmask ff:ff:f0:00  11111111.11111111.11110000.00000000
broadcast 10.104.223.255 
00001010.01101000.11011111.11111111

## Slide 59
Broadcast: is there a DHCP server out there?
Which protocol would you use to exchange these DHCP protocol messages?

## Slide 60
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 61
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 62
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 63
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 64
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 65
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 66
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 67
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 68
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 69
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 70
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 71
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 72
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 73
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 74
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 75
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!