## Slide 1
CMSC 417: Computer Networks
Nirupam Roy
M-W 2:00-3:15pm
CSI 2117
Spring 2026
Topic: ICMP, VPN, IPv6
(Textbook chapter 3)
March 9th, 2026

## Slide 2: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 3: ARP protocol: same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator
Notes: 3. Do Other Nodes See the ARP Reply?
Normally no, because:
Ethernet switches forward unicast frames only to the destination port
Other hosts do not receive the frame
So they cannot overhear the ARP reply. (Power saving Idea).

## Slide 4: Address Translation Protocol (ARP)
Map IP addresses into physical addresses
  destination host
  next hop router
Techniques
  encode physical address in host part of IP address
  table-based
ARP (Address Resolution Protocol)
  table of IP to physical address bindings
  broadcast request if IP address not in table
  target machine responds with its physical address
  table entries are discarded if not refreshed
  Query message include the physical address of the sending host. Why?

## Slide 5: ARP Packet Format
  HardwareType: type of physical network (e.g., Ethernet)
  ProtocolType: type of higher layer protocol (e.g., IP)
  HLEN & PLEN: length of physical and protocol addresses
  Operation: request or response
  Source/Target Physical/Protocol addresses

## Slide 6: Internet Control Message Protocol (ICMP)

## Slide 7: Internet Control Message Protocol (ICMP)
Defines a collection of error messages that are sent back to the source host.
E.g., ICMP messages are sent whenever a router or host is unable to process an IP datagram successfully
  Destination host unreachable due to link /node failure
  Reassembly process failed
  TTL had reached 0 (so datagrams don't cycle forever)
  IP header checksum failed
ICMP-Redirect
  From router to a source host
  With a better route information

## Slide 8
ICMP message types

## Slide 9
Ping example
Notes: The output often shows something like:
64 bytes from 8.8.8.8: icmp_seq=1 ttl=115 time=12.3 ms
The TTL=115 means:
When the ICMP Echo Reply reached your machine, the packet still had TTL = 115 remaining.
Typical Initial TTL Values for Ping Requests
Operating SystemInitial TTLL
inux64
macOS64
Windows128
Cisco routers255
BSD systems64

## Slide 10
Traceroute : An unintuitive application using ICMP

## Slide 11
Traceroute example

## Slide 12
Traceroute : An unintuitive application

## Slide 13: Virtual Networks and Tunnels

## Slide 14
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Untrusted/Shared network

## Slide 15
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
Untrusted/Shared network

## Slide 16
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
New IP Header Source: Gateway-A Dest: Gateway-B
IP Header
Data
Encapsulation
Untrusted/Shared network

## Slide 17
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
New IP Header Source: Gateway-A Dest: Gateway-B
IP Header
Data
Decapsulation
New IP Header Source: Gateway-A Dest: Gateway-B
IP Header
Data
Untrusted/Shared network

## Slide 18
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
IP Header
Data
Untrusted/Shared network

## Slide 19
Trusted network (Site A)
Trusted network (Site B)
Gateway A
Gateway B
IP Header
Data
Virtual Tunnel
New IP Header Source: Gateway-A Dest: Gateway-A
IP Header
Data
New IP Header Source: Gateway-A Dest: Gateway-A
IP Header
Data
Encryption/Decryption
Untrusted/Shared network

## Slide 20
Trusted network (Site A)
Trusted network (Site B)
Untrusted/Shared network
Gateway A
Gateway B
Virtual Tunnel
Virtual Private Network
(VPN)

## Slide 21
Picture: https://buzzclan.com/cyber-security/how-does-a-vpn-work/

## Slide 22: Three Major Types of VPNs
Remote Access VPN – Allows individual users to securely connect to a private network from a remote location using the internet (commonly used by employees working from home).
Site-to-Site VPN – Connects entire networks at different locations (e.g., branch offices) through secure tunnels over the internet.
Client-to-Site VPN (SSL/IPsec) – A client device uses VPN software to establish an encrypted connection to a company’s VPN gateway.

## Slide 23
Pic ref: https://www.siretta.com/2024/02/virtual-private-network/

## Slide 24
Why do we need virtual networks or tunnels?
1. Security
2. Special capabilities between routers (e.g., multicast)
3. Supporting heterogeneity

## Slide 25
Why do we need virtual networks or tunnels?
1. Security
2. Special capabilities between routers (e.g., multicast)
3. Supporting heterogeneity
Disadvantages:
1. Increases packet length
a) Wastage of bandwidth
b) More processing
c) Fragmentation
2. Increases management cost

## Slide 26: IPv6
1) Address and packet format
2) Unicast, Multicast, Anycast addressing
3) IPV4 and IPV6 coexistence

## Slide 27
Classless addressing/routing (similar to CIDR)
Notation: x:x:x:x:x:x:x:x (x = 16-bit hex number)
  contiguous 0s are compressed: 47CD::A456:0124
  IPv6 compatible IPv4 address: ::128.42.1.87
Address assignment
  provider-based
  geographic
IPv6: Address
Notes: IPv4-compatible IPv6 addresses were an early IPv6 transition mechanism designed to allow IPv6 hosts to communicate over IPv4 infrastructure using automatic tunneling. These addresses embedded an IPv4 address inside an IPv6 address so that IPv6 packets could be transported through IPv4 networks.
However, this mechanism is now deprecated and is no longer used in modern IPv6 deployments.

## Slide 28
47CD:1234:4422:AC02:0022:1234:A456:0124
47CD:0000:0000:0000:0000:0000:A456:0124
47CD::A456:0124
IPv6: Address

## Slide 29
IPv6: Scopes of Addresses

## Slide 30: IPv6: Address and packet format
Pic courtesy: https://techhub.hpe.com

## Slide 31: IPv6: Address and packet format
Pic courtesy: https://techhub.hpe.com
Q 1. Why is there no header checksum?
Q 2. Why is there no fragmenting related option?
Q 3. Is 128-bit IP address big enough?
Notes: IPv6 provides for a maximum of 3.4×10^38 (340 trillion trillion trillion) unique IP addresses, or about 47 octillion unique addresses for every person on the planet.
For comparison: One light-year is about 6 trillion miles (9 trillion km)
Q1: Does not provide much quality of service when the delivery policy itself is unreliable,
Q2: Pushing the responsibility to the edge. With increasing traffic fragmentation is computation costly.
fragmentation is now handled as an optional header, which means that the fragmentation-related fields of IPv4 are not included in the IPv6 header.

## Slide 32
Fragmentation in IPv4 (for comparison)
A router receives a packet larger than the MTU of the next link.
The router fragments the packet into smaller pieces.
Each fragment travels independently.
The destination host reassembles them.
This means routers perform fragmentation, which increases router processing overhead.
IPv6 Design Decision
IPv6 eliminates router fragmentation.
Instead:
Routers never fragment packets
If a packet is too large, the router drops it
The router sends an ICMPv6 Packet Too Big message
The sender adjusts the packet size
This mechanism is called: Path MTU Discovery (PMTUD)
IPv6: IP packet Fragmentation

## Slide 33
Path MTU Discovery (PMTUD)
The sender discovers the smallest MTU along the path.
Step-by-step
Sender transmits a packet.
Router finds packet larger than its MTU.
Router drops the packet.
Router sends:
ICMPv6: Packet Too Big
Message includes the MTU of the link.
Sender reduces packet size.
Sender retransmits.
IPv6: IP packet Fragmentation

## Slide 34
Fragmentation is done only by the source host using a Fragment Extension Header.
IPv6: IP packet Fragmentation
Notes: Fragmentations are possible in IPV6, but only at source. And in that case an extension header will be defined.

## Slide 35
Field | Purpose
Fragment Offset | Position of fragment
M flag | More fragments indicator
Identification | Used for reassembly
IPv6 Fragment Extension Header
The Fragment Header contains:
IPv6: IP packet Fragmentation

## Slide 36
Why IPv6 Removed Router Fragmentation?
Three main reasons:
1. Router performance
Routers operate in hardware and fragmentation is expensive.
2. Simpler routers
Edge hosts handle fragmentation instead.
3. Security
Fragmentation can enable evasion attacks on Firewalls and IDS (Intrusion Detection Systems).
IPv6: IP packet Fragmentation

## Slide 37
Evasion Attack
Security systems typically inspect packets to detect attacks. However, if an attacker splits the packet into fragments, the security device may:
inspect fragments individually, or
fail to reassemble them correctly
Meanwhile, the destination host reassembles them differently, revealing the malicious payload.
IPv6: IP packet Fragmentation

## Slide 38
Splitting Malicious Payload Across Fragments
An attacker splits a malicious signature across fragments so that the IDS cannot detect it.
Example attack payload:
GET /cmd.exe
Fragments sent:
Fragment 1
GET /cm
Fragment 2
d.exe
If the IDS inspects fragments separately:
Fragment 1 → benign Fragment 2 → benign
But the destination host reassembles:
GET /cmd.exe
This was historically used to bypass signature-based IDS systems.
IPv6: IP packet Fragmentation

## Slide 39: IPv6: Address and packet format
Pic courtesy: https://techhub.hpe.com
Q 1. Why is there no header checksum?
Q 2. Why is there no fragmenting related option?
Q 3. Is 128-bit IP address big enough?
Notes: IPv6 provides for a maximum of 3.4×10^38 (340 trillion trillion trillion) unique IP addresses, or about 47 octillion unique addresses for every person on the planet.
For comparison: One light-year is about 6 trillion miles (9 trillion km)
Q1: Does not provide much quality of service when the delivery policy itself is unreliable,
Q2: Pushing the responsibility to the edge. With increasing traffic fragmentation is computation costly.

## Slide 40: Unicast, Multicast, Anycast, Broadcast

## Slide 41: Unicast, Multicast, Anycast, Broadcast
IPv4
IPv4
IPv4

## Slide 42: Unicast, Multicast, Anycast, Broadcast
IPv4
IPv4
IPv4
IPv6
IPv6
IPv6

## Slide 43: Unicast, Multicast, Anycast, Broadcast
IP: Anycast example

## Slide 44: IPv4 and IPv6 Co-existence

## Slide 45: IPv4 and IPv6 Co-existence

## Slide 46
Computer Networks
Nirupam Roy
Tu-Th 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2025
Topic:
Transport Layer Protocols (UDP, TCP)
(Textbook chapter 5)
March 12th, 2025

## Slide 48
Transport layer: From the lens of two perspectives
(1) Abstraction of clients. (machines/networks/processes)
(2) Abstraction of services.

## Slide 49
(1) Abstraction of clients

## Slide 50
Network 1
Network 2
Network 3
128.2.0.0/16
16.20.0.0/20
200.30.0.0/16
Network layer abstraction

## Slide 51
Network 1
Network 2
Network 3
128.2.0.0/16
16.20.0.0/20
200.30.0.0/16
Network layer abstraction

## Slide 52
Network 1
Network 2
Network 3
128.2.0.0/16
16.20.0.0/20
200.30.0.0/16
Network layer abstraction
Network layer services

## Slide 53
Transport layer abstraction

## Slide 54
Transport layer abstraction
Transport layer services

## Slide 56
Connection between processes

## Slide 57
Implementation of networking algorithms

## Slide 58: Transport Protocols
Logical communication between processes
  Sender divides a message into segments
  Receiver reassembles segments into message
Transport services
  (De)multiplexing packets
  Detecting corrupted data
  Optionally: reliable delivery, flow control, …

## Slide 59: Two Basic Transport Features
Demultiplexing: port numbers
Error detection: checksums
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
OS
Client
IP
payload
detect corruption

## Slide 60: Multiplexing/demultiplexing
application
transport
network
link
physical
P1
application
transport
network
link
physical
application
transport
network
link
physical
P2
P3
P4
P1
host 1
host 2
host 3
= process
= socket
delivering received segments
to correct socket
Demultiplexing at rcv host:
Data headers helps flows
from multiple sockets to use
common the network channel,
Info in header later helps
Demultiplexing.
Multiplexing at send host:

## Slide 61: How demultiplexing works
1) host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries 1 transport-layer segment
  each segment has source, destination port number
2) host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format

## Slide 62
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2

## Slide 63
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2

## Slide 64
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2

## Slide 65
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2

## Slide 66
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2

## Slide 67
Connection-less mux/demux:
- User Datagram Protocol (UDP)
Connection-oriented mux/demux:
- Transmission Control Protocol (TCP)

## Slide 68: Connectionless demultiplexing
Create sockets with port numbers:
DatagramSocket mySocket1 = new DatagramSocket(99111);
DatagramSocket mySocket2 = new DatagramSocket(99222);
UDP socket identified by two-tuple:
(dest IP address, dest port number)
When host receives UDP segment:
  checks destination port number in segment
  directs UDP segment to socket with that port number
IP datagrams with different source IP addresses and/or source port numbers directed to same socket

## Slide 69: Connectionless demux (cont)
DatagramSocket serverSocket = new DatagramSocket(6428);
Client
IP:B
P2
client
IP: A
P1
P1
P3
server
IP: C
SP: 6428
DP: 9157
SP: 9157
DP: 6428
SP: 6428
DP: 5775
SP: 5775
DP: 6428
SP provides “return address”