## Slide 1
CMSC 417: Computer Networks
Nirupam Roy
M-W 2:00-3:15pm
CSI 2117
Spring 2026
Topic: IPv6
(Textbook chapter 3)
March 9th, 2026

## Slide 2: IPv6
1) Address and packet format
2) Unicast, Multicast, Anycast addressing
3) IPV4 and IPV6 coexistence

## Slide 3
Classless addressing/routing (similar to CIDR)
Notation: x:x:x:x:x:x:x:x (x = 16-bit hex number)
  contiguous 0s are compressed: 47CD::A456:0124
  IPv6 compatible IPv4 address: ::128.42.1.87
Address assignment
  provider-based
  geographic
IPv6: Address
Notes: IPv4-compatible IPv6 addresses were an early IPv6 transition mechanism designed to allow IPv6 hosts to communicate over IPv4 infrastructure using automatic tunneling. These addresses embedded an IPv4 address inside an IPv6 address so that IPv6 packets could be transported through IPv4 networks.
However, this mechanism is now deprecated and is no longer used in modern IPv6 deployments.

## Slide 4
47CD:1234:4422:AC02:0022:1234:A456:0124
47CD:0000:0000:0000:0000:0000:A456:0124
47CD::A456:0124
IPv6: Address

## Slide 5
IPv6: Scopes of Addresses
FE80::/10
FC00::/7
Unique Local Scope (similar to private address)
FF00::/8

## Slide 6: IPv6: Address and packet format
Pic courtesy: https://techhub.hpe.com

## Slide 7: IPv6: Address and packet format
Pic courtesy: https://techhub.hpe.com
Q 1. Why is there no header checksum?
Q 2. Why is there no fragmenting related option?
Q 3. Is 128-bit IP address big enough?
Notes: IPv6 provides for a maximum of 3.4×10^38 (340 trillion trillion trillion) unique IP addresses, or about 47 octillion unique addresses for every person on the planet.
For comparison: One light-year is about 6 trillion miles (9 trillion km)
Q1: Does not provide much quality of service when the delivery policy itself is unreliable,
Q2: Pushing the responsibility to the edge. With increasing traffic fragmentation is computation costly.
fragmentation is now handled as an optional header, which means that the fragmentation-related fields of IPv4 are not included in the IPv6 header.

## Slide 8
Fragmentation in IPv4 (for comparison)
A router receives a packet larger than the MTU of the next link.
The router fragments the packet into smaller pieces.
Each fragment travels independently.
The destination host reassembles them.
This means routers perform fragmentation, which increases router processing overhead.
IPv6 Design Decision
IPv6 eliminates router fragmentation.
Instead:
Routers never fragment packets
If a packet is too large, the router drops it
The router sends an ICMPv6 Packet Too Big message
The sender adjusts the packet size
This mechanism is called: Path MTU Discovery (PMTUD)
IPv6: IP packet Fragmentation

## Slide 9
Path MTU Discovery (PMTUD)
The sender discovers the smallest MTU along the path.
Step-by-step
Sender transmits a packet.
Router finds packet larger than its MTU.
Router drops the packet.
Router sends:
ICMPv6: Packet Too Big
Message includes the MTU of the link.
Sender reduces packet size.
Sender retransmits.
IPv6: IP packet Fragmentation

## Slide 10
Fragmentation is done only by the source host using a Fragment Extension Header.
IPv6: IP packet Fragmentation
Notes: Fragmentations are possible in IPV6, but only at source. And in that case an extension header will be defined.

## Slide 11
Field | Purpose
Fragment Offset | Position of fragment
M flag | More fragments indicator
Identification | Used for reassembly
IPv6 Fragment Extension Header
The Fragment Header contains:
IPv6: IP packet Fragmentation

## Slide 12
Why IPv6 Removed Router Fragmentation?
Three main reasons:
1. Router performance
Routers operate in hardware and fragmentation is expensive.
2. Simpler routers
Edge hosts handle fragmentation instead.
3. Security
Fragmentation can enable evasion attacks on Firewalls and IDS (Intrusion Detection Systems).
IPv6: IP packet Fragmentation

## Slide 13
Evasion Attack
Security systems typically inspect packets to detect attacks. However, if an attacker splits the packet into fragments, the security device may:
inspect fragments individually, or
fail to reassemble them correctly
Meanwhile, the destination host reassembles them differently, revealing the malicious payload.
IPv6: IP packet Fragmentation

## Slide 14
Splitting Malicious Payload Across Fragments
An attacker splits a malicious signature across fragments so that the IDS cannot detect it.
Example attack payload:
GET /cmd.exe
Fragments sent:
Fragment 1
GET /cm
Fragment 2
d.exe
If the IDS inspects fragments separately:
Fragment 1 → benign Fragment 2 → benign
But the destination host reassembles:
GET /cmd.exe
This was historically used to bypass signature-based IDS systems.
IPv6: IP packet Fragmentation

## Slide 15: IPv6: Address and packet format
Pic courtesy: https://techhub.hpe.com
Q 1. Why is there no header checksum?
Q 2. Why is there no fragmenting related option?
Q 3. Is 128-bit IP address big enough?
Notes: IPv6 provides for a maximum of 3.4×10^38 (340 trillion trillion trillion) unique IP addresses, or about 47 octillion unique addresses for every person on the planet.
For comparison: One light-year is about 6 trillion miles (9 trillion km)
Q1: Does not provide much quality of service when the delivery policy itself is unreliable,
Q2: Pushing the responsibility to the edge. With increasing traffic fragmentation is computation costly.

## Slide 16: Unicast, Multicast, Anycast, Broadcast

## Slide 17: Unicast, Multicast, Anycast, Broadcast
IPv4
IPv4
IPv4

## Slide 18: Unicast, Multicast, Anycast, Broadcast
IPv4
IPv4
IPv4
IPv6
IPv6
IPv6
Notes: The two main broadcast address types in IPv4 are the
Limited Broadcast address (
255.255
.
255.255
) and the Directed Broadcast address (e.g.,
192.168
.
1.255
).

## Slide 19: Anycast
IP: Anycast example

## Slide 20
Anycast: Is this a new concept?
a:b:x:x
Anycast effectively existed as a routing pattern even in IPv4; IPv6 formalized it as a first-class architectural concept.

## Slide 21
Anycast: Is this a new concept?
a:b:x:x
“Anycast” was possible as a routing pattern even in IPv4; IPv6 formalized it as a first-class architectural concept.
a:b:x:x

## Slide 22: Multicast
A multicast group exists
Interested nodes join the multicast group
On the local link, switches/NICs learn who is interested
The sender creates a packet addressed to the multicast group
On a single link, all members of that group receive it.
If the multicast is beyond one link, routers
forward it selectively

## Slide 23: Multicast: How the groups are formed
1. Predefined (Well-Known) Multicast Groups
Some groups are built into the IPv6 architecture.
Examples
ff02::1 → all-nodes
ff02::2 → all-routers
👉 These groups:
are defined by standards
every relevant node automatically joins them

## Slide 24: Multicast: How the groups are formed
2. Dynamically Joined Multicast Groups (Application-driven)
These are the multicast groups created and used by applications.
Examples:
streaming
conferencing
distributed systems

## Slide 25: Multicast: How the groups are formed
3. Algorithmically Derived Groups
Some multicast groups are created deterministically from unicast addresses.
How they “form”
Every node:
  computes its own multicast group
  automatically joins it
No signaling, no coordination
Example: Solicited-node multicast

## Slide 26: IPV6 Multicast: Solicited-Node Multicast
The Address Format
All solicited-node groups share this prefix:
ff02::1:ff00:0/104
A specific group is formed by taking the last 24 bits of a unicast (or anycast) IPv6 address and appending them:
Example
Unicast address: 2001:db8::abcd:1234
Last 24 bits = cd:1234 (i.e., the low-order 24 bits)
Solicited-node multicast: ff02::1:ffcd:1234

## Slide 27
IPV6 Neighbor Discovery Protocol (NDP)
What NDP Replaces (from IPv4)
IPv6 collapses multiple IPv4 mechanisms into one protocol:
ARP → address resolution
ICMP Router Discovery → router discovery
ICMP Redirect → route optimization
👉 NDP is a unified control-plane protocol over ICMPv6
Runs Over ICMPv6 (Architectural Placement)
NDP messages are ICMPv6 types
Uses multicast, not broadcast
👉 Important shift:
IPv4: broadcast-heavy
IPv6: multicast + scoped communication

## Slide 28
IPV6 Neighbor Discovery Protocol (NDP)
Key Functions of NDP
(a) Address Resolution
Map IPv6 → MAC address
Equivalent of ARP
How:
Neighbor Solicitation (NS) → “Who has this IP?”
Neighbor Advertisement (NA) → “I do”
(b) Router Discovery
Hosts discover routers on the link
How:
Router Solicitation (RS) → “Any routers here?”
Router Advertisement (RA) → “Yes, here is prefix + config”

## Slide 29
IPV6 Neighbor Discovery Protocol (NDP)
(c) Prefix Discovery
Learn:
  network prefix
  subnet information
From:
Router Advertisement (RA) messages
(d) Duplicate Address Detection (DAD)
Ensure an address is unique before use
How:
Host sends NS for its own address
If no reply → safe

## Slide 30
(e) Neighbor Unreachability Detection (NUD)
Detect if a neighbor is still alive
Mechanism:
Track reachability via:
  traffic
  probes (NS/NA)
IPV6 Neighbor Discovery Protocol (NDP)

## Slide 31
IPV6 Stateless Address Autoconfiguration (SLAAC)
It is the IPv6 mechanism by which a host can:
create its own IPv6 address,
learn the subnet prefix,
learn the default router,
without needing a DHCP server for address assignment.

## Slide 32
Step 1: The host comes online
When a device connects to an IPv6-enabled network, it first enables IPv6 on its interface.
At this point, it does not yet know:
the subnet prefix
the default router
whether it should use SLAAC or DHCPv6
So it starts with only local mechanisms.
IPV6 Stateless Address Autoconfiguration (SLAAC)

## Slide 33
Step 2: The host creates a link-local address
Before anything else, the host creates a link-local IPv6 address.
This always uses the prefix: fe80::/64
The remaining 64 bits are created locally by the host, using either:
EUI-64 from the MAC address, or
a randomly generated interface identifier, or
a stable privacy-preserving identifier
Example:
fe80::a1b2:c3d4:e5f6:7890
This address works only on the local link.
It is important because IPv6 control protocols, including Neighbor Discovery, use link-local addresses.
IPV6 Stateless Address Autoconfiguration (SLAAC)

## Slide 34
Step 3: The host performs Duplicate Address Detection for the link-local address
Before using even the link-local address, the host must check whether some other node is already using it.
It does this through Duplicate Address Detection (DAD).
The host sends a Neighbor Solicitation (NS) for its own tentative address.
If nobody responds, the address is unique and can be used.
If someone responds with a Neighbor Advertisement (NA), there is a conflict and the address cannot be used.
After successful DAD, the host can use its link-local address.
IPV6 Stateless Address Autoconfiguration (SLAAC)

## Slide 35
Step 4: The host discovers routers
Now the host needs to learn:
whether routers are present
what network prefix to use
what default gateway to use
whether SLAAC is allowed
It does this using Neighbor Discovery Protocol (NDP).
The host may send a Router Solicitation (RS) to:
ff02::2 (all-routers multicast)
This is basically asking:
“Are there any routers on this link? Please send configuration information.”
Even if the host does not send RS, routers may periodically send advertisements anyway.
IPV6 Stateless Address Autoconfiguration (SLAAC)

## Slide 36
Step 5: The router sends a Router Advertisement
A router replies with a Router Advertisement (RA).
The RA is the key message for SLAAC.
It contains information such as:
the network prefix, for example 2001:db8:abcd:1::/64
the prefix length
the default gateway information
lifetime values
flags indicating whether SLAAC and/or DHCPv6 should be used
IPV6 Stateless Address Autoconfiguration (SLAAC)

## Slide 37
Step 6: The host checks the RA flags
The important RA flags include:
A flag: Autonomous address-configuration flag
  if set, the prefix can be used for SLAAC
M flag: Managed flag
  if set, use DHCPv6 for address assignment
O flag: Other configuration flag
  if set, use DHCPv6 for other info such as DNS, while the address may still be formed through SLAAC
For pure SLAAC, the important condition is that the prefix is advertised with the A flag set.
IPV6 Stateless Address Autoconfiguration (SLAAC)

## Slide 38
Step 7: The host forms its global unicast address
Now the host has:
the network prefix from the router
its own interface identifier
It combines them to form a full IPv6 address.
Example:
prefix from RA: 2001:db8:abcd:1::/64
host-generated interface ID: a1b2:c3d4:e5f6:7890
Resulting address:
2001:db8:abcd:1:a1b2:c3d4:e5f6:7890
This is the host’s global unicast address.
IPV6 Stateless Address Autoconfiguration (SLAAC)

## Slide 39
Step 8: The host performs DAD again for the new global address
The host must again verify uniqueness.
It runs Duplicate Address Detection for the newly formed global address:
sends NS for that tentative address
waits to see if anyone objects
If no response comes back, the address is considered unique and becomes usable.
IPV6 Stateless Address Autoconfiguration (SLAAC)

## Slide 40
Step 9: The host installs the default router information
From the RA, the host also learns which router should be used as the default gateway.
This means the host can now:
communicate on the local link directly
send off-link traffic to the router
So after this step, the host has:
a link-local address
a global unicast address
a default router
Now it is fully operational on the IPv6 network.
The host may configure additional addresses
In practice, a host may create more than one IPv6 address on the same interface. Example: one stable address and one temporary privacy address.
This is common in modern systems to reduce long-term tracking.
IPV6 Stateless Address Autoconfiguration (SLAAC)

## Slide 41: IPv4 and IPv6 Co-existence

## Slide 42: IPv4 and IPv6 Co-existence

## Slide 43
Computer Networks
Nirupam Roy
M-W 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2026
Topic:
Transport Layer Protocols (UDP, TCP)
(Textbook chapter 5)
March 23th, 2026

## Slide 45
Transport layer: From the lens of two perspectives
(1) Abstraction of clients. (machines/networks/processes)
(2) Abstraction of services.

## Slide 46
(1) Abstraction of clients

## Slide 47
Network 1
Network 2
Network 3
128.2.0.0/16
16.20.0.0/20
200.30.0.0/16
Network layer abstraction

## Slide 48
Network 1
Network 2
Network 3
128.2.0.0/16
16.20.0.0/20
200.30.0.0/16
Network layer abstraction

## Slide 49
Network 1
Network 2
Network 3
128.2.0.0/16
16.20.0.0/20
200.30.0.0/16
Network layer abstraction
Network layer services

## Slide 50
Transport layer abstraction

## Slide 51
Transport layer abstraction
Transport layer services

## Slide 53
Connection between processes

## Slide 54
Implementation of networking algorithms

## Slide 55: Transport Protocols
Logical communication between processes
  Sender divides a message into segments
  Receiver reassembles segments into message
Transport services
  (De)multiplexing packets
  Detecting corrupted data
  Optionally: reliable delivery, flow control, …

## Slide 56: Two Basic Transport Features
Demultiplexing: port numbers
Error detection: checksums
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
OS
Client
IP
payload
detect corruption

## Slide 57: Multiplexing/demultiplexing
application
transport
network
link
physical
P1
application
transport
network
link
physical
application
transport
network
link
physical
P2
P3
P4
P1
host 1
host 2
host 3
= process
= socket
delivering received segments
to correct socket
Demultiplexing at rcv host:
Data headers helps flows
from multiple sockets to use
common the network channel,
Info in header later helps
Demultiplexing.
Multiplexing at send host:

## Slide 58: How demultiplexing works
1) host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries 1 transport-layer segment
  each segment has source, destination port number
2) host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format

## Slide 59
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2

## Slide 60
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2

## Slide 61
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2

## Slide 62
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2

## Slide 63
application
transport
network
link
physical
P1
application
transport
network
link
physical
P2
P3
P1
host 1
host 2

## Slide 64
Connection-less mux/demux:
- User Datagram Protocol (UDP)
Connection-oriented mux/demux:
- Transmission Control Protocol (TCP)

## Slide 65: Connectionless demultiplexing
Create sockets with port numbers:
DatagramSocket mySocket1 = new DatagramSocket(99111);
DatagramSocket mySocket2 = new DatagramSocket(99222);
UDP socket identified by two-tuple:
(dest IP address, dest port number)
When host receives UDP segment:
  checks destination port number in segment
  directs UDP segment to socket with that port number
IP datagrams with different source IP addresses and/or source port numbers directed to same socket

## Slide 66: Connectionless demux (cont)
DatagramSocket serverSocket = new DatagramSocket(6428);
Client
IP:B
P2
client
IP: A
P1
P1
P3
server
IP: C
SP: 6428
DP: 9157
SP: 9157
DP: 6428
SP: 6428
DP: 5775
SP: 5775
DP: 6428
SP provides “return address”