## Slide 1
Computer Networks
Nirupam Roy
M-W 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2026
Topic:
Transport Layer Protocols: ARQ, Flow-control
(Textbook chapter 5)
April 1st, 2026

## Slide 2
Revisiting “delay X bandwidth”
Consider two-way delay
or round-trip delay

## Slide 3: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
Network bandwidth = R bits-per-sec
Packet size = L bits

## Slide 4: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
Network bandwidth = R bits-per-sec
Packet size = L bits
1kB packet per 30.008 msec
~33KB/sec throughput over a 1GBPS link!!
Network protocol limits the full utilization of physical resources.
Transport-layer vs Link-layer capacity gap

## Slide 5: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
Increase utilization
by a factor of 3!

## Slide 6
Time
Round-trip delay
Sender
Receiver
Revisiting “delay X bandwidth”

## Slide 7
Time
Packet
ACK
Timeout
Sender
Receiver
Sliding Window
Stop-and-wait

## Slide 8
Sliding Window: Lost Packet/ACK

## Slide 9
Sliding Window Protocol

## Slide 10
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent

## Slide 11
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent
ACK

## Slide 12
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Packet 1 is delivered

## Slide 13
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Packet 1 is delivered. Slide the window.
Window = # pkt in flight
Sent
Sent

## Slide 14
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Packet 1 is delivered. Slide the window.
Window = # pkt in flight
Sent
Sent
Sent

## Slide 15
Time
Sender
Receiver
Sliding Window: A series of packets to be sent reliably

## Slide 16
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Packet 1 is delivered. Slide the window.
Window = # pkt in flight
Sent
Sent
Sent

## Slide 17
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Should we advance the window in the following scenario?
Window = # pkt in flight
Sent
Sent
Sent
ACK

## Slide 18
Time
Sender
Receiver
Sliding Window: A series of packets to be sent reliably

## Slide 19
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Should we advance the window in the following scenario?
Window = # pkt in flight
Sent
Sent
Sent
ACK

## Slide 20
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Should we advance the window in the following scenario?
Window = # pkt in flight
Sent
Sent
Sent
ACK
Note that the window size is not changed!

## Slide 21
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent
Can you make sliding window behave like
stop-and-wait?

## Slide 22
Sliding Window Protocol
(dealing packet loss)

## Slide 23
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent

## Slide 24
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent
(1) ARQ strategy 1: Retransmit all un-ACKed packets
Re-tx
Re-tx
Re-tx

## Slide 25
Time
Timeout
Sender
Receiver
Sliding Window: A series of packets to be sent reliably
X
1
2
3
1
2
3
(1) Go-back-N (Sender side)
Why sender retransmitted all packet in a window?
(1) Bursty losses
(2) Assumes receiver discarded out-of-order packets.

## Slide 26
Pkt:1
Pkt:2
Pkt:3
Pkt:4
Pkt:5
Pkt:6
Pkt:7
Pkt:8
Sliding Window: A series of packets to be sent reliably
Window = # pkt in flight
Sent
Sent
Sent
(2) ARQ strategy 2: Retransmit only the lost packet
Re-tx
(2) Selective retransmit (Sender side)

## Slide 27
Time
Timeout
Sender
Receiver
Sliding Window: A series of packets to be sent reliably
X
1
2
3
4
2
5
(2) Selective retransmit

## Slide 28
Sliding Window: Lost Packet/ACK
Timeout

## Slide 29
Which ARQ strategy does modern TCP implement?
TCP does not strictly implement either pure Go-Back-N (GBN) or pure Selective Repeat (SR)
—it is a hybrid, but in modern implementations it behaves much closer to Selective Repeat ARQ.

## Slide 30
TCP Cumulative ACK strategy (receiver side)
Cumulative ACK:
ACK the largest in-sequence packet received.
What will be ACK sequence if the receive sequence
is: 5, 7, 8, 6 ?

## Slide 31
TCP Cumulative ACK strategy (receiver side)
Cumulative ACK:
ACK the largest in-sequence packet received.
What will be ACK sequence if the receive sequence
is: 5, 7, 8, 6 ?
ACK: 6, 6, 6, 9

## Slide 32
TCP Cumulative ACK strategy (receiver side)
(An example)
X
Sender
Receiver

## Slide 33
TCP Cumulative ACK strategy (receiver side)
X
Seq. # | 234118
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234268
ACK flag | N/A
ACK # | N/A
Data Len | 120 bytes
Seq. # | 234388
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234218
ACK flag | N/A
ACK # | N/A
Data Len | 50 bytes
234118
234218
234268
234388
Sender
Receiver
(An example)

## Slide 34
TCP Cumulative ACK strategy (receiver side)
X
Seq. # | 234118
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234268
ACK flag | N/A
ACK # | N/A
Data Len | 120 bytes
Seq. # | 234388
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234218
ACK flag | N/A
ACK # | N/A
Data Len | 50 bytes
Timeout
234118
234218
234268
234388
Sender
Receiver
(An example)

## Slide 35
TCP Cumulative ACK strategy (receiver side)
X
Seq. # | 234118
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234268
ACK flag | N/A
ACK # | N/A
Data Len | 120 bytes
Seq. # | 234388
ACK flag | N/A
ACK # | N/A
Data Len | 100 bytes
Seq. # | 234218
ACK flag | N/A
ACK # | N/A
Data Len | 50 bytes
234118
234218
234268
234388
234218
Sender
Receiver
(An example)

## Slide 36
TCP Cumulative ACK strategy (receiver side)
X
Seq. # | 234118
Data Len | 100 bytes
Seq. # | 234268
Data Len | 120 bytes
Seq. # | 234388
Data Len | 100 bytes
Seq. # | 234218
Data Len | 50 bytes
234118
234218
234268
234388
234218
Sender
Receiver
(An example)

## Slide 37
TCP Cumulative ACK strategy (receiver side)
X
Seq. # | 234118
Data Len | 100 bytes
Seq. # | 234268
Data Len | 120 bytes
Seq. # | 234388
Data Len | 100 bytes
Seq. # | 234218
Data Len | 50 bytes
ACKs
ACK flag | 1
ACK # | 
ACK flag | 1
ACK # | 
ACK flag | 1
ACK # | 
ACK flag | 1
ACK # | 
234118
234218
234268
234388
234218
Sender
Receiver
(An example)

## Slide 38
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
TCP Cumulative ACK strategy (receiver side)

## Slide 39
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
TCP Cumulative ACK strategy (receiver side)
234118
100 bytes

## Slide 40
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
TCP Cumulative ACK strategy (receiver side)
234118
100 bytes
234218

## Slide 41
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
TCP Cumulative ACK strategy (receiver side)
234118
100 bytes
234218
234268
120 bytes

## Slide 42
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
TCP Cumulative ACK strategy (receiver side)
234118
100 bytes
234218
234268
120 bytes
234388
100 bytes

## Slide 43
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
TCP Cumulative ACK strategy (receiver side)
234118
100 bytes
234268
120 bytes
234388
100 bytes
234218
50 bytes

## Slide 44
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
TCP Cumulative ACK strategy (receiver side)
234118
100 bytes
234488
234268
120 bytes
234388
100 bytes
234218
50 bytes

## Slide 45
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
Sender buffer:
Receiver buffer:
234118
234218
234268
234388
100 bytes
50 bytes
120 bytes
100 bytes
TCP Cumulative ACK strategy (receiver side)

## Slide 46
TCP Cumulative ACK strategy (receiver side)
X
Seq. # | 234118
Data Len | 100 bytes
Seq. # | 234268
Data Len | 120 bytes
Seq. # | 234388
Data Len | 100 bytes
Seq. # | 234218
Data Len | 50 bytes
ACKs
ACK flag | 1
ACK # | 234218
ACK flag | 1
ACK # | 234218
ACK flag | 1
ACK # | 234218
ACK flag | 1
ACK # | 234488
234118
234218
234268
234388
234218
Sender
Receiver
(An example)

## Slide 47: Flow Control: TCP Sliding Window
Motivation: Maximum utilization of the resources without overwhelming the receiver.

## Slide 48
Sliding Window
Receiver should have enough space to buffer/save the received data !!

## Slide 49: Sliding Window: Implementation
Allow a larger amount of data “in flight” for better channel utilization, but should not exceed receiver’s capacity.
Sending process
Receiving process
Last byte ACKed
Last byte sent
TCP
TCP
Next byte expected
Last byte written
Last byte read
Last byte received
Window

## Slide 50: Sliding Window: Implementation
Allow a larger amount of data “in flight”
  Allow sender to get ahead of the receiver
  … though not too far ahead
Sending process
Receiving process
Last byte ACKed
Last byte sent
TCP
TCP
Next byte expected
Last byte written
Last byte read
Last byte received
Window

## Slide 51: Receiver Buffering: Flow control
Receive window size
  Amount that can be sent without acknowledgment
  Receiver must be able to store this amount of data
Receiver tells the sender the window
  Tells the sender the amount of free space left (i.e. sends an Advertised_Window size to the sender)

## Slide 52
How to send the Advertised_Window size

## Slide 53
Calculate Advertised_Window (Receiver side)
Receiving process
TCP
Next byte expected
Last byte read
Last byte received
AdvertisedWindow = MaxRcvBuffer –
((NextByteExpected-1) – LastByteRead)
AdvertisedWindow = MaxRcvBuffer – (bytes used)

## Slide 54
Sender buffer
Receiver buffer

## Slide 55
Sender buffer
Receiver buffer
AdvertisedWindow = MaxRcvBuffer –
((NextByteExpected-1) – LastByteRead)
EffectiveWindow (calculated at the sender side)
= AdvertisedWindow - (LastByteSent – LastByteACKed)
What if the AdvertisedWindow is zero?
>> Periodically send 1byte packets to break the deadlock. (uses the persist timer)

## Slide 56
(1) Adv_window > MSS
What if…
(2) Adv_window < MSS
Considering Maximum Segment Size (MSS)
Window vs segment size are different dimensions
rwnd or Adv_window (Advertised Window): total bytes
allowed in flight
MSS: maximum bytes per segment
They are not competing limits; they apply at different levels.
MSS = MTU − (IP header + TCP header)

## Slide 57: A few points of discussions on TCP flow control
Silly window syndrome
Nagle’s algorithm (self-clocking)
Karn-Partridge algorithm

## Slide 58
Byte 1
Byte 2
Byte 3
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
Byte 80
Data
ACK + Adv_Win
Silly-window syndrome

## Slide 59
Silly window syndrome
What happens when the receiving application program consumes data slowly?
Leads to smaller advertised_window

## Slide 60
Silly window syndrome
Discussion: What can be the possible solutions?

## Slide 61
(1) Delayed ACK (a receiver-side approach)
Solution 1: Receiver side approach

## Slide 62
(1) Delayed ACK (a receiver-side approach)
- How much delay is good enough?
Solution 1: Receiver side approach

## Slide 63
(1) Delayed ACK (a receiver-side approach)
- How much delay is good enough?
[RFC 1122] A TCP SHOULD implement a delayed ACK, but an
ACK should not be excessively delayed; in particular,
the delay MUST be less than 0.5 seconds, and in a stream
of full-sized segments there SHOULD be an ACK for at least
every second segment.
Typically, OSs are more conservative. Use 200ms of delay.
Solution 1: Receiver side approach

## Slide 64
(2) Nagle’s algorithm (a sender-side approach)
Solution 2: Sender side approach

## Slide 65
Condition 0: Assumes there are some data to send. Otherwise, the sender will have to wait anyway.
Solution 2: Sender side approach

## Slide 66
Condition 1: The system is capable of sending a full MSS.
Send immediately.
Solution 2: Sender side approach

## Slide 67
Condition 2: Not enough data OR window size for a full MSS.
But some packets are in-flight (yet to receive ACK for).
Buffer the data and wait.
Solution 2: Sender side approach

## Slide 68
Condition 3: No packet is in-flight (i.e., all ACKs are received).
Send immediately, no matter how small the packet is.
Solution 2: Sender side approach

## Slide 69
(2) Nagle’s algorithm
Because some applications cannot afford such a delay for each write it does to a
TCP connection, the socket interface allows the application to turn off
Nagel’s algorithm by setting the TCP_NODELAY socket option.
TCP_QUICKACK option disables the Delayed Ack protocol.
Solution 2: Sender side approach

## Slide 70
What if sender and receiver simultaneously applies the Nagle’s algo. and delayed ack (TCP’s default setting) ?
[Ref] https://betterprogramming.pub/redis-internals-client-connects-to-redis-by-tcp-faf6ad1a7df5

## Slide 71
What if sender and receiver simultaneously applies the Nagle’s algo. and delayed ack (TCP’s default setting) ?
Sender
Receiver
Time
Packet-1
Nagle’s algo:
Buffered next packet
waiting for the ACK
for packet-1.
Delayed ACK:
Delayed the ACK
for packet-1.
Waiting for the next packet
to send the cumulative ACK
OR
the timeout to occur.

## Slide 72
What if sender and receiver simultaneously applies the Nagle’s algo. and delayed ack (TCP’s default setting) ?
Sender
Receiver
Time
Packet-1
Nagle’s algo:
Buffered next packet
waiting for the ACK
for packet-1.
Delayed ACK:
Delayed the ACK
for packet-1.
Waiting for the next packet
to send the cumulative ACK
OR
the timeout to occur.
Timeout after 500ms (default)

## Slide 73
What if sender and receiver simultaneously applies the Nagle’s algo. and delayed ack (TCP’s default setting) ?
Sender
Receiver
Time
Packet-1
Nagle’s algo:
Buffered next packet
waiting for the ACK
for packet-1.
Delayed ACK:
Delayed the ACK
for packet-1.
Waiting for the next packet
to send the cumulative ACK
OR
the timeout to occur.
Timeout after 500ms (default)
ACK for 1

## Slide 74
What if sender and receiver simultaneously applies the Nagle’s algo. and delayed ack (TCP’s default setting) ?
Sender
Receiver
Packet-1
Nagle’s algo:
Buffered next packet
waiting for the ACK
for packet-1.
Delayed ACK:
Delayed the ACK
for packet-1.
Waiting for the next packet
to send the cumulative ACK
OR
the timeout to occur.
Timeout after 500ms (default)
ACK for 1
Packet-2
Time
Notes: When Nagle's algorithm and delayed acknowledgment (delayed ACK) are used together, they can create a "deadlock" scenario, leading to delays and reduced throughput, especially for applications requiring immediate data transmission.

## Slide 75
Sender-side Timeout value calculation and its limitations

## Slide 76
Calculating TCP timeout value: The original idea

## Slide 77
Calculating TCP timeout value: The original idea
Smoothing factor (recommended between 0.8 -0.9)

## Slide 78
Calculating TCP timeout value: The original idea
Smoothing factor (recommended between 0.8 -0.9)

## Slide 79
Calculating TCP timeout value: The original idea
Smoothing factor (recommended between 0.8 -0.9)
RTT estimation can be wrong

## Slide 80
RTT estimation can be wrong

## Slide 81
RTT estimation can be wrong

## Slide 82
Solution: Karn/Partridge algorithm
Stop taking RTT samples when TCP retransmits
Start again after a regular transmission/reception
3) Each time TCP retransmits, set next timeout to be twice the last timeout value
Can rules #1 & #2 create issues?
Notes: Answer (2) This simplistic implementation of Karn's algorithm can lead to problems as well. Consider what happens when TCP sends a segment after a sharp increase in delay. Using the prior round-trip time estimate, TCP computes a timeout and retransmits a segment. If TCP ignores the round-trip time of all retransmitted packets, the round trip estimate will never be updated, and TCP will continue retransmitting every segment, never adjusting to the increased delay.
[Ref] https://en.wikipedia.org/wiki/Karn%27s_algorithm

## Slide 83
Thank you