## Slide 1
Computer Networks
Nirupam Roy
M-W 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2026
Topic:
Transport Layer Protocols:
Flow-control & Congestion Control
(Textbook chapters 5 & 6)
April 6th, 2026

## Slide 2: A few points of discussions on TCP flow control
Silly window syndrome
Nagle’s algorithm (self-clocking)
Karn-Partridge algorithm

## Slide 3
(2) Nagle’s algorithm
Because some applications cannot afford such a delay for each write it does to a
TCP connection, the socket interface allows the application to turn off
Nagel’s algorithm by setting the TCP_NODELAY socket option.
TCP_QUICKACK option disables the Delayed Ack protocol.
Solution 2: Sender side approach

## Slide 4
(2) Nagle’s algorithm
Because some applications cannot afford such a delay for each write it does to a
TCP connection, the socket interface allows the application to turn off
Nagel’s algorithm by setting the TCP_NODELAY socket option.
TCP_QUICKACK option disables the Delayed Ack protocol.
Solution 2: Sender side approach
Send small data immediately only if no unacknowledged data is in flight; otherwise, buffer until an ACK arrives or
enough data accumulates (≈ MSS).

## Slide 5
What if sender and receiver simultaneously applies the Nagle’s algo. and delayed ack (TCP’s default setting) ?
[Ref] https://betterprogramming.pub/redis-internals-client-connects-to-redis-by-tcp-faf6ad1a7df5

## Slide 6
What if sender and receiver simultaneously applies the Nagle’s algo. and delayed ack (TCP’s default setting) ?
Sender
Receiver
Time
Packet-1
Nagle’s algo:
Buffered next packet
waiting for the ACK
for packet-1.
Delayed ACK:
Delayed the ACK
for packet-1.
Waiting for the next packet
to send the cumulative ACK
OR
the timeout to occur.

## Slide 7
What if sender and receiver simultaneously applies the Nagle’s algo. and delayed ack (TCP’s default setting) ?
Sender
Receiver
Time
Packet-1
Nagle’s algo:
Buffered next packet
waiting for the ACK
for packet-1.
Delayed ACK:
Delayed the ACK
for packet-1.
Waiting for the next packet
to send the cumulative ACK
OR
the timeout to occur.
Timeout after 500ms (default)

## Slide 8
What if sender and receiver simultaneously applies the Nagle’s algo. and delayed ack (TCP’s default setting) ?
Sender
Receiver
Time
Packet-1
Nagle’s algo:
Buffered next packet
waiting for the ACK
for packet-1.
Delayed ACK:
Delayed the ACK
for packet-1.
Waiting for the next packet
to send the cumulative ACK
OR
the timeout to occur.
Timeout after 500ms (default)
ACK for 1

## Slide 9
What if sender and receiver simultaneously applies the Nagle’s algo. and delayed ack (TCP’s default setting) ?
Sender
Receiver
Packet-1
Nagle’s algo:
Buffered next packet
waiting for the ACK
for packet-1.
Delayed ACK:
Delayed the ACK
for packet-1.
Waiting for the next packet
to send the cumulative ACK
OR
the timeout to occur.
Timeout after 500ms (default)
ACK for 1
Packet-2
Time
Notes: When Nagle's algorithm and delayed acknowledgment (delayed ACK) are used together, they can create a "deadlock" scenario, leading to delays and reduced throughput, especially for applications requiring immediate data transmission.

## Slide 10
Sender-side Timeout value calculation and its limitations

## Slide 11
Calculating TCP timeout value: The original idea

## Slide 12
Calculating TCP timeout value: The original idea
Smoothing factor (recommended between 0.8 -0.9)

## Slide 13
Calculating TCP timeout value: The original idea
Smoothing factor (recommended between 0.8 -0.9)

## Slide 14
Calculating TCP timeout value: The original idea
Smoothing factor (recommended between 0.8 -0.9)
RTT estimation can be wrong

## Slide 15
RTT estimation can be wrong
Notes: TCP ACKs are cumulative and carry no transmission identifier. They only say:
“I have received all bytes up to sequence number X.”
Now consider a segment with sequence number S:
You send segment S at time t₀.
It is delayed (not necessarily lost).
You timeout and retransmit S at time t₁.
The receiver eventually sends an ACK for S.
When that ACK arrives, you cannot tell:
Did it acknowledge the original transmission (t₀)?
Or the retransmission (t₁)?
Both lead to the same ACK value.

## Slide 16
RTT estimation can be wrong
Could this issue be solved by checking Sequence # and ACK # ?
Notes: TCP ACKs are cumulative and carry no transmission identifier. They only say:
“I have received all bytes up to sequence number X.”
Now consider a segment with sequence number S:
You send segment S at time t₀.
It is delayed (not necessarily lost).
You timeout and retransmit S at time t₁.
The receiver eventually sends an ACK for S.
When that ACK arrives, you cannot tell:
Did it acknowledge the original transmission (t₀)?
Or the retransmission (t₁)?
Both lead to the same ACK value.

## Slide 17
RTT estimation can be wrong

## Slide 18
Solution: Karn/Partridge algorithm
Stop taking RTT samples when TCP retransmits
Start again after a regular transmission/reception
3) Each time TCP retransmits, set next timeout to be twice the last timeout value
Can rules #1 & #2 create issues?
Notes: Answer (2) This simplistic implementation of Karn's algorithm can lead to problems as well. Consider what happens when TCP sends a segment after a sharp increase in delay. Using the prior round-trip time estimate, TCP computes a timeout and retransmits a segment. If TCP ignores the round-trip time of all retransmitted packets, the round trip estimate will never be updated, and TCP will continue retransmitting every segment, never adjusting to the increased delay.
[Ref] https://en.wikipedia.org/wiki/Karn%27s_algorithm
How modern TCP partially “fixes” this
With the TCP Timestamp option (RFC 7323):
Sender includes a timestamp in each segment
Receiver echoes it back in the ACK
Now you can measure RTT for each transmission instance, eliminating ambiguity.

## Slide 19
Summary of TCP learned so far

## Slide 20
TCP: Abstraction of Reliable Bytes Stream

## Slide 21
TCP: Abstraction of Reliable Bytes Stream

## Slide 22
TCP: Abstraction of Reliable Bytes Stream

## Slide 23
TCP: Abstraction of Reliable Bytes Stream

## Slide 24
TCP: Abstraction of Reliable Bytes Stream
Flow control: Do not overwhelm the resources at the receiver
AdvertisedWindow

## Slide 25
TCP: Abstraction of Reliable Bytes Stream

## Slide 26
TCP: Abstraction of Reliable Bytes Stream
Notes: Multiple processes running simulataneously.

## Slide 27
TCP: Abstraction of Reliable Bytes Stream

## Slide 28
TCP: Abstraction of Reliable Bytes Stream
Flows contend for two resources:
1) Link bandwidth
2) Queue space

## Slide 29: Congestion A network is considered congested if contention for resources leads toward queue build-ups and packet drops
Best-effort network does not “block” calls
  So, they can easily become overloaded
  Congestion == “Load higher than capacity”
Examples of congestion
  Link layer: Ethernet frame collisions
  Network layer: full IP packet buffers
Excess packets are simply dropped
  And the sender can simply retransmit
queue

## Slide 30
Throughput vs Load
Goodput: Application-level throughput.
Goodput
Notes: Picture: https://ocw.mit.edu/courses/electrical-engineering-and-computer-science/6-829-computer-networks-fall-2002/lecture-notes/L8e2ecc.pdf

## Slide 31
Throughput vs Load
Notes: Picture: https://ocw.mit.edu/courses/electrical-engineering-and-computer-science/6-829-computer-networks-fall-2002/lecture-notes/L8e2ecc.pdf

## Slide 32
Congestion Collapse
Notes: Picture: https://ocw.mit.edu/courses/electrical-engineering-and-computer-science/6-829-computer-networks-fall-2002/lecture-notes/L8e2ecc.pdf

## Slide 33: Congestion Collapse is real !!
Easily leads to congestion collapse
  Senders retransmit the lost packets
  Leading to even greater load
  … and even more packet loss
Increase in load that results in a decrease in useful work done.

## Slide 34: Detect and Respond to Congestion
What does the end host see?
What can the end host change?
?

## Slide 35: Congestion in a Drop-Tail FIFO Queue
Access to the bandwidth: first-in first-out queue
  Packets transmitted in the order they arrive
✗
Access to the buffer space: drop-tail queuing
  If the queue is full, drop the incoming packet

## Slide 36: How it Looks to the End Host
Delay: Packet experiences high delay
Loss: Packet gets dropped along path
✗

## Slide 37: How it Looks to the End Host
Delay: Packet experiences high delay
Loss: Packet gets dropped along path
How does TCP sender learn this?
✗

## Slide 38: How it Looks to the End Host
Delay: Packet experiences high delay
Loss: Packet gets dropped along path
How does TCP sender learn this?
  Delay: Round-trip time estimate
  Loss: Timeout and/or duplicate acknowledgments
✗

## Slide 39: Detecting Congestion
Link layer
  Carrier sense multiple access
  Seeing your own frame collide with others
Network layer
  Observing end-to-end performance
  Packet delay or loss over the path

## Slide 40: How TCP detects packet losses
(2) Timeout
  Packet# n is lost and detected via a timeout
(1) Duplicate ACKs
  Packet# n is lost, but packets n+1, n+2, etc. are received and ACKs are sent.

## Slide 41: Responding to Congestion
Upon detecting congestion
  Decrease the sending rate

## Slide 42: Responding to Congestion
Upon detecting congestion
  Decrease the sending rate
But, what if conditions change?
  If more bandwidth becomes available,
  … unfortunate to keep sending at a low rate

## Slide 43: Responding to Congestion
Upon detecting congestion
  Decrease the sending rate
But, what if conditions change?
  If more bandwidth becomes available,
  … unfortunate to keep sending at a low rate
Upon not detecting congestion
  Increase sending rate, a little at a time
  See if packets get through

## Slide 44: TCP Congestion Control

## Slide 45
ACK works as the indicator and the window controls the flow.
Congestion_window: Calculated by the sender

## Slide 46
How to find the right window size?
When to change? How much?
ACK works as the indicator and the window controls the flow.

## Slide 47: TCP Congestion Window
Each TCP sender maintains a congestion window
  Max number of bytes to have in transit (not yet ACK’d)
Adapting the congestion window
  Decrease upon losing a packet: backing off
  Increase upon success: optimistically exploring
  Always struggling to find right transfer rate
Tradeoff
  Pro: avoids needing explicit network feedback
  Con: continually under- and over-shoots “right” rate

## Slide 48: Additive Increase, Multiplicative Decrease
How much to adapt?
  Additive increase: On success of last window of data, increase window by 1 Max Segment Size (MSS)
  Multiplicative decrease: On loss of packet, divide congestion window in half
Much quicker to slow than speed up!
  Over-sized windows (causing loss) are much worse than under-sized windows (causing lower thruput)
  AIMD: A necessary condition for stability of TCP

## Slide 49: Leads to the TCP “Sawtooth”
t
Window
halved
Loss

## Slide 50: TCP Congestion Control: TCP “Sawtooth”
Additive increase, multiplicative decrease (AIMD)
  On packet loss, divide congestion window in half
  On success for last window, increase window linearly
t
Window
halved
Loss

## Slide 51: Why Exponential decrease?
Respond aggressively to bad news
  Congestion is (very) bad for everyone
  Need to react aggressively
Nice theoretical properties
  Makes efficient use of network resources

## Slide 52: Receiver/Advertised Window vs. Congestion Window
Flow control
  Keep a fast sender from overwhelming a slow receiver
Congestion control
  Keep a set of senders from overloading the network
Different concepts, but similar mechanisms
  TCP flow control: receiver window
  TCP congestion control: congestion window
  Sender TCP window =
  min { congestion window, receiver window }

## Slide 53: Congestion control: Slow start

## Slide 54: How Should a New Flow Start?
t
Window
halved
Loss
Start slow (a small CWND) to avoid overloading network

## Slide 55: How Should a New Flow Start?
t
Window
halved
Loss
But, could take a long time to get started!
Start slow (a small CWND) to avoid overloading network

## Slide 56: “Slow Start” Phase
Start with a small congestion window
  Initially, CWND is 1 MSS
  So, initial sending rate is MSS / RTT
Could be pretty wasteful
  Might be much less than actual bandwidth
  Linear increase takes a long time to accelerate
Slow-start phase (really “fast start”)
  Sender starts at a slow rate (hence the name)
  … but increases rate exponentially until the first loss

## Slide 57: Slow Start in Action
Double CWND per round-trip time
D
A
D
D
A
A
D
D
A
A
D
A
Src
Dest
D
A
1
2
4
8

## Slide 58: Slow Start and the TCP Sawtooth
Why is this called “slow start”?
TCP originally had no congestion control
  Source would start by sending entire receiver window
  Led to congestion collapse!
  “Slow start” is, comparatively, slower
t
Window
halved
Loss
Exponential “slow start”
Linear “congestion avoidance” phase

## Slide 59: Response to the two types of losses

## Slide 60: Response to the two types of losses
(1) Triple duplicate ACK (Fast retransmit)
  Packet n is lost, but packets n+1, n+2, etc. arrive
  Then, sender quickly resends packet n
  Do a multiplicative decrease and keep going

## Slide 61: Fast retransmit
ACK for 2
1st Dup-ACK for 2
2nd Dup-ACK
3rd Dup-ACK

## Slide 62: Congestion window during Fast retransmit
t
Window
Packet loss (3-dup ack, fast retransmit, multiplicative decrease)

## Slide 63: Two Kinds of Loss in TCP
(2) Timeout (Repeat slow start – slow start restart)
  Packet n is lost and detected via a timeout
  Blasting entire CWND would cause another burst
  Better to start over with a low CWND
(1) Triple duplicate ACK (Fast retransmit)
  Packet n is lost, but packets n+1, n+2, etc. arrive
  Then, sender quickly resends packet n
  Do a multiplicative decrease and keep going

## Slide 64: Repeating Slow Start After Timeout (slow-start restart)
t
Window
Slow-start restart: Go back to CWND of 1, but take advantage of knowing the previous value of CWND.
Slow start until reaching half of previous cwnd.
timeout
Packet loss (3-dup ack, fast retransmit)

## Slide 65: Repeating Slow Start After Idle Period
Suppose a TCP connection goes idle for a while
Eventually, the network conditions change
  Maybe many more flows are traversing the link
Dangerous to start transmitting at the old rate
  Previously-idle TCP sender might blast network
  … causing excessive congestion and packet loss
So, some TCP implementations repeat slow start
  Slow-start restart after an idle period

## Slide 66: TCP congestion control
Conservation of packets:
If the connection is running at the available capacity (bandwidth) then a packet is not injected into the network unless a packet is taken out.
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 67: TCP congestion control: CWND graph
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 68
Implementation details
Update Time: Per RTT vs Per ACK

## Slide 69
Implementation details
Update Time: Per RTT vs Per ACK
Double CWND per round-trip time
D
A
D
D
A
A
D
D
A
A
D
A
Src
Dest
D
A
1
2
4
8

## Slide 70
Implementation details
Update Time: Per RTT vs Per ACK
Double CWND per round-trip time
D
A
D
D
A
A
D
D
A
A
D
A
Src
Dest
D
A
1
2
4
8
Implemented as CWND = CWND + 1 (per ACK)

## Slide 71
Implementation details
Update Time: Per RTT vs Per ACK
Linear increase of CWND per round-trip time
D
A
D
D
A
A
D
D
A
A
D
A
Src
Dest
D
1
2
3
4
Implemented as CWND = CWND + 1/CWND (per ACK)

## Slide 72: TCP congestion control: CWND graph
CWND = 1
First packet loss (3-dup acks)
CWND = CWND/2
Congestion avoidance CWND = CWND + (1/CWND)
Packet loss
(3-dup acks)
CWND = CWND/2
Time out(no acks)
SSTHRES = CWND/2
Slow Start restart
Slow Start end
Congestion
avoidance
CWND =
CWND +
(1/CWND)
Slow start
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 73: TCP congestion control
SSTHRES = Slow-start threshold
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 74: Development of Congestion Control over TCP versions
Copyright, 1996 © Dale Carnegie & Associates, In

## Slide 75: TCP versions
TCP is not perfectly homogenous (200+)
4.2 BSD first widely available release of TCP/IP (1983)
4.3 BSD (1986)
4.3 BSD Tahoe (1988)
4.3 BSD Reno (1990)
Vegas (1994)
Windows 95
SunOS 4.1.3,4.1.4
4.4 BSD (1993)
HP/UX
Solaris 2.3,2.4
Digital OSF
Windows NT
Linux 1.0
IRIX
.....
NewReno (1999)
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications
BSD stands for Berkeley Software Distribution, a family of Unix-like operating systems developed at the University of California, Berkeley. BSD is connected to TCP congestion control because several key TCP congestion control algorithms, like TCP Tahoe and TCP Reno, were first implemented in the 4.3BSD operating system.

## Slide 76: TCP Congestion Controls
Tahoe (Jacobson 1988)
  Slow Start
  Congestion Avoidance
  Fast Retransmit (FR)

## Slide 77: TCP Tahoe (Jacobson 1988)
SS
time
window
CA
SS: Slow Start
CA: Congestion Avoidance
Notes: In TCP Tahoe, the initial value for ssthresh (slow start threshold) is 32 segments.

## Slide 78: Slow Start in Tahoe
Start with cwnd = 1 (slow start)
On each successful ACK increment cwnd
cwnd  cnwd + 1
Exponential growth of cwnd
each RTT: cwnd  2 x cwnd
Enter CA when cwnd >= ssthresh

## Slide 79: Slow Start
data packet
ACK
receiver
sender
1 RTT
cwnd
1
2
3
4
5
6
7
8
cwnd  cwnd + 1 (for each ACK)

## Slide 80: Congestion Avoidance
Starts when cwnd  ssthresh
On each successful ACK: cwnd  cwnd + 1/cwnd
Linear growth of cwnd
each RTT: cwnd  cwnd + 1

## Slide 81: Congestion Avoidance
cwnd
1
2
3
1 RTT
4
data packet
ACK
cwnd  cwnd + 1 (for each “cwnd number of ACKS”)
receiver
sender

## Slide 82: Packet Loss
Assumption: loss indicates congestion
Packet loss detected by
  Retransmission TimeOuts (RTO timer)
  Duplicate ACKs (at least 3)
1
2
3
4
5
6
1
2
3
Packets
Acknowledgements
3
3
7
3

## Slide 83: Fast Retransmit (Tahoe)
Wait for a timeout is quite long
Immediately retransmits after 3 dupACKs without waiting for timeout
Adjusts ssthresh
flightsize = min(awnd, cwnd)
ssthresh  max(flightsize/2, 2)
Enter Slow Start (cwnd = 1)
Notes: In TCP Tahoe, the initial value for ssthresh (slow start threshold) is 32 segments.

## Slide 84: Summary: Tahoe
Basic ideas
  Gently probe network for spare capacity
  Drastically reduce rate on congestion
  Windowing: self-clocking
  Other functions: round trip time estimation, error recovery
for every ACK {
if (W < ssthresh) then W++ (SS)
else W += 1/W (CA)
}
for every loss {
ssthresh = W/2
W = 1
}
Notes: In TCP Tahoe, the initial value for ssthresh (slow start threshold) is 32 segments.

## Slide 85: TCP Congestion Controls
Tahoe (Jacobson 1988)
  Slow Start
  Congestion Avoidance
  Fast Retransmit (FR)
Reno (Jacobson 1990)
  Fast Recovery

## Slide 86: Tahoe’s CWND recovers slowly
SS
time
window
CA
SS: Slow Start
CA: Congestion Avoidance

## Slide 87: TCP Reno
SS
time
window
CA
SS: Slow Start
CA: Congestion Avoidance
Fast retransmission/Fast recovery

## Slide 88: TCP Reno
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 89: TCP Reno: details of Fast Recovery
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 90: TCP Reno
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 91: TCP Reno: details of Fast Recovery
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 92: TCP Reno: details of Fast Recovery
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 93: TCP Reno: details of Fast Recovery
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 94
Sender
Receiver
CWND=1, UNACK=1
CWND=2, UNACK=1
CWND=2, UNACK=2
CWND=3, UNACK=2
CWND=4, UNACK=2
CWND=4, UNACK=3
CWND=4, UNACK=4
CWND=5, UNACK=4
CWND=6, UNACK=4
CWND=6, UNACK=5
CWND=6, UNACK=6, DuACK=1
CWND=6, UNACK=6, DuACK=2
X
SSTH=3, CWND=3+3, UNACK=6, DuACK=3
SSTH=3, CWND=3+4, UNACK=7, DuACK=4
SSTH=3, CWND=3+5, UNACK=8, DuACK=5
(New ACK) CWND=SSTH=3, UNACK=2
P=0, ACK=1
P=1, ACK=2
P=2, ACK=3
P=3, ACK=4
P=4, ACK=5
P=6, ACK=5
P=7, ACK=5
P=8, ACK=5
P=9, ACK=5
P=10, ACK=5
P=5, ACK=11
P=11, ACK=12
P=12, ACK=13
EXAMPLE:
With Fast
Recovery

## Slide 95
Sender
Receiver
CWND=1, UNACK=1
CWND=2, UNACK=1
CWND=2, UNACK=2
CWND=3, UNACK=2
CWND=4, UNACK=2
CWND=4, UNACK=3
CWND=4, UNACK=4
CWND=5, UNACK=4
CWND=6, UNACK=4
CWND=6, UNACK=5
CWND=6, UNACK=6, DuACK=1
CWND=6, UNACK=6, DuACK=2
X
SSTH=3, CWND=3, UNACK=6, DuACK=3
SSTH=3, CWND=3, UNACK=6, DuACK=4
SSTH=3, CWND=3, UNACK=6, DuACK=5
(New ACK) CWND=3+1/3, UNACK=1
P=0, ACK=1
P=1, ACK=2
P=2, ACK=3
P=3, ACK=4
P=4, ACK=5
P=6, ACK=5
P=7, ACK=5
P=8, ACK=5
P=9, ACK=5
P=10, ACK=5
P=5, ACK=11
P=11, ACK=12
EXAMPLE:
Without Fast
Recovery

## Slide 96: Fast Retransmit/Fast Recovery (FR/FR) (will work on this example during lecture)
13
14
15
16
17
18
X
14
14
14
14
14
19
STHRES
CWND
TX
RX
<Open>
19
20
6
6
N/A
Notes: After FR/FR, when CA is entered, cwnd is half of the window when lost was detected.
So the effect of lost is halving the window.
[Source: RFC 2581, Fall & Floyd, “Simulation based Comparison of Tahoe, Reno, and SACK TCP”]

## Slide 97: Fast Retransmit/Fast Recovery (FR/FR)
[Ref] https://www.mdpi.com/2076-3417/9/21/4698
10
TSF = Segments in flight
Notes: After FR/FR, when CA is entered, cwnd is half of the window when lost was detected.
So the effect of lost is halving the window.
[Source: RFC 2581, Fall & Floyd, “Simulation based Comparison of Tahoe, Reno, and SACK TCP”]

## Slide 98: Fast Retransmit/Fast Recovery (FR/FR)
Motivation: prevent `pipe’ from emptying after fast retransmit
Idea: each dupACK represents a packet having left the pipe (successfully received)
Enter FR/FR after 3 dupACKs
  Set ssthresh  max(flightsize/2, 2)
  Retransmit lost packet
  Set cwnd  ssthresh + ndup (window inflation)
  Wait till W=min(awnd, cwnd) is large enough; transmit new packet(s)
  On non-dup ACK (1 RTT later), set cwnd  ssthresh (window deflation)
Enter CA
Notes: After FR/FR, when CA is entered, cwnd is half of the window when lost was detected.
So the effect of lost is halving the window.
[Source: RFC 2581, Fall & Floyd, “Simulation based Comparison of Tahoe, Reno, and SACK TCP”]

## Slide 99: Summary: Reno
Basic ideas
  Fast recovery avoids slow start
  dupACKs: fast retransmit + fast recovery
  Timeout: fast retransmit + slow start
slow start
retransmit
congestion avoidance
FR/FR
dupACKs
timeout

## Slide 100: TCP congestion control: CWND graph
Notes: [source: G.R.Wright and W.R.Stevens, TCP/IP Illustrated, Vol 2; J. Hoe, MSc Thesis, pp.22]
Tahoe (1988): slow start, congestion avoidance, fast retransmit
Reno (1990): fast recovery, TCP header prediction, SLIP header compression, routing table changes
4.4BSD (1993): multicasting, long fat pipe modifications

## Slide 101: Problem with Reno
Reno retransmit at most 1 lost packet per RTT
  Pipe can be emptied during “Fast Retransmit/Fast Recovery” with multiple losses
Solution: TCP with Selective Acknowledgements (SACK) provides better estimate of packets in pipe
  SACK TCP option describes received packets
  On 3 dupACKs: retransmits, halves window, enters FR
  Updates pipe = packets in pipe
    Increment when lost or new packets sent
    Decrement when dupACK received
  Transmits a (lost or new) packet when pipe < cwnd
  Exit FR when all packets outstanding when FR was entered are acknowledged
Notes: [Sources: M. Mathis, J. Mahdavi, S. Floyd and A. Romanow, “TCP Selective Acknowledgement Options”, RFC 2018, Oct. 1996
K. Fall and S. Floyd, “Simulation-based comparisons of Tahoe, Reno and SACK TCP”, Computer Communication Review, July 1996 ]

## Slide 102: TCP Vegas (Brakmo & Peterson 1994)
Considers packet delay, not loss, as a hint for congestion
Reno with a new congestion avoidance algorithm
Converges (provided buffer is large) !
SS
time
window
CA

## Slide 103: Router-assisted Congestion Control
Copyright, 1996 © Dale Carnegie & Associates, In

## Slide 104: Congestion Control discussed so far
?
?
link
session
path
name
address
What can the end-points do to collectively to make good use of shared underlying resources?
Notes: This week, we’ll talk about how to share resources. Today we’ll talk about what the end-points can do in a distributed fashion, from the edge of the network. On Wednesday, we’ll talk about what the lower-level elements can do.

## Slide 105
link
session
path
name
address
What can the individual links do to make good use of shared underlying resources?
?
Router-assisted Congestion Control
Notes: This week, we’ll talk about how to share resources. Today we’ll talk about what the end-points can do in a distributed fashion, from the edge of the network. On Wednesday, we’ll talk about what the lower-level elements can do.

## Slide 106: Router
Switching
Fabric
Processor
Line card
Line card
Line card
Line card
Line card
Line card
data plane
control plane

## Slide 107: Line Cards (Interface Cards, Adaptors)
Packet handling
  Packet forwarding
  Buffer management
  Link scheduling
  Packet filtering
  Rate limiting
  Packet marking
  Measurement
to/from link
to/from switch
lookup
Receive
Transmit

## Slide 108: Packet Switching and Forwarding
R1
Link 1
Link 2
Link 3
Link 4
Link 1, ingress
Link 1, egress
Link 2, ingress
Link 2, egress
Link 3, ingress
Link 3, egress
Link 4, ingress
Link 4, egress
Choose
Egress
Choose
Egress
Choose
Egress
Choose
Egress
“4”
“4”

## Slide 109: Queue Management Issues
Scheduling discipline
  Which packet to send?
  Some notion of fairness? Priority?
Drop policy
  When should you discard a packet?
  Which packet to discard?
Goal: balance throughput and delay
  Huge buffers minimize drops, but add to queuing delay (thus higher RTT, longer slow start, …)

## Slide 110: Queue Management 1: Drop Policy

## Slide 111: FIFO Scheduling and Drop-Tail
Access to the bandwidth: first-in first-out queue
  Packets only differentiated when they arrive
Access to the buffer space: drop-tail queuing
  If the queue is full, drop the incoming packet
✗

## Slide 112: Bursty Loss From Drop-Tail Queuing
TCP depends on packet loss
  Packet loss is indication of congestion
  TCP additive increase drives network into loss
Drop-tail leads to bursty loss
  Congested link: many packets encounter full queue
  Synchronization: many connections lose packets at once

## Slide 113: Slow Feedback from Drop Tail
Feedback comes when buffer is completely full
  … even though the buffer has been filling for a while
Plus, the filling buffer is increasing RTT
  … making detection even slower
Better to give early feedback
  Get 1-2 connections to slow down before it’s too late!

## Slide 114: Random Early Detection (RED)
Router notices that queue is getting full
  … and randomly drops packets to signal congestion
Packet drop probability
  Drop probability increases as queue length increases
  Else, set drop probability f(avg queue length)
Average Queue Length
Drop
Probability
0 1

## Slide 115: Properties of RED
Drops packets before queue is full
  In the hope of reducing the rates of some flows
Drops packet in proportion to each flow’s rate
  High-rate flows selected more often
Drops are spaced out in time
  Helps desynchronize the TCP senders
Tolerant of burstiness in the traffic
  By basing the decisions on average queue length

## Slide 116: Problems With RED
Hard to get tunable parameters just right
  How early to start dropping packets?
  What slope for increase in drop probability?
  What time scale for averaging queue length?
RED has mixed adoption in practice
  If parameters aren’t set right, RED doesn’t help
Many other variations in research community
  Names like “Blue” (self-tuning), “FRED”…

## Slide 117: Feedback: From Loss to Notification
Early dropping of packets
  Good: gives early feedback
  Bad: has to drop the packet to give the feedback
Explicit Congestion Notification (ECN)
  Router marks the packet with an ECN bit, instead of dropping it.
  Receiver send this ECN info to the sender.
  Sending host interprets as a sign of congestion
  Requires participation of hosts and the routers
Notes: 17.6.2 Explicit Congestion Notification
Explicit congestion notification (ECN) is another feedback scheme that indicates congestion information by marking packets instead of dropping them. The destination of marked packets returns this congestion notification to the source. As a result, the source decreases its transmit rate. The implementation of ECN uses an ECN-specific field in the IP header with two bits—the ECN-capable Transport (ECT) bit and the Congestion Experienced (CE) bit.

## Slide 118: Queue Management 2: Link Scheduling

## Slide 119: First-In First-Out Scheduling
First-in first-out scheduling
  Simple, but restrictive
Example: two kinds of traffic
  Voice over IP needs low delay
  E-mail is not that sensitive about delay
Voice traffic waits behind e-mail

## Slide 120: Strict Priority
Multiple levels of priority
  Always transmit high-priority traffic, when present
Isolation for the high-priority traffic
  Almost like it has a dedicated link
  Except for (small) delay for packet transmission
But, lower priority traffic may starve 

## Slide 121: Weighted Fair Scheduling
Weighted fair scheduling
  Assign each queue a fraction of the link bandwidth
  Rotate across queues on a small time scale
Work-conserving
  Send extra traffic from one queue if others are idle
50% red, 25% blue, 25% green

## Slide 122: Implementation Trade-Offs
FIFO
  One queue, trivial scheduler
Strict priority
  One queue per priority level, simple scheduler
Weighted fair scheduling
  One queue per class, and more complex scheduler

## Slide 123
TCP Congestion Control

## Slide 124
TCP Congestion Control
Should TCP increment CWND during Dup-ACKs?

## Slide 125: Revisiting Dup ACKs (without Fast-Recovery)
13
14
15
16
17
18
X
14
14
14
14
14
19
STHRES
CWND
TX
RX
<Open>
19
20
5
6
N/A
14
21
Notes: After FR/FR, when CA is entered, cwnd is half of the window when lost was detected.
So the effect of lost is halving the window.
[Source: RFC 2581, Fall & Floyd, “Simulation based Comparison of Tahoe, Reno, and SACK TCP”]

## Slide 126
13
14
15
16
17
18
X
14
14
14
14
?
STHRES
CWND
TX
RX
<Open>
5
6
N/A
What if there are multiple losses in an RTT?
X
19
20
14
21
Revisiting Dup ACKs (without Fast-Recovery)
Notes: After FR/FR, when CA is entered, cwnd is half of the window when lost was detected.
So the effect of lost is halving the window.
[Source: RFC 2581, Fall & Floyd, “Simulation based Comparison of Tahoe, Reno, and SACK TCP”]

## Slide 127
TCP Selective ACK (SACK): RFC 2018
https://www.rfc-editor.org/rfc/rfc2018

## Slide 128
TCP Selective ACK (SACK): RFC 2018
[REF-1] https://www.rfc-editor.org/rfc/rfc2018
[REF-2] https://www.excentis.com/blog/measuring-throughput-effect-of-used-tcp-settings/

## Slide 129
Slides courtesy: https://cseweb.ucsd.edu/classes/wi01/cse222/lectures/attack-18.pdf
Paper link: https://dl.acm.org/doi/10.1145/505696.505704

## Slide 137
Today’s TCP versions

## Slide 138
Today’s TCP versions
Mac OS-X
OS-X Mountain Lion (2012)  TCP New Reno
OS-X Mavericks (2023) to Sonoma (2023)  TCP CUBIC
Linux kernel
2.6.13 (2005)  TCP BIC (default)
2.6.19 (2006) to 6.7+ (2024)  TCP CUBIC (default)
Windows
Windows 8 (2013)  Compound TCP (CTCP)
Windows 10.1709 (2017) TCP CUBIC
Windows 11 (2021) TCP CUBIC

## Slide 139
BIC/CUBIC slides are adopted from: Injong Rhee, Lisong Xu, Ahmed El-Hassany, Qian HE, Bob Kinicki
TCP BIC: Issues with Reno
Notes: Slides adopted from: Injong Rhee, Lisong Xu, Ahmed El-Hassany

## Slide 140: Response Function of TCP
Response function of TCP is the average throughput of a TCP connection in terms of the packet loss probability, the packet size, and the round-trip time.
  R : Average Throughput
  MSS: Packet Size
  RTT: Round-Trip Time
  P : Packet Loss Probability
Response Function of TCP is :
J. Padhye, V. Firoio, D. Towsley, J. Kurose, "Modeling TCP Throughput: a Simple Model and its Empirical Validation", Proceedings of SIGCOMM 98
Notes: Usually, we study the performance of TCP using its response function, which is defined as the average throughput of TCP in terms of packet loss probability.
Here is the response function of TCP. In this function, MSS is the packet size, RTT is the round trip time, and p is the packet loss probability. From this function, we can see that the throughput of TCP depends on the packet size, the round-trip time, and the packet loss probability. In order to increase the throughput of TCP, we can either increase the packet size, or decrease the round trip time, or decrease the packet loss probability. Usually for a TCP connection, the packet size and round-trip time are fixed. Therefore, the throughput of a TCP connection mainly depends on the packet loss probability.

## Slide 141
x ms
y1 ms
y2 ms
z1 ms
z2 ms
y1 + x + z1 >> y2 + x + z2
TCP BIC: Issues with Reno – RTT unfairness

## Slide 142: Why BIC (Response Function of TCP)
10Gbps requires a packet loss rate of 10-10, or correspondingly a link bit error rate of at most 10-14, which is an unrealistic (or at least hard) requirement for current networks
Using Log-Log scale, Assuming 1250-Byte packet size, and 100ms RTT
Notes: In this figure, we show how the throughput changes as we vary the packet loss probability. Note that the figure is shown in log-log scale. We can see that as the packet loss probability decreases, the TCP throughput increases. Assume the packet size is 1000 Bytes, and the RTT is 100ms, then TCP achieves the 10Gbps throughput when the packet loss probability is around 10-10.which corresponds to a link BER of 10-14. which is an unrealistic requirement for current networks. That is, in the current networks, it is impossible for TCP to achieve 10Gbps throughput.

## Slide 143: A Search Problem
A Search Problem
  BIC consider the increase part of congestion avoidance as a search problem, in which a connection looks for the available bandwidth by comparing its current throughput with the available bandwidth, and adjusting cwnd accordingly.
How does standard TCP find the available bandwidth?
Linear search
  while (no packet loss){
  cwnd++;
  }
Q: How to compare R with A?
  R = current throughput
  = cwnd/RTT
  A = available bandwidth
A: Check for packet losses
  No packet loss: R <= A
  Packet losses : R > A

## Slide 144: Linear Search
Available Bandwidth

## Slide 145
TCP slowly increases its congestion window (cwnd) for every RTT.
TCP reduces cwnd by half at a lost event.
TCP BIC: Issues with Reno

## Slide 146
“Binary Increase Congestion Control (BIC) for Fast Long-Distance Networks”, Lisong Xu, Khaled Harfoush, and Injong Rhee, IEEE INFOCOM 2004
TCP BIC

## Slide 147
BIC - Binary search
  while (Wmin <= Wmax){
  inc = (Wmin+Wmax)/2 - cwnd;
  if (inc > Smax)
  inc = Smax;
  else if (inc < Smin)
  inc = Smin;
  cwnd = cwnd + inc;
  if (no packet losses)
  Wmin = cwnd;
  else
  break;
  }
Wmax: Max Window
Wmin: Min Window
Smax: Max Increment
Smin: Min Increment
TCP BIC: The algorithm

## Slide 148
If cwnd < low_window, normal TCP:
  ACK received
    cwnd = cwnd + 1
  Enter recovery
    cwnd = cwnd * 0.5
Else, BIC
TCP BIC: The algorithm

## Slide 149
BIC Algorithm
ACK received
  If cwnd < Wmax
    cwnd += (Wmax – cwnd) / 2
  Else
    cwnd += cwnd - Wmax
Recovery
  If cwnd < Wmax
    Wmax = cwnd * (1 – ß / 2)
  Else
    Wmax = cwnd
  cwnd *= 1 - ß
Smin <= cwnd
&&
cwnd <=Smax

## Slide 150
BIC with no lost
Chart: Time (RTT)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Linear Search | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Binary Search with Smax and Smin | 0 | 64 | 128 | 192 | 224 | 240 | 248 | 252 | 254 | 255 | 256
Smax
Smin

## Slide 151: Binary Search with Smax and Smin
Smin
Smax
Wmax
Wmin
Available Bandwidth

## Slide 152: Setting Smax
Response Function of BIC on high-speed networks
Bandwidth scalability of BIC depends only on Smax
RTT Fairness of BIC on high-speed networks is the same as that of AIMD
Bandwidth scalability

## Slide 153: Setting Smin
Response Function of BIC on low-speed networks
TCP-friendliness of BIC depends only on Smin
TCP friendliness

## Slide 154: In Summary BIC function
BIC overall performs very well in evaluation of advanced TCP stacks on fast long-distance production.
BIC (also HSTCP & STCP) growth function can be still aggressive for TCP especially under short RTTs or low speed networks.

## Slide 155
Make window size growth function independent from RTT.
Use the elapsed real-time since the last loss event.
Goals
  TCP friendly
  RTT fair
  Co-existing flows with different RTTs are treated fairly
  Efficient use of available bandwidth
In Summary BIC function

## Slide 156
Window control of BIC is so complex!
BIC’s growth function can still be too aggressive for TCP, especially under short RTT or low speed networks.
BIC still has room for improving TCP-friendliness and RTT-fairness!
156
TCP CUBIC: Why CUBIC?

## Slide 157: The CUBIC function
where C is a scaling factor, t is the elapsed time from the last window reduction, and β is a constant multiplication decrease factor
accelerate
accelerate
slow down

## Slide 158
ACK received
  C is a scaling factor
  t is the elapsed time from the last window reduction
  Wmax is the window size just before the last window reduction
  K is updated at the time of last lost event
Recovery
  Update K with:
  Update Wmax with:
  β is a constant multiplication decrease factor
TCP CUBIC: The algorithm
Notes: The CUBIC function (simplified):
cwnd(t)=C⋅(t−K)3+Wmaxcwnd(t)=C⋅(t−K)3+Wmax​Where:
t: Time since last congestion event
K: Time at which the function reaches Wma
C: Scaling constant (aggressiveness)
Wmax​: Last maximum congestion window
As t gets close to K, (t−K)3 approaches zero, and the function flattens near WmaxWmax​.

## Slide 159
ACK received
  C is a scaling factor
  t is the elapsed time from the last window reduction
  Wmax is the window size just before the last window reduction
  K is updated at the time of last lost event
Recovery
  Update K with:
  Update Wmax with:
  β is a constant multiplication decrease factor
cwnd cannot be less than
as to keep the growth rate the same as standard TCP in short RTT networks.
TCP CUBIC: The algorithm

## Slide 160
CUBIC window curves with competing flows (NS simulation in a network with 500Mbps and 100ms RTT), C = 0.4, β = 0.8.

## Slide 161
TCP ex Machina: Remy
Link to the paper: https://web.mit.edu/remy/TCPexMachina.pdf