## Slide 1
Computer Networks
Nirupam Roy
M-W 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2026
Topic: Inter-domain Routing (BGP)
(Textbook chapter 2)

## Slide 2: Join EGP with IGP For Connectivity
Forwarding Table
Forwarding Table
AS 1
AS 2
192.0.2.1
135.207.0.0/16
10.10.10.10
EGP
192.0.2.1
135.207.0.0/16
destination
next hop
10.10.10.10
192.0.2.0/30
destination
next hop
135.207.0.0/16
Next Hop = 192.0.2.1
192.0.2.0/30
135.207.0.0/16
destination
next hop
10.10.10.10
+
192.0.2.0/30
10.10.10.10

## Slide 3: A dive into the BGP policies

## Slide 4: Nontransit vs. Transit ASes
ISP 1
ISP 2
Nontransit AS
might be a corporate
or campus network.
Could be a “content
provider”
NET A
Traffic NEVER
flows from ISP 1
through NET A to ISP 2
(At least not intentionally!)
IP traffic
Internet Service
providers (often)
have transit
networks

## Slide 5: Selective Transit
NET B
NET C
NET A provides transit
between NET B and NET C
and between NET D
and NET C
NET A
NET D
NET A DOES NOT
provide transit
Between NET D
and NET B
Most transit networks transit in a selective manner…
IP traffic

## Slide 6: Customers and Providers
Customer pays provider for access to the Internet
provider
customer
IP traffic
provider
customer

## Slide 7: Customers Don’t Always Need BGP
provider
customer
Nail up default routes 0.0.0.0/0
pointing to provider.
Nail up routes 192.0.2.0/24
pointing to customer
192.0.2.0/24
Static routing is the most common way of connecting an
autonomous routing domain to the Internet.
This helps explain why BGP is a mystery to many …

## Slide 8: Customer-Provider Hierarchy
IP traffic
provider
customer

## Slide 9: The Peering Relationship
peer
peer
customer
provider
Peers provide transit between
their respective customers
Peers do not provide transit
between peers
Peers (often) do not exchange $$$
traffic
allowed
traffic NOT
allowed

## Slide 10: Peering Provides Shortcuts
Peering also allows connectivity between
the customers of “Tier 1” providers.
peer
peer
customer
provider

## Slide 11: BGP-4
BGP = Border Gateway Protocol
Is a Policy-Based routing protocol
Is the de facto EGP of today’s global Internet
Relatively simple protocol, but configuration is complex and the entire world can see, and be impacted by, your mistakes.
1989 : BGP-1 [RFC 1105]
  Replacement for EGP (1984, RFC 904)
1990 : BGP-2 [RFC 1163]
1991 : BGP-3 [RFC 1267]
1995 : BGP-4 [RFC 1771]
  Support for Classless Interdomain Routing (CIDR)

## Slide 12: BGP Operations (Simplified)
Establish session on
TCP port 179
Exchange all
active routes
Exchange incremental
updates
AS1
AS2
While connection
is ALIVE exchange
route UPDATE messages
BGP session

## Slide 13: Four Types of BGP Messages
Open : Establish a peering session.
Keep Alive : Handshake at regular intervals.
Notification : Shuts down a peering session.
Update : Announcing new routes or withdrawing previously announced routes.
announcement
=
prefix + attributes values

## Slide 14: BGP Attributes
Value Code Reference
----- --------------------------------- ---------
1 ORIGIN [RFC1771]
2 AS_PATH [RFC1771]
3 NEXT_HOP [RFC1771]
4 MULTI_EXIT_DISC [RFC1771]
5 LOCAL_PREF [RFC1771]
6 ATOMIC_AGGREGATE [RFC1771]
7 AGGREGATOR [RFC1771]
8 COMMUNITY [RFC1997]
9 ORIGINATOR_ID [RFC2796]
10 CLUSTER_LIST [RFC2796]
11 DPA [Chen]
12 ADVERTISER [RFC1863]
13 RCID_PATH / CLUSTER_ID [RFC1863]
14 MP_REACH_NLRI [RFC2283]
15 MP_UNREACH_NLRI [RFC2283]
16 EXTENDED COMMUNITIES [Rosen]
...
255 reserved for development
From IANA: http://www.iana.org/assignments/bgp-parameters
Most important attributes
Not all attributes
need to be present in
every announcement
Notes: In BGP, the treat-as-withdraw path attribute is used to effectively rescind a path, meaning it removes a prefix from the BGP routing table if a specific path attribute is matched.

## Slide 15: Attributes are Used to Select Best Routes
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
Given multiple
routes to the same
prefix, a BGP speaker
must pick at most
one best route
(Note: it could reject
them all!)

## Slide 16: BGP Next Hop Attribute
Every time a route announcement crosses an AS boundary, the Next Hop attribute is changed to the IP address of the border router that announced the route.
AS 6431
AT&T Research
135.207.0.0/16
Next Hop = 12.125.133.90
AS 7018
AT&T
AS 12654
RIPE NCC
RIS project
12.125.133.90
135.207.0.0/16
Next Hop = 12.127.0.121
12.127.0.121

## Slide 17: Join EGP with IGP For Connectivity
Forwarding Table
Forwarding Table
AS 1
AS 2
192.0.2.1
135.207.0.0/16
10.10.10.10
EGP
192.0.2.1
135.207.0.0/16
destination
next hop
10.10.10.10
192.0.2.0/30
destination
next hop
135.207.0.0/16
Next Hop = 192.0.2.1
192.0.2.0/30
135.207.0.0/16
destination
next hop
10.10.10.10
+
192.0.2.0/30
10.10.10.10

## Slide 18: Implementing Customer/Provider and Peer/Peer relationships
Enforce transit relationships
  Outbound route filtering
Enforce order of route preference
  provider < peer < customer
Two parts:

## Slide 19: Import Routes
From
peer
From
peer
From
provider
From
provider
From
customer
From
customer
provider route
customer route
peer route
AS-219

## Slide 20: Import Routes
From
peer
From
peer
From
provider
From
provider
From
customer
From
customer
provider route
customer route
peer route

## Slide 21: Export Routes
To
peer
To
peer
To
customer
To
customer
To
provider
From
provider
provider route
customer route
peer route
ISP route
?
?
?
?
?
?
provider route
customer route
peer route

## Slide 22: Export Routes
To
peer
To
peer
To
customer
To
customer
To
provider
From
provider
provider route
customer route
peer route
ISP route
provider route
customer route
peer route

## Slide 23: Export Routes
To
peer
To
peer
To
customer
To
customer
To
provider
From
provider
provider route
customer route
peer route
ISP route
filters
block
provider route
customer route
peer route

## Slide 24: Export Routes
To
peer
To
peer
To
customer
To
customer
To
provider
From
provider
provider route
customer route
peer route
ISP route
filters
block
provider route
customer route
peer route

## Slide 25: How Can Routes be Colored? BGP Communities!
A community value is 32 bits
By convention,
first 16 bits is
ASN indicating
who is giving it
an interpretation
community
number
Very powerful
BECAUSE it
has no (predefined) meaning
Community Attribute = a list of community values.
(So one route can belong to multiple communities)
RFC 1997 (August 1996)
Used for signalling
within and between
ASes
Two reserved communities
no_advertise 0xFFFFFF02: don’t pass to BGP neighbors
  no_export = 0xFFFFFF01: don’t export out of AS

## Slide 26
BGP Communities examples
Notes: no-exportDon’t advertise this route to external (eBGP) peers.no-advertiseDon’t advertise this route to any peers (iBGP or eBGP).local-ASDon’t advertise this route outside the local AS, even within confederations.

## Slide 27
Tag customer routes with 64512:100.
Instruct Router B to only advertise routes with 64512:100.

## Slide 28
Instruct Router B to only advertise routes with 64512:100.
Tag customer routes with 64512:100. (on Router A)

## Slide 29
BGP Community attribute: Example

## Slide 30: Tweak Tweak Tweak
For inbound traffic
  Filter outbound routes
  Tweak attributes on outbound routes in the hope of influencing your neighbor’s best route selection
For outbound traffic
  Filter inbound routes
  Tweak attributes on inbound routes to influence best route selection
outbound
routes
inbound
routes
inbound
traffic
outbound
traffic
In general, an AS has more
control over outbound traffic

## Slide 31: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 32: Route Selection Summary
Highest Local Preference
Shortest ASPATH
Lowest MED
i-BGP < e-BGP
Lowest IGP cost
to BGP egress
Lowest router ID
traffic engineering
Enforce relationships
Throw up hands and
break ties

## Slide 33: Hot Potato Routing
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS1,AS3,X
OSPF link weights
201
152
112
263

## Slide 34: Back to Frank …
AS 1
AS 2
AS 4
AS 3
13.13.0.0/16
peer
peer
customer
provider
local pref = 80
local pref = 100
local pref = 90
Higher Local
preference values
are more preferred
Local preference only used in iBGP

## Slide 35: Implementing Backup Links with Local Preference (Outbound Traffic)
Forces outbound traffic to take primary link, unless link is down.
AS 1
primary link
backup link
Set Local Pref = 100
for all routes from AS 1
AS 65000
Set Local Pref = 50
for all routes from AS 1

## Slide 36: Multihomed Backups (Outbound Traffic)
Forces outbound traffic to take primary link, unless link is down.
AS 1
primary link
backup link
Set Local Pref = 100
for all routes from AS 1
AS 2
Set Local Pref = 50
for all routes from AS 3
AS 3
provider
provider

## Slide 37: ASPATH Attribute
AS7018
135.207.0.0/16
AS Path = 6341
AS 1239
Sprint
AS 1755
Ebone
AT&T
AS 3549
Global Crossing
135.207.0.0/16
AS Path = 7018 6341
135.207.0.0/16
AS Path = 3549 7018 6341
AS 6341
135.207.0.0/16
AT&T Research
Prefix Originated
AS 12654
RIPE NCC
RIS project
AS 1129
Global Access
135.207.0.0/16
AS Path = 7018 6341
135.207.0.0/16
AS Path = 1239 7018 6341
135.207.0.0/16
AS Path = 1755 1239 7018 6341
135.207.0.0/16
AS Path = 1129 1755 1239 7018 6341

## Slide 38: Interdomain Loop Prevention
BGP at AS YYY will never accept a route with ASPATH containing YYY.
AS 7018
12.22.0.0/16
ASPATH = 1 333 7018 877
Don’t Accept!
AS 1

## Slide 39: Traffic Often Follows ASPATH
AS 4
AS 3
AS 2
AS 1
135.207.0.0/16
135.207.0.0/16
ASPATH = 3 2 1
IP Packet
Dest =
135.207.44.66

## Slide 40: … But It Might Not
AS 4
AS 3
AS 2
AS 1
135.207.0.0/16
135.207.0.0/16
ASPATH = 3 2 1
IP Packet
Dest =
135.207.44.66
AS 5
135.207.44.0/25
ASPATH = 5
135.207.44.0/25
AS 2 filters all
subnets with masks
longer than /24
135.207.0.0/16
ASPATH = 1
From AS 4, it
may look like this
packet will take
path 3 2 1, but it
actually takes
path 3 2 5
Notes: This slide shows that in Border Gateway Protocol, the advertised path (control plane) may differ from the actual packet path (data plane) due to prefix filtering and longest-prefix match. AS2 filters out the more specific /25 route, so AS4 only sees the aggregate /16 and believes traffic will go via AS1. However, since the destination belongs to the more specific /25 owned by AS5, routers that know this route will forward packets using it, causing the actual path to deviate (going via AS5 instead of AS1).

## Slide 41: Shorter Doesn’t Always Mean Shorter
In fairness:
could you do
this “right” and
still scale?
Exporting internal
state would
dramatically
increase global
instability and
amount of routing
state
AS 4
AS 3
AS 2
AS 1
Mr. BGP says that
path 4 1 is better
than path 3 2 1
Duh!

## Slide 42: Shedding Inbound Traffic with ASPATH Padding Hack
Padding will (usually)
force inbound
traffic from AS 1
to take primary link
AS 1
192.0.2.0/24
ASPATH = 2 2 2
customer
AS 2
provider
192.0.2.0/24
backup
primary
192.0.2.0/24
ASPATH = 2

## Slide 43: Padding May Not Shut Off All Traffic
AS 1
192.0.2.0/24
ASPATH = 2 2 2 2 2 2 2 2 2 2 2 2 2 2
customer
AS 2
provider
192.0.2.0/24
192.0.2.0/24
ASPATH = 2
AS 3
provider
AS 3 will send
traffic on “backup”
link because it prefers
customer routes and local
preference is considered
before ASPATH length!
Padding in this way is often
used as a form of load
balancing
backup
primary

## Slide 44: COMMUNITY Attribute to the Rescue!
AS 1
customer
AS 2
provider
192.0.2.0/24
192.0.2.0/24
ASPATH = 2
AS 3
provider
backup
primary
192.0.2.0/24
ASPATH = 2
COMMUNITY = 3:70
Customer import policy at AS 3:
If 3:90 in COMMUNITY then
set local preference to 90
If 3:80 in COMMUNITY then
set local preference to 80
If 3:70 in COMMUNITY then
set local preference to 70
AS 3: normal
customer local
pref is 100,
peer local pref is 90

## Slide 45: Hot Potato Routing: Go for the Closest Egress Point
192.44.78.0/24
15
56
IGP distances
egress 1
egress 2
This Router has two BGP routes to 192.44.78.0/24.
Hot potato: get traffic off of your network as
Soon as possible. Go for egress 1!

## Slide 46: Getting Burned by the Hot Potato
15
56
17
2865
High bandwidth
Provider backbone
Low bandwidth
customer backbone
Heavy
Content
Web Farm
Many customers want
their provider to
carry the bits!
tiny http request
huge http reply
SFO
NYC
San Diego

## Slide 47: Cold Potato Routing with MEDs (Multi-Exit Discriminator Attribute)
15
56
17
2865
Heavy
Content
Web Farm
192.44.78.0/24
192.44.78.0/24
MED = 15
192.44.78.0/24
MED = 56
This means that MEDs must be considered BEFORE
IGP distance!
Prefer lower
MED values
Note1 : some providers will not listen to MEDs
Note2 : MEDs need not be tied to IGP distance

## Slide 48: Route Selection Summary
Highest Local Preference
Shortest ASPATH
Lowest MED
i-BGP < e-BGP
Lowest IGP cost
to BGP egress
Lowest router ID
traffic engineering
Enforce relationships
Throw up hands and
break ties

## Slide 49: BGP Attacks/Misconfiguration

## Slide 50: Prefix Hijacking
1
2
3
4
5
6
7
12.34.0.0/16
12.34.0.0/16
Originating someone else’s prefix
  What fraction of the Internet believes it?

## Slide 51: Prefix highjack
http://queue.acm.org/detail.cfm?id=2668966

## Slide 52: Sub-Prefix Hijacking
Originating a more-specific prefix
  Every AS picks the bogus route for that prefix
  Traffic follows the longest matching prefix
1
2
3
4
5
6
7
12.34.0.0/16
12.34.158.0/24

## Slide 53: Sub-prefix hijack
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
  February 2008 : Pakistan Telecom hijacks YouTube
Notes: -level of autonomous systems
-e.g., YouTube, AT&T, pakistan telecom
-routing is done on IP addresses, so when someone wants to go to YouTube they get YouTube’s IP address and YouTube announces to the world that they have the ip address and traffic is forwarded towards them. So here multinet would route to it’s provider pakistan telecom that then forwards the traffic on to youtube.
-these networks chosen for a specific reason which is that there was an incident in february 2008 pakistan telecom actually high jacked traffic going to youtube (misconfiguration).
-they announced to the world that they’re youtube and traffic destined to youtube was routed to them
-youtube was unavailable for a couple of hours as operators phone each other to figure out what was going on.

## Slide 54: Sub-prefix hijack
  Here’s what should have happened….
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
X
Hijack + drop packets going to YouTube
  Block your own customers.

## Slide 55: Sub-prefix hijack
  But here’s what Pakistan ended up doing…
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
No, I’m YouTube!
IP 208.65.153.0 / 24
Notes: Our works focuses on attacks of this flavor..

## Slide 56: Bogus AS Paths to Hide Hijacking
Adds AS hop(s) at the end of the path
  E.g., turns “701 88” into “701 88 3”
Motivations
  Evade detection for a bogus route
  E.g., by adding the legitimate AS to the end
Hard to tell that the AS path is bogus…
  Even if other ASes filter based on prefix ownership
701
88
3
18.0.0.0/8
18.0.0.0/8

## Slide 57: Path-Shortening Attacks
Remove ASes from the AS path
  E.g., turn “701 3715 88” into “701 88”
Motivations
  Make the AS path look shorter than it is
  Attract sources that normally try to avoid AS 3715
  Help AS 88 look like it is closer to the Internet’s core
Who can tell that this AS path is a lie?
  Maybe AS 88 *does* connect to AS 701 directly
701
88
3715
?

## Slide 58: Attacks that Add a Bogus AS Hop
Add ASes to the path
  E.g., turn “701 88” into “701 3715 88”
Motivations
  Trigger loop detection in AS 3715
    Denial-of-service attack on AS 3715
    Or, blocking unwanted traffic coming from AS 3715!
  Make your AS look like is has richer connectivity
Who can tell the AS path is a lie?
  AS 3715 could, if it could see the route
  AS 88 could, but would it really care as long as it received data traffic meant for it?
701
88

## Slide 59: Violating “Consistent Export” to Peers
Peers require consistent export
  Prefix advertised at all peering points
  Prefix advertised with same AS path length
Reasons for violating the policy
  Trick neighbor into “cold potato”
  Configuration mistake
Main defense
  Analyzing BGP updates
  … or data traffic
  … for signs of inconsistency
src
dest
Bad AS
data
BGP

## Slide 60: Other Attacks
Attacks on BGP sessions
  Confidentiality of BGP messages
  Denial-of-service on BGP session
  Inserting, deleting, modifying, or replaying messages
Resource exhaustion attacks
  Too many IP prefixes (e.g., BGP “512K Day”)
  Too many BGP update messages
Data-plane attacks
  Announce one BGP routes, but use another

## Slide 61: Solution Techniques
Protective filtering
  Know your neighbors
Anomaly detection
  Suspect the unexpected
Checking against registries
  Establish ground truth for prefix origination
Signing and verifying
  Prevent bogus AS PATHs
Data-plane verification
  Ensure the path is actually followed

## Slide 62
Computer Networks
Nirupam Roy
M-W 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2026
Topic: Application Layer Protocols
(Textbook chapter 9)

## Slide 63
Internet as a Platform
Process to process: Transport layer
Network to network: Network layer
Device to device: Link/Physical layer
Applications

## Slide 64
Internet as a Platform
Process to process: Transport layer
Network to network: Network layer
Device to device: Link/Physical layer
Applications
How did we address a host?
How do we address a host?

## Slide 65
Internet as a Platform
Process to process: Transport layer
Network to network: Network layer
Device to device: Link/Physical layer
Applications
How did we address a host?
How do we address a host?
IP addresses
URLs, Email IDs

## Slide 66
Internet as a Platform
Process to process: Transport layer
Network to network: Network layer
Device to device: Link/Physical layer
Applications (World wide web)
How did we address a host?
IP addresses
Webserver
https://www.cs.umd.edu
HTTP protocol responses

## Slide 67
We need a database on the Internet
for
Human readable domain name  IP address mapping
Questions:
(1) Centralized or distributed?
(2) Hierarchical or flat?
(3) At the application layer or at a lower layer?

## Slide 68
PC: https://blog.hubspot.com/marketing/parts-url

## Slide 69
https://www.cs.umd.edu
Anatomy of a domain name
https://www.ece.umd.edu
ftp://ftp.example.com/Batch_File
nirupam@cs.umd.edu

## Slide 70
https://www.cs.umd.edu
Anatomy of a domain name
https://www.ece.umd.edu
[Picture] https://strategylab.ca/parts-of-a-url/
ftp://ftp.example.com/Batch_File
nirupam@cs.umd.edu

## Slide 71: DNS: domain name system
people: many identifiers:
  SSN, name, passport #
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams
  “name”, e.g., www.yahoo.com - used by humans
Q: how to map between IP address and name, and vice versa ?
Domain Name System:
distributed database implemented in hierarchy of many name servers
application-layer protocol: hosts, name servers communicate to resolve names (address/name translation)
  note: core Internet function, implemented as application-layer protocol
  complexity at network’s “edge”

## Slide 72: DNS: a distributed, hierarchical database
client wants IP for www.amazon.com; 1st approximation:
client queries root server to find com DNS server
client queries .com DNS server to get amazon.com DNS server
client queries amazon.com DNS server to get IP address for www.amazon.com
Root DNS Servers
com DNS servers
org DNS servers
edu DNS servers
poly.edu
DNS servers
umass.edu
DNS servers
yahoo.com
DNS servers
amazon.com
DNS servers
pbs.org
DNS servers
…
…

## Slide 73: DNS: Root Name Servers
Contacted by local name server that cannot resolve name
Root name server:
  Contacts authoritative name server if name mapping not known
  Gets mapping
  Returns mapping to local name server
13 logical root name “servers” worldwide
each “server” replicated many times
(BGP Anycast / GSLB)
a. Verisign, Los Angeles CA
(5 other sites)
b. USC-ISI Marina del Rey, CA
l. ICANN Los Angeles, CA
(41 other sites)
e. NASA Mt View, CA
f. Internet Software C.
Palo Alto, CA (and 48 other sites)
i. Netnod, Stockholm (37 other sites)
k. RIPE London (17 other sites)
m. WIDE Tokyo
(5 other sites)
c. Cogent, Herndon, VA (5 other sites)
d. U Maryland College Park, MD
h. ARL Aberdeen, MD
j. Verisign, Dulles VA (69 other sites )
g. US DoD Columbus, OH (5 other sites)

## Slide 74: TLD, Authoritative DNS Servers
Top-level domain (TLD) servers:
  responsible for com, org, net, edu, aero, jobs, museums, and all top-level country domains, e.g.: uk, fr, ca, jp
  Network Solutions maintains servers for .com TLD
  Educause for .edu TLD
Authoritative DNS servers:
Organization’s own DNS server(s), providing authoritative hostname to IP mappings for organization’s named hosts
  can be maintained by organization or service provider

## Slide 75: Local DNS name server
does not strictly belong to hierarchy
each ISP (residential ISP, company, university) has one
  also called “default name server”
when host makes DNS query, query is sent to its local DNS server
  has local cache of recent name-to-address translation pairs (but may be out of date!)
  acts as proxy, forwards query into hierarchy

## Slide 76: DNS name resolution example
host at cs.stanford.edu wants IP address for cs.umd.edu
requesting host
cs.stanford.edu
cs.umd.edu
root DNS server
local DNS server
dns.stanford.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umd.edu
7
8
TLD DNS server
iterated query:
contacted server replies with name of server to contact
“I don’t know this name, but ask this server”

## Slide 77
4
5
6
3
recursive query:
puts burden of name resolution on contacted name server
heavy load at upper levels of hierarchy?
requesting host
cs.stanford.edu
cs.umd.edu
root DNS server
local DNS server
dns.stanford.edu
1
2
7
authoritative DNS server
dns.cs.umd.edu
8
DNS name resolution example
TLD DNS
server

## Slide 78: DNS: caching, updating records
once (any) name server learns mapping, it caches mapping
  cache entries timeout (disappear) after some time (TTL)
  TLD servers typically cached in local name servers
    thus root name servers not often visited
cached entries may be out-of-date (best effort name-to-address translation!)
  if name host changes IP address, may not be known Internet-wide until all TTLs expire
update/notify mechanisms proposed IETF standard
  RFC 2136

## Slide 79: DNS: services, structure
DNS services
hostname to IP address translation
host aliasing
  canonical, alias names
mail server aliasing
load distribution
  replicated Web servers: many IP addresses correspond to one name
why not centralize DNS?
single point of failure
traffic volume
distant centralized database
maintenance
Centralize DNS doesn‘t scale!

## Slide 80: DNS records
DNS: distributed database storing resource records (RR)
type=NS
  name is domain (e.g., foo.com)
  value is hostname of authoritative name server for this domain
RR format: (name, value, type, ttl)
type=A
  name is hostname
  value is IP address
type=CNAME
  name is alias name for some “canonical” (the real) name
  www.ibm.com is really
  servereast.backup2.ibm.com
  value is canonical name
type=MX
  value is name of mail server associated with name

## Slide 81: DNS protocol, messages
query and reply messages, both with same message format
message header
identification: 16 bit # for query, reply to query uses same #
flags:
  query or reply
  recursion desired
  recursion available
  reply is authoritative
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes

## Slide 82
name, type fields
for a query
RRs in response
to query
records for
authoritative servers
additional “helpful”
info that may be used
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
DNS protocol, messages
2 bytes
2 bytes
Notes: Does DNS use TCP or UDP? Why?

## Slide 83: Inserting records into DNS
example: new startup “Network Utopia”
register name networkuptopia.com at DNS registrar (e.g., Network Solutions)
  provide names, IP addresses of authoritative name server (primary and secondary)
  registrar inserts two RRs into .com TLD server: (networkutopia.com, dns1.networkutopia.com, NS)
  (dns1.networkutopia.com, 212.212.212.1, A)
create authoritative server type A record for www.networkuptopia.com; type NS record for networkutopia.com

## Slide 84
HTTP
(Hyper-Text Transfer Protocol)

## Slide 85: Web and HTTP
First, a review…
web page consists of objects
object can be HTML file, JPEG image, Java applet, audio file,…
web page consists of base HTML-file which includes several referenced objects
each object is addressable by a URL, e.g.,
www.someschool.edu/someDept/pic.gif
host name
path name

## Slide 86: HTTP overview
HTTP: hypertext transfer protocol
Web’s application layer protocol
client/server model
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
PC running
Firefox browser
server
running
Apache Web
server
iPhone running
Safari browser
HTTP request
HTTP response
HTTP request
HTTP response

## Slide 87: HTTP overview
Uses TCP:
client initiates TCP connection (creates socket) to server, port 80
server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
HTTP is “stateless”
server maintains no information about past client requests
protocols that maintain “state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 88: HTTP connections
non-persistent HTTP
at most one object sent over TCP connection
  connection then closed
downloading multiple objects required multiple connections
persistent HTTP
multiple objects can be sent over single TCP connection between client, server

## Slide 89: Non-persistent HTTP
suppose user enters URL:
1a. HTTP client initiates TCP connection to HTTP server (process) at www.someSchool.edu on port 80
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket. Message indicates that client wants object someDepartment/home.index
1b. HTTP server at host www.someSchool.edu waiting for TCP connection at port 80. “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object, and sends message into its socket
time
(contains text, references to 10 jpeg images)
www.someSchool.edu/someDepartment/home.index
5. HTTP client receives response message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects
6. Steps 1-5 repeated for each of 10 jpeg objects
4. HTTP server closes TCP connection.

## Slide 90: Non-persistent HTTP: response time
RTT (Round Trip Time): time for a small packet to travel from client to server and back
HTTP response time:
one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return
file transmission time
non-persistent HTTP response time
  = 2RTT+ file transmission time
time to
transmit
file
initiate TCP
connection
RTT
request
file
RTT
file
received
time
time

## Slide 91: Persistent HTTP
Persistent HTTP:
server leaves connection open after sending response
subsequent HTTP messages between same client/server sent over open connection
client sends requests as soon as it encounters a referenced object
as little as one RTT for all the referenced objects
initiate TCP
connection
RTT
RTT
request
new file
request
file
time
time
Notes: Breakdown of layering

## Slide 92: Other optimizations
Pipelining
  Send several requests at once
initiate TCP
connection
RTT
RTT
request
new files
request
file
time
time

## Slide 93: Other optimizations
Pipelining
  Send several requests at once
HTTP/2
  Push resources
initiate TCP
connection
RTT
RTT
request
file
send
file
push
objects
time
time

## Slide 94: Other optimizations
Pipelining
  Send several requests at once
HTTP/2
  Push resources
QUIC
  Eliminate first RTT
initiate QUIC
connection
RTT
time
time
request
file
send
file
push
objects

## Slide 95: HTTP request message
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
request line
(GET, POST,
HEAD commands)
header
lines
carriage return,
line feed at start
of line indicates
end of header lines
GET /index.html HTTP/1.1\r\n
Host: www-net.cs.umass.edu\r\n
User-Agent: Firefox/3.6.10\r\n
Accept: text/html,application/xhtml+xml\r\n
Accept-Language: en-us,en;q=0.5\r\n
Accept-Encoding: gzip,deflate\r\n
Accept-Charset: ISO-8859-1,utf-8;q=0.7\r\n
Keep-Alive: 115\r\n
Connection: keep-alive\r\n
\r\n
carriage return character
line-feed character

## Slide 96: HTTP request message: general format
request
line
header
lines
body
method
sp
sp
cr
lf
version
URL
cr
lf
value
header field name
cr
lf
value
header field name
~
~
~
~
cr
lf
entity body
~
~
~
~
:
:

## Slide 97: Uploading form input
POST method:
web page often includes form input
input is uploaded to server in entity body
URL method:
uses GET method
input is uploaded in URL field of request line:
www.somesite.com/animalsearch?monkeys&banana

## Slide 98: Method types
HTTP/1.0:
GET
POST
HEAD
  asks server to leave requested object out of response
HTTP/1.1:
GET, POST, HEAD
PUT
  uploads file in entity body to path specified in URL field
DELETE
  deletes file specified in the URL field

## Slide 99: HTTP response message
status line
(protocol
status code
status phrase)
header
lines
data, e.g.,
requested
HTML file
HTTP/1.1 200 OK\r\n
Date: Sun, 26 Sep 2010 20:09:20 GMT\r\n
Server: Apache/2.0.52 (CentOS)\r\n
Last-Modified: Tue, 30 Oct 2007 17:00:02 GMT\r\n
ETag: "17dc6-a5c-bf716880"\r\n
Accept-Ranges: bytes\r\n
Content-Length: 2652\r\n
Keep-Alive: timeout=10, max=100\r\n
Connection: Keep-Alive\r\n
Content-Type: text/html; charset=ISO-8859-1\r\n
\r\n
data data data data data ...

## Slide 100: HTTP response status codes
200 OK
  request succeeded, requested object later in this msg
301 Moved Permanently
  requested object moved, new location specified later in this msg (Location:)
400 Bad Request
  request msg not understood by server
404 Not Found
  requested document not found on this server
505 HTTP Version Not Supported
status code appears in 1st line in server-to-client response message.
some sample codes:
Notes: cats

## Slide 101: Trying out HTTP (client side) for yourself
1. Telnet to your favorite Web server:
opens TCP connection to port 80
(default HTTP server port)
at gaia.cs.umass. edu.
anything typed in will be sent
to port 80 at gaia.cs.umass.edu
telnet gaia.cs.umass.edu 80
2. type in a GET HTTP request:
GET /kurose_ross/interactive/index.php HTTP/1.1
Host: gaia.cs.umass.edu
by typing this in (hit carriage
return twice), you send
this minimal (but complete)
GET request to HTTP server
3. look at response message sent by HTTP server!
(or use Wireshark to look at captured HTTP request/response)

## Slide 102: Trying out HTTP (client side) for yourself
1. Telnet to your favorite Web server:
opens TCP connection to port 80
(default HTTP server port)
at gaia.cs.umass. edu.
anything typed in will be sent
to port 80 at gaia.cs.umass.edu
telnet gaia.cs.umass.edu 80
2. type in a GET HTTP request:
GET /kurose_ross/interactive/index.php HTTP/1.1
Host: gaia.cs.umass.edu
by typing this in (hit carriage
return twice), you send
this minimal (but complete)
GET request to HTTP server
3. look at response message sent by HTTP server!
(or use Wireshark to look at captured HTTP request/response)

## Slide 103: User-server state: cookies
Many Web sites use cookies
four components:
  1) Cookie header line of HTTP response message
  2) Cookie header line in next HTTP request message
  3) Cookie file kept on user’s host, managed by user’s browser
  4) Back-end database at Website
example:
Susan always access Internet from PC
visits specific e-commerce site for first time
when initial HTTP requests arrives at site, site creates:
  unique ID
  entry in backend database for ID

## Slide 104: Cookies: keeping “state” (cont.)
client
server
usual http response msg
usual http response msg
cookie file
one week later:
usual http request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
usual http request msg
Amazon server
creates ID
1678 for user
create
entry
usual http response
set-cookie: 1678
ebay 8734
amazon 1678
usual http request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
amazon 1678
backend
database

## Slide 105: Cookies (continued)
what cookies can be used for:
authorization
shopping carts
recommendations
user session state (Web e-mail)
cookies and privacy:
cookies permit sites to learn a lot about you
you may supply name and e-mail to sites
aside
how to keep “state”:
protocol endpoints: maintain state at sender/receiver over multiple transactions
cookies: http messages carry state
Notes: tracking

## Slide 106
HTTPS: TLS handshake
Notes: Image refs:
https://www.cloudflare.com/learning/ssl/what-happens-in-a-tls-handshake/
https://www.researchgate.net/figure/TLS-handshake-protocol_fig1_298065605

## Slide 107
QUIC: Quick UDP Internet Connections A new transport layer protocol for web

## Slide 108
HTTP/0.9
The one-line protocol
Initial version. Simple.
One-line request
Only the GET method works
Server sends HTML files
Status code included, helped
application caching and failure
management.
Metadata sent over HTTP header,
Helped extensibility.
Documents other than HTML files
can be sent.
Connection reuse.
Pipeline
Content negotiation—Language,
encoding etc.
HTTP/1.0
Added extensibility
HTTP/1.1
Standardization
HTTP/2.0
Performance
Binary protocol, not text
Multiplexed: Multiple requests
(streams) over the same
connection.
Header compression
Notes: [Ref] https://developer.mozilla.org/en-US/docs/Web/HTTP/Guides/Evolution_of_HTTP

## Slide 109
Binary protocol, not text
HTTP/2.0
Performance
Multiplexed: Multiple requests
(streams) over the same
connection.
Header compression
Transport layer (TCP) limitation for HTTP/2.0 streaming
Head-of-Line Blocking (HOLB): HTTP/2.0 resolves application layer
HOLB through multiplexing, but transport layer HOLB persists.
If a packet for a particular stream is lost or delayed (head-of-line), it can
block all other streams using that same TCP connection
TCP resolves order before sending to application layer.
Notes: [Ref] https://developer.mozilla.org/en-US/docs/Web/HTTP/Guides/Evolution_of_HTTP

## Slide 110
QUIC: A cross-layer approach
(+TLS 1.3)
QUIC can exist by itself, HTTP/3 can’t exist without QUIC.
Notes: Image ref: https://medium.com/codavel-blog/quic-vs-tcp-tls-and-why-quic-is-not-the-next-big-thing-d4ef59143efd
[Ref] https://javascript-conference.com/blog/quic-and-http-3-the-next-step-in-web-performance/
QUIC is a general-purpose transport layer network protocol initially designed by Jim Roskind at Google. It was first implemented and deployed in 2012 and was publicly announced in 2013 as experimentation broadened.
[Ref] https://blog.apnic.net/2022/11/03/comparing-tcp-and-quic/
It is a grossly inaccurate simplification, but at its simplest level, QUIC is simply TCP encapsulated and encrypted in a User Datagram Protocol (UDP) payload. To the external network, QUIC has the appearance of a bidirectional UDP packet sequence where the UDP payload is concealed. To the endpoints, QUIC can be used as a reliable full duplex data flow protocol. Even at this level, QUIC has a number of advantages over TCP.

## Slide 111
QUIC: A cross-layer approach
Notes: Image ref: https://blog.apnic.net/2022/11/03/comparing-tcp-and-quic/

## Slide 112
QUIC: Expedited secure handshake

## Slide 113
QUIC: Stream multiplexing
Notes: [Ref] https://www.catchpoint.com/http3-vs-http2

## Slide 114
QUIC: A cross-layer approach
Seamless migration between multiple <IP, port>
Notes: Image ref:
https://pulse.internetsociety.org/blog/how-quic-helps-you-seamlessly-connect-to-different-networks

## Slide 115: Web caches (proxy server)
user sets browser: Web accesses via cache
browser sends all HTTP requests to cache
  object in cache: cache returns object
  else cache requests object from origin server, then returns object to client
goal: satisfy client request without involving origin server
client
proxy
server
client
HTTP request
HTTP response
HTTP request
HTTP request
origin
server
origin
server
HTTP response
HTTP response

## Slide 116: More about Web caching
cache acts as both client and server
  server for original requesting client
  client to origin server
typically cache is installed by ISP (university, company, residential ISP)
why Web caching?
reduce response time for client request
reduce traffic on an institution’s access link
Internet dense with caches: enables “poor” content providers to effectively deliver content
Notes: proxy