## Slide 1
Computer Networks
Nirupam Roy
M-W 2:00-3:15pm
CSI 2117
CMSC 417 : Spring 2026
Topic: Application Layer Protocols
(Textbook chapter 9)
May 6th, 2026

## Slide 2
Internet as a Platform
Process to process: Transport layer
Network to network: Network layer
Device to device: Link/Physical layer
Applications

## Slide 3
Internet as a Platform
Process to process: Transport layer
Network to network: Network layer
Device to device: Link/Physical layer
Applications
How did we address a host?
How do we address a host?

## Slide 4
Internet as a Platform
Process to process: Transport layer
Network to network: Network layer
Device to device: Link/Physical layer
Applications
How did we address a host?
How do we address a host?
IP addresses
URLs, Email IDs

## Slide 5
Internet as a Platform
Process to process: Transport layer
Network to network: Network layer
Device to device: Link/Physical layer
Applications (World wide web)
How did we address a host?
IP addresses
Webserver
https://www.cs.umd.edu
HTTP protocol responses

## Slide 6
We need a database on the Internet
for
Human readable domain name  IP address mapping
Questions:
(1) Centralized or distributed?
(2) Hierarchical or flat?
(3) At the application layer or at a lower layer?

## Slide 7
PC: https://blog.hubspot.com/marketing/parts-url

## Slide 8
https://www.cs.umd.edu
Anatomy of a domain name
https://www.ece.umd.edu
ftp://ftp.example.com/Batch_File
nirupam@cs.umd.edu

## Slide 9
https://www.cs.umd.edu
Anatomy of a domain name
https://www.ece.umd.edu
[Picture] https://strategylab.ca/parts-of-a-url/
ftp://ftp.example.com/Batch_File
nirupam@cs.umd.edu

## Slide 10: DNS: domain name system
people: many identifiers:
  SSN, name, passport #
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams
  “name”, e.g., www.yahoo.com - used by humans
Q: how to map between IP address and name, and vice versa ?
Domain Name System:
distributed database implemented in hierarchy of many name servers
application-layer protocol: hosts, name servers communicate to resolve names (address/name translation)
  note: core Internet function, implemented as application-layer protocol
  complexity at network’s “edge”

## Slide 11: DNS: a distributed, hierarchical database
client wants IP for www.amazon.com; 1st approximation:
client queries root server to find com DNS server
client queries .com DNS server to get amazon.com DNS server
client queries amazon.com DNS server to get IP address for www.amazon.com
Root DNS Servers
com DNS servers
org DNS servers
edu DNS servers
poly.edu
DNS servers
umass.edu
DNS servers
yahoo.com
DNS servers
amazon.com
DNS servers
pbs.org
DNS servers
…
…

## Slide 12: DNS: Root Name Servers
Contacted by local name server that cannot resolve name
Root name server:
  Contacts authoritative name server if name mapping not known
  Gets mapping
  Returns mapping to local name server
13 logical root name “servers” worldwide
each “server” replicated many times
(BGP Anycast / GSLB)
a. Verisign, Los Angeles CA
(5 other sites)
b. USC-ISI Marina del Rey, CA
l. ICANN Los Angeles, CA
(41 other sites)
e. NASA Mt View, CA
f. Internet Software C.
Palo Alto, CA (and 48 other sites)
i. Netnod, Stockholm (37 other sites)
k. RIPE London (17 other sites)
m. WIDE Tokyo
(5 other sites)
c. Cogent, Herndon, VA (5 other sites)
d. U Maryland College Park, MD
h. ARL Aberdeen, MD
j. Verisign, Dulles VA (69 other sites )
g. US DoD Columbus, OH (5 other sites)

## Slide 13: TLD, Authoritative DNS Servers
Top-level domain (TLD) servers:
  responsible for com, org, net, edu, aero, jobs, museums, and all top-level country domains, e.g.: uk, fr, ca, jp
  Network Solutions maintains servers for .com TLD
  Educause for .edu TLD
Authoritative DNS servers:
Organization’s own DNS server(s), providing authoritative hostname to IP mappings for organization’s named hosts
  can be maintained by organization or service provider

## Slide 14: Local DNS name server
does not strictly belong to hierarchy
each ISP (residential ISP, company, university) has one
  also called “default name server”
when host makes DNS query, query is sent to its local DNS server
  has local cache of recent name-to-address translation pairs (but may be out of date!)
  acts as proxy, forwards query into hierarchy

## Slide 15: DNS name resolution example
host at cs.stanford.edu wants IP address for cs.umd.edu
requesting host
cs.stanford.edu
cs.umd.edu
root DNS server
local DNS server
dns.stanford.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umd.edu
7
8
TLD DNS server
iterated query:
contacted server replies with name of server to contact
“I don’t know this name, but ask this server”

## Slide 16
4
5
6
3
recursive query:
puts burden of name resolution on contacted name server
heavy load at upper levels of hierarchy?
requesting host
cs.stanford.edu
cs.umd.edu
root DNS server
local DNS server
dns.stanford.edu
1
2
7
authoritative DNS server
dns.cs.umd.edu
8
DNS name resolution example
TLD DNS
server

## Slide 17: DNS: caching, updating records
once (any) name server learns mapping, it caches mapping
  cache entries timeout (disappear) after some time (TTL)
  TLD servers typically cached in local name servers
    thus root name servers not often visited
cached entries may be out-of-date (best effort name-to-address translation!)
  if name host changes IP address, may not be known Internet-wide until all TTLs expire
update/notify mechanisms proposed IETF standard
  RFC 2136

## Slide 18: DNS: services, structure
DNS services
hostname to IP address translation
host aliasing
  canonical, alias names
mail server aliasing
load distribution
  replicated Web servers: many IP addresses correspond to one name
why not centralize DNS?
single point of failure
traffic volume
distant centralized database
maintenance
Centralize DNS doesn‘t scale!

## Slide 19: DNS records
DNS: distributed database storing resource records (RR)
type=NS
  name is domain (e.g., foo.com)
  value is hostname of authoritative name server for this domain
RR format: (name, value, type, ttl)
type=A
  name is hostname
  value is IP address
type=CNAME
  name is alias name for some “canonical” (the real) name
  www.ibm.com is really
  servereast.backup2.ibm.com
  value is canonical name
type=MX
  value is name of mail server associated with name

## Slide 20: DNS protocol, messages
query and reply messages, both with same message format
message header
identification: 16 bit # for query, reply to query uses same #
flags:
  query or reply
  recursion desired
  recursion available
  reply is authoritative
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes

## Slide 21
name, type fields
for a query
RRs in response
to query
records for
authoritative servers
additional “helpful”
info that may be used
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
DNS protocol, messages
2 bytes
2 bytes
Notes: Does DNS use TCP or UDP? Why?

## Slide 22: Inserting records into DNS
example: new startup “Network Utopia”
register name networkuptopia.com at DNS registrar (e.g., Network Solutions)
  provide names, IP addresses of authoritative name server (primary and secondary)
  registrar inserts two RRs into .com TLD server: (networkutopia.com, dns1.networkutopia.com, NS)
  (dns1.networkutopia.com, 212.212.212.1, A)
create authoritative server type A record for www.networkuptopia.com; type NS record for networkutopia.com

## Slide 23
HTTP
(Hyper-Text Transfer Protocol)

## Slide 24: Web and HTTP
First, a review…
web page consists of objects
object can be HTML file, JPEG image, Java applet, audio file,…
web page consists of base HTML-file which includes several referenced objects
each object is addressable by a URL, e.g.,
www.someschool.edu/someDept/pic.gif
host name
path name

## Slide 25: HTTP overview
HTTP: hypertext transfer protocol
Web’s application layer protocol
client/server model
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
PC running
Firefox browser
server
running
Apache Web
server
iPhone running
Safari browser
HTTP request
HTTP response
HTTP request
HTTP response

## Slide 26: HTTP overview
Uses TCP:
client initiates TCP connection (creates socket) to server, port 80
server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
HTTP is “stateless”
server maintains no information about past client requests
protocols that maintain “state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 27: HTTP connections
non-persistent HTTP
at most one object sent over TCP connection
  connection then closed
downloading multiple objects required multiple connections
persistent HTTP
multiple objects can be sent over single TCP connection between client, server

## Slide 28: Non-persistent HTTP
suppose user enters URL:
1a. HTTP client initiates TCP connection to HTTP server (process) at www.someSchool.edu on port 80
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket. Message indicates that client wants object someDepartment/home.index
1b. HTTP server at host www.someSchool.edu waiting for TCP connection at port 80. “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object, and sends message into its socket
time
(contains text, references to 10 jpeg images)
www.someSchool.edu/someDepartment/home.index
5. HTTP client receives response message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects
6. Steps 1-5 repeated for each of 10 jpeg objects
4. HTTP server closes TCP connection.

## Slide 29: Non-persistent HTTP: response time
RTT (Round Trip Time): time for a small packet to travel from client to server and back
HTTP response time:
one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return
file transmission time
non-persistent HTTP response time
  = 2RTT+ file transmission time
time to
transmit
file
initiate TCP
connection
RTT
request
file
RTT
file
received
time
time

## Slide 30: Persistent HTTP
Persistent HTTP:
server leaves connection open after sending response
subsequent HTTP messages between same client/server sent over open connection
client sends requests as soon as it encounters a referenced object
as little as one RTT for all the referenced objects
initiate TCP
connection
RTT
RTT
request
new file
request
file
time
time
Notes: Breakdown of layering

## Slide 31: Other optimizations
Pipelining
  Send several requests at once
initiate TCP
connection
RTT
RTT
request
new files
request
file
time
time

## Slide 32: Other optimizations
Pipelining
  Send several requests at once
HTTP/2
  Push resources
initiate TCP
connection
RTT
RTT
request
file
send
file
push
objects
time
time

## Slide 33: Other optimizations
Pipelining
  Send several requests at once
HTTP/2
  Push resources
QUIC
  Eliminate first RTT
initiate QUIC
connection
RTT
time
time
request
file
send
file
push
objects

## Slide 34: HTTP request message
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
request line
(GET, POST,
HEAD commands)
header
lines
carriage return,
line feed at start
of line indicates
end of header lines
GET /index.html HTTP/1.1\r\n
Host: www-net.cs.umass.edu\r\n
User-Agent: Firefox/3.6.10\r\n
Accept: text/html,application/xhtml+xml\r\n
Accept-Language: en-us,en;q=0.5\r\n
Accept-Encoding: gzip,deflate\r\n
Accept-Charset: ISO-8859-1,utf-8;q=0.7\r\n
Keep-Alive: 115\r\n
Connection: keep-alive\r\n
\r\n
carriage return character
line-feed character

## Slide 35: HTTP request message: general format
request
line
header
lines
body
method
sp
sp
cr
lf
version
URL
cr
lf
value
header field name
cr
lf
value
header field name
~
~
~
~
cr
lf
entity body
~
~
~
~
:
:

## Slide 36: Uploading form input
POST method:
web page often includes form input
input is uploaded to server in entity body
URL method:
uses GET method
input is uploaded in URL field of request line:
www.somesite.com/animalsearch?monkeys&banana

## Slide 37: Method types
HTTP/1.0:
GET
POST
HEAD
  asks server to leave requested object out of response
HTTP/1.1:
GET, POST, HEAD
PUT
  uploads file in entity body to path specified in URL field
DELETE
  deletes file specified in the URL field

## Slide 38: HTTP response message
status line
(protocol
status code
status phrase)
header
lines
data, e.g.,
requested
HTML file
HTTP/1.1 200 OK\r\n
Date: Sun, 26 Sep 2010 20:09:20 GMT\r\n
Server: Apache/2.0.52 (CentOS)\r\n
Last-Modified: Tue, 30 Oct 2007 17:00:02 GMT\r\n
ETag: "17dc6-a5c-bf716880"\r\n
Accept-Ranges: bytes\r\n
Content-Length: 2652\r\n
Keep-Alive: timeout=10, max=100\r\n
Connection: Keep-Alive\r\n
Content-Type: text/html; charset=ISO-8859-1\r\n
\r\n
data data data data data ...

## Slide 39: HTTP response status codes
200 OK
  request succeeded, requested object later in this msg
301 Moved Permanently
  requested object moved, new location specified later in this msg (Location:)
400 Bad Request
  request msg not understood by server
404 Not Found
  requested document not found on this server
505 HTTP Version Not Supported
status code appears in 1st line in server-to-client response message.
some sample codes:
Notes: cats

## Slide 40: Trying out HTTP (client side) for yourself
1. Telnet to your favorite Web server:
opens TCP connection to port 80
(default HTTP server port)
at gaia.cs.umass. edu.
anything typed in will be sent
to port 80 at gaia.cs.umass.edu
telnet gaia.cs.umass.edu 80
2. type in a GET HTTP request:
GET /kurose_ross/interactive/index.php HTTP/1.1
Host: gaia.cs.umass.edu
by typing this in (hit carriage
return twice), you send
this minimal (but complete)
GET request to HTTP server
3. look at response message sent by HTTP server!
(or use Wireshark to look at captured HTTP request/response)

## Slide 41: Trying out HTTP (client side) for yourself
1. Telnet to your favorite Web server:
opens TCP connection to port 80
(default HTTP server port)
at gaia.cs.umass. edu.
anything typed in will be sent
to port 80 at gaia.cs.umass.edu
telnet gaia.cs.umass.edu 80
2. type in a GET HTTP request:
GET /kurose_ross/interactive/index.php HTTP/1.1
Host: gaia.cs.umass.edu
by typing this in (hit carriage
return twice), you send
this minimal (but complete)
GET request to HTTP server
3. look at response message sent by HTTP server!
(or use Wireshark to look at captured HTTP request/response)

## Slide 42: User-server state: cookies
Many Web sites use cookies
four components:
  1) Cookie header line of HTTP response message
  2) Cookie header line in next HTTP request message
  3) Cookie file kept on user’s host, managed by user’s browser
  4) Back-end database at Website
example:
Susan always access Internet from PC
visits specific e-commerce site for first time
when initial HTTP requests arrives at site, site creates:
  unique ID
  entry in backend database for ID

## Slide 43: Cookies: keeping “state” (cont.)
client
server
usual http response msg
usual http response msg
cookie file
one week later:
usual http request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
usual http request msg
Amazon server
creates ID
1678 for user
create
entry
usual http response
set-cookie: 1678
ebay 8734
amazon 1678
usual http request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
amazon 1678
backend
database

## Slide 44: Cookies (continued)
what cookies can be used for:
authorization
shopping carts
recommendations
user session state (Web e-mail)
cookies and privacy:
cookies permit sites to learn a lot about you
you may supply name and e-mail to sites
aside
how to keep “state”:
protocol endpoints: maintain state at sender/receiver over multiple transactions
cookies: http messages carry state
Notes: tracking

## Slide 45
HTTPS: TLS handshake
Notes: Image refs:
https://www.cloudflare.com/learning/ssl/what-happens-in-a-tls-handshake/
https://www.researchgate.net/figure/TLS-handshake-protocol_fig1_298065605

## Slide 46
QUIC: Quick UDP Internet Connections A new transport layer protocol for web

## Slide 47
HTTP/0.9
The one-line protocol
Initial version. Simple.
One-line request
Only the GET method works
Server sends HTML files
Status code included, helped
application caching and failure
management.
Metadata sent over HTTP header,
Helped extensibility.
Documents other than HTML files
can be sent.
Connection reuse.
Pipeline
Content negotiation—Language,
encoding etc.
HTTP/1.0
Added extensibility
HTTP/1.1
Standardization
HTTP/2.0
Performance
Binary protocol, not text
Multiplexed: Multiple requests
(streams) over the same
connection.
Header compression
Notes: [Ref] https://developer.mozilla.org/en-US/docs/Web/HTTP/Guides/Evolution_of_HTTP

## Slide 48
Binary protocol, not text
HTTP/2.0
Performance
Multiplexed: Multiple requests
(streams) over the same
connection.
Header compression
Transport layer (TCP) limitation for HTTP/2.0 streaming
Head-of-Line Blocking (HOLB): HTTP/2.0 resolves application layer
HOLB through multiplexing, but transport layer HOLB persists.
If a packet for a particular stream is lost or delayed (head-of-line), it can
block all other streams using that same TCP connection
TCP resolves order before sending to application layer.
Notes: [Ref] https://developer.mozilla.org/en-US/docs/Web/HTTP/Guides/Evolution_of_HTTP

## Slide 49
QUIC: A cross-layer approach
(+TLS 1.3)
QUIC can exist by itself, HTTP/3 can’t exist without QUIC.
Notes: Image ref: https://medium.com/codavel-blog/quic-vs-tcp-tls-and-why-quic-is-not-the-next-big-thing-d4ef59143efd
[Ref] https://javascript-conference.com/blog/quic-and-http-3-the-next-step-in-web-performance/
QUIC is a general-purpose transport layer network protocol initially designed by Jim Roskind at Google. It was first implemented and deployed in 2012 and was publicly announced in 2013 as experimentation broadened.
[Ref] https://blog.apnic.net/2022/11/03/comparing-tcp-and-quic/
It is a grossly inaccurate simplification, but at its simplest level, QUIC is simply TCP encapsulated and encrypted in a User Datagram Protocol (UDP) payload. To the external network, QUIC has the appearance of a bidirectional UDP packet sequence where the UDP payload is concealed. To the endpoints, QUIC can be used as a reliable full duplex data flow protocol. Even at this level, QUIC has a number of advantages over TCP.

## Slide 50
QUIC: A cross-layer approach
Notes: Image ref: https://blog.apnic.net/2022/11/03/comparing-tcp-and-quic/

## Slide 51
QUIC: Expedited secure handshake

## Slide 52
QUIC: Stream multiplexing
Notes: [Ref] https://www.catchpoint.com/http3-vs-http2

## Slide 53
QUIC: A cross-layer approach
Seamless migration between multiple <IP, port>
Notes: Image ref:
https://pulse.internetsociety.org/blog/how-quic-helps-you-seamlessly-connect-to-different-networks

## Slide 54: Web caches (proxy server)
user sets browser: Web accesses via cache
browser sends all HTTP requests to cache
  object in cache: cache returns object
  else cache requests object from origin server, then returns object to client
goal: satisfy client request without involving origin server
client
proxy
server
client
HTTP request
HTTP response
HTTP request
HTTP request
origin
server
origin
server
HTTP response
HTTP response

## Slide 55: More about Web caching
cache acts as both client and server
  server for original requesting client
  client to origin server
typically cache is installed by ISP (university, company, residential ISP)
why Web caching?
reduce response time for client request
reduce traffic on an institution’s access link
Internet dense with caches: enables “poor” content providers to effectively deliver content
Notes: proxy