## Slide 1
CMSC 417: Computer Networks
Nirupam Roy
M-W 2:00-3:15pm
CSI 2117
Spring 2026
Topic: Internetworking – Routing protocols
(Textbook chapter 3)
Feb 16th, 2026

## Slide 2
Distance Vector Routing (cont…)

## Slide 3
A says <B, 19>
A’s DVs
A says <C, 2>
A says <P, 6>
Neighbor A’s--
Identity (IP/interface)
Timestamp of last update
+
DV database
DV algorithm
Database maintenance
Add new database entry
Update timestamp
Update a DV
Purge old information
Bellman-Ford algo.
dx(y) = min {c(x,v) + dv(y) }
Dest | Cost | N. Hop
B | 7 | A
C | 11 | B
P | 0 | C
Routing table
Implementation perspective
B says <A, 5>
B’s DVs
B says <C, 12>
B says <Q, 9>
Neighbor B’s--
Identity (IP/interface)
Timestamp of last update
+
X
Notes: How are old vectors purged?
There are two levels of aging in RIP.
A. Neighbor-Level Aging
If a neighbor stops sending updates:
RIP expects updates every 30 seconds
If no update is heard within the invalid timer (~180 seconds):
  All routes learned via that neighbor are marked invalid (metric = 16)
  Triggered update may be sent
Eventually (after flush timer ~240 seconds):
Routes are removed from the table
The neighbor entry itself is also removed.
B. Route-Level Aging (More Important)
Each route has its own timers:
Update timer (~30 sec) — periodic advertisement
Invalid timer (~180 sec) — route considered dead
Flush timer (~240 sec) — route deleted
So routes are not stored indefinitely. They age out automatically.

## Slide 4
1
1
1
1
A
B
C
D
X
X
X
C updates the route from its old database (which contains an old advertisement from D) to <A,3,D>.
C advertises the poisoned route <A, inf.> to D due to Poisoned-reverse rule.
This advertisement from C changes D’s database indicating “cost to reach A via C is inf.”
D finds no path to A. D considers A unreachable (correct behavior). D may send this <A,inf> to C.
This prevents count to infinity, as well as prevents the routing loop.
An example where split-horizon is not enough
<A, 2, B>
<A, 2, B>
Case C:
With poison reverse.
(this means Split-horizon
with poisoned reverse)
B says <A, 1>
DV Database @ C
D says <A, Infinity>
B says <A, 1>
DV Database @ D
C says <A, Infinity>
<No route to A>
<No route to A>

## Slide 5
Distance vector: Poisoned reverse
Does poison reverse solve the general count-to-infinity problem?
It does not. It may be possible that loops involving three or more nodes (rather than simply two immediately neighboring nodes, as we shown in last example) will not be detected by the poison reverse technique.

## Slide 6: DV Implementation: Routing Information Protocol (RIP)
  Example Network
  running RIP RIPv2 Packet Format
RFC 1058 formally specifies the original Routing Information Protocol (RIP), which is a classic distance vector routing algorithm.

## Slide 7
What is RFC?
Request for Comments (RFC):
A peer reviewed publication in a series from the
principal technical development and standards-setting
bodies for the Internet, most prominently
the Internet Engineering Task Force (IETF).
How to Read an RFC: https://www.ietf.org/blog/how-read-rfc/
[ref] https://www.ietf.org/standards/rfcs/

## Slide 8
Limitations of DV routing
Small network assumption
Possibility of
routing loops
Static and
pre-determined
link costs
Notes: What is RFC: https://www.techtarget.com/whatis/definition/Request-for-Comments-RFC

## Slide 9
Link State Routing
Routing by rumor
Consistent
view of topology

## Slide 10: Link State Routing
Strategy:
Send to all nodes (not just neighbors) information about neighbors (not connection to all nodes).
All nodes will know the link-state information of all other nodes

## Slide 11: Link State Routing
Link State Packet (LSP):
  The ID of the node that created the LSP
  (2) Costs of links to each directly connected neighbor
  (3) A sequence number (SEQNO)
  [To distinguish a newer LSP from the old ones]
  [Smaller number == older LSP]
  (4) A Time-To-Live (TTL) for this packet
  [To make sure old information is eventually removed
  from the network]
Strategy:
Send to all nodes (not just neighbors) information about neighbors (not connection to all nodes).
What is the unit of the “Time-to-Live”?

## Slide 12: Link State Routing
“Aging” and removing a Link State Packet (LSP):
Strategy:
Send to all nodes (not just neighbors) information about neighbors (not connection to all nodes).
1. During control packet forwarding: “Time-to-Live” field (# of hops)
2. In the host’s database: Timer (seconds)

## Slide 13
Link State Routing
(1) Reliable flooding
[Makes sure all nodes in the network get a copy of LSP from all other nodes]
(2) Route calculation
(Dijkstra’s shortest path algorithm)
[Calculates the shortest path from each node to all other nodes and the corresponding next-hop]

## Slide 14
Link State Routing: Reliable flooding
Goals:
0) Ensure all nodes get LSPs from all other
Flood in minimum time
Minimize total routing traffic

## Slide 15
Link State Routing: Reliable flooding
  Store most recent LSP from each node
  Forward LSP to all nodes but one that sent it
  Generate new LSP periodically; increment SEQNO
  Start SEQNO at 0 when reboot
  Decrement TTL before flooding it to neighbors.
  Discard when TTL=0.
  (Also age the stored LSP and discard when ‘expired’)
Goals:
0) Ensure all nodes get LSPs from all other
Flood in minimum time
Minimize total routing traffic
Basic rules:

## Slide 16: Link State
Reliable Flooding
Flooding of link-state packets. (a) LSP arrives at node X; (b) X floods LSP to A and C; (c) A and C flood LSP to B (but not X); (d) flooding is complete
Gets two identical copies of LSP.
Accepts the one arrived first

## Slide 17: Link State
Reliable Flooding
Flooding of link-state packets. (a) LSP arrives at node X; (b) X floods LSP to A and C; (c) A and C flood LSP to B (but not X); (d) flooding is complete
If B receives this LSP from A first, will B send the second copy received from C to A?
This copy is not added to database.
But will ‘B’ flood it?

## Slide 18
LSP processing

## Slide 19
LSP processing flow
LSP available
Exists in
Database?
Flood LSP
Add to database
Run shortest path
algorithm
End
Ignore
Is it
a newer LSP?
(seq. #)
Yes
No
No
Yes

## Slide 20
A
B
D
C
E
7
11
4
15
5
13
19
C
11
15
5
A
7
19
B
4
19
D
4
13
E
5
13
After flooding every node will have the following information:
B
C
A
D
B
D
E
B
E
D
C
Consider this network:
Each node has complete knowledge of the network topology
Apply shortest path algorithm to find routes

## Slide 21
A
B
D
C
E
7
11
4
15
5
13
19
Consider this network:

## Slide 22
A
B
D
C
E
7
11
4
15
5
13
19
C
11
15
5
A
7
19
B
4
19
D
4
13
E
5
13
After flooding every node will have the following information:
B
C
A
D
B
D
E
B
E
D
C
Consider this network:
C
15
A
7
C
11

## Slide 23
A
B
D
C
E
7
11
4
15
5
13
19
C
11
15
5
A
7
19
B
4
19
D
4
13
E
5
13
After flooding every node will have the following information:
B
C
A
D
B
D
E
B
E
D
C
Consider this network:
C
15
A
7
C
11
Each node has complete knowledge of the network topology
Apply shortest path algorithm to find routes

## Slide 24: Shortest Path Routing
Dijkstra’s Algorithm - Assume non-negative link weights
  N: set of nodes in the graph
  l((i, j): the non-negative cost associated with the edge between nodes i, j N and l(i, j) =  if no edge connects i and j
  Let s N be the starting node which executes the algorithm to find shortest paths to all other nodes in N
  Two variables used by the algorithm
    M: set of nodes incorporated so far by the algorithm
    C(n) : the cost of the path from s to each node n
    The algorithm
      M = {s}
      For each n in N – {s}
        C(n) = l(s, n)
      while ( N  M)
        M = M  {w} such that C(w) is the minimum
        for all w in (N-M)
        For each n in (N-M)
        C(n) = MIN (C(n), C(w) + l(w, n))

## Slide 25: Shortest Path Routing
In practice, each switch computes its routing table directly from the LSP’s it has collected using a realization of Dijkstra’s algorithm called the forward search algorithm.
Specifically, each switch maintains two lists, known as Tentative and Confirmed
Each of these lists contains a set of entries of the form (Destination, Cost, NextHop)

## Slide 26
A
B
D
C
E
7
11
4
15
5
13
19
C
11
15
5
A
7
19
B
4
19
D
4
13
E
5
13
After flooding every node will have the following information:
B
C
A
D
B
D
E
B
E
D
C
Consider this network:
C
15
A
7
C
11

## Slide 27
>

## Slide 28
A
7
19
B
C
>

## Slide 29
A
7
19
B
C
>

## Slide 30
A
7
19
B
C
>
Unvisited nodes
Confirmed nodes
Tentative nodes

## Slide 31
A
7
19
B
C
>
Unvisited nodes
Confirmed nodes
Tentative nodes

## Slide 32
A
7
19
B
C
>
‘Confirm’ the lowest cost nodes
from the list of ‘tentative’ nodes.

## Slide 33
A
7
19
B
C
>
C
11
15
5
B
D
E
7
A
X
X
= Ignore the confirmed nodes
‘Confirm’ the lowest cost nodes
from the list of ‘tentative’ nodes.
… and find out this newly ‘confirmed’
node’s LSP (i.e., C’s LSP).

## Slide 34
A
7
19
B
C
>
C
11
15
5
B
D
E
Update costs
7
A
X
By adding the cost
to reach ‘C’.

## Slide 35
A
7
19
B
C
>
C
18
22
12
B
D
E
Costs updated
7
A
X

## Slide 36
22
12
D
E
A
7
18
B
C
C
18
22
12
B
D
E
>
7
A
X
Join with minimum link costs
Costs updated
Note that B’s link is updated.

## Slide 37
22
12
D
E
A
7
18
B
C
>

## Slide 38
22
12
D
E
A
7
C
18
B
>
E
5
13
D
C
‘Confirm’ the lowest cost nodes
from the list of ‘tentative’ nodes.
… and find out this newly ‘confirmed’
node’s LSP.

## Slide 39
E
5
13
25
D
C
No addition to the topology as the links are already at minimum costs.
X
22
12
D
E
A
7
C
18
B
>

## Slide 40
22
12
D
E
A
7
C
18
B
>
B
4
19
A
D
X
18
C
11
X
‘Confirm’ the lowest cost nodes
from the list of ‘tentative’ nodes.
… and find out this newly ‘confirmed’
node’s LSP (this time B’s LSP).

## Slide 41
B
4
19
A
D
22
12
D
E
A
7
C
18
X
18
22
>
B
C
11
X
No addition to the topology as the links are already at minimum costs.

## Slide 42
22
12
D
E
A
7
C
18
B
>
D
4
13
B
E
X
X
C
15
X
No addition to the topology as the links are already at minimum costs.
‘Confirm’ the lowest cost nodes
from the list of ‘tentative’ nodes.
… and find out this newly ‘confirmed’
node’s LSP (this time D’s LSP).

## Slide 43
A
B
D
C
E
7
11
4
15
5
13
19
22
12
D
E
A
7
C
18
B
Notes: Is this a minimum spanning tree?
No, it is a Shortest path tree.

## Slide 44: Shortest Path Routing
Dijkstra’s Algorithm
M = {s}
      For each n in N – {s}
        C(n) = l(s, n)
      while ( N  M)
        M = M  {w} such that C(w) is the minimum
        for all w in (N-M)
        For each n in (N-M)
        C(n) = MIN (C(n), C(w) + l(w, n))
Confirmed list
Tentative list
Newly added member to the confirmed list

## Slide 45: Open Shortest Path First (OSPF)
  OSPF Header Format OSPF Link State Advertisement
OSPF runs over IPv4 and IPv6 (does not use a transport protocol such
as UDP or TCP).
It encapsulates its data directly in IP packets with protocol number 89.

## Slide 46: Comparison of LS and DV algorithms
message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time varies
speed of convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network

## Slide 47
 | Distance Vector routing | Link State routing
Convergence time/Latency |  | ✅
Robustness to Loop |  | ✅
Processing overhead | ✅ | 
Bandwidth requirement (for control plane) | ✅ | 
Scalability (and robustness to complex topology and changes) |  | ✅

## Slide 48
Internet Protocol

## Slide 49
Pic courtesy: https://www.are.na/block/881873

## Slide 50: The Internet network layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 51: Internetworking
What is IP
  IP stands for Internet Protocol
  Key tool used today to build scalable, heterogeneous internetworks
  It runs on all the nodes in a collection of networks and defines the infrastructure that allows these nodes and networks to function as a single logical internetwork
  A simple internetwork showing the protocol layers

## Slide 52: IP Service Model
Packet Delivery Model
  Connectionless model for data delivery (packet switched)
  Best-effort delivery (unreliable service)
    packets are lost
    packets are delivered out of order
    duplicate copies of a packet are delivered
    packets can be delayed for a long time
Global Addressing Scheme
  Provides a way to identify all hosts in the network

## Slide 53
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP datagram format (i.e., Packet format)
Variable size header.
(20 bytes default
without options)
Variable size data.
Data size =
(Datagram Len – Header Len)

## Slide 54: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version number
(4 bits)
header length
in # of 4-bytes (4 bits)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
(real-time, non-real-time etc.)
max number remaining hops
(decremented at each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit, Min-MTU
discovery
for
fragmentation/
reassembly
Why header only?

## Slide 56: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
for
fragmentation/
reassembly

## Slide 57
IP Fragmentation and Reassembly

## Slide 58
Maximum Transmission Unit (MTU)
[packet size limit for the network layer]
R1
H5
H8
R2
R3
IP Fragmentation and Reassembly

## Slide 59
Rational behind the MTU limit:

## Slide 60
Rational behind the MTU limit:

## Slide 61
MTU=1500
(bytes)
MTU=1500
MTU=532
MTU=1500
Datagram Len=1500
Datagram Len=1500
?
R1
R2
R3
IP Fragmentation and Reassembly

## Slide 62
Analogy:

## Slide 63
MTU
Data
Header
Analogy:

## Slide 64
Analogy:

## Slide 65
Data index: 0
Analogy:

## Slide 66
Data index: 0
Data index: 0
Analogy:

## Slide 67
Data index: 0
Data index: 0
Data index: 13
Data index: 13
Analogy:

## Slide 68
Data index: 0
Data index: 0
Data index: 13
Data index: 13
Data index: 26
Data index: 26
Analogy:

## Slide 69
Data index: 0
Data index: 0
Data index: 13
Data index: 13
Data index: 26
Data index: 26
Analogy:
Fragmented
Fragmented
Fragmented & last

## Slide 70
Data index: 0
Data index: 13
Data index: 26
Analogy:
Fragmented
Fragmented
Fragmented & last
Data index: 0
Virtually infinite buffer
for reassembly
1
2
3
…

## Slide 71
Data index: 0
Data index: 13
Data index: 26
Analogy:
Fragmented
Fragmented
Fragmented & last
Data index: 0
Virtually infinite buffer
for reassembly
1
2
…
Data index: 13

## Slide 72
Data index: 0
Data index: 13
Data index: 26
Analogy:
Fragmented
Fragmented
Fragmented & last
Data index: 0
Virtually infinite buffer
for reassembly
1
2
…
Data index: 13

## Slide 73
Data index: 0
Data index: 13
Data index: 26
Analogy:
Fragmented
Fragmented
Fragmented & last
Data index: 0
Virtually infinite buffer
for reassembly
1
2
…
Data index: 26
Data index: 13

## Slide 74
Data index: 13
Analogy:
Data index: 0
Virtually infinite buffer
for reassembly
1
2
…
Data index: 26
Assembled packet
(The fragmentation and assembly process
Is transparent to the higher layers)

## Slide 75
MTU=1500
(bytes)
MTU=1500
MTU=532
MTU=1500
Datagram Len=1500
Datagram Len=1500
?
R1
R2
R3
IP Fragmentation and Reassembly

## Slide 76
MTU=1500
(bytes)
MTU=1500
MTU=532
MTU=1500
Datagram Len=1500
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
Where should reassembly take place?
R1
R2
R3
IP Fragmentation and Reassembly

## Slide 77
MTU=1500
(bytes)
MTU=1500
MTU=532
MTU=1500
Datagram Len=1500
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R1
R2
R3
IP Fragmentation and Reassembly
During assembly,
A. How can the destination identify all fragments of a packet?
Notes: RFC page 24: https://www.rfc-editor.org/rfc/rfc791
The internet identification field (ID) is used together with the source and destination address, and the protocol fields, to identify datagram fragments for reassembly.
Comments of the limited ID:
https://www.rfc-editor.org/rfc/rfc6864
Introduction
In IPv4, the Identification (ID) field is a 16-bit value that is unique for every datagram for a given source address, destination address, and protocol, such that it does not repeat within the maximum datagram lifetime (MDL) [RFC791] [RFC1122]. As currently specified, all datagrams between a source and destination of a given protocol must have unique IPv4 ID values over a period of this MDL, which is typically interpreted as two minutes and is related to the recommended reassembly timeout [RFC1122]. This uniqueness is currently specified as for all datagrams, regardless of fragmentation settings.
Uniqueness of the IPv4 ID is commonly violated by high-speed devices; if strictly enforced, it would limit the speed of a single protocol between two IP endpoints to 6.4 Mbps for typical MTUs of 1500 bytes (assuming a 2-minute MDL, using the analysis presented in [RFC4963]). It is common for a single connection to operate far in excess of these rates, which strongly indicates that the uniqueness of the IPv4 ID as specified is already moot. Further, some sources have been generating non-varying IPv4 IDs for many years (e.g., cellphones), which resulted in support for such in RObust Header Compression (ROHC) [RFC5225].
And
4.1. IPv4 ID Used Only for Fragmentation
Although RFC 1122 suggests that the IPv4 ID field has other uses, including datagram de-duplication, such uses are already not interoperable with known implementations of sources that do not vary their ID. This document thus defines this field's value only for fragmentation and reassembly:
>> The IPv4 ID field MUST NOT be used for purposes other than fragmentation and reassembly.
Datagram de-duplication can still be accomplished using hash-based duplicate detection for cases where the ID field is absent (IPv6 unfragmented datagrams), which can also be applied to IPv4 atomic datagrams without utilizing the ID field [RFC6621].

## Slide 78
MTU=1500
(bytes)
MTU=1500
MTU=532
MTU=1500
Datagram Len=1500
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R1
R2
R3
IP Fragmentation and Reassembly
During assembly,
B. How will the destination know if the last fragment is received?
Notes: RFC page 24: https://www.rfc-editor.org/rfc/rfc791
The internet identification field (ID) is used together with the source and destination address, and the protocol fields, to identify datagram fragments for reassembly.
If this is a whole datagram (that is both the fragment offset and the more fragments fields are zero), then it concludes that no fragmentation happened.

## Slide 79
Fragments
IP Fragmentation and Reassembly
Identifies the fragment location, relative to the beginning of the unfragmented data.
Fragments are counted in units of 8 octets (i.e., 8-bytes blocks).
0
2
Data from fgmt offset: 2
Notes: RFC page 24: https://www.rfc-editor.org/rfc/rfc791
The internet identification field (ID) is used together with the source and destination address, and the protocol fields, to identify datagram fragments for reassembly.
If this is a whole datagram (that is both the fragment offset and the more fragments fields are zero), then it concludes that no fragmentation happened.

## Slide 80
Fragments
IP Fragmentation and Reassembly
Identifies the fragment location, relative to the beginning of the unfragmented data.
Fragments are counted in units of 8 octets (i.e., 8-bytes blocks).
0
2
Data from fgmt offset: 2
Note that this offset numbers are
in “8-octet” not bytes.
Notes: RFC page 24: https://www.rfc-editor.org/rfc/rfc791
The internet identification field (ID) is used together with the source and destination address, and the protocol fields, to identify datagram fragments for reassembly.
If this is a whole datagram (that is both the fragment offset and the more fragments fields are zero), then it concludes that no fragmentation happened.

## Slide 81
110100010001101101110001011000000111101001
Bits
Byte-1
Byte-2
Byte-3
Byte-4
Bytes
8-Octets == 8 Bytes
Byte-1
Byte-2
Byte-3
Byte-4
Byte-5
Byte-6
Byte-7
Byte-8
Byte-9
Byte-10
“8-octet” - 1
“8-octet” - 2

## Slide 82
Data index: 0
Data index: 0
Data index: 13
Data index: 13
Data index: 26
Data index: 26
Analogy:
Data size should be integer multiple of
“8-octet” or “8 bytes”

## Slide 83
Data index: 0
Data index: 0
Data index: 13
Data index: 13
Data index: 26
Data index: 26
Analogy:
Data size should be integer multiple of
“8-octet” or “8 bytes”
…the last one can be smaller.

## Slide 84
MTU=1500
(bytes)
MTU=1500
MTU=532
MTU=1500
Datagram Len=1500
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R1
R2
R3
IP Fragmentation and Reassembly
During assembly,
C. How will the destination know how to rearrange the data?
D. How can the destination know if a packet is unfragmented/whole?
Identifies the fragment location, relative to the beginning of the unfragmented data.
Fragments are counted in units of 8 octets (i.e., 8-bytes blocks).
Notes: RFC page 24: https://www.rfc-editor.org/rfc/rfc791
The internet identification field (ID) is used together with the source and destination address, and the protocol fields, to identify datagram fragments for reassembly.
If this is a whole datagram (that is both the fragment offset and the more fragments fields are zero), then it concludes that no fragmentation happened.

## Slide 85
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | 
MF bit | 
F. off. | 
H. Len. | 
<D Len.> | 
Pkt Len | 
Original Packet
Frag. Pkt #1
Example: IP Fragmentation

## Slide 86
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 
H. Len. | 20
<D Len.> | 
Pkt Len | 532
Original Packet
Frag. Pkt #1
Max. Data Len. =
Max. Packet Len. – Header Len
Calculate in integer multiple of 8-octets (8 bytes block)
Example: IP Fragmentation

## Slide 87
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Original Packet
Frag. Pkt #1
Max. Data Len. =
Max. Packet Len. – Header Len
Calculate in integer multiple of 8-octets (8 bytes block)
(532-20) = 512
Example: IP Fragmentation

## Slide 88
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Original Packet
Frag. Pkt #1
Max. Data Len. =
Max. Packet Len. – Header Len
Calculate in integer multiple of 8-octets (8 bytes block)
(532-20) = 512
Example: IP Fragmentation

## Slide 89
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Original Packet
Frag. Pkt #1
Max. Data Len. =
Max. Packet Len. – Header Len
Calculate in integer multiple of 8-octets (8 bytes block)
(532-20) = 512
Starting 8-octet number
Example: IP Fragmentation

## Slide 90
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Original Packet
Frag. Pkt #1
Frag. Pkt #2
512 bytes/8 =
64 (in 8-octets)
Example: IP Fragmentation

## Slide 91
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Example: IP Fragmentation
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Original Packet
Frag. Pkt #1
Frag. Pkt #2
Frag. Pkt #3

## Slide 92
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Example: IP Reassembly
Data buffer
Header buffer

## Slide 93
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Data buffer
Header buffer
Header from
fgmt 1
(updated later)
Example: IP Reassembly

## Slide 94
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Data from fgmt 1
0
64
128
Data from fgmt 2
Data from fgmt 3
Data buffer
Header buffer
Header from
fgmt 1
(updated later)
Example: IP Reassembly
What if assembly is not possible?

## Slide 95
Thank you