## Slide 1
CMSC 417: Computer Networks
Nirupam Roy
M-W 2:00-3:15pm
CSI 2117
Spring 2026
Topic: Internetworking
(Textbook chapter 3)
Feb 18th, 2026

## Slide 2: The Internet “network layer”
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 3
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
peering link
Internet exchange point
IXP
The Internet: How far we learned

## Slide 4
ISP C
ISP B
ISP A
…
IXP
peering link
Internet exchange point
IXP
The Internet: How far we learned

## Slide 5
The Internet: How far we learned

## Slide 6
The Internet: How far we learned
To: Router-B
Router-A
Router-B

## Slide 7
The Internet: How far we learned
To: Router-B
Router-A
Router-B

## Slide 8
The Internet: How far we learned
To: Router-B
Router-A
Router-B

## Slide 9: The Internet “network layer”
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 10: The Internet “network layer”
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 11
IP: Internet Protocol

## Slide 12
Pic courtesy: https://www.are.na/block/881873
Network
Layer of
The Internet
Notes: IP is not the only protocol that makes the Network layer. There are other supporting protocols.

## Slide 13
Pic courtesy: https://www.are.na/block/881873
Routing protocols,
Address resolution protocols,
Error messaging protocols
Network
Layer of
The Internet

## Slide 14: Internetworking
What is IP
  IP stands for Internet Protocol
  Key tool used today to build scalable, heterogeneous internetworks
  It runs on all the nodes in a collection of networks and defines the infrastructure that allows these nodes and networks to function as a single logical internetwork
  A simple internetwork showing the protocol layers

## Slide 15: IP Service Model
Packet Delivery Model
  Connectionless model for data delivery
  Best-effort delivery (unreliable service)
    packets are lost
    packets are delivered out of order
    duplicate copies of a packet are delivered
    packets can be delayed for a long time
Global Addressing Scheme
  Provides a way to identify all hosts in the network

## Slide 16
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP datagram format (i.e., Packet format)
Variable size header.
(20 bytes default
without options)
Variable size data.
Data size =
(Datagram Len – Header Len)

## Slide 17: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version number
(4 bits)
header length
in # of 4-bytes (4 bits)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
(real-time, non-real-time etc.)
max number remaining hops
(decremented at each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit, Min-MTU
discovery
for
fragmentation/
reassembly
Why header only?
Notes: Header Fields (in order)
FieldSizePurposeVersion4 bitsIP version (4)IHL (Internet Header Length)4 bitsHeader length in 32-bit wordsDSCP/ECN (Type of Service)8 bitsQoS & congestion notificationTotal Length16 bitsEntire packet length (header + data)Identification16 bitsFragmentation reassemblyFlags3 bitsDF, MF control bitsFragment Offset13 bitsFragment positionTTL (Time To Live)8 bitsHop limitProtocol8 bitsUpper-layer protocol (TCP=6, UDP=17, ICMP=1)Header Checksum16 bitsHeader integrity checkSource Address32 bitsSender IPDestination Address32 bitsReceiver IPOptions + PaddingVariableOptional control information
In Internet Protocol version 4, the checksum:
Covers only the header (not payload)
Is 16 bits
Is recomputed at every router hop (because TTL changes)
It detects bit errors in the header.
Step-by-Step Calculation
Step 1: Set Checksum Field to Zero
Before computing, the checksum field is set to: 0x0000
Step 2: Divide Header into 16-bit Words
Step 3: Add Using One’s Complement Arithmetic
Step 4: Take One’s Complement
Why One’s Complement?
Properties:
Simple hardware implementation
Detects all 1-bit errors
Detects most multi-bit errors
Fast to compute

## Slide 19: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
for
fragmentation/
reassembly

## Slide 20
IP Fragmentation and Reassembly

## Slide 21
Maximum Transmission Unit (MTU)
[packet size limit for the network layer]
R1
H5
H8
R2
R3
IP Fragmentation and Reassembly

## Slide 22
Rational behind the MTU limit:

## Slide 23
Rational behind the MTU limit:

## Slide 24
MTU=1500
(bytes)
MTU=1500
MTU=532
MTU=1500
Datagram Len=1500
Datagram Len=1500
?
R1
R2
R3
IP Fragmentation and Reassembly

## Slide 25
Analogy:

## Slide 26
MTU
Data
Header
Analogy:

## Slide 27
Analogy:

## Slide 28
Data index: 0
Analogy:

## Slide 29
Data index: 0
Data index: 0
Analogy:

## Slide 30
Data index: 0
Data index: 0
Data index: 13
Data index: 13
Analogy:

## Slide 31
Data index: 0
Data index: 0
Data index: 13
Data index: 13
Data index: 26
Data index: 26
Analogy:

## Slide 32
Data index: 0
Data index: 0
Data index: 13
Data index: 13
Data index: 26
Data index: 26
Analogy:
Fragmented
Fragmented
Fragmented & last

## Slide 33
Data index: 0
Data index: 13
Data index: 26
Analogy:
Fragmented
Fragmented
Fragmented & last
Data index: 0
Virtually infinite buffer
for reassembly
1
2
3
…

## Slide 34
Data index: 0
Data index: 13
Data index: 26
Analogy:
Fragmented
Fragmented
Fragmented & last
Data index: 0
Virtually infinite buffer
for reassembly
1
2
…
Data index: 13

## Slide 35
Data index: 0
Data index: 13
Data index: 26
Analogy:
Fragmented
Fragmented
Fragmented & last
Data index: 0
Virtually infinite buffer
for reassembly
1
2
…
Data index: 13

## Slide 36
Data index: 0
Data index: 13
Data index: 26
Analogy:
Fragmented
Fragmented
Fragmented & last
Data index: 0
Virtually infinite buffer
for reassembly
1
2
…
Data index: 26
Data index: 13

## Slide 37
Data index: 13
Analogy:
Data index: 0
Virtually infinite buffer
for reassembly
1
2
…
Data index: 26
Assembled packet
(The fragmentation and assembly process
Is transparent to the higher layers)

## Slide 38
MTU=1500
(bytes)
MTU=1500
MTU=532
MTU=1500
Datagram Len=1500
Datagram Len=1500
?
R1
R2
R3
IP Fragmentation and Reassembly

## Slide 39
MTU=1500
(bytes)
MTU=1500
MTU=532
MTU=1500
Datagram Len=1500
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
Where should reassembly take place?
R1
R2
R3
IP Fragmentation and Reassembly

## Slide 40
MTU=1500
(bytes)
MTU=1500
MTU=532
MTU=1500
Datagram Len=1500
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R1
R2
R3
IP Fragmentation and Reassembly
During assembly,
A. How can the destination identify all fragments of a packet?
Notes: RFC page 24: https://www.rfc-editor.org/rfc/rfc791
The internet identification field (ID) is used together with the source and destination address, and the protocol fields, to identify datagram fragments for reassembly.
Comments of the limited ID:
https://www.rfc-editor.org/rfc/rfc6864
Introduction
In IPv4, the Identification (ID) field is a 16-bit value that is unique for every datagram for a given source address, destination address, and protocol, such that it does not repeat within the maximum datagram lifetime (MDL) [RFC791] [RFC1122]. As currently specified, all datagrams between a source and destination of a given protocol must have unique IPv4 ID values over a period of this MDL, which is typically interpreted as two minutes and is related to the recommended reassembly timeout [RFC1122]. This uniqueness is currently specified as for all datagrams, regardless of fragmentation settings.
Uniqueness of the IPv4 ID is commonly violated by high-speed devices; if strictly enforced, it would limit the speed of a single protocol between two IP endpoints to 6.4 Mbps for typical MTUs of 1500 bytes (assuming a 2-minute MDL, using the analysis presented in [RFC4963]). It is common for a single connection to operate far in excess of these rates, which strongly indicates that the uniqueness of the IPv4 ID as specified is already moot. Further, some sources have been generating non-varying IPv4 IDs for many years (e.g., cellphones), which resulted in support for such in RObust Header Compression (ROHC) [RFC5225].
And
4.1. IPv4 ID Used Only for Fragmentation
Although RFC 1122 suggests that the IPv4 ID field has other uses, including datagram de-duplication, such uses are already not interoperable with known implementations of sources that do not vary their ID. This document thus defines this field's value only for fragmentation and reassembly:
>> The IPv4 ID field MUST NOT be used for purposes other than fragmentation and reassembly.
Datagram de-duplication can still be accomplished using hash-based duplicate detection for cases where the ID field is absent (IPv6 unfragmented datagrams), which can also be applied to IPv4 atomic datagrams without utilizing the ID field [RFC6621].

## Slide 41
MTU=1500
(bytes)
MTU=1500
MTU=532
MTU=1500
Datagram Len=1500
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R1
R2
R3
IP Fragmentation and Reassembly
During assembly,
B. How will the destination know if the last fragment is received?
Notes: RFC page 24: https://www.rfc-editor.org/rfc/rfc791
The internet identification field (ID) is used together with the source and destination address, and the protocol fields, to identify datagram fragments for reassembly.
If this is a whole datagram (that is both the fragment offset and the more fragments fields are zero), then it concludes that no fragmentation happened.

## Slide 42
Fragments
IP Fragmentation and Reassembly
Identifies the fragment location, relative to the beginning of the unfragmented data.
Fragments are counted in units of 8 octets (i.e., 8-bytes blocks).
0
2
Data from fgmt offset: 2
Notes: RFC page 24: https://www.rfc-editor.org/rfc/rfc791
The internet identification field (ID) is used together with the source and destination address, and the protocol fields, to identify datagram fragments for reassembly.
If this is a whole datagram (that is both the fragment offset and the more fragments fields are zero), then it concludes that no fragmentation happened.

## Slide 43
Fragments
IP Fragmentation and Reassembly
Identifies the fragment location, relative to the beginning of the unfragmented data.
Fragments are counted in units of 8 octets (i.e., 8-bytes blocks).
0
2
Data from fgmt offset: 2
Note that this offset numbers are
in “8-octet” not bytes.
Notes: RFC page 24: https://www.rfc-editor.org/rfc/rfc791
The internet identification field (ID) is used together with the source and destination address, and the protocol fields, to identify datagram fragments for reassembly.
If this is a whole datagram (that is both the fragment offset and the more fragments fields are zero), then it concludes that no fragmentation happened.

## Slide 44
110100010001101101110001011000000111101001
Bits
Byte-1
Byte-2
Byte-3
Byte-4
Bytes
8-Octets == 8 Bytes
Byte-1
Byte-2
Byte-3
Byte-4
Byte-5
Byte-6
Byte-7
Byte-8
Byte-9
Byte-10
“8-octet” - 1
“8-octet” - 2

## Slide 45
Data index: 0
Data index: 0
Data index: 13
Data index: 13
Data index: 26
Data index: 26
Analogy:
Data size should be integer multiple of
“8-octet” or “8 bytes”

## Slide 46
Data index: 0
Data index: 0
Data index: 13
Data index: 13
Data index: 26
Data index: 26
Analogy:
Data size should be integer multiple of
“8-octet” or “8 bytes”
…the last one can be smaller.

## Slide 47
MTU=1500
(bytes)
MTU=1500
MTU=532
MTU=1500
Datagram Len=1500
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R1
R2
R3
IP Fragmentation and Reassembly
During assembly,
C. How will the destination know how to rearrange the data?
D. How can the destination know if a packet is unfragmented/whole?
Identifies the fragment location, relative to the beginning of the unfragmented data.
Fragments are counted in units of 8 octets (i.e., 8-bytes blocks).
Notes: RFC page 24: https://www.rfc-editor.org/rfc/rfc791
The internet identification field (ID) is used together with the source and destination address, and the protocol fields, to identify datagram fragments for reassembly.
If this is a whole datagram (that is both the fragment offset and the more fragments fields are zero), then it concludes that no fragmentation happened.

## Slide 48
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | 
MF bit | 
F. off. | 
H. Len. | 
<D Len.> | 
Pkt Len | 
Original Packet
Frag. Pkt #1
Example: IP Fragmentation

## Slide 49
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 
H. Len. | 20
<D Len.> | 
Pkt Len | 532
Original Packet
Frag. Pkt #1
Max. Data Len. =
Max. Packet Len. – Header Len
Calculate in integer multiple of 8-octets (8 bytes block)
Example: IP Fragmentation

## Slide 50
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Original Packet
Frag. Pkt #1
Max. Data Len. =
Max. Packet Len. – Header Len
Calculate in integer multiple of 8-octets (8 bytes block)
(532-20) = 512
Example: IP Fragmentation

## Slide 51
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Original Packet
Frag. Pkt #1
Max. Data Len. =
Max. Packet Len. – Header Len
Calculate in integer multiple of 8-octets (8 bytes block)
(532-20) = 512
Example: IP Fragmentation

## Slide 52
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Original Packet
Frag. Pkt #1
Max. Data Len. =
Max. Packet Len. – Header Len
Calculate in integer multiple of 8-octets (8 bytes block)
(532-20) = 512
Starting 8-octet number
Example: IP Fragmentation

## Slide 53
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Original Packet
Frag. Pkt #1
Frag. Pkt #2
512 bytes/8 =
64 (in 8-octets)
Example: IP Fragmentation

## Slide 54
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Example: IP Fragmentation
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Original Packet
Frag. Pkt #1
Frag. Pkt #2
Frag. Pkt #3

## Slide 55
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Example: IP Reassembly
Data buffer
Header buffer

## Slide 56
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Data buffer
Header buffer
Header from
fgmt 1
(updated later)
Example: IP Reassembly

## Slide 57
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Data from fgmt 1
0
64
128
Data from fgmt 2
Data from fgmt 3
Data buffer
Header buffer
Header from
fgmt 1
(updated later)
Example: IP Reassembly
What if assembly is not possible?

## Slide 58: Network Addresses

## Slide 59: IP Address (IPv4)
A unique 32-bit number
Identifies an interface (on a host, on a router, …)
Represented in dotted-quad notation
00001100
00100010
10011110
00000101
12
34
158
5
12:34:158:5

## Slide 60: Grouping Related Hosts
The Internet is an “inter-network”
  Used to connect networks together, not hosts
  Need to address a network (i.e., group of hosts)
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
LAN = Local Area Network
WAN = Wide Area Network

## Slide 61: Scalability Challenge
Suppose hosts had arbitrary addresses
  Then every router would need a lot of information
  …to know how to direct packets toward every host
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
5.6.7.8
2.4.6.8
1.2.3.5
5.6.7.9
2.4.6.9
1.2.3.4
1.2.3.5
forwarding table

## Slide 62: Hierarchical Addressing: IP Prefixes
Network and host portions (left and right)
00001100
00100010
10011110
00000101
Network (24 bits)
Host (8 bits)
12
34
158
5
(N bits)
(32-N bits)

## Slide 63: Hierarchical Addressing in U.S. Mail
Addressing in the U.S. mail
  Zip code: 08540
  Building: 35 Olden Street
  Room in building: 306
  Name of occupant: Jennifer Rexford
Forwarding the U.S. mail
  Deliver to the post office in the zip code
  Assign to mailman covering the building
  Drop letter into mailbox for building/room
  Give letter to the appropriate person
???

## Slide 64: Easy to Add New Hosts
No need to update the routers
  E.g., adding a new host 5.6.7.213 on the right
  Doesn’t require adding a new forwarding-table entry
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table
host
5.6.7.213

## Slide 65: Hierarchical Addressing: IP Prefixes
Network and host portions (left and right)
00001100
00100010
10011110
00000101
Network (24 bits)
Host (8 bits)
12
34
158
5
(N bits)
(32-N bits)

## Slide 66: Hierarchical Addressing: IP Prefixes
Network and host portions (left and right)
00001100
00100010
10011110
00000101
Network (24 bits)
Host (8 bits)
12
34
158
5
(N bits)
(32-N bits)
N = ?

## Slide 67: “Classes” of networks
The sizes of networks can be different
host
host
host
LAN 1
...
host
host
LAN 2
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
1.2.3.0/24
5.6.7.0/24
forwarding table
Large networks (many hosts)
Fewer such networks exist
Small networks (fewer hosts)
Many such networks exist

## Slide 68: Class-full addressing

## Slide 69
Picture courtesy: https://www.geeksforgeeks.org/introduction-of-classful-ip-addressing/
How can you tell network class from the IP address?

## Slide 70
Picture courtesy: https://www.ictshore.com/free-ccna-course/network-layer-ipv4-addressing/attachment/1013-05-classful_addressing/
What percentage of addresses and allocated to each class?

## Slide 71: Global Addresses
Properties
  globally unique
  hierarchical: network + host
  4 Billion IP address, half are A type, ¼ is B type, and 1/8 is C type
Format
Dot notation
  10.3.2.4
  128.96.33.81
  192.12.69.77

## Slide 72
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Let’s assume we have 4-bit address (instead of 32 bit)
Class A (Half of all possible addresses)
Class B (1/4 of all possible addresses)
Class C (1/8 of all possible addresses)

## Slide 73
0000
0001
0010
0011
0100
0101
0110
0111
Let’s assume we have 4-bit address (instead of 32 bit)
Class A (Half of all possible addresses)
Say, 1 bit for network part = 2 different networks
Say, 2 bits for host part = 4 hosts per network

## Slide 74: Global Addresses
Properties
  globally unique
  hierarchical: network + host
  4 Billion IP address, half are A type, ¼ is B type, and 1/8 is C type
Format
Dot notation
  10.3.2.4
  128.96.33.81
  192.12.69.77

## Slide 75: Classful Addressing
In the olden days, only fixed allocation sizes
  Class A: 0*
    Very large /8 blocks (e.g., MIT has 18.0.0.0/8)
    There can be 126 different class A networks (0 and 127 values are reserved) and (224-2) different hosts (2 values are reserved)
  Class B: 10*
    Large /16 blocks (e.g,. Princeton has 128.112.0.0/16)
  Class C: 110*
    Small /24 blocks (e.g., AT&T Labs has 192.20.225.0/24)
    221 different networks possible, 254 hosts (255 is reserved for broadcast and 0 is reserved)
  Class D: 1110* for multicast groups
  Class E: 11110* reserved for future use
This is why folks use dotted-quad notation!

## Slide 76: IP Datagram Forwarding
Strategy
  every datagram contains destination's address
  if directly connected to destination network, then forward to host
  if not directly connected to destination network, then forward to some router
  forwarding table maps network number into next hop
  each host has a default router
  each router maintains a forwarding table
Example (router R2)

## Slide 77: IP Datagram Forwarding
Algorithm
if (NetworkNum of destination = NetworkNum of one of my interfaces) then
deliver packet to destination over that interface
else
if (NetworkNum of destination is in my forwarding table) then
deliver packet to NextHop router
else
deliver packet to default router
First: find the NetworkNum. How?

## Slide 78: IP Datagram Forwarding
Algorithm
if (NetworkNum of destination = NetworkNum of one of my interfaces) then
deliver packet to destination over that interface
else
if (NetworkNum of destination is in my forwarding table) then
deliver packet to NextHop router
else
deliver packet to default router
For a host with only one interface and only a default router in its forwarding table, this simplifies to
if (NetworkNum of destination = my NetworkNum)then
deliver packet to destination directly
else
deliver packet to default router

## Slide 79: Obtaining a Block of Addresses
Internet Corporation for Assigned Names and Numbers (ICANN)
  Allocates large blocks to Regional Internet Registries
Regional Internet Registries (RIRs)
  E.g., ARIN (American Registry for Internet Numbers)
  Allocates to ISPs and large institutions
Internet Service Providers (ISPs)
  Allocate address blocks to their customers
  Who may, in turn, allocate to their customers…

## Slide 80
Obtaining a Block of Addresses
Your organization: XYZ
Maximum # of hosts is estimated to be 10 millions.
What class of IP address will you request for?
Maximum # of hosts is estimated to be 64K ?
Maximum # of hosts is estimated to be 250?
Maximum # of hosts is estimated to be 100?
Maximum # of hosts is estimated to be 20?
Maximum # of hosts is estimated to be 300?
Maximum # of hosts is estimated to be 66K?
Notes: Class A can have 16 millions (16777214 = 2^24-2)
Class B can have 65K (65534 = 2^16 - 2)
Class C can have 254 (2^8-2)

## Slide 81
Problems with the classes of addresses
Wastage of addresses
Bigger tables to look up at routers

## Slide 82
Thank you