## Slide 1
CMSC 417: Computer Networks
Nirupam Roy
M-W 2:00-3:15pm
CSI 2117
Spring 2026
Topic: Internetworking
(Textbook chapter 3)
Feb 23rd, 2026

## Slide 2
Pic courtesy: https://www.are.na/block/881873
Routing protocols,
Address resolution protocols,
Error messaging protocols
Network
Layer of
The Internet

## Slide 3: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version number
(4 bits)
header length
in # of 4-bytes (4 bits)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
(real-time, non-real-time etc.)
max number remaining hops
(decremented at each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit, Min-MTU
discovery
for
fragmentation/
reassembly
Why header only?
Notes: Header Fields (in order)
FieldSizePurposeVersion4 bitsIP version (4)IHL (Internet Header Length)4 bitsHeader length in 32-bit wordsDSCP/ECN (Type of Service)8 bitsQoS & congestion notificationTotal Length16 bitsEntire packet length (header + data)Identification16 bitsFragmentation reassemblyFlags3 bitsDF, MF control bitsFragment Offset13 bitsFragment positionTTL (Time To Live)8 bitsHop limitProtocol8 bitsUpper-layer protocol (TCP=6, UDP=17, ICMP=1)Header Checksum16 bitsHeader integrity checkSource Address32 bitsSender IPDestination Address32 bitsReceiver IPOptions + PaddingVariableOptional control information
In Internet Protocol version 4, the checksum:
Covers only the header (not payload)
Is 16 bits
Is recomputed at every router hop (because TTL changes)
It detects bit errors in the header.
Step-by-Step Calculation
Step 1: Set Checksum Field to Zero
Before computing, the checksum field is set to: 0x0000
Step 2: Divide Header into 16-bit Words
Step 3: Add Using One’s Complement Arithmetic
Step 4: Take One’s Complement
Why One’s Complement?
Properties:
Simple hardware implementation
Detects all 1-bit errors
Detects most multi-bit errors
Fast to compute

## Slide 4
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Original Packet
Frag. Pkt #1
Frag. Pkt #2
512 bytes/8 =
64 (in 8-octets)
Example: IP Fragmentation

## Slide 5
MTU=1500
MTU=532
Datagram Len=1500
Dgram Len<=532
Dgram Len<=532
Dgram Len<=532
Fragments
R2
Example: IP Fragmentation
Header field/<info> | Value
P. Identifier | XYZ
More Frag. bit | 0
Frag. offset | 0
Header Len. | 20 (bytes)
<Data Len.> | 1400
Packet Length | 1420
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Original Packet
Frag. Pkt #1
Frag. Pkt #2
Frag. Pkt #3

## Slide 6
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Example: IP Reassembly
Data buffer
Header buffer

## Slide 7
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Data buffer
Header buffer
Header from
fgmt 1
(updated later)
Example: IP Reassembly

## Slide 8
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 0
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 1
F. off. | 64
H. Len. | 20
<D Len.> | 512
Pkt Len | 532
Fields | Val.
P. Id | XYZ
MF bit | 0
F. off. | 128
H. Len. | 20
<D Len.> | 376
Pkt Len | 396
Data from fgmt 1
0
64
128
Data from fgmt 2
Data from fgmt 3
Data buffer
Header buffer
Header from
fgmt 1
(updated later)
Example: IP Reassembly
What if assembly is not possible?

## Slide 9
3. Fragmentation of fragmentation
1. The packet “Identifier”
4. Assembly of mixed fragmentation of different size
(possibly from different paths)
IP Fragmentation-Reassembly: Q&A
2. Does fragmentation and reassembly set a new limit on the total
packet size? Is it consistent with “packet length” header field?
RFC 791, page 24: https://www.rfc-editor.org/rfc/rfc791

## Slide 10
1. The packet “Identifier”
In IPv4, the Identification (ID) field is a 16-bit value that is unique for every datagram for a given source address, destination address, and protocol, such that it does not repeat within the maximum datagram lifetime (MDL) [RFC791] [RFC1122]. As currently specified, all datagrams between a source and destination of a given protocol must have unique IPv4 ID values over a period of this MDL, which is typically interpreted as two minutes and is related to the recommended reassembly timeout [RFC1122]. This uniqueness is currently specified as for all datagrams, regardless of fragmentation settings.
What can violate the uniqueness of the “identifier”?

## Slide 11
2. Does fragmentation and reassembly set a new limit on the total
packet size? Is it consistent with “packet length” header field?
Notes: Packet length = 2^16
Fragment offet = 2^13 + 2^3 (because of 8 byte blocks, 8 = 2^3) = 16 bit of coverage.

## Slide 12
3. Fragmentation of fragmentation
How “More Fragments (MF)” flag is decided?
How “fragment offset” is calculated?
Notes: 1)
All newly created sub-fragments except the last one get MF = 1.
The last sub-fragment inherits the MF value of the original fragment being split.
2) New fragment offset = original fragment offset + (local byte shift ÷ 8)

## Slide 13
4. Assembly of mixed fragmentation of different size
(possibly from different paths)
“Fragment offsets” always represent the absolute position of a data-fragment relative to the original (unfragmented) packet.
The last fragment decides the total data size in the reassembly process.
Reassembly fails only if there are missing data before the timer goes off. (Recommended initial value for the time is 15 seconds)

## Slide 14: Network Addresses

## Slide 15: IP Address (IPv4)
A unique 32-bit number
Identifies an interface (on a host, on a router, …)
Represented in dotted-quad notation
00001100
00100010
10011110
00000101
12
34
158
5
12:34:158:5

## Slide 16: Grouping Related Hosts
The Internet is an “inter-network”
  Used to connect networks together, not hosts
  Need to address a network (i.e., group of hosts)
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
LAN = Local Area Network
WAN = Wide Area Network

## Slide 17: Scalability Challenge
Suppose hosts had arbitrary addresses
  Then every router would need a lot of information
  …to know how to direct packets toward every host
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
5.6.7.8
2.4.6.8
1.2.3.5
5.6.7.9
2.4.6.9
1.2.3.4
1.2.3.5
forwarding table

## Slide 18: Hierarchical Addressing: IP Prefixes
Network and host portions (left and right)
00001100
00100010
10011110
00000101
Network (24 bits)
Host (8 bits)
12
34
158
5
(N bits)
(32-N bits)

## Slide 19: Hierarchical Addressing in U.S. Mail
Addressing in the U.S. mail
  Zip code: 08540
  Building: 35 Olden Street
  Room in building: 306
  Name of occupant: Jennifer Rexford
Forwarding the U.S. mail
  Deliver to the post office in the zip code
  Assign to mailman covering the building
  Drop letter into mailbox for building/room
  Give letter to the appropriate person
???

## Slide 20: Easy to Add New Hosts
No need to update the routers
  E.g., adding a new host 5.6.7.213 on the right
  Doesn’t require adding a new forwarding-table entry
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table
host
5.6.7.213

## Slide 21: Hierarchical Addressing: IP Prefixes
Network and host portions (left and right)
00001100
00100010
10011110
00000101
Network (24 bits)
Host (8 bits)
12
34
158
5
(N bits)
(32-N bits)

## Slide 22: Hierarchical Addressing: IP Prefixes
Network and host portions (left and right)
00001100
00100010
10011110
00000101
Network (24 bits)
Host (8 bits)
12
34
158
5
(N bits)
(32-N bits)
N = ?

## Slide 23: “Classes” of networks
The sizes of networks can be different
host
host
host
LAN 1
...
host
host
LAN 2
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
1.2.3.0/24
5.6.7.0/24
forwarding table
Large networks (many hosts)
Fewer such networks exist
Small networks (fewer hosts)
Many such networks exist

## Slide 24: Class-full addressing

## Slide 25
Picture courtesy: https://www.geeksforgeeks.org/introduction-of-classful-ip-addressing/
How can you tell network class from the IP address?

## Slide 26
Picture courtesy: https://www.ictshore.com/free-ccna-course/network-layer-ipv4-addressing/attachment/1013-05-classful_addressing/
What percentage of addresses and allocated to each class?

## Slide 27: Global Addresses
Properties
  globally unique
  hierarchical: network + host
  4 Billion IP address, half are A type, ¼ is B type, and 1/8 is C type
Format
Dot notation
  10.3.2.4
  128.96.33.81
  192.12.69.77

## Slide 28
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Let’s assume we have 4-bit address (instead of 32 bit)
Class A (Half of all possible addresses)
Class B (1/4 of all possible addresses)
Class C (1/8 of all possible addresses)

## Slide 29
0000
0001
0010
0011
0100
0101
0110
0111
Let’s assume we have 4-bit address (instead of 32 bit)
Class A (Half of all possible addresses)
Say, 1 bit for network part = 2 different networks
Say, 2 bits for host part = 4 hosts per network

## Slide 30: Global Addresses
Properties
  globally unique
  hierarchical: network + host
  4 Billion IP address, half are A type, ¼ is B type, and 1/8 is C type
Format
Dot notation
  10.3.2.4
  128.96.33.81
  192.12.69.77

## Slide 31: Classful Addressing
In the olden days, only fixed allocation sizes
  Class A: 0*
    Very large /8 blocks (e.g., MIT has 18.0.0.0/8)
    There can be 126 different class A networks (0 and 127 values are reserved) and (224-2) different hosts (2 values are reserved)
  Class B: 10*
    Large /16 blocks (e.g,. Princeton has 128.112.0.0/16)
  Class C: 110*
    Small /24 blocks (e.g., AT&T Labs has 192.20.225.0/24)
    221 different networks possible, 254 hosts (255 is reserved for broadcast and 0 is reserved)
  Class D: 1110* for multicast groups
  Class E: 11110* reserved for future use
This is why folks use dotted-quad notation!

## Slide 32: IP Datagram Forwarding
Strategy
  every datagram contains destination's address
  if directly connected to destination network, then forward to host
  if not directly connected to destination network, then forward to some router
  forwarding table maps network number into next hop
  each host has a default router
  each router maintains a forwarding table
Example (router R2)

## Slide 33: IP Datagram Forwarding
R1
R2
R3
I-0
I-1
Forwarding table at R2

## Slide 34: IP Datagram Forwarding
R1
R2
R3
I-0
I-1
Forwarding table at R2
IP data packet (datagram)

## Slide 35: IP Datagram Forwarding
Algorithm
if (NetworkNum of destination = NetworkNum of one of my interfaces) then
deliver packet to destination over that interface
else
if (NetworkNum of destination is in my forwarding table) then
deliver packet to NextHop router
else
deliver packet to default router
First: find the NetworkNum. How?
R1
R2
R3
I-0
I-1
Forwarding table at R2

## Slide 36: IP Datagram Forwarding
Algorithm
if (NetworkNum of destination = NetworkNum of one of my interfaces) then
deliver packet to destination over that interface
else
if (NetworkNum of destination is in my forwarding table) then
deliver packet to NextHop router
else
deliver packet to default router
First: find the NetworkNum. How?

## Slide 37: IP Datagram Forwarding
Algorithm
if (NetworkNum of destination = NetworkNum of one of my interfaces) then
deliver packet to destination over that interface
else
if (NetworkNum of destination is in my forwarding table) then
deliver packet to NextHop router
else
deliver packet to default router
For a host with only one interface and only a default router in its forwarding table, this simplifies to
if (NetworkNum of destination = my NetworkNum)then
deliver packet to destination directly
else
deliver packet to default router

## Slide 38: Obtaining a Block of Addresses
Internet Corporation for Assigned Names and Numbers (ICANN)
  Allocates large blocks to Regional Internet Registries
Regional Internet Registries (RIRs)
  E.g., ARIN (American Registry for Internet Numbers)
  Allocates to ISPs and large institutions
Internet Service Providers (ISPs)
  Allocate address blocks to their customers
  Who may, in turn, allocate to their customers…

## Slide 39
Obtaining a Block of Addresses
Your organization: XYZ
Maximum # of hosts is estimated to be 10 millions.
What class of IP address will you request for?
Maximum # of hosts is estimated to be 64K ?
Maximum # of hosts is estimated to be 250?
Maximum # of hosts is estimated to be 100?
Maximum # of hosts is estimated to be 20?
Maximum # of hosts is estimated to be 300?
Maximum # of hosts is estimated to be 66K?
Notes: Class A can have 16 millions (16777214 = 2^24-2)
Class B can have 65K (65534 = 2^16 - 2)
Class C can have 254 (2^8-2)

## Slide 40
Problems with the classes of addresses
Wastage of addresses
Bigger tables to look up at routers

## Slide 41: Subnetting

## Slide 42
Router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
223.1.1.6
ISP
The ISP provided the network address space: 223.1.1.X

## Slide 43
Router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
223.1.1.6
ISP
The ISP provided the network address space: 223.1.1.X
223.1.2.X
223.1.3.X

## Slide 44
Router
The ISP provided the network address space: 223.1.1.X
Two separate networks are needed. How can we assign addresses to these “sub” networks?

## Slide 45
Router
The ISP provided the network address space: 223.1.1.X

## Slide 46
Router
The ISP provided the network address space: 223.1.1.X
Use subnetting

## Slide 47
Router
The ISP provided the network address space: 223.1.1.X
11011111.00000001.00000001.XXXXXXX
Use part of the host bits to identify separate subnets.

## Slide 48
Router
The ISP provided the network address space: 223.1.1.X
11011111.00000001.00000001.XXXXXXX
Use part of the host bits to identify separate subnets.
11011111.00000001.00000001.0XXXXXX
11011111.00000001.00000001.1XXXXXX
Subnet mask = 11111111. 11111111. 11111111.10000000

## Slide 49: Subnetting
Add another level to address/routing hierarchy: subnet
Subnet masks define variable partition of host part of class A and B addresses
Subnets visible only within site
“Bitwise and”

## Slide 50: Subnetting
Forwarding Table at Router R1

## Slide 51: Subnetting
Forwarding Table at Router R1
Forwarding Algorithm
D = destination IP address
for each entry < SubnetNum, SubnetMask, NextHop>
  D1 = SubnetMask & D
  if D1 = SubnetNum
    if NextHop is an interface
    deliver datagram directly to destination
    else
    deliver datagram to NextHop (a router)

## Slide 52: Subnetting
Notes
Would use a default router if nothing matches
Not necessary for all ones in subnet mask to be contiguous
Can put multiple subnets on one physical network
Subnets not visible from the rest of the Internet

## Slide 53
Subnets “toy” example

## Slide 54
Address space assigned to you:

## Slide 55
30 hosts max.
22 hosts max.
18 hosts max.

## Slide 58: Class-less Interdomain Routing (CIDR)
Generalizes the ideas of subnetting

## Slide 59
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0

## Slide 60
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
223.1.1.128
223.1.1.192
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0

## Slide 61
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
223.1.1.128
223.1.1.192
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0
223.1.2.0
223.1.3.0
Lesson 1:
Address classes are not needed. Mask can define the number of bits for the network part.
Lesson 2:
Network hierarchies can be hidden from the outside world.
Network addresses can be aggregated/summarized/combined

## Slide 62: CIDR: Classless address

## Slide 63
CIDR: Classless InterDomain Routing
  Network portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
200.23.16.0–200.23.17.255
IP addressing: CIDR
This X bit network part is often called Prefix or Network-prefix

## Slide 64
IP addressing: CIDR
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
forwarding table
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address

## Slide 65: CIDR: Super-netting/ Route aggregation

## Slide 66
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Forwarding tab.
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.0.0/16

## Slide 67
Lessons learned from subnetting
ISP
223.1.1.0
223.1.2.0
223.1.3.0
Forwarding tab.
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Forwarding tab.
223.1.0.0/16
223.1.0.0/16

## Slide 68
200.20.0.0/24
200.20.1.0/24
200.20.2.0/24

## Slide 69
200.20.0.0/24
200.20.1.0/24
200.20.2.0/24

## Slide 70
200.20.0.0/24
200.20.1.0/24
200.20.2.0/24
Route aggregation

## Slide 71
Route aggregation with CIDR

## Slide 72: Classless Inter-Domain Routing (CIDR)
IP Address : 12.4.0.0 IP Mask: 255.254.0.0
00001100
00000100
00000000
00000000
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network.
Network number = IP address + Mask
Written as 12.4.0.0/15

## Slide 73: Hierarchical Address Allocation
Hierarchy is key to scalability
  Address allocated in contiguous chunks (prefixes)
  Today, the Internet has about 1,132,452 prefixes
12.0.0.0/8
12.0.0.0/16
12.254.0.0/16
12.1.0.0/16
12.2.0.0/16
12.3.0.0/16
:
:
:
12.3.0.0/24
12.3.1.0/24
:
:
12.3.254.0/24
12.253.0.0/19
12.253.32.0/19
12.253.160.0/19
:
:
:
:
:
  (March 4, 2025. Source: https://ipv4.bgp.he.net/report/netstats)

## Slide 74: Separate Forwarding Entry Per Prefix
Prefix-based forwarding
  Map the destination address to matching prefix
  Forward to the outgoing interface
host
host
host
LAN 1
...
host
host
host
LAN
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 75
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1

## Slide 76
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homing

## Slide 77
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homing
Forwarding tab.

## Slide 78
CIDR Makes Packet Forwarding Harder
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homing
Forwarding tab.
201.10.0.0/21
201.10.6.0/23

## Slide 79
11001001.00001010.00000000.00000000/21
11001001.00001010.00000110.00000000/23
11001001.00001010.00000110.00010001
A packet with dest. Addr.: 201.10.6.17
201.10.0.0/21
201.10.6.0/23
CIDR Makes Packet Forwarding Harder
Forwarding table

## Slide 80: CIDR Makes Packet Forwarding Harder
Forwarding table may have many matches
  E.g., entries for 201.10.0.0/21 and 201.10.6.0/23
  The IP address 201.10.6.17 would match both!
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2

## Slide 81: Longest Prefix Match Forwarding
Destination-based forwarding
  Packet has a destination address
  Router identifies longest-matching prefix
  Cute algorithmic problem: very fast lookups
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
201.10.6.17
destination
forwarding table
outgoing link

## Slide 82: Getting an IP address: DHCP Protocol

## Slide 83
Thank you